# Document Change Notice (DCN) Title:  ETM & ITM ROC Specification Change

| Document No. Doc-Rev | Title | New Rev |
| --- | --- | --- |
| E080512-v2 | Advanced LIGO End Test Mass (ETM) | v3 |
| D080658-v2 | ETM substrate | v3 |
| E080511-v2 | Advanced LIGO Input Test mass (ITM) | v3 |
| D080657-v2 | ITM Substrate | v3 |
| (Continue on sheet 2 if needed) |

CHANGE DESCRIPTION (FROM/TO) – Continue on next sheet if needed:

See sheet 2

REASON FOR CHANGE: Changing the Radii of Curvature (ROC) specification of the Test Masses to call out a ROC precision as well as an absolute range.

ACTION:                 Incorporate Change        Attach DCN to Drawings           Other Action (specify):

DISPOSITION OF HARDWARE
(IDENTIFY SERIAL NUMBERS)

DCN DISTRIBUTION

Required:

excomm (Lab Grp Leads, LSC Spokesperson)

Michael Landry (LHO AdL Liaison)

Brian O'Reilly (LLO AdL Liaison)

Bill Tyler (Lab Safety & QA)

| Recommended (AdL Area/Subsys Leads & Cog. Sci./Eng., subsystem email distribution lists): [please delete if/as appropriate for this DCN] |
| --- |
|  |  | GariLynn Billingsley |
|  |  | Bill Kells |
|  | Mike Smith |  |
| Phil Willems | Benno Willke |  |
|  | aligo_sys | aligo_aos |
| aligo_coc | aligo_io | aligo_isc |

Additional Distribution List for this DCN:

SAFETY, COST, SCHEDULE, REQUIREMENTS IMPACT?           NO           YES

(If YES, enter CR (CCB) or TCP (TRB) #)

Other disposition/instructions or additional comments:

List S/Ns to be retested per this change:

| APPROVALS: | DATE | OTHER APPROVALS (SPECIFY) | DATE |
| --- | --- | --- | --- |
| ORIGINATOR: G Billingsley | 3-26-09 |  |  |
| TASK LEADER: G Billingsley | 3-26-09 |  |  |
| GROUP LEADER: D Coyne | 3-26-09 |  |  |
| DCC RELEASE: see QA/approval setting in DCC |  |  |

List S/Ns to be reworked/scrapped:

List S/N’s to be built with this change: all

No hardware was affected (record change only):

List S/Ns which comply already:

CHANGE DESCRIPTION (FROM/TO) -- continued:

ITM E080511-v2 
FROM 
Optical Surface Figure, measured over the central 160 mm diameter 
Surface 1: Spherical, concave. Radius of curvature: 1934m ± 3m. 

TO - V3 
Optical Surface Figure, measured over the central 160 mm diameter 
Surface 1: Spherical, concave. Radius of curvature (R): 1934 m -5, +15 m absolute accuracy 
ROC precision: R ± 3 m where 1929 m </= R </= 1949 m for all ITM optics 



Similarly 
ETM E080512-V2 
FROM 
Optical Surface Figure, measured over the central 160 mm diameter 
Surface 1: Spherical, concave. Radius of curvature: 2245 m ± 3 m.

TO - V3 
Optical Surface Figure, measured over the central 160 mm diameter 
Surface 1: Spherical, concave. Radius of curvature (R): 2245 m -5, +15 m absolute accuracy 
ROC precision: R ± 3 m where 2240 m </= R </= 2260 m for all ETM optics

D080657 and D080658: updated to include references to version -v3 of the associated polishing specification. No other changes