LIGO Laboratory / LIGO Scientific Collaboration

LIGO-T0900229-v2	Advanced LIGO UK         2 June 2009

Quad Monitor Board Test Plan

R. M. Cutler, University of Birmingham

Distribution of this document:

Inform aligo_sus

This is an internal working note

of the Advanced LIGO Project, prepared by members of the UK team.

| Institute for Gravitational Research University of Glasgow Phone +44 (0) 141 330 5884 Fax +44 (0) 141 330 6833 E-mail k.strain@physics.gla.ac.uk | School of Physics and Astronomy University of Birmingham Phone +44 (0) 121 414 6447 Fax +44 (0) 121 414 3722 E-mail av@star.sr.bham.ac.uk |
| --- | --- |
| Engineering Department CCLRC Rutherford Appleton Laboratory Phone +44 (0) 1235 445 297 Fax +44 (0) 1235 445 843 E-mail J.Greenhalgh@rl.ac.uk | Department of Physics University of Strathclyde Phone +44 (0) 1411 548 3360 Fax +44 (0) 141 552 2891 E-mail N.Lockerbie@phys.strath.ac.uk |

http://www.ligo.caltech.edu/

http://www.physics.gla.ac.uk/igr/sus/

http://www.sr.bham.ac.uk/research/gravity/rh,d,2.html

http://www.eng-external.rl.ac.uk/advligo/papers_public/ALUK_Homepage.htm

QUAD MONITOR BOARD TEST PLAN

Serial No …………………………………...

Test Engineer ………………………………

Date …………………………………………

Contents

1. Block diagram

2. Test equipment

3. Description

4. Inspection

5. Power

6. Circuit operation

6.1.1 Noise Amplifier

6.1.2 Voltage Monitor

6.1.3 Current Monitor

6.1.4 RMS Circuit

1. BLOCK DIAGRAM

1. Block diagram of one channel of the monitor board.

Each board houses four such channels.

2. TEST EQUIPMENT

Variable +/- 15v power supply

Precise DVM

Oscilloscope

Signal generator

The Coil Drive Simulator test equipment output is similar to the Coil Driver Channel shown above, except that the Coil is replaced by two 3.9K resistors in series.

Other resistors may be connected in parallel with this as required during the tests which follow.

3. DESCRIPTION

The function of the Monitor Board is to monitor the outputs from a drive board. It has four identical channels, one per drive board channel. Similar Monitor Boards are used to monitor the UIM Driver, the Top Driver and the PUM drivers.

Inputs

The inputs of the monitor Board are connected to the two amplifier outputs and the coil feeds. The Driver Board and the monitor Board are both mounted in a Drive unit.

The signals which are monitored on each channel are: the positive and negative output voltages from the drive amplifiers, and the positive and negative output voltages developed across the coil.

These four signals are used to measure the amplifier output voltage, the current through the coil and the output noise on each of the drive amplifier channels.

Output Voltage

The Amplifier Output Voltage is measured in IC9, by subtracting the Positive Amplifier output from the Negative Amplifier Output. The output is scaled by a factor of 3, so, for example, inputs of +15v and -15v, the sum of which is 30v, would give an output of 30v/3 = 10v.

Coil Current

The coil current is calculated by IC8, by measuring the sum of the voltages across the two output resistors (R1 and R2 on the block diagram.) The amplifier performs the following calculation:

{(Pos Voltage Output) – (Negative Voltage Output)} -

{(Pos Coil Voltage) - (Negative Coil Voltage)}

The voltage across the coil is subtracted from the voltage across the Amplifier output. This gives the voltage across the output resistors, which is proportional the coil current.

The test equipment has 3.9K resistors for R1 and R2. The coil is simulated by two 3.9K resistors in series. Each resistor will therefore drop a quarter of the sum of the two outputs. The summing amplifier has a gain of 1/3, so for +/- 15v in the output will be 5v.

IC10 is an r.m.s. converter chip, which calculates the true r.m.s. output current. It is followed by an amplifier. The overall scaling factor of the r.m.s. converter and amplifier circuits is 1/3.

Noise Measurement

As the noise level amounts to a few pico amps, it is extremely difficult to measure directly. Instead, the noise voltage across the amplifier outputs is monitored. This enables the coil noise current to be estimated.  Four amplifier stages each coupled with a high pass filter are used, followed by a two stage low pass filter.

Serial No …………………………………...

Test Engineer ………………………………

Date …………………………………………

4. Inspection

Workmanship

General			OK?

Comments

Visual overall check	OK?

Solder joint			OK?

Placement			OK?

Modifications

Serial No …………………………………...

Test Engineer ………………………………

Date …………………………………………

NOTES

Serial No …………………………………...

Test Engineer ………………………………

Date …………………………………………

5. Power

Measure output voltages from the regulators as follows:

Increase input voltages from zero up to +/-3v.

Determine that polarities are correct.

If they are correct, increase the voltages until rated input voltages are reached (+/-16.5v)

Record regulator the regulator output voltages:

| Regulator | Output voltage | Pass/Fail (Nominal +/-0.5v) |
| --- | --- | --- |
| +15v (TP4) |  |  |
| -15v (TP6) |  |  |

If output voltages are satisfactory, proceed to next section.

Record the regulator noise levels, check for stability, and record the powe supply current.

| Regulator | Stable? | Output Noise level pk/pk | Current (Amps) |
| --- | --- | --- | --- |
| +15v (TP4) |  |  |  |
| -15v (TP6) |  |  |  |

Serial No …………………………………...

Test Engineer ………………………………

Date …………………………………………

6. Circuit operation

Test the operation of each channel. The Coil Driver Simulator board will normally be used for these tests.

6.1.1 NOISE AMPLIFIER

6.1.1.1 INPUT BUFFER GAINS

Test that the gain of each of the input buffers, IC1 and IC6 is 25.

Pass band Gain

Set frequency to 20 Hz

Set Amplitude 100mV peak (Signal generator indicates 100mV pk/pk)

Ground reference = Power 0v

Positive input:

|  | Input (TP8) (mV peak) | Output -IC1/6 (V peak) | Expected value (V peak) | Pass/Fail |
| --- | --- | --- | --- | --- |
| Ch1 |  |  | 2.4V to 2.6V |  |
| Ch2 |  |  | 2.4V to 2.6V |  |
| Ch3 |  |  | 2.4V to 2.6V |  |
| Ch4 |  |  | 2.4V to 2.6V |  |

Negative Input:

|  | Input (TP9) (mV peak) | Output - IC6/6 (V peak) | Expected value (V peak) | Pass/Fail |
| --- | --- | --- | --- | --- |
| Ch1 |  |  | 2.4V to 2.6V |  |
| Ch2 |  |  | 2.4V to 2.6V |  |
| Ch3 |  |  | 2.4V to 2.6V |  |
| Ch4 |  |  | 2.4V to 2.6V |  |

6.1.1.2 GAIN AT THE CORNER FREQUENCY

Set frequency to 5 Hz:

Amplitude= 100mV pk/pk

Ground reference = Power 0v

Positive input:

|  | Input - TP8 mV peak | Output - IC1/6 V peak | Expected value (V peak) | Pass/Fail |
| --- | --- | --- | --- | --- |
| Ch1 |  |  | 1.6v to 1.9v |  |
| Ch2 |  |  | 1.6v to 1.9v |  |
| Ch3 |  |  | 1.6v to 1.9v |  |
| Ch4 |  |  | 1.6v to 1.9v |  |

Serial No …………………………………...

Test Engineer ………………………………

Date …………………………………………

Negative Input:

|  | Input - TP9 mV peak | Output - IC6/6 V peak | Expected value V peak | Pass/Fail |
| --- | --- | --- | --- | --- |
| Ch1 |  |  | 1.6v to 1.9v |  |
| Ch2 |  |  | 1.6v to 1.9v |  |
| Ch3 |  |  | 1.6v to 1.9v |  |
| Ch4 |  |  | 1.6v to 1.9v |  |

6.1.1.3 Summing Amplifier

Pass band Gain

Set frequency to 20 Hz

Set Amplitude 100mV pk/pk (sig gen o/p = 100mV peak)

Apply input between TP8 and TP9

|  | Input - TP8 toTP9 (mV peak) | Output TP5 V peak | Expected value (V Peak) | Pass/Fail |
| --- | --- | --- | --- | --- |
| Ch1 |  |  | 4.8v to 5.2v |  |
| Ch2 |  |  | 4.8v to 5.2v |  |
| Ch3 |  |  | 4.8v to 5.2v |  |
| Ch4 |  |  | 4.8v to 5.2v |  |

Serial No …………………………………...

Test Engineer ………………………………

Date …………………………………………

Gains of Successive Stages:

Make measurements at 100 Hz, then at 5 Hz starting by setting the TP5 voltage to 1V peak for each frequency.

|  | 100Hz | 5Hz |
| --- | --- | --- |
|  | Ch1 mV | Ch2 mV | Ch3 mV | Ch4 mV | Ch1 mV | Ch2 mV | Ch3 mV | Ch4 mV |
| TP5 |  |  |  |  |  |  |  |  |
| TP4 |  |  |  |  |  |  |  |  |
| TP6 |  |  |  |  |  |  |  |  |
| TP7 |  |  |  |  |  |  |  |  |

Calculate the ratios of successive outputs from the table above. Check that successive outputs have a ratio of x2 ± 0.1 at 100Hz, and 1.4 ± 0.1 at the 5 Hz the corner frequency.

|  | 100Hz | 5Hz | P/F |
| --- | --- | --- | --- |
|  | Ch1 | Ch2 | Ch3 | Ch4 | Ch1 | Ch2 | Ch3 | Ch4 |  |
| TP4/TP5 |  |  |  |  |  |  |  |  |  |
| TP6/TP4 |  |  |  |  |  |  |  |  |  |
| TP7/TP6 |  |  |  |  |  |  |  |  |  |

Low Pass Output Stage

Set signal generator to give 10V peak on TP7. Measure and record the output at 500Hz and  5Khz TP10, and compare with the specifications at those frequencies.

|  |  | 500Hz (V peak) | Spec @ 500hz | OK? | 5 KHz (V peak) | Spec @ 5KHz | OK? |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Ch1 | TP10 |  | 9.7 to 10v |  |  | 4 to 5.5v |  |
| Ch2 | TP10 |  | 9.7 to 10v |  |  | 4 to 5.5v |  |
| Ch3 | TP10 |  | 9.7 to 10v |  |  | 4 to 5.5v |  |
| Ch4 | TP10 |  | 9.7 to 10v |  |  | 4 to 5.5v |  |

Serial No …………………………………...

Test Engineer ………………………………

Date …………………………………………

6.1.2 VOLTAGE MONITOR

Set the signal generator to give 3V peak at 30 Hz between TP8 and TP9. Measure the output on TP12.

|  | Input -TP8, TP9 (Volts peak) | Output -TP12 (Volts peak) | Expected value (Volts peak) | Pass/Fail |
| --- | --- | --- | --- | --- |
| Ch1 |  |  | 1.9 to 2.1v |  |
| Ch2 |  |  | 1.9 to 2.1v |  |
| Ch3 |  |  | 1.9 to 2.1v |  |
| Ch4 |  |  | 1.9 to 2.1v |  |

6.1.3 CURRENT MONITOR

Current monitoring is done by measuring the voltage dropped across two resistors carrying the output current. The current monitor circuit has a gain of 1/3.

The circuit is tested by applying selected voltages across the current monitor inputs, and observing the current monitor output.

Connect the Monitor Test Unit to the 16 way header on the monitor board, and power it up.

Connect the signal generator to its input.

Set

Frequency to 100Hz

The input voltage between TP8 and TP9 to 3v Peak

Ground reference = Power 0V

Select the following four settings in turn:

(1) Open circuit – representing zero current - zero output expected

(2) Half – giving 3 volts of current monitor signal and 1 volt out.

(3) Quarter – giving 4.5 volts of current monitor signal and 1.5 volts out

(4) Short circuit - giving 6 volts of monitor signal and 2 volts out

| Test | TP11 Expected V | TP11 Ch1 (V) | TP11 Ch2 (V) | TP11 Ch3 (V) | TP11 Ch4 (V) | Pass/ Fail (V) |
| --- | --- | --- | --- | --- | --- | --- |
| (1) 0v in | 0v +/- 0.1v |  |  |  |  |  |
| (2) 3v in | 1v +/- 0.1v |  |  |  |  |  |
| (3) 4.5vin | 1.5v +/- 0.1v |  |  |  |  |  |
| (4) 6v in | 2v +/- 0.1v |  |  |  |  |  |

Serial No …………………………………...

Test Engineer ………………………………

Date …………………………………………

6.1.4 RMS CIRCUIT

The r.m.s circuit monitors the r.m.s current flowing in the coil. A square wave of the same peak amplitude as a sine wave should give an output √2  times as high.

Sine Wave Test

Set frequency to 30 Hz

Without the resistance box,

| I/p sine wave amplitude (between TP8 and TP9) | r.m.s dc output (TP13) | Expected value (volts DC) | Pass/ Fail |
| --- | --- | --- | --- |
| 3V Peak |  |  |  |
| Ch1 |  | 0.707 (0.69 to 0.71) |  |
| Ch2 |  | 0.707 (0.69 to 0.71) |  |
| Ch3 |  | 0.707 (0.69 to 0.71) |  |
| Ch4 |  | 0.707 (0.69 to 0.71) |  |
| 1.5V peak |  |  |  |
| Ch1 |  | 0.35v (0.33 to 0.37) |  |
| Ch2 |  | 0.35v (0.33 to 0.37) |  |
| Ch3 |  | 0.35v (0.33 to 0.37) |  |
| Ch4 |  | 0.35v (0.33 to 0.37) |  |

Square Wave Test

Compare the output for a sine wave input just measured with the output for a square wave input. Set input level to a 3v peak and the frequency to 30 Hz.

| 3v peak Square Wave |  | Expected value (volts dc) | Pass/ Fail |
| --- | --- | --- | --- |
| Ch1, TP13 |  | 1v (0.9 to 1.1v) |  |
| Ch2, TP13 |  | 1v (0.9 to 1.1v) |  |
| Ch3, TP13 |  | 1v (0.9 to 1.1v) |  |
| Ch4, TP13 |  | 1v (0.9 to 1.1v) |  |

DC input

Apply a 3v dc input between TP8 and TP9.

| 3v DC |  | Expected value (volts dc) | Pass/ Fail |
| --- | --- | --- | --- |
| Ch1, TP13 |  | 1v (0.9 to 1.1v) |  |
| Ch2, TP13 |  | 1v (0.9 to 1.1v) |  |
| Ch3, TP13 |  | 1v (0.9 to 1.1v) |  |
| Ch4, TP13 |  | 1v (0.9 to 1.1v) |  |

# Text boxes

Vp-Vn

R2

Coil

Coil Driver Channel

Vmon

Cp

Vp

Vn

Imonn

Cn

R1

(Vp-Cp)+(Cn-Vn)

Noise Monitor