## Slide 1
The AEI
10 m prototype interferometer
Stefan Goßler for the 10 m prototype team
QUEST Project Partners

## Slide 2: Purpose of our prototype
Ultra-low displacement noise test environment
  to probe at and beyond the Standard Quantum Limit (SQL) for of order 100 g to kilogram scale masses
  Entanglement of macroscopic test masses
Maximal overlap with GEO-HF subsystems
  develop and prove as many of the techniques needed for GEO 600 upgrades as possible (e.g. laser, digital control infrastructure)
  provide training for people who will install and run GEO-HF

## Slide 3: Layout vacuum system
Tanks:
3 m diameter, 3.4 m tall
Tubes:
1.5 m diameter
Volume ca. 100 m3
22 t stainless steel
Roughing: One 170 l/s screw pump
Main pumps: Two 2000 l/s turbo-molecular pumps
Backing and differential pumping: Two scroll pumps
All-metal gaskets for flanges up to 600 mm
Differential pumping system with viton O-rings at all bigger flanges
10-6 mbar after about 12 hours

## Slide 4: The prototype hall
Assembly area
SPI laser & modulation bench
LISA lab
Prelimn.
control room
CDS test & training setup

## Slide 5: Vacuum system 180° view
100 m3 volume @10-7mbar after about 2 weeks of pumping
He leak check: 1500 mm flanges are leaky, thicker O-rings are installed as we speak

## Slide 6: Walk-in tanks
600 mm flanges
to fit viewports
100 mm flanges
to fit feed throughs
100 mm flanges
to fit feed throughs

## Slide 7: Soft isolation tables
GAS Filters
Inverted pendulum legs
Experimental platform

## Slide 8: Table assembly

## Slide 9: Interferometric link between tables: SPI
Designed custom interface between
FPGA based phasemeter and digital control system
Suspension Platform Interferometer based on LISA Pathfinder phasemeter
Mach-Zehnder interferometer with unequal arm length (by 20 m), requires stable laser to reach design sensitivity of 100 pm/sqrt(Hz) @ 10 mHz: Iodine-stabilised Nd:YAG
Thermal drift requires components to be bonded onto plate with low CTE

## Slide 10: Mirror suspensions
Upper mass with 2nd vertical stage
Middle
mass
Mirror
Monolithic last stage
100 g mirror, four 28 µm silica fibres
Pre-installed suspension
cartridge

## Slide 11: Light source: 35 W @ 1064 nm
Crystals: 3 x 3 x 10 mm3 Nd:YVO4
8 mm 0,3 % dot.
2 mm undoped endcap
Pump diode:
808 nm, 45 W
400 µm fiber diameter
NA=0,22
Amplifier: 38 W for 2 W seed and 150 W pump
Notes: 11

## Slide 12: Fibre coupling/modecleaning
Fibre coupling via PCF
is promising:
24 W with 3 m fibre
TEM00 > 99%
High degree of modecleaning
Well defined polarisation
Conventional single-mode fibre was found to be limited by SBS to about 30 W transmission at a length of 1.7 m
To be solved:
UHV compatible cladding and feed through
Thermal drift at incoupler
24 W measurement
TEM00 model
Frequency [FSR]
Normalised power

## Slide 13: Frequency-reference cavity
Mirror mass: 850 g
Triple cascaded suspension
4 steel wires of 30µm diameter
Laser
35 W
1064 nm
Pre-modecleaner
(optional)
Fibre
coupling
N
E
BS
Length: 12.3 m
Finesse: 7300
Input: 133 mW
Main IFO
To West tank
R: 99.965 %
R: 99.945 %
R: 99.994 %
ROC: 37.5 m

## Slide 14: Noise budget ref. cavity
Displacement eq. noise [m/ sqrt Hz]
Frequency [Hz]
With safety Factor 10
Requirement
Seismic longitudinal
Seismic vertical
Suspension
Thermal
Coating Thermal
Radiation pressure
Shot noise
Total
20 Hz – 1 kHz

## Slide 15: Digital control
Based on real-time Linux system and EPICS software
Experiment
sensors
&
actuators
Field box
Front end
Workstation
Expansion
chassis
Timing slave
Timing master
GPS clock
6 x 32 channel PCI-X
DA/AD & DIO
Opteron based,
64bit real-time Linux
Frame
builder
Fibre link for
real-time network
Signal conditioning
AA/AI
Linux,
Simulink
based input
10 GHz

## Slide 16: Design of sub-SQL IFO
Frequency-reference cavity:
Length: 12.3 m
Finesse: 7300
Triple pendulum suspension
Mirror mass: 850 g
10 m Fabry-Perot arm cavity
Finesse ca. 670
100 g mirrors
triple cascaded pendulum suspensions
with monolithic all-silica last stage
four filaments of 28 µm diameter
Optional:
Power recycling
~ 5 W input @ 1064 nm
Optional:
Signal recycling
Anti-resonant Fabry-Perot cavity
as compound end mirror
to minimise coating thermal noise
Tap off
~135 mW
BS
IETM
EETM
ITM
cETM

## Slide 17: Noise budget

## Slide 18: The 10 m team
Ken Strain: Scientific leader
Stefan Goßler: Coordinator
Kasem Mossavi: Vacuum system and pumps control
Jens Breyer: Mechanical design
Benno Willke: High power laser
Gerhard Heinzel: LISA/LPF related experiments
Yanbei Chen, Kentaro Somiya, Stefan Danilishin, Helge Müller-Ebhardt: Noise analysis, experiment design
Roman Schnabel: Squeezing and QND experiments
Harald Lück: Vacuum system and GEO 600 related experiments
Hartmut Grote: Electronics and GEO 600 related experiments
Gerrit Kühn, Michael Born, Martin Hewitson: Real time control system
GEO operators: Filter design and construction, environmental monitoring
Andreas Weidner: Electronics design
Henning Ryll: Laser and fibre-modecleaner
Katrin Dahl (PhD), Oliver Kranz (diploma): Suspension platform interferometer
Bob Taylor (postdoc): Seismic isolation and control
Alexander Wanner (PhD): Inertial control
Fumiko Kawazoe (postdoc): Frequency reference cavity and global control
Alessandro Bertolini: Seismic isolation
Tobias Westphal (PhD): Monolithic suspensions
Christian Gräf (PhD): RT control
Thomas Brockt (Diploma): DC-Power supplies and voltage distribution
Daniel Gering (Diploma): Interface SPI - CDS