# Walk-through for Monolithic

- Brett needs to make some measurements on the reaction chain inside the chamber

- Remove door

- Put up tooling

- Remove chain

- Split chains

- Do alignment check/reference

- Rebalance masses (swap parts between dummy ultimate and penultimate masses)

- Remove masses

- Marielle takes lower mass

  - Bond ears to upper mass

  - Glue prisms to upper mass

  - Removes ears from lower mass

  - Remove prisms from lower mass

  - Bond ears to lower mass

  - Glue prisms to lower mass

  - Wait 28 days

- Joe brings in modified structure

- If all looks good, new structure is used, otherwise existing structure will need to be modified

- Fit check for ring heater

- Fit check for fibre guard

- Fit check for violin mode sensor

- Mass (PUM) loaded into upper position

- Suspension wires put in place

- Does PUM need to be suspended (aligned?) at this point?

- Mass (ITM/ETM) loaded into lower position

- ETM aligned along laser beam axis (z-horizontal position)

- ETM aligned around laser beam axis (rotation)

- ETM aligned across the laser beam axis (x-horizontal position)

- ETM vertical position set (y-vertical position)

- ETM aligned around laser beam axis (rotation)

- Remove ergo arm

- Weld in fibres

- Check PUM/ ETM alignment after release (remove some first contact?)

- Put chains together

- Move chains back to chamber