| Author: | Daniel Sigg/Sheila Dwyer |
| --- | --- |
| Refer to: | LIGO-T040189-B |
| Date: | March 4, 2010 |

Common Mode Servo Board Test Procedure

Required equipment:

A description of the mode cleaner common mode board can be found in T040148.

- Beckhoff system for common mode slow controls

- Signal generator

- Oscilloscope

- Network analyzer (1Hz to 10MHz)

- Spectrum analyzer (100kHz bandwidth)

- SR560 low noise preamplifier

Preparations:

| Test Engineer | Date | Pass |
| --- | --- | --- |

Write down revision, serial number and whether it is a mode cleaner board or a interferometer common mode board.

| Board | Revision C/D | Serial | MC/CM |
| --- | --- | --- | --- |
| D040180 |  |  |  |

Hook up the slow controls and enable the fast path. Hook up the power and check that the current drawn from the ±17V power supply is between 0.3A and 0.6A.

| Power supply | Current | Nominal |
| --- | --- | --- |
| +24V |  | 0.02 |
| 24V |  | 0.02 |
| +17 |  | .45 |
| -17 |  | .45 |

Test for oscillations:

Use scope on all outputs and make sure they are not oscillating.

| Output | OUT1 | OUT2 | SERVO | A:IN1 | A:IN2 | B:IN1 | B:IN2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Check |  |  |  |  |  |  |  |
| Output | DAQ1 "14" | DAQ1 "23" | DAQ2 "14" | DAQ2 "23" | D32 Input Mon | D33 Split Mon | D34 Fast Mon |
| Check |  |  |  |  |  |  |  |
| Output | D39 Slow FB Mon | D40 Slow Mon | D35 Limit Indicat. |  |  |  |  |
| Check |  |  |  |  |  |  |  |

Adjust dc bias:

Ground IN1 and adjust the dc bias (R37 and Common offset (D36)) so that the output voltage at SERVO (MC board) or OUT1 (CM board)  and input mon(D32) become zero.

| Check R37 |  |
| --- | --- |
| Common Offset |  |

Gain slider A:

Apply a 1kHz/1Vpp (CM) or 0.225Vpp (MC) sine wave to IN1, with input 1 enabled. Measure the voltage at OUT1 while pulling the specified binary inputs to GND. The measured voltages should be within 0.5dB of the nominal values.

| Binary input (gain slider setting) | Measured [Vpp] | Nominal [Vpp] |
| --- | --- | --- |
| —(0dB) |  | 1 |
| D0 (1dB) |  | 1.12 |
| D1 (2dB) |  | 1.26 |
| D2 (4dB) |  | 1.59 |
| D3 (8dB) |  | 2.51 |
| D4 (16dB) |  | 6.31 |
| D3 & D4 (24dB) |  | 15.9 |
| D5 (-32dB) |  | 0.025 |
| D5 & D3 (-24dB) |  | 0.063 |
| D5 & D4 (-16dB) |  | 0.159 |
| D5 & D3 & D4 (-8dB) |  | 0.398 |

Gain slider B:

Apply a 1kHz/1Vpp sine wave to IN2. Measure the voltage at OUT2 while pulling the specified binary inputs to GND. The measured voltages should be within 0.5dB of the nominal values.

| Binary input (slider gain) | Measured [Vpp] | Nominal [Vpp] |
| --- | --- | --- |
| — |  | 1 |
| D6 (1dB) |  | 1.12 |
| D7 (2dB) |  | 1.26 |
| D8 (4dB) |  | 1.59 |
| D9 (8dB) |  | 2.51 |
| D10 (16dB) |  | 6.31 |
| D9 & D10 (24dB) |  | 15.9 |
| D11 (-32dB) |  | 0.025 |
| D11 & D9 (-24dB) |  | 0.063 |
| D11 & D10 (-16dB) |  | 0.159 |
| D11 & D9 & D10 (-8dB) |  | 0.398 |

Crossbar switches:

Apply a 1kHz/1Vpp sine wave to IN1. Measure the voltage at OUT1 and OUT2 while pulling the specified binary inputs to GND. The measured voltages are either on or off.

| Binary input | OUT1 state | Nominal | OUT2 state | Nominal |
| --- | --- | --- | --- | --- |
| — |  | On |  | Off |
| D12 (input 1 disabled) |  | Off |  | Off |
| D13 (input 2 enabled) |  | On |  | Off |
| D14 (output switch) |  | On |  | On |

Apply a 1kHz/1Vpp sine wave to IN2. Measure the voltage at OUT1 and OUT2 while pulling the specified binary inputs to GND. The measured voltages are either on or off.

| Binary input | OUT1 state | Nominal | OUT2 state | Nominal |
| --- | --- | --- | --- | --- |
| -- |  | Off |  | On |
| D12 (input 1 disabled) |  | Off |  | On |
| D13 (input 2 enabled) |  | On |  | On |
| D14 (output switch) |  | Off |  | Off |

Excitation A:

Apply a 1kHz/1Vpp sine wave to IN1. Measure the voltage at A:TEST1 and A:TEST2 while pulling the specified binary inputs to GND. The measured voltages should be within 0.5dB of the nominal values.

| Binary input | A:TEST1 | Nominal [Vpp] | A:TEST2 | Nominal [Vpp] |
| --- | --- | --- | --- | --- |
| — |  | 1.00 |  | -1.00 |

Apply a 1kHz/1Vpp sine wave to A:EXC. Measure the voltage at A:TEST2 and OUT1 while pulling the specified binary inputs to GND. The measured voltages should be within 0.5dB of the nominal values. Nominal values are given for CM/MC.

| Binary input | A:TEST2 | Nominal [Vpp] | OUT1 | Nominal [Vpp] |
| --- | --- | --- | --- | --- |
| — |  | Off |  | Off |
| D18 (com exc enable) |  | 0.10 |  | 0.10/0.45 |
| D18 & D19 (com option) |  | 0.10 |  | Off |

Split:

Apply a 1kHz/1Vpp(CM) or 0.225Vpp(MC) sine wave to IN1. Measure the voltage at OUT1 and SERVO while pulling the specified binary inputs to GND. Use R100  and slow offset (D37) to zero offset at Slow FB mon when slow comp is enabled.  The measured voltages should be within 0.5dB of the nominal values. Nominal values are given for CM/MC.

| Binary input | OUT1 | Nominal [Vpp] | SERVO | Nominal [Vpp] |
| --- | --- | --- | --- | --- |
| — |  | 1.00 |  | -1.00/+0.11 |
| lift D22 (disable fast) |  | 1.00 |  | Off |
| D21 (common filter) |  | 1.00 |  | -1.00/+0.11 |
| D23 (fast polarity) |  | 1.00 |  | +1.00/-0.11 |
| D20 (slow polarity) |  | -1.00 |  | -1.00/+0.11 |
| D24 (slow option) |  | 0 |  | -1.00/+0.11 |
| Lift D28 (slow comp) |  | 0 |  | -1.00/+0.11 |
| D29 (slow boost) |  | 1.00 (offset) |  | -1.00/+0.11 |
| D30 (slow filter) |  | 1.00 |  | -1.00/+0.11 |
| D25 and lift D28 (slow bypass and slow comp) |  | 1.00 |  | -1.00/+0.11 |
| D27 (slow offset enable) |  | 1.00 (change offset with slow offset, D38) |  | -1.00/+0.11 |
| D27 and D26 (slow 5V offset) |  | 1.00 (5 V offset) |  | -1.00/+0.11 |

Latching:

Apply a 1kHz/1Vpp sine wave to IN1. Measure the voltage at SERVO. Ground P1/11 (latch enable). Now ground D12 (input 1 enable) and make sure the signal at the output stays on all the time.

| Check |  |
| --- | --- |

Excitation B:

Apply a 1kHz/1Vpp sine wave to IN1. Measure the voltage at B:TEST1 and B:TEST2 while pulling the specified binary inputs to GND. The measured voltages should be within 0.5dB of the nominal values.

| Binary input | B:TEST1 | Nominal [Vpp] | B:TEST2 | Nominal [Vpp] |
| --- | --- | --- | --- | --- |
| — |  | 1.00 |  | -1.00 |

Apply a 1kHz/1Vpp sine wave to B:EXC. Measure the voltage at B:TEST2 and SERVO while pulling the specified binary inputs to GND. The measured voltages should be within 0.5dB of the nominal values. Nominal values are given for CM/MC.

| Binary input | B:TEST2 | Nominal [Vpp] | SERVO | Nominal [Vpp] |
| --- | --- | --- | --- | --- |
| — |  | Off |  | Off |
| D47 (fast exc. enable) |  | 0.10 |  | -0.10/0.05 |
| D47 & D48 (fast option) |  | 0.10 |  | Off |

Limiter:

Apply a 1kHz/20Vpp sine wave to IN1. Measure the voltage at SERVO while pulling the specified binary inputs to GND. The measured voltage should be within 25% of the nominal value. Nominal values are given for CM/MC.

| Binary input | Measured [Vpp] | Nominal [Vpp] |
| --- | --- | --- |
| - |  | 20.0/10.0 |
| D31 (fast limiter) |  | 2 * (zener + 0.6) / 1 * (zener + 0.6) [6.6/3.3] |

Gain slider C:

Apply a 1kHz/1Vpp(CM) or 2Vpp(MC) sine wave to IN1. Measure the voltage at SERVO while pulling the specified binary inputs to GND. Short D31 to GND. The measured voltages should be within 0.5dB of the nominal values.

| Binary input (slider gain) | Measured [Vpp] | Nominal [Vpp] |
| --- | --- | --- |
| — |  | 1 |
| D41 (1dB) |  | 1.12 |
| D42 (2dB) |  | 1.26 |
| D43 (4dB) |  | 1.59 |
| D44 (8dB) |  | 2.51 |
| D45 (16dB) |  | 6.31 |
| D44 & D45 (24dB) |  | 15.9 (scale for MC) |
| D46 (-32dB) |  | 0.025 |
| D46 & D44 (-24dB) |  | 0.063 |
| D46 & D45 (-16dB) |  | 0.159 |
| D46 & D45 & D44 (-8dB) |  | 0.398 |

EPICS readbacks:

Apply first a 1Hz/1Vpp and then a 99Hz/1Vpp sine wave to IN1. Watch analog outputs for a peak to peak value. The measured voltage should be within 1 dB (6dB for D34) of the nominal value.

| EPICS readback | 1Hz | Nominal [Vpp] | 100Hz | Nominal [Vpp] |
| --- | --- | --- | --- | --- |
| D32 (input mon) |  | 1.00 |  | 0.080 |
| D33 (split mon) |  | 1.00 |  | 0.080 |
| D34 (fast mon) (MC/CM) |  | 10.00/0.4 |  | 0.80/0.03 |
| D39 (slow FB mon) |  | 1.00 |  |  |
| D40 (slow mon) |  | 1.00 |  |  |

Limit indicator:

Apply a 0.1Hz/10Vpp square wave to IN1. Look at the signal at D35(limit indicator) compare with the nominal response; see Appendix A6.

| Check |  |
| --- | --- |

Apply a 1kHz sine wave to IN1. Increase its amplitude from 0.0V in 0.1V steps until D35 goes from high to low.

| Binary input | Measured [Vpp] | Nominal [Vpp] |
| --- | --- | --- |
| — |  | 30 xR175/(R170+R175+R176) (6.0) |

Distortion:

Apply a 1kHz/1Vrms sine wave to IN1(with D12 on, input 1 enabled, fast enabled (D21). Use a spectrum analyzer to measure the harmonic components at SERVO; see Appendix A7. Repeat the measurement with IN2 (Input2 enabled ,D13 on).

| Harmonic | IN1 | SERVO [dBc] | IN2 | SERVO [dBc] |
| --- | --- | --- | --- | --- |
| 1 (1kHz) |  | 0 |  | 0 |
| 2 (2kHz) |  | >70 |  | >70 |
| 3 (3kHz) |  | >70 |  | >70 |
| 4 (4kHz) |  | >70 |  | >70 |
| 5 (5kHz) |  | >70 |  | >70 |

Noise spectra:

Ground IN1 and IN2. Measure the noise density at OUT1, OUT2 and SERVO. Write down the values at 100Hz, 1kHz, 10kHz and 100kHz. Nominal values are given for CM/MC. Attach hardcopies of the measured spectra; see Appendix A1 for typical examples.

| Frequency | OUT1 | < [nV/Hz] | OUT2 | < [nV/Hz] | SERVO | < [nV/Hz] |
| --- | --- | --- | --- | --- | --- | --- |
| 100Hz |  | 40/300 |  | 30 |  | 50 |
| 1kHz |  | 30/200 |  | 30 |  | 40 |
| 10kHz |  | 30/50 |  | 30 |  | 40 |
| 100kHz |  | 30/20 |  | 30 |  | 40 |

Basic transfer functions:

Use a network analyzer to measure the transfer function from IN1 to OUT1, from IN1 to SERVO and from IN2 to OUT. Sweep the frequency from 100kHz down to 1Hz with 100mV source amplitude. Write down the values at 10Hz, 100Hz, 1kHz, 10kHz and 100kHz. They should be within 1dB and 5 of nominal. Nominal values are given for CM/MC. Attach hardcopies of the measured transfer function; see Appendix A2 for typical examples.

| Frequency | OUT1/IN1 [dB] | Nominal | OUT1/IN1[deg] | Nominal |
| --- | --- | --- | --- | --- |
| 10Hz |  | 0/14 |  | 0/0 |
| 100Hz |  | 0/14 |  | 0/3 |
| 1kHz |  | 0/13 |  | 0/28 |
| 10kHz |  | 0/0 |  | 5/80 |
| 100kHz |  | 3/20 |  | 50/90 |

Input 1 enable (D12) and fast enable (D22):

| Frequency | SERVO/IN1 [dB] | Nominal | SERVO/IN1 [deg] | Nominal |
| --- | --- | --- | --- | --- |
| 10Hz |  | 2/6.0 |  | 115/0 |
| 100Hz |  | 0/6.0 |  | 173/0 |
| 1kHz |  | 0/6.0 |  | 179/0 |
| 10kHz |  | 0/6.0 |  | 181/3 |
| 100kHz |  | 0/3.0 |  | 189/10 |

| Frequency | OUT2/IN2 [dB] | Nominal | OUT2/IN2 [deg] | Nominal |
| --- | --- | --- | --- | --- |
| 10Hz |  | 0/0 |  | 180/180 |
| 100Hz |  | 0/0 |  | 180/180 |
| 1kHz |  | 0/0 |  | 180/180 |
| 10kHz |  | 0/0 |  | 180/180 |
| 100kHz |  | 0/0 |  | 183/183 |

High frequency transfer function:

Use a network analyzer to measure the transfer function from IN1 to SERVO. Sweep the frequency from 10MHz down to 10kHz with –20dBm source. Write down the values at 100kHz, 300kHz and 1MHz. To remove cable delays first measure the transfer function against a BNC barrel and use as a reference. They should be within 1dB and 5 of nominal. Nominal values are given for CM/MC. Attach a hardcopy of the measured transfer function; see Appendix A3 for typical examples.

| Frequency | SERVO/IN1 [dB] | Nominal | SERVO/IN1 [deg] | Nominal |
| --- | --- | --- | --- | --- |
| 100kHz |  | 0/3 |  | 170/4 |
| 300kHz |  | 0/1 |  | 150/30 |
| 1MHz |  | 2/2 |  | 75/130 |

Transfer functions of boost gain stages:

Use a SR560 low noise preamplifier, turn the filter off, set its gain to 1 or 2, select invert and connect its input to OUT1 (CM) or SERVO (MC) and its output to IN1. Make sure the feedback loop is stable and that it does not oscillate. Now use a network analyzer to measure the transfer function from A:TEST2 to A:TEST1 by injecting into A:EXC. Short D18 (common excitation enable) to GND and sweep the frequency from 100kHz down to 1Hz with 5V source amplitude. Make a reference trace when the boost gain stages are off and measure the transfer functions of the boost gain stages relative to the reference. Determine the poles and zeros of the boost gain stages and write down their values (last stage may be too difficult; check at least the dc gain). They should be within 20% of nominal. For 2 and 3 stages use the previous measurement as the reference. It is also possible to measure these boost stages by using TP3, TP8, TP9, TP10 and TP11A. Attach hardcopies of the measured transfer functions; see Appendix A4 for typical examples.

| Boost # | Pole [Hz] | Nominal | Zero [Hz] | Nominal |
| --- | --- | --- | --- | --- |
| Common Compensation (D17) |  | 40 |  | 4000 |
| 1 (D15) |  | 1000 |  | 20000 |
| 2 (D16) |  | 1000 |  | 20000 |
| 3 (D15+D16) |  | 500 |  | 10000 |

Slow boost gain stages:

Connect SR560’s output to OUT1, and check transfer function with the following settings, and common exc enabled (D18).

|  | Pole [Hz] | Nominal | Zero [Hz] | Nominal |
| --- | --- | --- | --- | --- |
| -- |  | 100kHz |  | - |
| D28 (slow comp) |  | 4 |  | - |
| D29 (slow boost) |  | 4 |  | 400 |

Transfer functions of DAQ channels:

Use a network analyzer to measure the transfer function from IN1 to the DAQ chanels. Sweep the frequency from 10kHz down to 1Hz with 1mV source amplitude. Write down the values at dc and 10kHz. They should be within 1dB and 5 of nominal. Nominal values are given for CM/MC. Attach hardcopies of the measured transfer function; see Appendix A5 for typical examples.

| Frequency | DAQ1B (3)/IN1 [dB] | Nominal | DAQ1B(3)/IN1 [deg] | Nominal |
| --- | --- | --- | --- | --- |
| dc |  | -20 |  | 0 |
| 10kHz |  | 20 |  | -12 |

| Frequency | DAQ1A(4)/IN1 [dB] | Nominal | DAQ1A(4)/IN1 [deg] | Nominal |
| --- | --- | --- | --- | --- |
| dc |  | 20 |  | 0 |
| 10kHz |  | 20 |  | 0 |

| Frequency | DAQ2B (3)/IN1 [dB] | Nominal | DAQ2B(3)/IN1 [deg] | Nominal |
| --- | --- | --- | --- | --- |
| dc |  | 20 |  | 0 |
| 10kHz |  | 20 |  | 0 |

| Frequency | DAQ2A (4)/IN1 [dB] | Nominal | DAQ2A (4)/IN1 [deg] | Nominal |
| --- | --- | --- | --- | --- |
| dc |  | -- |  | -- |
| 10kHz |  | 40 |  | -180 |