Statement of Work

PS-129b aLIGO LLO Laser Area Enclosure Acoustic Shell

The following documents are incorporated into and made a part this Statement of Work (SOW).  Click on the following LIGO Document Control Center (DCC) links to access these documents or go on line to the LIGO Public DCC at https://dcc.ligo.org/ to access the DCC#.

- Terms:

| DCC # | Description |
| --- | --- |
| C080185-v1 | Laser Interferometer Gravitational Wave Observatory (LIGO) Commercial Items or Services Contract General Provisions California Institute of Technology “Institute”, LIGO Rev 11/12/08 |
| F0810001-v4 | Technical Direction Memorandum. |

- Quality Control:

The supplier shall:

- Meet or exceed all specifications and requirements

- Identify the corresponding sections/paragraphs in their existing QA/QC system or proposed QA/QC plan for each of the boxes checked in the table below.

| DCC # | Description |
| --- | --- |
| Q0900001-v4 | Advanced LIGO Supplier Quality Requirements, dated 2/10/10, describes the following contractor/supplier QA/QC actions for this procurement: |
|  | 3.1 Pre-Award Inspection |  | 3.9 Discrepant Material Storage |  | 4.4 Calibration Program |
|  | 3.2 Supplier In Process Quality Control |  | 3.10 Quality Records |  | 4.5 Critical Interface |
|  | 3.3 In Process Inspection |  | 3.11 Drawing and Specification Change Control |  | 4.6 Cleanliness |
|  | 3.4 Pre-Ship Inspection |  | 3.12 Welding Certification |  | 4.7 Packaging |
|  | 3.5 Receiving Inspection |  | 3.13 End Item Data Package (including Certifications of Compliance) |  | 4.8 Storage |
|  | 3.6 Discrepant Material |  | 4.1 Design Verification |  | 4.9 Transport |
|  | 3.7 Material Review Action |  | 4.2 Raw Material Procurement |  | 4.10 Customs |
|  | 3.8 Material Review Actions at Contractor |  | 4.3 Traceability of Materials |  |  |

- Included Documents:

Required Drawings:

| DCC # | Description |
| --- | --- |
| D1002391-v3 | Mechanical Plan, L1 Laser Area Enclosure Acoustic Shell |
| D1002392-v2 | Mechanical Plan and Schedules, L1 Laser Area Enclosure Acoustic Shell |
| D1002393-v2 | Mechanical Sections and Details, L1 Laser Area Enclosure Acoustic Shell |
| D1002394-v2 | Room Layout/Framing Plan, L1 Laser Area Enclosure Acoustic Shell |
| D1002395-v2 | Framing Plans and Elevations, L1 Laser Area Enclosure Acoustic Shell |

LAE Cleanroom Specifications (For Reference Only):

| DCC # | Description |
| --- | --- |
| C1002229-v1 | PSL Laser Area Enclosure Cleanrooms - Specifications, Requirements, and Design Considerations |
| D1002787-v2 | Ante-room Plan, L1 Laser Area Enclosure |
| D1002789-v2 | Ante-room Elevations, L1 Laser Area Enclosure |

- Scope:

This SOW is for the fabrication of the aLIGO PSL Laser Area Enclosure Acoustic Shell, for the L1 interferometer, at the LIGO Livingston Observatory.  The structure is to be fabricated as shown in the “Required Drawings” in Section 3.0.

Constraints: 
1) Welded, sheet vinyl flooring will be in place before construction of the Acoustic Shell and must be protected from damage during construction.

2) The 5 ft. x 16 ft. x 40" surface height PSL optical table will be grouted in place prior to construction of the Acoustic Shell and must be protected from damage.

3) Acoustic shell to be constructed inside the Lasers and Vacuum Equipment Area (LVEA), a cleanroom facility.  No sanding of gypsum board, etc.

4) Activities that generate particulates, such as sanding, grinding, and painting must be avoided or controlled.  Alternatives such as trowel finish on drywall joints, brushing and rolling as opposed to spray painting, etc. are preferred.  Exceptions, along with particulate mitigation plans must be approved by LIGO in advance.

Information to be updated prior to start of construction: 
1) Exact dimensions of finished opening for double doors between Ante-room and Laser Room. 
2) Exact dimensions of finished opening for exhaust damper in wall between Ante-room and Laser Room.

- Quantity Required:

| 1 ea. | LIGO Livingston Observatory, Livingston, LA |
| --- | --- |

Acoustic Shell Installation Dates:

L1 Acoustic Shell Installation: January 19 - February 8, 2011

For Reference Only:

L1 Cleanroom Installation: February 9 - March 2, 2011

# Text boxes

# LIGO LABORATORY

California Institute of Technology

1200 E. California Blvd.

Pasadena, CA  91125