## Slide 1: LLO Electronics Racks
Search by
AREA
Search by SUBSYSTEM
This document provides details about the LLO electronics racks. It may be examined through four separate but interconnected methods: racks may be found searching MAPS of the observatory, or for AREAS in which they reside, or by searching SUBSYSTEMS that they service., or through the DocDB references to their D-numbers or S-numbers.
Search by
LOCATION
Search by
DocDB

## Slide 2: Locations
X-End – D0901465
Y-Mid-station
Y-End - D0901464
Corner Station - D0901466
Staging Building - D000294
Science Education Building
Warehouse
<< Start
X-Mid-station

## Slide 3: Corner Station – D0901490
CER
LDR
CPR
LVEA - Racks
LVEA - Tables
D0901466
MSR
CUR
Y-End - D0901464
X-End – D0901465
OCR
D0901490
Staging Building – D000294
<< Locations

## Slide 4: Staging Building, HPLF As Built
D000294
<< Locations

## Slide 5: LLO Racks by AREA
Mass Storage
Room (MSR)
Operator Control
Room (OCR)
CDS Electronics
Room (CER)
Laser Diode
Room (LDR)
CDS Power
Room (CPR)
LVEA Racks
(LVEA)
X-End Racks
(X-End)
X-End Tables
(X-End)
Computer User Room (CUR)
Electronics Test Racks (ETR)
LLO electronics racks are installed in a variety of LOCATIONS. Generally speaking, each location houses a specific type of rack. Front-end computers are housed in the MSR. Electronics racks with IO chasses are housed in the CER. Other electronics racks that interface to chambers are located in the LVEA, X-End and Y-End areas. Power supplies are housed in the CPR. And finally, test racks for electronics are spread throughout the facility, housed wherever they are required.
<< Start
Other Areas
(Other)
LVEA Tables
(LVEA)
Y-End Racks
(Y-End)
Y-End Tables
(Y-End)

## Slide 6: LLO Racks by Subsystem
Auxiliary Optics
CER:(AOS / TCS)
LVEA:(AOS / TCS)
CERX:(AOS / TCS)
VEAX:(AOS / TCS)
CERY:(AOS / TCS)
VEAY:(AOS / TCS)
Data Acquisition
CER:(DAQ / PEM / OAF)
LVEA:(DAQ / PEM / OAF)
CERX:(DAQ / PEM / OAF)
VEAX:(DAQ / PEM / OAF)
CERY:(DAQ / PEM / OAF)
VEAY:(DAQ / PEM / OAF)
Interferometer Sensing and Control
CER:(ISC)
LVEA:(ISC)
CERX:(ISC)
VEAX:(ISC)
CERY:(ISC)
VEAY:(ISC)
Pre-stabilized Laser CER:(PSL)
LVEA:(PSL)
CERX:(PSL)
VEAX:(PSL)
CERY:(PSL)
VEAY:(PSL)
Seismic Isolation
CER:(SEI)
LVEA:(SEI)
CERX:(SEI)
VEAX:(SEI)
CERY:(SEI)
VEAY:(SEI)
Suspensions
CER:(SUS)
LVEA:(SUS)
CERX:(SUS)
VEAX:(SUS)
CERY:(SUS)
VEAY:(SUS)
IFO Subsystems are another way to view the racks that are installed in a variety of locations. Generally speaking, each subsystem has racks that are positioned in several physical locations. The subsystems are: AOS, DAQ, ISC, PSL, SEI, SUS, VAC, and VDC. TCS is a part of AOS. PEM and OAF are part of DAQ. HEPI is part of SEI.
Vacuum
CER:(VAC)
LVEA:(VAC)
CERX:(VAC)
VEAX:(VAC)
CERY:(VAC)
VEAY:(VAC)
DC Power
CER:(VDC)
LVEA:(VDC)
CERX:(VDC)
VEAX:(VDC)
CERY:(VDC)
VEAY:(VDC)
<< Start
Facilities
CER:(FAC)
LVEA:(FAC)
CERX:(FAC)
VEAX:(FAC)
CERY:(FAC)
VEAY:(FAC)

## Slide 7: LLO Rack Naming Scheme
CDS racks are named according to site, IFO designation, subsystem use, station (location) and sequence. (See G1001030)
Site | Description | IFO | Subsystem | Description | Station | Description | Rack Number
L | Livingston | 1 | AOS | Auxiliary Optics | C | [Corner] Common | 1
H | Hanford | 2 | DAQ | Data Acquisition | MS | Mass Storage | 2
M | MIT |  | ETR | Electronics Test Rack | R | [Corner] Remote (Field) | 3
C | CIT |  | FAC | Facilities and Infrastructure | XC | X-End Common | 4
 |  |  | ISC | IFO Sensing and Control | XR | X-End Remote [Field] | 5
 |  |  | LDR | Laser Diode Room | YC | Y-End Common | 6
 |  |  | OAF | Online Adaptive Filtering | YR | Y-End Remote [Field] | 7
 |  |  | PEM | Physical Environment Monitoring |  |  | 8
 |  |  | PSL | Pre-stabilized Laser |  |  | 9
 |  |  | SEI | Seismic Isolation |  |  | 10
 |  |  | SUS | Suspensions |  |  | 11
 |  |  | TCS | Thermal Compensation System |  |  | 12
 |  |  | VAC | Vacuum |  |  | etc.
 |  |  | VDC | Voltage - DC |  |  | 

## Slide 8: LLO Rack Names
Rack | Rack Designator | Subsystem | Location | Comment
1 | L1-TCS-C1 | AOS | Common Electronics Room | 
2 | L1-TCS-R1 | AOS | Remote Electronics Rack | 
3 | L1-TCS-R2 | AOS | Remote Electronics Rack | 
4 | L1-TCS-XC1 | AOS | X End Remote Electronics Rack | 
5 | L1-TCS-XR1 | AOS | X End Remote Electronics Rack | 
6 | L1-TCS-YC1 | AOS | Y End Common Electronics Rack | 
7 | L1-TCS-YR1 | AOS | Y End Remote Electronics Rack | 
8 | L1-OAF-C1 | DAQ | Common Electronics Room | 
9 | L1-ETR-01 | DAQ | DAQ Electronics Test Rack | DAQ Electronics Test Rack
10 | L1-OAF-XC1 | DAQ/ISC | X End Common Electronics Rack | 
11 | L1-OAF-YC1 | DAQ/ISC | Y End Common Electronics Rack | 
12 | L1-ISC-C1 | ISC | Common Electronics Room | 
13 | L1-ISC-C2 | ISC | Common Electronics Room | 
14 | L1-ISC-C3 | ISC | Common Electronics Room | 
15 | L1-ISC-C4 | ISC | Common Electronics Room | 
16 | L1-ISC-R1 | ISC | Remote Electronics Rack | 
17 | L1-ISC-R2 | ISC | Remote Electronics Rack | 
18 | L1-ISC-R3 | ISC | Remote Electronics Rack | 
19 | L1-ISC-XR1 | ISC | X End Remote Electronics Rack | 
20 | L1-ISC-YR1 | ISC | Y End Remote Electronics Rack | 
21 | L1-ETR-04 | OPTICS | Optics Electronics Lab Rack | Optics Electronics Lab Rack
22 | L1-LDR-C1 | PSL | Laser Diode Room Rack | 
23 | L1-LDR-C2 | PSL | Laser Diode Room Rack | 
24 | L1-PSL-C1 | PSL | Common Electronics Room | 
25 | L1-PSL-R1 | PSL | Remote Electronics Rack | 
26 | L1-PSL-R2 | PSL | Remote Electronics Rack | 
27 | L1-SEI-C1 | SEI | Common Electronics Room | SEI HAM 1 and HAM 6
28 | L1-SEI-C2 | SEI | Common Electronics Room | SEI HAM 2 and HAM 3
29 | L1-SEI-C3 | SEI | Common Electronics Room | SEI HAM 4 and HAM 5
30 | L1-SEI-C4 | SEI | Common Electronics Room | SEI BCS1
31 | L1-SEI-C5 | SEI | Common Electronics Room | SEI BCS2
32 | L1-SEI-C6 | SEI | Common Electronics Room | SEI BCS3
33 | L1-SEI-XC1 | SEI | X End Common Electronics Rack | SEI BCS4
34 | L1-SEI-YC1 | SEI | Y End Common Electronics Rack | SEI BCS5
35 | L1-ETR-05 | SEI | HAM ISI Electronics Test Rack | HAM ISI Electronics Test Rack
36 | L1-ETR-07 | SEI | Triple Electronics Test Rack | Triple Electronics Test Rack
37 | L1-SUS-C1 | SUS | Common Electronics Room | SUS ITM, FM, and BS (1 of 2)
38 | L1-SUS-C2 | SUS | Common Electronics Room | SUS ITM, FM, and BS (2 of 2)
39 | L1-SUS-C3 | SUS | Common Electronics Room | SUS HAM 2 (1 of 2)
40 | L1-SUS-C4 | SUS | Common Electronics Room | SUS HAM 2 (2 of 2)
41 | L1-SUS-C5 | SUS | Common Electronics Room | SUS ITMX, ITMY, and BS (1 of 2)
42 | L1-SUS-C6 | SUS | Common Electronics Room | SUS ITMX, ITMY, and BS (2 of 2)
43 | L1-SUS-C7 | SUS | Common Electronics Room | SUS HAM 5 and HAM 6 (1 of 2)
44 | L1-SUS-C8 | SUS | Common Electronics Room | SUS HAM 5 and HAM 6 (2 of 2)
45 | L1-SUS-R1 | SUS | Remote Electronics Rack | 
46 | L1-SUS-R2 | SUS | Remote Electronics Rack | 
47 | L1-SUS-R3 | SUS | Remote Electronics Rack | 
48 | L1-SUS-R4 | SUS | Remote Electronics Rack | 
49 | L1-SUS-R5 | SUS | Remote Electronics Rack | 
50 | L1-SUS-R6 | SUS | Remote Electronics Rack | 
51 | L1-SUS-XC1 | SUS | X End Common Electronics Rack | 
52 | L1-SUS-XC2 | SUS | X End Common Electronics Rack | 
53 | L1-SUS-XR1 | SUS | X End Remote Electronics Rack | 
54 | L1-SUS-YC1 | SUS | Y End Common Electronics Rack | 
55 | L1-SUS-YC2 | SUS | Y End Common Electronics Rack | 
56 | L1-SUS-YR1 | SUS | Y End Remote Electronics Rack | 
57 | L1-ETR-02 | SUS | BSC Electronics Test Rack | BSC Electronics Test Rack
58 | L1-ETR-03 | SUS | RM Electronics Test Rack | RM Electronics Test Rack
59 | L1-ETR-06 | SUS | STS Huddle Electronics Test Rack | STS Huddle Electronics Test Rack
60 | L1-VAC-R1 | VAC | Remote Electronics Rack | 
61 | L1-VAC-R2 | VAC | Remote Electronics Rack | 
62 | L1-VAC-R3 | VAC | Remote Electronics Rack | 
63 | L1-VAC-XR1 | VAC | X End Remote Electronics Rack | 
64 | L1-VAC-YR1 | VAC | Y End Remote Electronics Rack | 
65 | L1-VDC-C1 | VDC | DC Voltage Rack - CPR | 
66 | L1-VDC-C2 | VDC | DC Voltage Rack - CPR | 
67 | L1-VDC-C3 | VDC | DC Voltage Rack - CPR | 
68 | L1-VDC-C4 | VDC | DC Voltage Rack - CPR | 
69 | L1-VDC-C5 | VDC | DC Voltage Rack - CPR | 
70 | L1-VDC-C6 | VDC | DC Voltage Rack - CPR | 
71 | L1-VDC-C6 | VDC | DC Voltage Rack - CPR | 
72 | L1-VDC-XC1 | VDC | DC Voltage Rack - VEAX | 
73 | L1-VDC-XC2 | VDC | DC Voltage Rack - VEAX | 
74 | L1-VDC-YC1 | VDC | DC Voltage Rack - VEAY | 
75 | L1-VDC-YC2 | VDC | DC Voltage Rack - VEAY | 
76 | L1-MS1 |  |  | 
77 | L1-MS2 |  |  | 
78 | L1-MS3 |  |  | 
79 | L1-MS4 |  |  | 
80 | L1-MS5 |  |  | 
81 | L1-MS6 |  |  | 
82 | L1-DAQ-MS7 | DAQ | Front end computers | 
83 | L1-DAQ-MS8 | DAQ | Front end computers | 
84 | L1-DAQ-MS9 | DAQ | Front end computers | 
85 | L1-MS10 |  |  | 
86 | L1-MS11 |  |  | 
87 | L1-MS12 |  |  | 
88 | L1-MS13 |  |  | 
89 | L1-FAC-XC1 | FAC | Facilities – VEAX | 
90 | L1-FAC-YC1 | FAC | Facilities - VEAY | 
CDS racks are named according to site, IFO designation, subsystem use, station (location) and sequence. (See G1001030)

## Slide 9: LLO CDS Electronics Rack Names
Rack | Rack Designator | Subsystem | Location | Comment | Rack Type | Dxxxxxxx | Sxxxxxxx
1 | L1-AOS-C1 | AOS | CER |  | Standard | D1201119 | S1202974
2 | L1-TCS-R1 | AOS | LVEA |  | Standard | D1201122 | S1202975
3 | L1-TCS-R2 | AOS | LVEA |  | Standard | D1201123 | S1202976
4 | L1-TCS-XC1 | AOS | CERX |  | Standard | D1201129 | S1202980
5 | L1-TCS-YC1 | AOS | CERY |  | Standard | D1201130 | S1202981
6 | L1-OAF-C1 | DAQ | CER | OAF/PEM | Standard | D1200941 | S1202404
7 | L1-DAQ-XC1 | DAQ | CERX |  | Standard | D1201085 | S1202949
8 | L1-DAQ-YC1 | DAQ | CERY |  | Standard | D1201092 | S1202956
9 | L1-ISC-C1 | ISC | CER |  | Standard | D1200949 | S1201186
10 | L1-ISC-C2 | ISC | CER |  | Standard | D1200975 | S1201187
11 | L1-ISC-C3 | ISC | CER |  | Standard | D1200976 | S1201188
12 | L1-ISC-C4 | ISC | CER |  | Standard | D1200977 | S1201189
13 | L1-ISC-R1 | ISC | LVEA |  | Standard | D1001460 | S1201192
14 | L1-ISC-R2 | ISC | LVEA |  | Standard | D1001425 | S1201193
15 | L1-ISC-R3 | ISC | LVEA |  | Standard | D1001426 | S1201194
16 | L1-ISC-R4 | ISC | LVEA |  | Standard | D1101904 | S1201195
17 | L1-ISC-R5 | ISC | LVEA |  | Standard | D1200196 | S1201196
18 | L1-ISC-XC1 | ISC | CERX |  | Standard | D1201084 | S1202948
19 | L1-ISC-YC1 | ISC | CERY |  | Standard | D1201091 | S1202955
20 | L1-ISC-XR1 | ISC | VEAX |  | Standard | D1201087 | S1202951
21 | L1-ISC-YR1 | ISC | VEAY |  | Standard | D1201094 | S1202958
22 | L1-ETR-04 | OPTICS | Test Rack | Optics Electronics Lab Rack | 11U |  | 
23 | L1-LDR-C1 | PSL | LDR |  | Vendor |  | 
24 | L1-LDR-C2 | PSL | LDR |  | Vendor |  | 
25 | L1-PSL-C1 | PSL | CER |  | Standard | D1201118 | S1202977
26 | L1-PSL-R1 | PSL | LVEA |  | Standard | D1201120 | S1202978
27 | L1-PSL-R2 | PSL | LVEA |  | Standard | D1201121 | S1202979
28 | L1-SEI-C1 | SEI | CER | SEI HAM 1 and HAM 6 | Standard | D1201112 | S1200743
29 | L1-SEI-C2 | SEI | CER | SEI HAM 2 and HAM 3 | Standard | D1201113 | S1200744
30 | L1-SEI-C3 | SEI | CER | SEI HAM 4 and HAM 5 | Standard | D1201114 | S1200745
31 | L1-SEI-C4 | SEI | CER | SEI BCS1 | Standard | D1201115 | S1200746
32 | L1-SEI-C5 | SEI | CER | SEI BCS2 | Standard | D1201116 | S1200747
33 | L1-SEI-C6 | SEI | CER | SEI BCS3 | Standard | D1201117 | S1200748
34 | L1-SEI-XC1 | SEI | CERX | SEI BCS4 | Standard | D1201081 | S1202945
35 | L1-SEI-YC1 | SEI | CERY | SEI BCS5 | Standard | D1201088 | S1202952
36 | L1-ETR-05 | SEI | Test Rack | HAM ISI Electronics Test Rack |  |  | 
37 | L1-ETR-07 | SEI | Test Rack | Triple Electronics Test Rack |  |  | 
38 | L1-SUS-C1 | SUS | CER | SUS ITM, FM, and BS (1 of 2) | Standard | D1200856 | S1104062
39 | L1-SUS-C2 | SUS | CER | SUS ITM, FM, and BS (2 of 2) | Standard | D1200859 | S1104356
40 | L1-SUS-C3 | SUS | CER | SUS HAM 2 (1 of 2) | Standard | D1200864 | S1104357
41 | L1-SUS-C4 | SUS | CER | SUS HAM 2 (2 of 2) | Standard | D1200867 | S1104358
42 | L1-SUS-C5 | SUS | CER | SUS ITMX, ITMY, and BS (1 of 2) | Standard | D1200874 | S1105375
43 | L1-SUS-C6 | SUS | CER | SUS ITMX, ITMY, and BS (2 of 2) | Standard | D1200875 | S1105376
44 | L1-SUS-C7 | SUS | CER | SUS HAM 5 and HAM 6 (1 of 2) | Standard | D1200876 | S1105377
45 | L1-SUS-C8 | SUS | CER | SUS HAM 5 and HAM 6 (2 of 2) | Standard | D1200877 | S1105378
46 | L1-SUS-R1 | SUS | LVEA |  | Standard | D1200879 | S1200749
47 | L1-SUS-R2 | SUS | LVEA |  | Standard | D1200880 | S1200750
48 | L1-SUS-R3 | SUS | LVEA |  | Standard | D1200883 | S1202300
49 | L1-SUS-R4 | SUS | LVEA |  | Standard | D1201134 | S1202995
50 | L1-SUS-R5 | SUS | LVEA |  | Standard | D1201135 | S1202996
51 | L1-SUS-R6 | SUS | LVEA |  | Standard | D1201136 | S1202997
52 | L1-SUS-XC1 | SUS | CERX |  | Standard | D1201082 | S1202946
53 | L1-SUS-XC2 | SUS | CERX |  | Standard | D1201083 | S1202947
54 | L1-SUS-XR1 | SUS | VEAX |  | Standard | D1201131 | S1202993
55 | L1-SUS-YC1 | SUS | CERY |  | Standard | D1201089 | S1202953
56 | L1-SUS-YC2 | SUS | CERY |  | Standard | D1201090 | S1202954
57 | L1-SUS-YR1 | SUS | VEAY |  | Standard | D1201132 | S1202994
58 | L1-ETR-02 | SUS | Test Rack | BSC Electronics Test Rack |  |  | 
59 | L1-ETR-03 | SUS | Test Rack | RM Electronics Test Rack |  |  | 
60 | L1-ETR-06 | SUS | Test Rack | STS Huddle Electronics Test Rack |  |  | 
61 | L1-VAC-R1 | VAC | LVEA | Vacuum Rack - X Arm | Knurr |  | 
62 | L1-VAC-R2 | VAC | LVEA | Vacuum Rack - Y Arm | Knurr |  | 
63 | L1-VAC-R3 | VAC | Mechanical Room | Vacuum Rack - Mechanical Room | Knurr |  | 
64 | L1-VAC-XR1 | VAC | VEAX | Vacuum Rack - X End | Knurr |  | 
65 | L1-VAC-YR1 | VAC | VEAY | Vacuum Rack - Y End | Knurr |  | 
66 | L1-VDC-C1 | VDC | CPR |  | DC | D1200890 | S1105247
67 | L1-VDC-C2 | VDC | CPR |  | DC | D1200891 | S1105248
68 | L1-VDC-C3 | VDC | CPR |  | DC | D1200892 | S1105249
69 | L1-VDC-C4 | VDC | CPR |  | DC | D1200893 | S1105250
70 | L1-VDC-C5 | VDC | CPR |  | DC | D1200894 | S1105251
71 | L1-VDC-C6 | VDC | CPR |  | DC | D1200895 | S1105252
72 | L1-VDC-C7 | VDC | CPR |  | DC | D1200896 | S1105253
73 | L1-VDC-C8 | VDC | CPR | Planned | DC | D1201137 | S1202998
74 | L1-VDC-XC1 | VDC | CERX |  | DC | D1200897 | S1202311
75 | L1-VDC-XC2 | VDC | CERX |  | DC | D1200898 | S1202312
76 | L1-VDC-YC1 | VDC | CERY |  | DC | D1200899 | S1202313
77 | L1-VDC-YC2 | VDC | CERY |  | DC | D1200900 | S1202314
78 | L1-MSR-01 | CDS | MSR | Atomic Clock | Knurr | D1201372 | S1203487
79 | L1-MSR-02 | CDS | MSR | Fiber Patch | Knurr | D1201373 | S1203488
80 | L1-MSR-03 | CDS | MSR | EPICS | Knurr | D1201374 | S1203489
81 | L1-MSR-04 | CDS | MSR | EPICS | Knurr | D1201375 | S1203490
82 | L1-MSR-05 | CDS | MSR | Backup Tape | Knurr | D1201376 | S1203491
83 | L1-MSR-06 | CDS | MSR | Video | Knurr | D1201377 | S1203492
84 | L1-MSR-07 | CDS | MSR | IFO Front End Computers | Standard | D1201378 | S1203493
85 | L1-MSR-08 | CDS | MSR | IFO Front End Computers | Standard | D1201379 | S1203494
86 | L1-MSR-09 | CDS | MSR | CDS Computers | Standard | D1201380 | S1203495
87 | L1-MSR-10 | CDS | MSR | CDS Computers | Standard | D1201381 | S1203496
88 | L1-MSR-11 | CDS | MSR | General Computing | Standard | D1201382 | S1203497
89 | L1-MSR-12 | CDS | MSR | DAQ Electronics Test Rack | Standard | D1201383 | S1203498
90 | L1-MSR-13 | CDS | MSR | UPS for IFO and CDS Computers | Linier | D1201384 | S1203499
91 | L1-FAC-C1 | FAC | CER |  | Standard | D1200940 | S1202403
92 | L1-FAC-XC1 | FAC | CERX |  | Standard | D1201086 | S1202950
93 | L1-FAC-YC1 | FAC | CERY |  | Standard | D1201093 | S1202957
94 | L1-UNK-C1 |  | CER |  | Standard | D1201356 | S1203450
95 | L1-UNK-C2 |  | CER |  | Standard | D1201357 | S1203451
96 | L1-UNK-C3 |  | CER |  | Standard | D1201358 | S1203452
CDS racks are named according to site, IFO designation, subsystem use, station (location) and sequence. (See G1001030)

## Slide 10: Electronics Racks – Counts and Accounting
Subsystem | Count | Percent | MSR | CER / CPR | LVEA | CERX | VEAX | CERY | VEAY | Other | Comment
SUS | 20 | 39.22 | 0 | 8 | 6 | 2 | 1 | 2 | 1 | 0 | Suspensions
SEI | 8 | 15.69 | 0 | 6 | 0 | 1 | 0 | 1 | 0 | 0 | Seismic
ISC | 8 | 15.69 | 0 | 3 | 3 | 0 | 1 | 0 | 1 | 0 | IFO Sensing and Control
PEM / DAQ | 3 | 5.88 | 3 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | Data Acquisition
AOS - TCS | 7 | 13.73 | 0 | 1 | 2 | 1 | 1 | 1 | 1 | 0 | Thermal Compensation
PSL / LDR | 5 | 9.80 | 0 | 3 | 2 | 0 | 0 | 0 | 0 | 0 | Pre-stabilized Laser
Subsystem Subtotal | 51 | 100.00 | 3 | 22 | 13 | 5 | 3 | 5 | 3 | 0 | 
Infrastructure | Count |  | MSR | CER / CPR | LVEA | CERX | VEAX | CERY | VEAY | Other | Comment
DC Power | 11 |  | 0 | 7 | 0 | 2 | 0 | 2 | 0 | 0 | DC Power Supplies
MSR | 13 |  | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 13 | MSR Racks
Vacuum | 5 |  | 0 | 0 | 3 | 0 | 1 | 0 | 1 | 0 | Vacuum Racks
Facilities | 2 |  | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | Facilities Racks
Test Racks | 7 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 7 | Subsystem Test Racks
Infrastructure Subtotal | 38 |  | 10 | 7 | 3 | 3 | 1 | 3 | 1 | 20 | 
Total | 89 |  | 13 | 29 | 16 | 8 | 4 | 8 | 4 | 20 | 

## Slide 11: DC Power Supplies – Counts and Accounting
Subsystem | Supply Count | Percent | %
SUS | 50 | 29.07 | 29
SEI | 40 | 23.26 | 23
ISC | 33 | 19.19 | 19
DAQ | 13 | 7.56 | 8
AOS | 25 | 14.53 | 15
PSL | 11 | 6.40 | 6
Total | 172 | 100.00 | 100

## Slide 12: LLO CDS Components
Front End Computer
Front End Computer
Timing Master
18VDC
I/O Extension
Timing Fanout
24VDC
Chassis
Chassis
Chassis
Chassis
Chassis
Chassis
DC Power
DC Power
DC Power
DC Power
DC Power
DC Power
AC Voltage
Chassis
Chassis
Chassis
Chassis
Chassis
Chassis
Mass
Storage
Room (MSR)
Operator
Control
Room (OCR)
CDS
Electronics
Room (CER)
Laser
Diode
Room (LDR)
CDS
Power
Room (CPR)
Field
I/O
Cables
Timing
Distribution
Cables
DC
Power
Racks
Field Satellite
Racks
Subsystem
Electronics
Racks
Front
End
Racks
Fiber
Optic
Cables
DC
Extension
Cables
Field
DC
Extension
Cords
Computer Users Room (CUR)
Racks and Rooms (RAR)
LVEA Racks
(LVEA)
X-End Racks
(X-End)
Y-End Racks (Y-End)
Electronics Test Racks (ETR)
<< Start

## Slide 13: OCR (Operations Control Room)
OCR
<< LLO Racks by AREA
OCR Documentation
<< LLO CDS Components
<< LLO Corner Station

## Slide 14: CUR (Computer User’s Room)
CUR
CUR Documentation
<< LLO Racks by AREA
<< LLO CDS Components
<< LLO Corner Station

## Slide 15: MSR (Mass Storage Room)
MSR
MSR Documentation
MSR Layout
<< LLO Racks by AREA
<< LLO CDS Components
<< LLO Corner Station

## Slide 16: MSR (Mass Storage Room) Layout
<< LLO Corner Station
<< LLO Racks by AREA
<< LLO CDS Components
L1-MS1
L1-UPS2
L1-MS7
L1-MS8
L1-MS9
L1-MS2
L1-MS3
L1-MS4
L1-MS5
L1-MS6
L1-MS10
L1-MS11
L1-MS12
L1-UPS1
L1-BM1
Y
|
V
1
2
3
4
5
6
7
<-X
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20

## Slide 17: MSR (Mass Storage Room) Layout
<< LLO Corner Station
<< LLO Racks by AREA
<< LLO CDS Components
Y
|
V
1
2
3
4
5
6
7
<-X
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20

## Slide 18: L1-UPS1
<< MSR

## Slide 19: L1-MS7
<< MSR

## Slide 20: L1-MS8
<< MSR

## Slide 21: L1-MS9
CDS MSR Rack 9 Layout (T1000588)
Timing IRIG-B Chassis
D0900301
±12@1A
S1202405
110VAC 20A
UPS Power Strip
110VAC 20A
Non-UPS Power Strip
110VAC 20A
UPS Power Strip
110VAC 20A
Non-UPS Power Strip
MasterClock GPS Seconds Display
ALD-118
UPS
SN: 09050004
<< MSR
Power 10 DC Power Supply
3300D-3020
UPS
SN: 1009264

## Slide 22: D0900301 – S1107510
Timing IRIG-B Interface Chassis
D0900301
+12VDC
S1202405
D0900301
Front
S1202405
Rear
<< L1-MS9

## Slide 23: MasterClock ALD118
MadterClock GPS Seconds Display
ALD118
UPS
SN: 09050004
D0900301
Front
S1202405
Rear
<< L1-MS9

## Slide 24: Power 10 DC Power Supply
Power 10 DC Power Supply
3300D-3020
UPS
SN: 1009264
D0900301
Front
S1202405
Rear
<< L1-MS9

## Slide 25: CER (Corner Electronics Room)
CER
<< LLO Racks by AREA
<< LLO CDS Components
<< LLO Corner Station
Rack Layout >>

## Slide 26: LLO CER – Rack Layout
<< LLO Corner Station
<< LLO Racks by Area
<< LLO CDS Components
2feet
Each Rack is 39” Deep and 24” Wide
2 feet
L1-FAC-C1
L1-SUS-C1
L1-SUS-C2
L1-SUS-C3
L1-SUS-C4
L1-SUS-C5
L1-SUS-C6
L1-SUS-C7
L1-SUS-C8
L1-SEI-C1
Front
Front
Front
Front
Front
Front
L1-SEI-C2
L1-TCS-C1
L1-SEI-C3
L1-SEI-C4
L1-SEI-C5
L1-SEI-C6
L1-UNK-C3
L1-UNK-C2
L1-UNK-C1
L1-ISC-C1
L1-ISC-C2
L1-ISC-C3
L1-PSL-C1
L1-ISC-C4
L1-OAF-C1
SUS ITMX, ITMY, FMX, FMY, and BS Rack 1
SUS HAM3 and HAM4 Rack 2
SUS HAM3 and HAM4 Rack 1
SUS HAM2 Rack 1
SUS HAM2 Rack 2
SUS ITMX, ITMY, FMX, FMY, and BS Rack 2
SUS HAM5 and HAM6 Rack 1
SUS HAM5 and HAM6 Rack 2
ISC LVEA Rack 1
ISC LVEA Rack 2
ISC LVEA Rack 3
PSL Rack 1
FAC Rack 1
TCS Rack 1
Front
SEI HAM1 and HAM6
SEI HAM2 and HAM3
SEI HAM4 and HAM5
SEI BSC1
SEI BSC2
SEI BSC3
ISC LVEA Rack 4
DAQ Rack 1
L1-AOS-C1
CDS Electronics Room (CER)

## Slide 27: LLO CER, LDR, and CPR Cable Tray Layout
From MSR
Fibers and DC Cables
DC Cables
AC Cables
Signal Cables
Signal Cables
CER
LDR
CPR
138”
120”
102”

## Slide 28: LLO CER – 8.5ft Cable Tray Layout
2feet
2 feet
All posts are E-Posts
L1-PSL-C3
L1-PSL-C2
L1-PSL-C1
L1-ISC-C1
L1-ISC-C2
L1-ISC-C3
L1-SUS-C1
L1-SUS-C2
L1-SUS-C3
L1-SUS-C4
L1-SUS-C5
L1-SUS-C6
L1-SUS-C7
L1-SUS-C8
L1-SEI-C1
Front
Front
Front
Front
Front
Front
L1-SEI-C2
L1-SEI-C3
L1-SEI-C4
L1-SEI-C5
L1-SEI-C6
43”
207”
8.5”
293”
54”
231”
139”
48”
Each Rack is 39” Deep and 24” Wide
CDS Electronics Room (CER)

## Slide 29: LLO CER – 10ft Cable Tray Layout
2feet
2 feet
All posts are E-Posts
10 Foot
L1-PSL-C3
L1-PSL-C2
L1-PSL-C1
L1-ISC-C1
L1-ISC-C2
L1-ISC-C3
L1-SUS-C1
L1-SUS-C2
L1-SUS-C3
L1-SUS-C4
L1-SUS-C5
L1-SUS-C6
L1-SUS-C7
L1-SUS-C8
L1-SEI-C1
Front
Front
Front
Front
Front
Front
L1-SEI-C2
L1-SEI-C3
L1-SEI-C4
L1-SEI-C5
L1-SEI-C6
14 Foot
LDR cables and chiller water pipes
Each Rack is 39” Deep and 24” Wide
CDS Electronics Room (CER)

## Slide 30: LLO CER – 11.5ft Cable Tray Layout
2feet
2 feet
All posts are E-Posts
L1-PSL-C3
L1-PSL-C2
L1-PSL-C1
L1-ISC-C1
L1-ISC-C2
L1-ISC-C3
L1-SUS-C1
L1-SUS-C2
L1-SUS-C3
L1-SUS-C4
L1-SUS-C5
L1-SUS-C6
L1-SUS-C7
L1-SUS-C8
L1-SEI-C1
Front
Front
Front
Front
Front
Front
L1-SEI-C2
L1-SEI-C3
L1-SEI-C4
L1-SEI-C5
L1-SEI-C6
Waterfall down from the LDR for DC Power Cables
Each Rack is 39” Deep and 24” Wide
Waterfall down from the ceiling connects the fiber cable tray to the MSR
CDS Electronics Room (CER)

## Slide 31: LLO CER – Rack Layout
2feet
Each Rack is 39” Deep and 24” Wide
2 feet
L1-FAC-C1
L1-SUS-C1
L1-SUS-C2
L1-SUS-C3
L1-SUS-C4
L1-SUS-C5
L1-SUS-C6
L1-SUS-C7
L1-SUS-C8
L1-SEI-C1
Front
Front
Front
Front
Front
Front
L1-SEI-C2
L1-TCS-C1
L1-SEI-C3
L1-SEI-C4
L1-SEI-C5
L1-SEI-C6
L1-UNK-C3
L1-UNK-C2
L1-UNK-C1
L1-ISC-C1
L1-ISC-C2
L1-ISC-C3
L1-PSL-C1
L1-ISC-C4
L1-OAF-C1
SUS ITMX, ITMY, FMX, FMY, and BS Rack 1
SUS HAM3 and HAM4 Rack 2
SUS HAM3 and HAM4 Rack 1
SUS HAM2 Rack 1
SUS HAM2 Rack 2
SUS ITMX, ITMY, FMX, FMY, and BS Rack 2
SUS HAM5 and HAM6 Rack 1
SUS HAM5 and HAM6 Rack 2
ISC LVEA Rack 1
ISC LVEA Rack 2
ISC LVEA Rack 3
PSL Rack 1
FAC Rack 1
TCS Rack 1
Front
SEI HAM1 and HAM6
SEI HAM2 and HAM3
SEI HAM4 and HAM5
SEI BSC1
SEI BSC2
SEI BSC3
ISC LVEA Rack 4
DAQ Rack 1
3’
11’
18’
25’
8’
28’
6’
21’
8’
Point A
Point B
Point C
6’
L1-AOS-C1
CDS Electronics Room (CER)

## Slide 32: LDR (Laser Diode Room)
LDR
<< LLO Racks by AREA
<< LLO CDS Components
<< LLO Corner Station

## Slide 33: LLO LDR – Rack Layout
<< LLO Racks by AREA
<< LLO CDS Components
<< LLO Corner Station
No posts
CDS Power Room (CPR)
Front
Front
L1-VDC-C5
L1-VDC-C7
L1-VDC-C1
L1-VDC-C2
L1-VDC-C3
L1-VDC-C4
L1-VDC-C6
2feet
Each Rack is 39” Deep and 24” Wide
Laser Diode Room (LDR)
Changing Room
480V Distribution
Panel
208V Distribution
Panel
DC Supplies
2feet
208V Distribution
Panel – CDS1
208V Distribution
Panel – CDS2
LDR Chiller
L1-LDR-C2
L1-LDR-C1
2 feet
Transformer
11’

## Slide 34: LLO LDR – 10ft Cable Tray Layout
Front
Front
L1-VDC-C5
L1-VDC-C7
L1-VDC-C1
L1-VDC-C2
L1-VDC-C3
L1-VDC-C4
L1-VDC-C6
2feet
Each Rack is 39” Deep and 24” Wide
Laser Diode Room (LDR)
Changing Room
480V Distribution
Panel
208V Distribution
Panel
DC Supplies
2feet
208V Distribution
Panel – CDS1
208V Distribution
Panel – CDS2
LDR Chiller
L1-LDR-C2
L1-LDR-C1
2 feet
No posts
L1-LDR-C2
L1-LDR-C1
10 Foot
CDS Power Room (CPR)
Transformer

## Slide 35: CPR (CDS Power Room)
CPR
<< LLO Racks by AREA
<< LLO CDS Components
<< LLO Corner Station

## Slide 36: LLO CPR – Rack Layout
<< LLO Racks by AREA
<< LLO CDS Components
<< LLO Corner Station
Transformer
2feet
Each Rack is 39” Deep and 24” Wide
2 feet
Laser Diode Room (LDR)
Changing Room
480V Distribution
Panel
208V Distribution
Panel
DC Supplies
2feet
208V Distribution
Panel – CDS1
208V Distribution
Panel – CDS2
LDR Chiller
L1-LDR-C2
L1-LDR-C1
CDS Power Room (CPR)
Front
Front
L1-VDC-C5
L1-VDC-C7
L1-VDC-C1
L1-VDC-C2
L1-VDC-C3
L1-VDC-C4
L1-VDC-C6
5.5’

## Slide 37: LLO CPR – 8.5ft (AC) Cable Tray Layout
Front
Front
L1-VDC-C5
L1-VDC-C7
L1-VDC-C1
L1-VDC-C2
L1-VDC-C3
L1-VDC-C4
L1-VDC-C6
2feet
Each Rack is 39” Deep and 24” Wide
2 feet
Laser Diode Room (LDR)
Changing Room
480V Distribution
Panel
208V Distribution
Panel
DC Supplies
2feet
208V Distribution
Panel – CDS1
208V Distribution
Panel – CDS2
LDR Chiller
L1-LDR-C2
L1-LDR-C1
CDS Power Room (CPR)
Transformer
No posts
All posts are F-Posts

## Slide 38: LLO CPR – 10ft (DC) Cable Tray
2feet
Each Rack is 39” Deep and 24” Wide
2 feet
Laser Diode Room (LDR)
Changing Room
480V Distribution
Panel
208V Distribution
Panel
DC Supplies
2feet
No posts
208V Distribution
Panel – CDS1
208V Distribution
Panel – CDS2
LDR Chiller
L1-LDR-C2
L1-LDR-C1
Front
Front
L1-VDC-C5
L1-VDC-C7
L1-VDC-C1
L1-VDC-C2
L1-VDC-C3
L1-VDC-C4
L1-VDC-C6
2feet
CDS Power Room (CPR)
Transformer
All posts are F-Posts
Waterfall up over the LDR for DC Power Cables
Cable tray penetrates wall into CER

## Slide 39: Subsystem: DC Power (VDC)
VDC
<< IFO Subsystems
<< LLO Racks by AREA
<< LLO CDS Components
<< LLO Corner Station
DC Power Supplies >>
CPR Rack Layout >>
CERX DC Rack Layout >>
CERY DC Rack Layout >>

## Slide 40: DC Power Supplies
<< VDC
KEPCO JQE25-20MVPY27274
KEPCO BHK500-80MG
KEPCO JQE36-30M

## Slide 41: KEPCO BHK500-80MG
<< DC Power Supplies
Picture: Front Panel
Picture: Rear Panel
Specifications
Inventory of Serial Numbers / Dates received / scheduled maintenance / assigned use / etc.
Acceptance Testing: LIGO-Txxxxxxx

## Slide 42: KEPCO JQE25-20MVPY27274
<< DC Power Supplies
Acceptance Testing: LIGO-T1100478
Picture: Front Panel
Picture: Rear Panel
Specifications
Inventory of Serial Numbers / Dates received / scheduled maintenance / assigned use / etc.

## Slide 43: KEPCO JQE36-30
<< DC Power Supplies
Acceptance Testing: LIGO-Txxxxxxx
Picture: Front Panel
Picture: Rear Panel
Specifications
Inventory of Serial Numbers / Dates received / scheduled maintenance / assigned use / etc.

## Slide 44: DC Power Rack – Required VDC
A Standard Bank (SB) of power supplies consists of 4 supplies, and services 1 Electronics Rack. The 4 supplies are:
+18V@20A, -18V@20A, +24V@20A, and -24V@20A.
Each Standard Bank of DC Power Supplies provides
18V * 20A => 360W
360W * 2 PS => 720W
24V * 20A => 480W
480W * 2 PS => 960W
720W + 960W => 1680W
There are 5 SB (20 PS) / Power Rack. Each Power Rack therefore provides 8400W
Each Power Rack services 5 Electronics Racks.
There are roughly 22 racks per interferometer.
Therefore 5 DC Power Racks are required and will provide for a total of 42,000 W.
10 x 4U => 40U
5 Standard Banks per Rack
DC Power Rack
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
<< CPR
Notes: For a JQE25-20M: AC power calculations:
125 VAC * 10.5 A => 1312.5 W/PS
20 PS/Rack * 1312.5 W/PS => 26,250 W/Rack
7 Racks * 26,250 W/Rack => 183,750 W
20 PS/Rack * 10.5 A/PS => 210 A/Rack
7 Racks * 210A/Rack => 1470 A

## Slide 45: DC Power Rack – Required VAC
A Standard Bank (SB) of power supplies consists of 4 supplies, and services 1 Electronics Rack. The 4 supplies are:
+18V@20A, -18V@20A, +24V@20A, and -24V@20A.
Each (~JQE25-20M) DC Power Supply requires 10.5A @ 125VAC
Each Standard Bank of DC Power Supplies requires 42A @ 125VAC
There are 5 SB (20 PS) / Power Rack. Each Power Rack therefore requires 210A @ 125VAC.
10 - 125V@20A circuits per Power Rack should suffice.
Each Power Rack services 5 Electronics Racks.
There are roughly 22 racks per interferometer.
70 - 125V @20A circuits are required for a total of 183,750W.
Therefore 2 - 480VAC * 200A circuits would provide 192,000W
10 x 4U => 40U
5 Standard Banks per Rack
DC Power Rack
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
<< CPR
Notes: 125 VAC * 10.5 A => 1312.5 W/PS
20 PS/Rack * 1312.5 W/PS => 26,250 W/Rack
7 Racks * 26,250 W/Rack => 183,750 W
20 PS/Rack * 10.5 A/PS => 210 A/Rack
7 Racks * 210A/Rack => 1470 A

## Slide 46: DC Power Rack – VAC Wiring
12 @ 125V, 20A Circuits per Rack
Rear
Outlet 7
Outlet 8
Outlet 9
Outlet 10
Outlet 11
Outlet 12
Outlet 1
Outlet 2
Outlet 3
Outlet 4
Outlet 5
Outlet 6
DC Power Rack
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
±XVDC @ 20A
Kepco JQE
A
B
A
B
<< CPR
Notes: 12 @ 125V, 20A Circuits

## Slide 47: L1-VDC-C1 Power Racks – Required Supplies
Cable Runs >>
L1-VDC-C1 Power Rack
B
A
L1-VDC-C1 Power Rack
A
B
L1-SUS-C2
L1-SUS-C2
L1-SUS-C3
L1-SUS-C3
L1-SUS-C4
L1-SUS-C4
L1-SUS-C4
L1-SUS-C4
L1-SUS-C5
L1-SUS-C5
L1-SUS-C6
L1-SUS-C6
L1-SUS-C6
L1-SUS-C6
L1-SUS-C7
L1-SUS-C7
L1-SUS-C8
L1-SUS-C8
L1-SUS-C1
L1-SUS-C1
L1-SUS-C2
L1-SUS-C2
L1-SUS-C3
L1-SUS-C3
L1-SUS-C4
L1-SUS-C4
L1-SUS-C4
L1-SUS-C4
L1-SUS-C5
L1-SUS-C5
L1-SUS-C6
L1-SUS-C6
L1-SUS-C6
L1-SUS-C6
L1-SUS-C7
L1-SUS-C7
L1-SUS-C8
L1-SUS-C8
L1-SUS-C1
L1-SUS-C1
<< CPR
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
-18VDC
+18VDC
L1-VDC-C1 Corner Station DC Power Rack Layout (D1200890) (S1105247)

## Slide 48: L1-VDC-C1 Cable Runs
<< L1-VDC-C1
L1-VDC-C1 Corner Station DC Cable Runs (D1200890) (S1105247)
L1-VDC-C1 S1105247 | Power Panel | Circuit | DC Power Rack | Outlet | Plug Position | Rack U | Power Supply Model | Power Supply Serial | Polarity | DC Extension Cable | Electronics Rack | DC Power Strip
1 | CDS-1 | 06 | L1-VDC-C1 | 08 | Top | U37-A (Left) | JQE 25V 20A | H236464 | Plus | PTO-001 | L1-SUS-C8 | PSO-001
2 | CDS-1 | 06 | L1-VDC-C1 | 08 | Bottom | U37-B (Right) | JQE 25V 20A | H236467 | Minus | PTO-001 | L1-SUS-C8 | PSO-001
3 | CDS-1 | 27 | L1-VDC-C1 | 02 | Top | U33-A (Left) | JQE 25V 20A | H236434 | Plus | PTO-002 | L1-SUS-C7 | PSO-002
4 | CDS-1 | 27 | L1-VDC-C1 | 02 | Bottom | U33-B (Right) | JQE 25V 20A | H236427 | Minus | PTO-002 | L1-SUS-C7 | PSO-002
5 | CDS-1 | 08 | L1-VDC-C1 | 09 | Top | U29-A (Left) | JQE 25V 20A | H236468 | Plus | PTO-021 | L1-SUS-C6A | PSO-003
6 | CDS-1 | 08 | L1-VDC-C1 | 09 | Bottom | U29-B (Right) | JQE 25V 20A | H236372-R1 | Minus | PTO-021 | L1-SUS-C6A | PSO-003
7 | CDS-1 | 29 | L1-VDC-C1 | 03 | Top | U25-A (Left) | JQE 25V 20A | H236447 | Plus | PTO-003 | L1-SUS-C6B | PSO-021
8 | CDS-1 | 29 | L1-VDC-C1 | 03 | Bottom | U25-B (Right) | JQE 25V 20A | H236463 | Minus | PTO-003 | L1-SUS-C6B | PSO-021
9 | CDS-1 | 10 | L1-VDC-C1 | 10 | Top | U21-A (Left) | JQE 25V 20A | H236388 | Plus | PTO-004 | L1-SUS-C5 | PSO-004
10 | CDS-1 | 10 | L1-VDC-C1 | 10 | Bottom | U21-B (Right) | JQE 25V 20A | H236406 | Minus | PTO-004 | L1-SUS-C5 | PSO-004
11 | CDS-1 | 31 | L1-VDC-C1 | 04 | Top | U17-A (Left) | JQE 25V 20A | H236396 | Plus | PTO-005 | L1-SUS-C4A | PSO-005
12 | CDS-1 | 31 | L1-VDC-C1 | 04 | Bottom | U17-B (Right) | JQE 25V 20A | H236404 | Minus | PTO-005 | L1-SUS-C4A | PSO-005
13 | CDS-1 | 12 | L1-VDC-C1 | 11 | Top | U13-A (Left) | JQE 25V 20A | H236418 | Plus | PTO-022 | L1-SUS-C4B | PSO-022
14 | CDS-1 | 12 | L1-VDC-C1 | 11 | Bottom | U13-B (Right) | JQE 25V 20A | H236424 | Minus | PTO-022 | L1-SUS-C4B | PSO-022
15 | CDS-1 | 33 | L1-VDC-C1 | 05 | Top | U09-A (Left) | JQE 25V 20A | H236469 | Plus | PTO-006 | L1-SUS-C3 | PSO-006
16 | CDS-1 | 33 | L1-VDC-C1 | 05 | Bottom | U09-B (Right) | JQE 25V 20A | H236443 | Minus | PTO-006 | L1-SUS-C3 | PSO-006
17 | CDS-1 | 14 | L1-VDC-C1 | 12 | Top | U05-A (Left) | JQE 25V 20A | H210616 | Plus | PTO-007 | L1-SUS-C2 | PSO-007
18 | CDS-1 | 14 | L1-VDC-C1 | 12 | Bottom | U05-B (Right) | JQE 25V 20A | H210622 | Minus | PTO-007 | L1-SUS-C2 | PSO-007
19 | CDS-1 | 02 | L1-VDC-C1 | 06 | Top | U01-A (Left) | JQE 25V 20A | H210617 | Plus | PTO-008 | L1-SUS-C1 | PSO-008
20 | CDS-1 | 02 | L1-VDC-C1 | 06 | Bottom | U01-B (Right) | JQE 25V 20A | H210619 | Minus | PTO-008 | L1-SUS-C1 | PSO-008
D1200890 |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 49: L1-VDC-C2 Power Racks – Required Supplies
Cable Runs >>
L1-VDC-C2 Power Rack
B
A
L1-VDC-C2 Power Rack
A
B
L1-ISC-C1
L1-ISC-C1
L1-ISC-C1
L1-ISC-C1
L1-ISC-C2
L1-ISC-C2
L1-ISC-C2
L1-ISC-C2
L1-ISC-C3
L1-ISC-C3
L1-ISC-C3
L1-ISC-C3
L1-ISC-C4
L1-ISC-C4
L1-ISC-C4
L1-ISC-C4
L1-ISC-C3
L1-ISC-C4
L1-ISC-C1
L1-ISC-C2
L1-ISC-C1
L1-ISC-C1
L1-ISC-C1
L1-ISC-C1
L1-ISC-C2
L1-ISC-C2
L1-ISC-C2
L1-ISC-C2
L1-ISC-C3
L1-ISC-C3
L1-ISC-C3
L1-ISC-C3
L1-ISC-C4
L1-ISC-C4
L1-ISC-C4
L1-ISC-C4
L1-ISC-C4
L1-ISC-C3
L1-ISC-C2
L1-ISC-C1
<< CPR
+24VDC
-24VDC
+12VDC
+12VDC
+12VDC
+12VDC
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
-24VDC
-24VDC
+24VDC
+24VDC
-24VDC
-24VDC
+24VDC
+18VDC
-18VDC
-18VDC
+18VDC
-24VDC
+24VDC
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
-24VDC
-24VDC
+24VDC
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
+24VDC
+24VDC
+24VDC
L1-VDC-C2 Corner Station DC Power Rack Layout (D1200891) (S1105248)

## Slide 50: L1-VDC-C2 Cable Runs
<< L1-VDC-C2
L1-VDC-C2 Corner Station DC Cable Runs (D1200891) (S1105248)
L1-VDC-C2 S1105248 | Power Panel | Circuit | DC Power Rack | Outlet | Plug Position | Rack U | Power Supply Model | Power Supply Serial | Polarity | DC Extension Cable | Electronics Rack | DC Power Strip
1 | CDS-1 | 15 | L1-VDC-C2 | 08 | Top | U37-A (Left) | JQE 15V 6A |  | Plus | PTG-002 | L1-ISC-C3 | PSG-003
2 | CDS-1 | 15 | L1-VDC-C2 | 08 | Bottom | U37-B (Right) | JQE 15V 6A |  | Plus | PTG-003 | L1-ISC-C4 | PSG-004
3 | CDS-1 | 03 | L1-VDC-C2 | 02 | Top | U33-A (Left) | JQE 25V 20A | H236408 | Plus | PTY-012 | L1-ISC-C4 | 
4 | CDS-1 | 03 | L1-VDC-C2 | 02 | Bottom | U33-B (Right) | JQE 25V 20A | H236466 | Minus | PTY-012 | L1-ISC-C4 | 
5 | CDS-1 | 17 | L1-VDC-C2 | 09 | Top | U29-A (Left) | JQE 25V 20A | H236426 | Plus | PTO-057 | L1-ISC-C4 | 
6 | CDS-1 | 17 | L1-VDC-C2 | 09 | Bottom | U29-B (Right) | JQE 25V 20A | H236439 | Minus | PTO-057 | L1-ISC-C4 | 
7 | CDS-1 | 05 | L1-VDC-C2 | 03 | Top | U25-A (Left) | JQE 25V 20A | H236437 | Plus | PTY-011 | L1-ISC-C3 | 
8 | CDS-1 | 05 | L1-VDC-C2 | 03 | Bottom | U25-B (Right) | JQE 25V 20A | H236425 | Minus | PTY-011 | L1-ISC-C3 | 
9 | CDS-1 | 19 | L1-VDC-C2 | 10 | Top | U21-A (Left) | JQE 25V 20A | H236444 | Plus | PTO-056 | L1-ISC-C3 | 
10 | CDS-1 | 19 | L1-VDC-C2 | 10 | Bottom | U21-B (Right) | JQE 25V 20A | H236471 | Minus | PTO-056 | L1-ISC-C3 | 
11 | CDS-1 | 07 | L1-VDC-C2 | 04 | Top | U17-A (Left) | JQE 25V 20A | H236431 | Plus | PTY-047 | L1-ISC-C2 | 
12 | CDS-1 | 07 | L1-VDC-C2 | 04 | Bottom | U17-B (Right) | JQE 25V 20A | H236470 | Minus | PTY-047 | L1-ISC-C2 | 
13 | CDS-1 | 21 | L1-VDC-C2 | 11 | Top | U13-A (Left) | JQE 25V 20A | H236430 | Plus | PTO-055 | L1-ISC-C2 | 
14 | CDS-1 | 21 | L1-VDC-C2 | 11 | Bottom | U13-B (Right) | JQE 25V 20A | H236445 | Minus | PTO-055 | L1-ISC-C2 | 
15 | CDS-1 | 09 | L1-VDC-C2 | 05 | Top | U09-A (Left) | JQE 25V 20A |  | Plus | PTY-046 | L1-ISC-C1 | 
16 | CDS-1 | 09 | L1-VDC-C2 | 05 | Bottom | U09-B (Right) | JQE 25V 20A |  | Minus | PTY-046 | L1-ISC-C1 | 
17 | CDS-1 | 23 | L1-VDC-C2 | 12 | Top | U05-A (Left) | JQE 25V 20A | H236475 | Plus | PTO-054 | L1-ISC-C1 | 
18 | CDS-1 | 23 | L1-VDC-C2 | 12 | Bottom | U05-B (Right) | JQE 25V 20A | H236455 | Minus | PTO-054 | L1-ISC-C1 | 
19 | CDS-1 | 06 | L1-VDC-C2 | 06 | Top | U01-A (Left) | JQE 25V 20A | H236399 | Plus | L1-TB02 | L1-ISC-C1 | 
20 | CDS-1 | 06 | L1-VDC-C2 | 06 | Bottom | U01-B (Right) | JQE 25V 20A | H236407 | Plus | L1-TB07 | L1-ISC-C2 | 
D1200891 |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 51: L1-VDC-C3 Power Racks – Required Supplies
Cable Runs >>
L1-VDC-C3 Power Rack
B
A
L1-VDC-C3 Power Rack
A
B
L1-SEI-C1
L1-SEI-C1
L1-SEI-C1
L1-SEI-C1
L1-SEI-C2
L1-SEI-C2
L1-SEI-C2
L1-SEI-C2
L1-SEI-C3
L1-SEI-C4
L1-SEI-C3
L1-SEI-C3
L1-SEI-C3
L1-SEI-C3
L1-SEI-C4
L1-SEI-C4
L1-SEI-C4
L1-SEI-C4
L1-SEI-C1
L1-SEI-C2
L1-SEI-C1
L1-SEI-C1
L1-SEI-C1
L1-SEI-C1
L1-SEI-C2
L1-SEI-C2
L1-SEI-C2
L1-SEI-C2
L1-SEI-C4
L1-SEI-C3
L1-SEI-C3
L1-SEI-C3
L1-SEI-C3
L1-SEI-C3
L1-SEI-C4
L1-SEI-C4
L1-SEI-C4
L1-SEI-C4
L1-SEI-C2
L1-SEI-C1
<< CPR
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
-24VDC
-24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
-24VDC
-24VDC
+24VDC
+24VDC
-24VDC
-24VDC
+24VDC
+24VDC
-24VDC
-24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
L1-VDC-C3 Corner Station DC Power Rack Layout (D1200892) (S1105249)

## Slide 52: L1-VDC-C3 Cable Runs
<< L1-VDC-C3
L1-VDC-C3 Corner Station DC Cable Runs (D1200892) (S1105249)
L1-VDC-C3 S1105249 | Power Panel | Circuit | DC Power Rack | Outlet | Plug Position | Rack U | Power Supply Model | Power Supply Serial | Polarity | DC Extension Cable | Electronics Rack | DC Power Strip
1 | CDS-2 | 15 | L1-VDC-C3 | 08 | Top | U37-A (Left) | JQE 25V 20A | H236457 | Plus | PTO-014 | L1-SEI-C4 | PSO-014
2 | CDS-2 | 15 | L1-VDC-C3 | 08 | Bottom | U37-B (Right) | JQE 25V 20A | H236456 | Minus | PTO-014 | L1-SEI-C4 | PSO-014
3 | CDS-2 | 03 | L1-VDC-C3 | 02 | Top | U33-A (Left) | JQE 25V 20A | H236450 | Plus | PTY-013 | L1-SEI-C4 | PSY-013
4 | CDS-2 | 03 | L1-VDC-C3 | 02 | Bottom | U33-B (Right) | JQE 25V 20A | H236454 | Minus | PTY-013 | L1-SEI-C4 | PSY-013
5 | CDS-2 | 17 | L1-VDC-C3 | 09 | Top | U29-A (Left) | JQE 25V 20A | H236452 | Plus | PTO-015 | L1-SEI-C3 | PSO-015
6 | CDS-2 | 17 | L1-VDC-C3 | 09 | Bottom | U29-B (Right) | JQE 25V 20A | H236451 | Minus | PTO-015 | L1-SEI-C3 | PSO-015
7 | CDS-2 | 05 | L1-VDC-C3 | 03 | Top | U25-A (Left) | JQE 25V 20A | H236458 | Plus | PTY-014 | L1-SEI-C3 | PSY-014
8 | CDS-2 | 05 | L1-VDC-C3 | 03 | Bottom | U25-B (Right) | JQE 25V 20A | H236432 | Minus | PTY-014 | L1-SEI-C3 | PSY-014
9 | CDS-2 | 19 | L1-VDC-C3 | 10 | Top | U21-A (Left) | JQE 25V 20A | H236435 | Plus | PTY-015 | L1-SEI-C3 | PSY-015
10 | CDS-2 | 19 | L1-VDC-C3 | 10 | Bottom | U21-B (Right) | JQE 25V 20A | H236436 | Plus | PTY-016 | L1-SEI-C4 | PSY-016
11 | CDS-2 | 07 | L1-VDC-C3 | 04 | Top | U17-A (Left) | JQE 25V 20A | H236402 | Plus | PTO-016 | L1-SEI-C2 | PSO-016
12 | CDS-2 | 07 | L1-VDC-C3 | 04 | Bottom | U17-B (Right) | JQE 25V 20A | H236477 | Minus | PTO-016 | L1-SEI-C2 | PSO-016
13 | CDS-2 | 21 | L1-VDC-C3 | 11 | Top | U13-A (Left) | JQE 25V 20A | H236384 | Plus | PTY-017 | L1-SEI-C2 | PSY-017
14 | CDS-2 | 21 | L1-VDC-C3 | 11 | Bottom | U13-B (Right) | JQE 25V 20A | H236390 | Minus | PTY-017 | L1-SEI-C2 | PSY-017
15 | CDS-2 | 09 | L1-VDC-C3 | 05 | Top | U09-A (Left) | JQE 25V 20A | H236383 | Plus | PTO-017 | L1-SEI-C1 | PSO-017
16 | CDS-2 | 09 | L1-VDC-C3 | 05 | Bottom | U09-B (Right) | JQE 25V 20A | H236391 | Minus | PTO-017 | L1-SEI-C1 | PSO-017
17 | CDS-2 | 23 | L1-VDC-C3 | 12 | Top | U05-A (Left) | JQE 25V 20A | H236372-R2 | Plus | PTY-018 | L1-SEI-C1 | PSY-018
18 | CDS-2 | 23 | L1-VDC-C3 | 12 | Bottom | U05-B (Right) | JQE 25V 20A | H236377 | Minus | PTY-018 | L1-SEI-C1 | PSY-018
19 | CDS-2 | 11 | L1-VDC-C3 | 06 | Top | U01-A (Left) | JQE 25V 20A | H236401 | Plus | PTY-019 | L1-SEI-C1 | PSY-019
20 | CDS-2 | 11 | L1-VDC-C3 | 06 | Bottom | U01-B (Right) | JQE 25V 20A | H236392 | Plus | PTY-020 | L1-SEI-C2 | PSY-020
D1200892 |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 53: L1-VDC-C4 Power Racks – Required Supplies
Cable Runs >>
L1-VDC-C4 Power Rack
B
A
L1-VDC-C4 Power Rack
A
B
L1-SEI-C5
L1-SEI-C5
L1-SEI-C5
L1-SEI-C5
L1-SEI-C6
L1-SEI-C6
L1-SEI-C6
L1-SEI-C6
L1-SUS-C5B
L1-SUS-C8
L1-SUS-C2
L1-SUS-C3B
L1-PSL-C1
L1-PSL-C1
L1-SEI-C5
L1-SEI-C6
L1-SEI-C5
L1-SEI-C5
L1-SEI-C5
L1-SEI-C5
L1-SEI-C6
L1-SEI-C6
L1-SEI-C6
L1-SEI-C6
L1-SUS-C8
L1-SUS-C5B
L1-SUS-C3B
L1-SUS-C2
L1-PSL-C1
L1-PSL-C1
L1-SEI-C6
L1-SEI-C5
<< CPR
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
-24VDC
-24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
-24VDC
-24VDC
+24VDC
L1-SUS-C5A
L1-SUS-C3A
+24VDC
+24VDC
Unused
L1-PSL-C1
Unused
+24VDC
L1-SUS-C5A
L1-SUS-C3A
+24VDC
+24VDC
L1-PSL-C1
Unused
+24VDC
Unused
L1-VDC-C4 Corner Station DC Power Rack Layout (D1200893) (S1105250)

## Slide 54: L1-VDC-C4 Cable Runs
<< L1-VDC-C4
L1-VDC-C4 S1105250 | Power Panel | Circuit | DC Power Rack | Outlet | Plug Position | Rack U | Power Supply Model | Power Supply Serial | Polarity | DC Extension Cable | Electronics Rack | DC Power Strip
1 | CDS-2 | 26 | L1-VDC-C4 | 08 | Top | U37-A (Left) | JQE 25V 20A | H236442 | Plus | PTO-018 | L1-PSL-C1 | PSO-018
2 | CDS-2 | 26 | L1-VDC-C4 | 08 | Bottom | U37-B (Right) | JQE 25V 20A | H236416 | Minus | PTO-018 | L1-PSL-C1 | PSO-018
3 | CDS-2 | 14 | L1-VDC-C4 | 02 | Top | U33-A (Left) | JQE 25V 20A | H236449 |  |  |  | 
4 | CDS-2 | 14 | L1-VDC-C4 | 02 | Bottom | U33-B (Right) | JQE 25V 20A | H236453 | Plus | PTY-009 | L1-PSL-C1 | PSY-009
5 | CDS-2 | 28 | L1-VDC-C4 | 09 | Top | U29-A (Left) | JQE 25V 20A | H236495 | Plus | PTY-002 | L1-SUS-C5A | None
6 | CDS-2 | 28 | L1-VDC-C4 | 09 | Bottom | U29-B (Right) | JQE 25V 20A | H236375 | Plus | PTY-005 | L1-SUS-C3A | PSY-027
7 | CDS-2 | 16 | L1-VDC-C4 | 03 | Top | U25-A (Left) | JQE 25V 20A | H210621 | Plus | L1-TB03 | L1-SUS-C2 | PSY-004
8 | CDS-2 | 16 | L1-VDC-C4 | 03 | Bottom | U25-B (Right) | JQE 25V 20A | H210620 | Plus | L1-TB04 | L1-SUS-C3B | PSY-005
9 | CDS-2 | 30 | L1-VDC-C4 | 10 | Top | U21-A (Left) | JQE 25V 20A | H210618 | Plus | L1-TB01 | L1-SUS-C5B | PSY-002
10 | CDS-2 | 30 | L1-VDC-C4 | 10 | Bottom | U21-B (Right) | JQE 25V 20A | H236386 | Plus | PTY-001 | L1-SUS-C8 | PSY-001
11 | CDS-2 | 18 | L1-VDC-C4 | 04 | Top | U17-A (Left) | JQE 25V 20A | H236374 | Plus | PTO-019 | L1-SEI-C6 | PSO-019
12 | CDS-2 | 18 | L1-VDC-C4 | 04 | Bottom | U17-B (Right) | JQE 25V 20A | H236382 | Minus | PTO-019 | L1-SEI-C6 | PSO-019
13 | CDS-2 | 32 | L1-VDC-C4 | 11 | Top | U13-A (Left) | JQE 25V 20A | H236373 | Plus | PTY-021 | L1-SEI-C6 | PSY-021
14 | CDS-2 | 32 | L1-VDC-C4 | 11 | Bottom | U13-B (Right) | JQE 25V 20A | H236387 | Minus | PTY-021 | L1-SEI-C6 | PSY-021
15 | CDS-2 | 20 | L1-VDC-C4 | 05 | Top | U09-A (Left) | JQE 25V 20A | H236376 | Plus | PTO-020 | L1-SEI-C5 | PSO-020
16 | CDS-2 | 20 | L1-VDC-C4 | 05 | Bottom | U09-B (Right) | JQE 25V 20A | H236379 | Minus | PTO-020 | L1-SEI-C5 | PSO-020
17 | CDS-2 | 34 | L1-VDC-C4 | 12 | Top | U05-A (Left) | JQE 25V 20A | H236381 | Plus | PTY-022 | L1-SEI-C5 | PSY-022
18 | CDS-2 | 34 | L1-VDC-C4 | 12 | Bottom | U05-B (Right) | JQE 25V 20A | H236385 | Minus | PTY-022 | L1-SEI-C5 | PSY-022
19 | CDS-2 | 22 | L1-VDC-C4 | 06 | Top | U01-A (Left) | JQE 25V 20A | H236415 | Plus | PTY-023 | L1-SEI-C5 | PSY-023
20 | CDS-2 | 22 | L1-VDC-C4 | 06 | Bottom | U01-B (Right) | JQE 25V 20A | H236403 | Plus | PTY-024 | L1-SEI-C6 | PSY-024
D1200893 |  |  |  |  |  |  |  |  |  |  |  | 
L1-VDC-C4 Corner Station DC Cable Runs (D1200893) (S1105250)

## Slide 55: L1-VDC-C5 Power Racks – Required Supplies
Cable Runs >>
<< CPR
L1-VDC-C5 Power Rack
B
A
L1-VDC-C5 Power Rack
A
B
L1-PSL-R1
L1-PSL-R1
L1-PSL-R2
L1-PSL-R2
L1-PSL-R2
L1-PSL-R2
L1-SUS-R1
L1-SUS-R2
L1-SUS-R1
L1-SUS-R2
L1-SUS-R3
L1-SUS-R4
L1-SUS-R6
L1-SUS-R3
L1-SUS-R4
L1-SUS-R6
L1-PSL-R1
L1-PSL-R1
L1-PSL-R1
L1-PSL-R1
L1-PSL-R2
L1-PSL-R2
L1-PSL-R2
L1-PSL-R2
L1-SUS-R1
L1-SUS-R2
L1-SUS-R1
L1-SUS-R2
L1-SUS-R3
L1-SUS-R4
L1-SUS-R6
L1-SUS-R3
L1-SUS-R4
L1-SUS-R6
L1-PSL-R1
L1-PSL-R1
+24VDC
-24VDC
-24VDC
+24VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
-24VDC
-24VDC
+24VDC
L1-VDC-C5 Corner Station DC Power Rack Layout (D1200894) (S1105251)
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused

## Slide 56: L1-VDC-C5 Cable Runs
<< L1-VDC-C5
L1-VDC-C5 Corner Station DC Cable Runs (D1200894) (S1105251)
L1-VDC-C5 S1105251 | Power Panel | Circuit | DC Power Rack | Outlet | Plug Position | Rack U | Power Supply Model | Power Supply Serial | Polarity | DC Extension Cable | Electronics Rack | DC Power Strip
1 | CDS-1 | 25 | L1-VDC-C5 | 08 | Top | U37-A (Left) |  |  |  |  |  | 
2 | CDS-1 | 25 | L1-VDC-C5 | 08 | Bottom | U37-B (Right) |  |  |  |  |  | 
3 | CDS-2 | 13 | L1-VDC-C5 | 02 | Top | U33-A (Left) |  |  |  |  |  | 
4 | CDS-2 | 13 | L1-VDC-C5 | 02 | Bottom | U33-B (Right) |  |  |  |  |  | 
5 | CDS-1 | 13 | L1-VDC-C5 | 09 | Top | U29-A (Left) |  |  |  |  |  | 
6 | CDS-1 | 13 | L1-VDC-C5 | 09 | Bottom | U29-B (Right) |  |  |  |  |  | 
7 | CDS-2 | 38 | L1-VDC-C5 | 03 | Top | U25-A (Left) |  |  |  |  |  | 
8 | CDS-2 | 38 | L1-VDC-C5 | 03 | Bottom | U25-B (Right) |  |  |  |  |  | 
9 | CDS-1 | 01 | L1-VDC-C5 | 10 | Top | U21-A (Left) | JQE 25V 20A | H236420 | Plus | PTO-027 PTO-028 PTO-030 | L1-SUS-R3 L1-SUS-R5 L1-SUS-R6 | 
10 | CDS-1 | 01 | L1-VDC-C5 | 10 | Bottom | U21-B (Right) | JQE 25V 20A | H236378 | Minus | PTO-027 PTO-028 PTO-030 | L1-SUS-R3 L1-SUS-R5 L1-SUS-R6 | 
11 | CDS-2 | 12 | L1-VDC-C5 | 04 | Top | U17-A (Left) | JQE 25V 20A | H236409 | Plus | PTO-023 PTO-024 | L1-SUS-R1 L1-SUS-R2 | 
12 | CDS-2 | 12 | L1-VDC-C5 | 04 | Bottom | U17-B (Right) | JQE 25V 20A | H236410 | Minus | PTO-023 PTO-024 | L1-SUS-R1 L1-SUS-R2 | 
13 | CDS-1 | 04 | L1-VDC-C5 | 11 | Top | U13-A (Left) | JQE 25V 20A | H236380 | Plus | PTO-025 | L1-PSL-R2 | PSO-025
14 | CDS-1 | 04 | L1-VDC-C5 | 11 | Bottom | U13-B (Right) | JQE 25V 20A | H236465 | Minus | PTO-025 | L1-PSL-R2 | PSO-025
15 | CDS-2 | 24 | L1-VDC-C5 | 05 | Top | U09-A (Left) | JQE 25V 20A | H236459 | Plus | PTY-025 | L1-PSL-R2 | PSY-025
16 | CDS-2 | 24 | L1-VDC-C5 | 05 | Bottom | U09-B (Right) | JQE 25V 20A | H236394 | Minus | PTY-025 | L1-PSL-R2 | PSY-025
17 | CDS-2 | 01 | L1-VDC-C5 | 12 | Top | U05-A (Left) | JQE 25V 20A | H236397 | Plus | PTO-026 | L1-PSL-R1 | PSO-026
18 | CDS-2 | 01 | L1-VDC-C5 | 12 | Bottom | U05-B (Right) | JQE 25V 20A | H236400 | Minus | PTO-026 | L1-PSL-R1 | PSO-026
19 | CDS-2 | 36 | L1-VDC-C5 | 06 | Top | U01-A (Left) | JQE 25V 20A | H236393 | Plus | L1-TB05 | L1-PSL-R1 | PSY-026
20 | CDS-2 | 36 | L1-VDC-C5 | 06 | Bottom | U01-B (Right) | JQE 25V 20A | H236398 | Minus | L1-TB05 | L1-PSL-R1 | PSY-026
D1200894 |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 57: L1-VDC-C6 Power Racks – Required Supplies
Cable Runs >>
<< CPR
L1-VDC-C6 Power Rack
B
A
L1-VDC-C6 Power Rack
A
B
L1-OAF-C1
L1-OAF-C1
L1-TCS-C1
L1-TCS-C1
L1-TCS-R2
L1-TCS-R2
L1-TCS-R1
L1-TCS-R1
Unused
Unused
Unused
Unused
L1-PSL-R2
L1-PSL-R2
L1-TCS-C1
L1-OAF-C1
L1-OAF-C1
L1-OAF-C1
L1-TCS-C1
L1-TCS-C1
L1-TCS-R2
L1-TCS-R2
L1-TCS-R1
L1-TCS-R1
Unused
Unused
Unused
Unused
L1-PSL-R2
L1-PSL-R2
L1-OAF-C1
L1-TCS-C1
Unused
Unused
Unused
L1-PSL-R2
L1-FAC-C1
Unused
Unused
Unused
L1-FAC-C1
L1-PSL-R2
Unused
Unused
Unused
Unused
+160VDC
-160VDC
-160VDC
+160VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
+24VDC
+24VDC
+24VDC
Unused
unused
Unused
Unused
L1-PSL-R2
L1-PSL-R2
+12VDC
+12VDC
L1-PSL-R2
L1-PSL-R2
+12VDC
+12VDC
+18VDC
-18VDC
+18VDC
-18VDC
+500VDC
+500VDC
L1-VDC-C6 Corner Station DC Power Rack Layout (D1200895) (S1105252)

## Slide 58: L1-VDC-C6 Cable Runs
<< L1-VDC-C6
L1-VDC-C6 S1105252 | Power Panel | Circuit | DC Power Rack | Outlet | Plug Position | Rack U | Power Supply Model | Power Supply Serial | Polarity | DC Extension Cable | Electronics Rack | DC Power Strip
1 | CDS-2 | 37 | L1-VDC-C6 | 08 | Top | U37-A (Left) | JQE 15V 6A |  | Plus | PTB-001 | L1-PSL-R2 | PSG-002
2 | CDS-2 | 37 | L1-VDC-C6 | 08 | Bottom | U37-B (Right) | JQE 15V 6A |  | Plus | PTG-001 | L1-FAC-C1 | PSG-001
3 | CDS-2 | 31 | L1-VDC-C6 | 02 | Top | U33-A (Left) | BHK 500V 0.4A | C72508 | Plus | PBX-001 | L1-PSL-R2 | 
4 | CDS-2 | 31 | L1-VDC-C6 | 02 | Bottom | U33-B (Right) | BHK 500V 0.4A | C72508 | Plus | PBX-001 | L1-PSL-R2 | 
5 | CDS-2 | 27 | L1-VDC-C6 | 09 | Top | U29-A (Left) | PCX 200V 0.1A |  | Plus | PBX-002 | L1-PSL-R2 | 
6 | CDS-2 | 27 | L1-VDC-C6 | 09 | Bottom | U29-B (Right) | PCX 200V 0.1A |  | Minus | PBX-002 | L1-PSL-R2 | 
7 | CDS-2 | 08 | L1-VDC-C6 | 03 | Top | U25-A (Left) | BHK 500V 80mA | A107262 | Plus | Spare |  | 
8 | CDS-2 | 08 | L1-VDC-C6 | 03 | Bottom | U25-B (Right) | BHK 500V 80mA | A107265 | Minus | Spare |  | 
9 | CDS-2 | 39 | L1-VDC-C6 | 10 | Top | U21-A (Left) | JQE 25V 10A | H222053 |  |  |  | 
10 | CDS-2 | 39 | L1-VDC-C6 | 10 | Bottom | U21-B (Right) | JQE 25V 10A | H207953 |  |  |  | 
11 | CDS-2 | 33 | L1-VDC-C6 | 04 | Top | U17-A (Left) | JQE 25V 10A | H222050 | Plus | PTO-038 | L1-TCS-R1 | 
12 | CDS-2 | 33 | L1-VDC-C6 | 04 | Bottom | U17-B (Right) | JQE 25V 10A | H222056 | Minus | PTO-038 | L1-TCS-R1 | 
13 | CDS-2 | 29 | L1-VDC-C6 | 11 | Top | U13-A (Left) | JQE 25V 10A | H222052 | Plus | PTO-037 | L1-TCS-R2 | 
14 | CDS-2 | 29 | L1-VDC-C6 | 11 | Bottom | U13-B (Right) | JQE 25V 10A | H192369 | Minus | PTO-037 | L1-TCS-R2 | 
15 | CDS-2 | 10 | L1-VDC-C6 | 05 | Top | U09-A (Left) | JQE 25V 10A | H207939 | Plus | PTO-013 | L1-TSC-C1 | 
16 | CDS-2 | 10 | L1-VDC-C6 | 05 | Bottom | U09-B (Right) | JQE 25V 10A | H207941 | Minus | PTO-013 | L1-TSC-C1 | 
17 | CDS-2 | 41 | L1-VDC-C6 | 12 | Top | U05-A (Left) | JQE 25V 20A | H236423 | Plus | PTO-012 | L1-OAF-C1 | 
18 | CDS-2 | 41 | L1-VDC-C6 | 12 | Bottom | U05-B (Right) | JQE 25V 20A | H236413 | Minus | PTO-012 | L1-OAF-C1 | 
19 | CDS-2 | 35 | L1-VDC-C6 | 06 | Top | U01-A (Left) | JQE 25V 20A | H236491 | Plus | PTY-055 | L1-TSC-C1 | 
20 | CDS-2 | 35 | L1-VDC-C6 | 06 | Bottom | U01-B (Right) | JQE 25V 20A | H236472 | Plus | PTY-053 | L1-OAF-C1 | 
D1200895 |  |  |  |  |  |  |  |  |  |  |  | 
L1-VDC-C6 Corner Station DC Cable Runs (D1200895) (S1105252)

## Slide 59: L1-VDC-C7 Power Racks – Required Supplies
Cable Runs >>
<< CPR
L1-VDC-C7 Power Rack
B
A
L1-VDC-C7 Power Rack
A
B
L1-ISC-R5
L1-ISC-R5
+18VDC
-18VDC
L1-ISC-R5
L1-ISC-R5
-18VDC
+18VDC
L1-ISC-R2
L1-ISC-R2
+18VDC
-18VDC
L1-ISC-R2
L1-ISC-R2
-18VDC
+18VDC
L1-ISC-R3 L1-ISC-R5
L1-ISC-R3 L1-ISC-R5
+24VDC
-24VDC
L1-ISC-R3 L1-ISC-R5
L1-ISC-R3 L1-ISC-R5
-24VDC
+24VDC
L1-ISC-R4
L1-ISC-R4
+18VDC
-18VDC
L1-ISC-R4
L1-ISC-R4
-18VDC
+18VDC
L1-ISC-R1 L1-ISC-R2
L1-ISC-R4
L1-ISC-R1 L1-ISC-R2
L1-ISC-R4
+24VDC
-24VDC
L1-ISC-R1 L1-ISC-R2
L1-ISC-R4
L1-ISC-R1 L1-ISC-R2
L1-ISC-R4
-24VDC
+24VDC
L1-ISC-R3
L1-ISC-R3
+18VDC
-18VDC
L1-ISC-R3
L1-ISC-R3
-18VDC
+18VDC
L1-ISC-R1
L1-ISC-R1
-18VDC
+18VDC
L1-ISC-R1
L1-ISC-R1
+18VDC
-18VDC
L1-VDC-C7 Corner Station DC Power Rack Layout (D1200896) (S1105253)

## Slide 60: L1-VDC-C7 Cable Runs
<< L1-VDC-C7
L1-VDC-C7 S1105253 | Power Panel | Circuit | DC Power Rack | Outlet | Plug Position | Rack U | Power Supply Model | Power Supply Serial | Polarity | DC Extension Cable | Electronics Rack | DC Power Strip
1 | CDS-1 | 22 | L1-VDC-C5 | 07 | Top | U37-A (Left) |  |  |  |  |  | 
2 | CDS-1 | 22 | L1-VDC-C5 | 07 | Bottom | U37-B (Right) |  |  |  |  |  | 
3 | CDS-1 | 16 | L1-VDC-C5 | 01 | Top | U33-A (Left) |  |  |  |  |  | 
4 | CDS-1 | 16 | L1-VDC-C5 | 01 | Bottom | U33-B (Right) |  |  |  |  |  | 
5 | CDS-1 | 34 | L1-VDC-C7 | 08 | Top | U29-A (Left) |  |  |  |  |  | 
6 | CDS-1 | 34 | L1-VDC-C7 | 08 | Bottom | U29-B (Right) |  |  |  |  |  | 
7 | CDS-1 | 28 | L1-VDC-C7 | 02 | Top | U25-A (Left) | JQE 25V 20A | H236405 | Plus | L1-TB06 PTY-048 PTY-049 | L1-ISC-R1 L1-ISC-R2 L1-ISC-R4 | 
8 | CDS-1 | 28 | L1-VDC-C7 | 02 | Bottom | U25-B (Right) | JQE 25V 20A | H236411 | Minus | L1-TB06 PTY-048 PTY-049 | L1-ISC-R1 L1-ISC-R2 L1-ISC-R4 | 
9 | CDS-1 | 24 | L1-VDC-C7 | 09 | Top | U21-A (Left) | JQE 25V 20A | H236460 | Plus | PTY-050 PTY-051 | L1-ISC-R3 L1-ISC-R5 | 
10 | CDS-1 | 24 | L1-VDC-C7 | 09 | Bottom | U21-B (Right) | JQE 25V 20A | H236433 | Minus | PTY-050 PTY-051 | L1-ISC-R3 L1-ISC-R5 | 
11 | CDS-1 | 18 | L1-VDC-C7 | 03 | Top | U17-A (Left) | JQE 25V 20A | H236448 | Plus | PTO-061 | L1-ISC-R5 | 
12 | CDS-1 | 18 | L1-VDC-C7 | 03 | Bottom | U17-B (Right) | JQE 25V 20A | H236446 | Minus | PTO-061 | L1-ISC-R5 | 
13 | CDS-2 | 02 | L1-VDC-C7 | 10 | Top | U13-A (Left) | JQE 25V 20A | H236440 | Plus | PTO-060 | L1-ISC-R4 | 
14 | CDS-2 | 02 | L1-VDC-C7 | 10 | Bottom | U13-B (Right) | JQE 25V 20A | H236485 | Minus | PTO-060 | L1-ISC-R4 | 
15 | CDS-1 | 30 | L1-VDC-C7 | 04 | Top | U09-A (Left) | JQE 25V 20A | H236419 | Plus | PTO-059 | L1-ISC-R3 | 
16 | CDS-1 | 30 | L1-VDC-C7 | 04 | Bottom | U09-B (Right) | JQE 25V 20A | H236412 | Minus | PTO-059 | L1-ISC-R3 | 
17 | CDS-1 | 26 | L1-VDC-C7 | 11 | Top | U05-A (Left) | JQE 25V 20A | H236429 | Plus | PTO-059 | L1-ISC-R2 | 
18 | CDS-1 | 26 | L1-VDC-C7 | 11 | Bottom | U05-B (Right) | JQE 25V 20A | H236462 | Minus | PTO-059 | L1-ISC-R2 | 
19 | CDS-1 | 20 | L1-VDC-C7 | 05 | Top | U01-A (Left) | JQE 25V 20A | H236417 | Plus | PTO-058 | L1-ISC-R1 | 
20 | CDS-1 | 20 | L1-VDC-C7 | 05 | Bottom | U01-B (Right) | JQE 25V 20A | H236421 | Minus | PTO-058 | L1-ISC-R1 | 
D1200896 |  |  |  |  |  |  |  |  |  |  |  | 
L1-VDC-C7 Corner Station DC Cable Runs (D1200896) (S1105253)

## Slide 61: Subsystem: AOS / TCS (Auxiliary Optics)
<< IFO Subsystems
2feet
Each Rack is 39” Deep and 24” Wide
2 feet
L1-FAC-C1
L1-SUS-C1
L1-SUS-C2
L1-SUS-C3
L1-SUS-C4
L1-SUS-C5
L1-SUS-C6
L1-SUS-C7
L1-SUS-C8
L1-SEI-C1
Front
Front
Front
Front
Front
Front
L1-SEI-C2
L1-AOS-C1
L1-SEI-C3
L1-SEI-C4
L1-SEI-C5
L1-SEI-C6
L1-UNK-C3
L1-UNK-C2
L1-UNK-C1
L1-PSL-C1
CDS Electronics Room (CER)
L1-OAF-C1
SUS ITMX, ITMY, FMX, FMY, and BS Rack 1
SUS HAM3 and HAM4 Rack 2
SUS HAM3 and HAM4 Rack 1
SUS HAM2 Rack 1
SUS HAM2 Rack 2
SUS ITMX, ITMY, FMX, FMY, and BS Rack 2
SUS HAM5 and HAM6 Rack 1
SUS HAM5 and HAM6 Rack 2
ISC LVEA Rack 1
ISC LVEA Rack 2
ISC LVEA Rack 3
PSL Rack 1
DAQ Rack 1
TCS Rack 1
Front
SEI HAM1 and HAM6
SEI HAM2 and HAM3
SEI HAM4 and HAM5
SEI BSC1
SEI BSC2
SEI BSC3
ISC LVEA Rack 4
Op Lev Docs : E1200031 and T1000097
LIGO-D1200258
IO Diagram: D1100909
L1-ISC-C1
L1-ISC-C2
L1-ISC-C3
L1-ISC-C4
AOS
TCS

## Slide 62: L1-AOS-C1
AOS Rack Layout (D1200258) (S1202974)
<< CER
PSO-013
PSY-011
l1tcs0 I/O Extension Chassis
D1001715
+24@5A
S1103894
Anti-Image Chassis
D070081
±18@0.5A
SN:
Anti-Alias Chassis
D0902783
±18@0.5A
Sxxxxxx
Anti-Alias Chassis
D0902783
±18@0.5A
Sxxxxxx
Ring Heater Driver
D1003254
±18@?A
S1201846
Ring Heater Driver
D1003254
±18@?A
S1201844
TCS Beckhoff Chassis
D1102207
+24@5.0A
SN:
L1-AOS-C1 is part of E1100895

## Slide 63: L1-AOS-C1 Details
L1-AOS-C1 Details
<< L1-AOS-C1

## Slide 64: D1003254–S1201844
S1201844
Rear
D1003254
Front
<< L1-AOS-C1
Ring Heater Driver
D1003254
±18@?A
S1201844
This is an early revision of the front panel. It now has one DB37M connector.
20121205 dlk
D1003254
White label
20121205 dlk
Label
Cable to Ring Heater
Label
Description

## Slide 65: D1003254–S1201846
D1003254
Front
<< L1-AOS-C1
Ring Heater Driver
D1003254
±18@?A
S1201846
S1201846
Rear
D1003254
Front
This is an early revision of the front panel. It now has one DB37M connector.
20121205 dlk
Label
Cable to Ring Heater
Label
Description
D1003254
White label
20121205 dlk

## Slide 66: D070081-Sxxxxxxx
Anti-Image Chassis
D070081
±18@0.5A
Sxxxxxxx
D070081
Front
Sxxxxxxx
Rear
From DAC Adapter
XXX
From DAC Adapter
XXX
OUT 1-4
XXX
OUT 5-8
XXX
OUT 9-12
XXX
OUT 13-16
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
<< L1-AOS-C1

## Slide 67: D0902783-Sxxxxxxx
D070081
Front
Sxxxxxx
Rear
Anti-Alias Chassis
D0902783
±18@0.5A
Sxxxxxx
XXX
IN 1-4
XXX
IN 17-20
XXX
IN 5-8
XXX
IN 9-12
XXX
IN 13-16
XXX
IN 21-24
XXX
IN 25-28
XXX
IN 29-32
To ADC Adapter
XXX
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-AOS-C1

## Slide 68: D0902783-Sxxxxxxx
D070081
Front
Sxxxxxx
Rear
Anti-Alias Chassis
D0902783
±18@0.5A
Sxxxxxx
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-AOS-C1
XXX
IN 1-4
XXX
IN 17-20
XXX
IN 5-8
XXX
IN 9-12
XXX
IN 13-16
XXX
IN 21-24
XXX
IN 25-28
XXX
IN 29-32
XXX
To ADC Adapter

## Slide 69: D1001715 – S1103894
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1103894
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1tcs0 I/O Extension Chassis
D1001715
110VAC
S1103894
l1aos0 – IO Chassis
Slot P7
ADC Adapter
Sxxxxxxx
<< L1-AOS-C1

## Slide 70: D1102207-Sxxxxxxx
TCS Beckhoff Chassis
D1102207
+24@5.0A
SN:
Sxxxxxx
Rear
D1102207
Front
<< L1-AOS-C1

## Slide 71: Subsystem: FAC (Facilities)
2feet
Each Rack is 39” Deep and 24” Wide
2 feet
L1-SUS-C1
L1-SUS-C2
L1-SUS-C3
L1-SUS-C4
L1-SUS-C5
L1-SUS-C6
L1-SUS-C7
L1-SUS-C8
L1-SEI-C1
Front
Front
Front
Front
Front
Front
L1-SEI-C2
L1-AOS-C1
L1-SEI-C3
L1-SEI-C4
L1-SEI-C5
L1-SEI-C6
L1-UNK-C3
L1-UNK-C2
L1-UNK-C1
L1-PSL-C1
CDS Electronics Room (CER)
L1-OAF-C1
SUS ITMX, ITMY, FMX, FMY, and BS Rack 1
SUS HAM3 and HAM4 Rack 2
SUS HAM3 and HAM4 Rack 1
SUS HAM2 Rack 1
SUS HAM2 Rack 2
SUS ITMX, ITMY, FMX, FMY, and BS Rack 2
SUS HAM5 and HAM6 Rack 1
SUS HAM5 and HAM6 Rack 2
ISC LVEA Rack 1
ISC LVEA Rack 2
ISC LVEA Rack 3
PSL Rack 1
DAQ Rack 1
TCS Rack 1
Front
SEI HAM1 and HAM6
SEI HAM2 and HAM3
SEI HAM4 and HAM5
SEI BSC1
SEI BSC2
SEI BSC3
ISC LVEA Rack 4
L1-FAC-C1
<< IFO Subsystems
L1-ISC-C1
L1-ISC-C2
L1-ISC-C3
L1-ISC-C4
FAC

## Slide 72: L1-FAC-C1
L1-FAC-C1 Rack Layout (D1200940) (S1202403)
<< CER
Fiber Patch Panel
Dxxxxxxx
No Power
Sxxxxxxx
Timing Master (Fanout)
D070011
+12VDC
S1107512
Fiber Patch Panel
No Power
Sxxxxxxx
Dxxxxxxx
Shelf
Shelf
Shelf

## Slide 73: L1-FAC-C1 Details
L1-FAC-C1 Details
<< L1-FAC-C1

## Slide 74: Dxxxxxxx – Sxxxxxxx
Fiber Patch Panel
Dxxxxxxx
No Power
Sxxxxxxx
D070011
Front
S1107511
Rear
<< L1-FAC-C1
Fibercables.com

## Slide 75: D070011 – S1107512
Timing Master (Fanout)
D070011
+12VDC
S1107512
D070011
Front
S1107512
Rear
x
x
x
<< L1-FAC-C1
x

## Slide 76: Fiber Patch Panel
Fiber Patch Panel
No Power
Sxxxxxxx
Dxxxxxxx
<< L1-FAC-C1

## Slide 77: Subsystem: OAF (Online Adaptive Filtering)
2feet
Each Rack is 39” Deep and 24” Wide
2 feet
L1-SUS-C1
L1-SUS-C2
L1-SUS-C3
L1-SUS-C4
L1-SUS-C5
L1-SUS-C6
L1-SUS-C7
L1-SUS-C8
L1-SEI-C1
Front
Front
Front
Front
Front
Front
L1-SEI-C2
L1-AOS-C1
L1-SEI-C3
L1-SEI-C4
L1-SEI-C5
L1-SEI-C6
L1-UNK-C3
L1-UNK-C2
L1-UNK-C1
L1-PSL-C1
CDS Electronics Room (CER)
L1-OAF-C1
SUS ITMX, ITMY, FMX, FMY, and BS Rack 1
SUS HAM3 and HAM4 Rack 2
SUS HAM3 and HAM4 Rack 1
SUS HAM2 Rack 1
SUS HAM2 Rack 2
SUS ITMX, ITMY, FMX, FMY, and BS Rack 2
SUS HAM5 and HAM6 Rack 1
SUS HAM5 and HAM6 Rack 2
ISC LVEA Rack 1
ISC LVEA Rack 2
ISC LVEA Rack 3
PSL Rack 1
DAQ Rack 1
TCS Rack 1
Front
SEI HAM1 and HAM6
SEI HAM2 and HAM3
SEI HAM4 and HAM5
SEI BSC1
SEI BSC2
SEI BSC3
ISC LVEA Rack 4
L1-FAC-C1
<< IFO Subsystems
L1-ISC-C1
L1-ISC-C2
L1-ISC-C3
L1-ISC-C4
OAF
PEM DAQ

## Slide 78: L1-OAF-C1
+12VDC ?A
-12VDC ?A
+18VDC ?A
-18VDC ?A
+24VDC ?A
-24VDC ?A
High Voltage ?A
l1oaf0 I/O Extension Chassis
D1001715
+24@5A
S1103894
Accelerometer Power Supply
Isotron 2973
Power
Sxxxxxxx
<< CER
PSO-012
PSY-012
L1-OAF-C1 Rack Layout (D1200941) (S1202404)
aLIGO AA Interface Chassis (32 BNC x10 Gain Version)
D1001421
+/-18VDC
S1001057

## Slide 79: L1-OAF-C1 Details
L1-OAF-C1 Details
<< L1-OAF-C1

## Slide 80: Endevco Isotron 2793
<< L1-OAF-C1
Sxxxxxxx
Rear
Isotron 2793
Front
ACCX
ACCY
Unused
ACCZ
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
ACCZ
Unused
ACCY
ACCX
Accelerometer Power Supply
Isotron 2973
Power
Sxxxxxxx

## Slide 81: Endevco Isotron 2793
Sxxxxxxx
Rear
Isotron 2793
Front
ACCX
ACCY
Unused
ACCZ
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
ACCZ
Unused
ACCY
ACCX
Accelerometer Power Supply
Isotron 2973
Power
Sxxxxxxx
<< L1-OAF-C1

## Slide 82: D1001421 – S1001057
S1001057
Rear
To ADC Adapter
To l1oaf0 Slot P1
To ADC Adapter
D1001421
Front
aLIGO AA Interface Chassis (32 BNC, x10 Gain Version)
D1001421
Power
S1001057 :
MAG X
1
MAG Y
2
MAG Z
3
SEI X
4
SEI Y
5
SEI Z
6
Isotron 1
7
Isotron 2
8
Isotron 4
9
BSC4 MIC
10
BAY MIC
11
BSC4 TEMP
12
OPLEV 10
13
Unused
14
Unused
15
Unused
16
Unused
17
Unused
18
Unused
19
Unused
20
Unused
21
Unused
22
Unused
23
Unused
24
Unused
25
Unused
26
Unused
27
Unused
28
Unused
29
Unused
30
Unused
31
Unused
32
<< L1-OAF-C1

## Slide 83: l1oaf0 - D1001715 – S1103844
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1103844
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
D1001421
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1oaf0 I/O Extension Chassis
D1001715
+24VDC
S1103844
l1oaf0 - D1001715 – I/O Extender
<< L1-OAF-C1
ADC Adapter
Sxxxxxxx

## Slide 84: L1 PEM Sensor Details
<< L1-OAF-C1
D1200615

## Slide 85: Current PEM (2008)
Accelerometers
  10-8 f-2 m Hz-1/2
  10-200Hz (256Hz, 16bit)
Seismometers
  3 x 10-10 f-2 m Hz-1/2
  0-10 Hz (256Hz, 16bit, 3 axis)
Microphones
  10 Pa Hz-1/2
  10-1000Hz (2048Hz, 16bit)
RF receivers
  10μV/m
  1.3GHz (2048Hz, 6x16bit)
Residual Gas in Vacuum System
Vacuum contamination Monitor
Weather Station
  T (1K), RH (10%), percipitation (10%), Wind (1mph)

## Slide 86: Current PEM (2008)
Tiltmeters
  2 x 10-9 f-2 rad Hz-1/2
  0-10Hz (256Hz, 16bit, 2 axis)
Dust Monitors
Muon (Charged Particle) Detector
  10-4μ/s/m2
  1 msec (2048Hz, 16bit)
Cosmic Rays
Magnetometer
  2 x 10-11 T.Hz-1/2
  1 kHz (2048Hz, 3x16bit)
Coil magnetometer
  2 x 10-12 T.Hz-1/2
  1 kHz (2048Hz, 16bit)
Scintillator detector
Power Line Monitor

## Slide 87: D1001715 – S1103894
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1103894
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1oaf0 I/O Extension Chassis
D1001715
110VAC
S1103894
<< L1-OAF-C1
l1oaf0 – IO Chassis
Slot P7
ADC Adapter
Sxxxxxxx

## Slide 88: PCIe to Fiber Cable Adapter

## Slide 89: Accelerometers (1)
Isotron Power Supply Model 2793 has 16 channels
This model does NOT come with a DC option.
There is a 3-channel Power Supply that has a DC option, but it has many other features not desired.
It appears that a short (6”) 10-32 to BNC cable can be ordered, but care should be given to strain relief considerations.
Only Wilcoxon Accelerometers are used for PEM
Isotron Model 2793
DAQIC
Isotron Model 2793
DAQIC
Front
Rear
AC Powered
15VDC Powered
DB25 Cable “hardwired”
Accelerometer (in the field)
PSL X
PSL Y
PSL Z
ISCT1 X
ISCT1 Y
ISCT1 Z
HAM1 X
HAM1 Y aka HAM6 X
HAM1 Z
HAM2 X
HAM2 Y aka HAM6 Y
HAM2 Z
HAM3 X
HAM3 Y aka HAM6 Z
HAM3 Z
BSC1 X
BSC1 Y
BSC1 Z
BSC2 X
BSC2 Y
BSC2 Z
BSC3 X
BSC3 Y
BSC3 Z
HAM6 X
HAM6 Y
HAM6 Z
BSC4 X (VEAX)
BSC4 Y (VEAX)
BSC4 Z (VEAX)
BSC5 X (VEAY)
BSC5 Y (VEAY)
BSC5 Z (VEAY)
Accelerometer locations:
1X5
1X20
1Y20

## Slide 90: Accelerometers (2)

## Slide 91: Accelerometers (3)

## Slide 92: Accelerometers (3)

## Slide 93: Antennas
Converter?
AOR (Authority On Radio) AR5000 Radio Receiver
Doug Lormand?
There are two antennas of interest.
Roof Antenna
CDS High-bay Antenna
The Roof Antenna
Receiver is located in the MSR
219.84 MHz FM
Agilent E3610A DC Power Supply (8V, 3A; 16V, 1.5A)
12VDC Wall Wart
To Roof?
IF Output
AC Power
To where?

## Slide 94: Cameras (Video)
Mike Fyffe?

## Slide 95: Humidity (and Temperature) Sensors
(J.) David Barker says this is the Siemens System
Humidity sensor locations
Room 172 – LDR Changing Room

## Slide 96: Magnetometer (1)
12VDC Wall Wart
D070443
Magnetometer Filter
Magnetometer Power Supply
(MAG-03PSU)
Magnetometer
MAG-03MCES
X
Y
Z
X
Y
Z
Magnetometer: Bartington Instruments MAG-03MC
5 meter
X
Y
Z
D030574
Pin 1: +15VDC … Red/Blk RED
Pin 2: Ground … Red/Blk BLACK
Pin 3: -15VDC … Wht/Blk WHITE
Pin 4: Ground … Wht/Blk BLACK
T1100382
9-18VDC Power

## Slide 97: Magnetometers (2) Filter Schematic
D030574

## Slide 98: Magnetometers (3) Amplifier Sketch

## Slide 99: Microphones
The Manufacturer is Bruel & Kjaer
Microphone locations / Pair
PSL / ISCT1
ISCT1 / PSL
HAM1 / HAM3
HAM3 / HAM1
BSC2 (aka LVEA) / HAM6
BSC1 / BSC3
BSC3 / BSC1
HAM6 / LVEA
BSC4 (X) / not paired
BSC5 (Y)/ not paired
LSR (aka CDS High-bay) / not paired
VEAX Bay Mic / not paired
VEAY Bay Mic / not paired
2 meter cable
Extension cables are available – 3m, 10m, and 30m
Since the power supply handles two microphones, the microphones are ‘paired’ in certain places.

## Slide 100: Microphones – Power Adaptor Cable

## Slide 101: Particle Counters (Dust Monitors)
Dust Monitors are not on during Science Mode due to the acoustic noise.
This noise is the air pump. It is always on.
The manufacturer is Pacific Scientific
Old ones (being replaced) are MET One 227B. (9VDC)
New ones (replacements) are MET One GT-321. (9VDC, 2A)
These are scattered throughout the LVEA and usually two of them share a power supply via a cable to a junction box. They are powered from the serial interface port. Not sure if this is a homemade adaptation.
The Junction Box needs documentation.
9VDC Wall Wart
MET One 227B
MET One
GT-321
9VDC Wall Wart

## Slide 102: Comtrol DeviceMaster with DB9 Ports
Comtrol DeviceMaster 4 with DB9 Ports
3M Shell 3357-9209
3M Shell 3357-9209
2.1mm Socket
(Note polarity)

## Slide 103: Particle Counter Y-Cable – Comtrol End
This cable is configured to carry both DC Power and RS485 Signals. The 2.1mm Socket can come from a commercially available 2.1mm Cable Assembly. Note the center pin of the 2.1mm is NEGATIVE. And both shields are tied together and tied to both backshells.

## Slide 104: Particle Counter Y-Cable – Particle Counter End
This cable is configured to carry both DC Power and RS485 Signals. The 2.1mm Plug can come from a commercially available 2.1mm Cable Assembly. Note the center conductor of the 2.1mm is NEGATIVE. And both shields are tied together and are tied only to the backshell that connects to the cable. The backshell connected to the Particle Counter is NOT tied to the shields.

## Slide 105: Particle Counter Extension Cable
This cable is configured to carry both DC Power and RS485 Signals. Note that both shields are tied together and tied to both backshells.
It is 70’ from the L1-FAC-XC1 Rack to the knee of the waterfall in the VEAX.
It is 65’ from the L1-FAC-YC1 Rack to the knee of the waterfall in the VEAY.

## Slide 106: 3M Backshell Assembly
This is a sample drawing of the 3M backshell showing how the E-Ring is attached to the Lock Screw, and showing how the Cover Nut holds the backshell in place.

## Slide 107: Particle Counters (Met One 227B)
3M Shell 3357-9209
3M Shell 3357-9209

## Slide 108: Particle Counters (GT-321)

## Slide 109: Temperature Sensors
Temperature Sensor locations
BSC1 (LVEA) – one old, one new
BSC3 (LVEA)
BSC4 (VEAX)
BSC5 (VEAY)
Temperature Sensors include thermocouples:
Are there any read in the chiller lines? TCS, PSL?
There are thermocouples in the vacuum system for the N2 tanks.

## Slide 110: Temperature Sensors
T0900287
These cables can be replaced with standard +-18VDC

## Slide 111: Voltage Monitor (1)
PEM Voltage Monitor locations:
LVEA - Rack 1X5 – DAQIC2, BNC Port 13
VEAX – Rack 1X20 – DAQIC2, BNC Port ?
VEAY – Rack 1Y20 – DAQIC2, BNC Port 10
This monitor is labeled, “PEM Voltage Monitor No. CAS-Vxx.” The circuit board inside says, “LHO EE Power Monitor Board D0000TBD.” Documentation is scarce. This device is probably OK for monitoring the single balanced power into which it is plugged in Rack 1X5. It is intended to record the differential between the two phases of the balanced power. But if it is used on any ‘real’ AC circuit, it creates the potential for a ½ line voltage ground loop between neutral and ground, and another between hot and ground.
Additionally, even in the balanced power situation, NEUTRAL is the wrong designation, for none of the conductors is neutral in a balanced power circuit: it is the negative AC power.
The circuit ties all shields together, so current loops exist between 2 potentially different AC circuits.
And also the cable ties all shields together, creating the same problem.
And most ironic, the monitor in Rack 1X5 is NOT being read at all: there is no signal name, but it is plugged in. (This was NOT true in September 2009 when inventory of the DAQIC signals was last taken.)
At the Y-end, the AC cable has only three BNC connectors. Two are connected to the Voltage Monitor box.
At the X-end, the AC cable has all four BNC connectors, but they are cross-connected to the Voltage Monitor Box: Cable HOT1, NEU1, HOT2, NEU2 are connected to Box HOT2, NEU2, HOT1, NEU1 and I did not check the cable for accuracy. I did note it only has 2 wires coming into the CP4 port, however, but which two is not clear.
Comments as of 20100525
LHO EE
Power Monitor Board
D000TBD?

## Slide 112: Voltage Monitor (2)
Photos as of 20100525

## Slide 113: Voltage Monitor (3)
CP-4 Socket Pins:
Hot 1 - fused
Neutral 1
Hot 2 - fused
Neutral 2
R1,R3,R5,R7 = 1MΩ
R2,R4,R6,R8 = 1kΩ
Fuse1,2 = 250V, ¼A
R1
R2
R3
R5
R7
R4
R6
R8
Fuse 2
Fuse 1
J1 – Hot 1
J2 – Neutral 1
J4 – Neutral 2
J3 – Hot 2
PEM Voltage Monitor No. CAS-V11
J2 – Neutral 1
J1 – Hot 1
2 - Fuses – 250V ¼A
AC Power (input to monitor)
J4 – Neutral 2
J3 – Hot 2
Outputs
CP-4 Plug Pins:
Hot 1
Neutral 1
Hot
Ground
Neutral
Internal Design and Interfaces as of 20100525

## Slide 114: Voltage Monitor (4)
Lemo 4-Pin:
Neutral 1
Neutral 2
Hot 2 - fused
Hot 1 - fused
Shield
J1 – Hot 1
J2 – Neutral 1
J4 – Neutral 2
J3 – Hot 2
Cable: From 4 BNC connectors to 4-Pin Lemo on DAQIC-2
Cable design as of 20100525

## Slide 115: Wall Warts and Other Items Requiring Power
Lights
Vacuum Equipment
Rechargeable Flashlights
Computer Monitors
Optical Isolators
Trouble Lights
Warning Signs
Laser Hazard Status Signs
Laser Danger Signs
Loudspeakers
Telephones

## Slide 116: Weather Sensors
Weather Sensor locations
LLO network
LSU network

## Slide 117: Subsystem: ISC (Interferometer Sensing and Control)
2feet
Each Rack is 39” Deep and 24” Wide
2 feet
L1-SUS-C1
L1-SUS-C2
L1-SUS-C3
L1-SUS-C4
L1-SUS-C5
L1-SUS-C6
L1-SUS-C7
L1-SUS-C8
L1-SEI-C1
Front
Front
Front
Front
Front
Front
L1-SEI-C2
L1-AOS-C1
L1-SEI-C3
L1-SEI-C4
L1-SEI-C5
L1-SEI-C6
L1-UNK-C3
L1-UNK-C2
L1-UNK-C1
L1-ISC-C1
L1-ISC-C2
L1-ISC-C3
L1-PSL-C1
CDS Electronics Room (CER)
L1-ISC-C4
L1-OAF-C1
SUS ITMX, ITMY, FMX, FMY, and BS Rack 1
SUS HAM3 and HAM4 Rack 2
SUS HAM3 and HAM4 Rack 1
SUS HAM2 Rack 1
SUS HAM2 Rack 2
SUS ITMX, ITMY, FMX, FMY, and BS Rack 2
SUS HAM5 and HAM6 Rack 1
SUS HAM5 and HAM6 Rack 2
ISC LVEA Rack 1
ISC LVEA Rack 2
ISC LVEA Rack 3
PSL Rack 1
DAQ Rack 1
TCS Rack 1
Front
SEI HAM1 and HAM6
SEI HAM2 and HAM3
SEI HAM4 and HAM5
SEI BSC1
SEI BSC2
SEI BSC3
ISC LVEA Rack 4
L1-FAC-C1
<< IFO Subsystems
ISC

## Slide 118: LLO ISC Equipment
CER
LDR
CPR
LVEA
MSR
CUR
VEAY
VEAX
D1000653
D1002803
D1002803
D1100909
IO Stuff

## Slide 119: L1-ISC-C1
ISC LVEA Rack 1 Layout (D1200949) (S1201186)
OMC Piezo Driver
Dxxxxxxx
+?@1A
Sxxxxxx
ISC HAM-A Coil Driver (Tip/Tilt OMC)
D1100687
±18@0.25A
S1106047
<< CER
IO Diagram: D1100909
l1lsc0 I/O Extension Chassis
D1001715
+24@5A
S1106342
l1asc0 I/O Extension Chassis
D1001715
+24@5A
S1106300
ISC Anti-Image Chassis (LSC)
D070081
±18@0.5A
S1102757
ISC Anti-Alias Chassis (LSC)
D0902783
±18@0.5A
S1102779
ISC Anti-Alias Chassis (LSC)
D0902783
±18@0.5A
S1102768
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
Sxxxxxx
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102708
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102771
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102775
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102769
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102767
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102772
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102773
Beam Diverter Controller
Dxxxxxxx
+?@1A
Sxxxxxx
Beam Diverter Controller
Dxxxxxxx
+?@1A
Sxxxxxx
ISC Anti-Image Chassis (ASC)
D070081
±18@0.5A
S1102756
ISC HAM-A Coil Driver (Tip/Tilt OMC)
D1100687
±18@0.25A
S1100603
ISC HAM-A Coil Driver (Tip/Tilt OMC)
D1100687
±18@0.25A
S1100607
ISC HAM-A Coil Driver (Tip/Tilt REFL)
D1100687
±18@0.25A
S1100610
ISC HAM-A Coil Driver (Tip/Tilt REFL)
D1100687
±18@0.25A
Sxxxxxx
0
18
2
ISC Anti-Image Chassis (ASC)
D070081
±18@0.5A
Sxxxxxx
Vertex ISC: D1100170
ISC-C1 is part of D1001427.

## Slide 120: L1-ISC-C1
<< CER
(D1100170)
ISC LVEA Rack 1 Layout (D1200949) (S1201186)
(D1001427)

## Slide 121: L1-ISC-C1 Details
L1-ISC-C1 Details
<< L1-ISC-C1

## Slide 122: D0902783-S1102773
D070081
Front
S1102773
Rear
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102773
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-ISC-C1
XXX
IN 1-4
XXX
IN 17-20
XXX
IN 5-8
XXX
IN 9-12
XXX
IN 13-16
XXX
IN 21-24
XXX
IN 25-28
XXX
IN 29-32
XXX
To ADC Adapter

## Slide 123: D0902783-S1102772
D070081
Front
S1102772
Rear
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102772
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-ISC-C1
XXX
IN 1-4
XXX
IN 17-20
XXX
IN 5-8
XXX
IN 9-12
XXX
IN 13-16
XXX
IN 21-24
XXX
IN 25-28
XXX
IN 29-32
XXX
To ADC Adapter

## Slide 124: D0902783-S1102767
D070081
Front
S1102767
Rear
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102767
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-ISC-C1
XXX
IN 1-4
XXX
IN 17-20
XXX
IN 5-8
XXX
IN 9-12
XXX
IN 13-16
XXX
IN 21-24
XXX
IN 25-28
XXX
IN 29-32
XXX
To ADC Adapter

## Slide 125: D0902783-S1102769
D070081
Front
S1102769
Rear
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102769
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-ISC-C1
XXX
IN 1-4
XXX
IN 17-20
XXX
IN 5-8
XXX
IN 9-12
XXX
IN 13-16
XXX
IN 21-24
XXX
IN 25-28
XXX
IN 29-32
XXX
To ADC Adapter

## Slide 126: D0902783-S1102775
D070081
Front
S1102775
Rear
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102775
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-ISC-C1
XXX
IN 1-4
XXX
IN 17-20
XXX
IN 5-8
XXX
IN 9-12
XXX
IN 13-16
XXX
IN 21-24
XXX
IN 25-28
XXX
IN 29-32
XXX
To ADC Adapter

## Slide 127: D0902783-S1102771
D070081
Front
S1102771
Rear
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102771
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-ISC-C1
XXX
IN 1-4
XXX
IN 17-20
XXX
IN 5-8
XXX
IN 9-12
XXX
IN 13-16
XXX
IN 21-24
XXX
IN 25-28
XXX
IN 29-32
XXX
To ADC Adapter

## Slide 128: D0902783-S1102708
D070081
Front
S1102708
Rear
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
S1102708
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-ISC-C1
XXX
IN 1-4
XXX
IN 17-20
XXX
IN 5-8
XXX
IN 9-12
XXX
IN 13-16
XXX
IN 21-24
XXX
IN 25-28
XXX
IN 29-32
XXX
To ADC Adapter

## Slide 129: D0902783-Sxxxxxxx
D070081
Front
Sxxxxxx
Rear
Anti-Alias Chassis (ASC)
D0902783
±18@0.5A
Sxxxxxx
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-ISC-C1
XXX
IN 1-4
XXX
IN 17-20
XXX
IN 5-8
XXX
IN 9-12
XXX
IN 13-16
XXX
IN 21-24
XXX
IN 25-28
XXX
IN 29-32
XXX
To ADC Adapter

## Slide 130: D1100687-Sxxxxxxx
ISC HAM-A Coil Driver (Tip/Tilt REFL)
D1100687
±18@0.25A
Sxxxxxxx
<< L1-ISC-C1
PD Inputs
PD Inputs
Coil Inputs
Coil Inputs
Binary Inputs
Binary Inputs
Binary Outputs
Binary Outputs
D1100687
Front
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
Sxxxxxxx
Rear
Monitors
Monitors
Coil Driver Out
Coil Driver Out
To/From Sat Amp
To/From Sat Amp

## Slide 131: D1100687-S1100610
ISC HAM-A Coil Driver (Tip/Tilt REFL)
D1100687
±18@0.25A
S1100610 :
<< L1-ISC-C1
PD Inputs
PD Inputs
Coil Inputs
Coil Inputs
Binary Inputs
Binary Inputs
Binary Outputs
Binary Outputs
D1100687
Front
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
S1100610
Rear
Monitors
Monitors
Coil Driver Out
Coil Driver Out
To/From Sat Amp
To/From Sat Amp

## Slide 132: D1100687-S1100607
ISC HAM-A Coil Driver (Tip/Tilt OMC)
D1100687
±18@0.25A
S1100607 :
<< L1-ISC-C1
PD Inputs
PD Inputs
Coil Inputs
Coil Inputs
Binary Inputs
Binary Inputs
Binary Outputs
Binary Outputs
D1100687
Front
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
S1100607
Rear
Monitors
Monitors
Coil Driver Out
Coil Driver Out
To/From Sat Amp
To/From Sat Amp

## Slide 133: D1100687-S1100603
ISC HAM-A Coil Driver (Tip/Tilt OMC)
D1100687
±18@0.25A
S1100603
<< L1-ISC-C1
PD Inputs
PD Inputs
Coil Inputs
Coil Inputs
Binary Inputs
Binary Inputs
Binary Outputs
Binary Outputs
D1100688
Front
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
S1100603
Rear
Monitors
Monitors
Coil Driver Out
Coil Driver Out
To/From Sat Amp
To/From Sat Amp

## Slide 134: D1100687-S1106047
ISC HAM-A Coil Driver (Tip/Tilt OMC)
D1100687
±18@0.25A
S1106047
<< L1-ISC-C1
PD Inputs
PD Inputs
Coil Inputs
Coil Inputs
Binary Inputs
Binary Inputs
Binary Outputs
Binary Outputs
D1100687
Front
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
S1106047
Rear
Monitors
Monitors
Coil Driver Out
Coil Driver Out
To/From Sat Amp
To/From Sat Amp

## Slide 135: D070081-Sxxxxxxx
D070081
Front
Sxxxxxxx
Rear
From DAC Adapter
From DAC Adapter
From DAC Adapter
OUT 1-4
OUT 1-4
OUT 5-8
OUT 5-8
OUT 9-12
OUT 9-12
OUT 13-16
OUT 13-16
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
ISC Anti-Image Chassis (ASC)
D070081
±18@0.5A
SN:
<< L1-ISC-C1

## Slide 136: D070081-S1102756
ISC Anti-Image Chassis (ASC)
D070081
±18@0.5A
S1102756
D070081
Front
S1102756
Rear
From DAC Adapter
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
<< L1-ISC-C1
From DAC Adapter
From DAC Adapter
OUT 1-4
OUT 1-4
OUT 5-8
OUT 5-8
OUT 9-12
OUT 9-12
OUT 13-16
OUT 13-16

## Slide 137: D1001715-S1106300
l1asc0 I/O Extension Chassis
D1001715
24 VDC
S1106300
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
Sxxxxxxx
DAC Adapter
Sxxxxxxx
24 VDC
S1106300
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1asc0 – I/O Extender
ADC Adapter
ADC Adapter
ADC Adapter
ADC Adapter
Sxxxxxxx
Sxxxxxxx
<< L1-ISC-C1

## Slide 138: D0902783-S1102768
D070081
Front
S1102768
Rear
ISC Anti-Alias Chassis (LSC)
D0902783
±18@0.5A
S1102768
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-ISC-C1
XXX
IN 1-4
XXX
IN 17-20
XXX
IN 5-8
XXX
IN 9-12
XXX
IN 13-16
XXX
IN 21-24
XXX
IN 25-28
XXX
IN 29-32
XXX
To ADC Adapter

## Slide 139: D0902783-S1102779
D070081
Front
S1102779
Rear
ISC Anti-Alias Chassis (LSC)
D0902783
±18@0.5A
S1102779
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-ISC-C1
XXX
IN 1-4
XXX
IN 17-20
XXX
IN 5-8
XXX
IN 9-12
XXX
IN 13-16
XXX
IN 21-24
XXX
IN 25-28
XXX
IN 29-32
XXX
To ADC Adapter

## Slide 140: D070081-S1102757
ISC Anti-Image Chassis-(LSC)
D070081
±18@0.5A
S1102757
D070081
Front
S1102757
Rear
From DAC Adapter
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
<< L1-ISC-C1
From DAC Adapter
From DAC Adapter
OUT 1-4
OUT 1-4
OUT 5-8
OUT 5-8
OUT 9-12
OUT 9-12
OUT 13-16
OUT 13-16

## Slide 141: D1001715-S1106342
<< L1-ISC-C1
l1lsc0 I/O Extension Chassis
D1001715
24 VDC
S1106342
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1106342
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1lsc0 – I/O Extender

## Slide 142: L1-ISC-C2
ISC LVEA Rack 2 Layout (D1200975) (S1201187)
<< CER
384 Channel Binary Output (R6 Whitening)
D1100251
+24VDC
S1203281
384 Channel Binary Output (R5 & R6 Whitening)
D1100251
+24VDC
S1201217
384 Channel Binary Output (R2 & R4 Whitening)
D1100251
+24VDC
S1201216
384 Channel Binary Output (R1 & R2 Whitening)
D1100251
+24VDC
S1201215
ISC Common Beckhoff Concentrator
(CM Servo, VCO, Delay Line)
D1102961
+24VDC
S1102617
Corner 1 Beckhoff Concentrator
(Picomotor, Serial Ports, Modbus)
D1100680
+24VDC
S1107446
Corner 2 Beckhoff Concentrator
(LSC Demod, VCO, Delay Line, RF Amps)
D1100681
+24VDC
S1107449
Beckhoff Concentrator
(ASC Demod)
D1101266
+24VDC
Sxxxxxxx
Beckhoff Concentrator
(Beam Diverters, Shutters, Aux Channels)
D1200132
+24VDC
Sxxxxxxx
Slow Controls Concentrator Serial Ports
D1100632
±18VDC
S1103476
4
1
?
Shelf
Shelf
Shelf
Shelf
Shelf
ISC-C2 is part of D1001427.

## Slide 143: L1-ISC-C2
<< CER
(D1100170)
ISC LVEA Rack 2 Layout (D1001427) (S1201187)
(D1001427)

## Slide 144: L1-ISC-C2 Details
L1-ISC-C2 Details
<< L1-ISC-C2

## Slide 145: D1100632 – S1103476
S1103476
Rear
D1100632
Front
<< L1-ISC-C2
Serial Port Concentrator for Timing
D1100632
±18VDC
S1103476

## Slide 146: D1100251 – S1201215
<< L1-ISC-C2
384 Channel Binary Output (R1 & R2 Whitening)
D1100251
+24VDC
S1201215
D1100251
Front
Front
Chassis 1 – Board 1
Front
Chassis 1 – Board 2
Front
Chassis 2 – Board 1
Front
Chassis 2 – Board 2
Front
Chassis 3 – Board 1
Front
Chassis 3 – Board 2
S1201215
Rear
Rear
Chassis 6 – Board 1
Rear
Chassis 6 – Board 2
Rear
Chassis 5 – Board 1
Rear
Chassis 5 – Board 2
Rear
Chassis 4 – Board 1
Rear
Chassis 4 – Board 2
Rear
In
Rear
Out

## Slide 147: D1100251 – S1201216
384 Channel Binary Output (R2 & R4 Whitening)
D1100251
+24VDC
S1201216
<< L1-ISC-C2
D1100251
Front
Front
Chassis 1 – Board 1
Front
Chassis 1 – Board 2
Front
Chassis 2 – Board 1
Front
Chassis 2 – Board 2
Front
Chassis 3 – Board 1
Front
Chassis 3 – Board 2
S1201216
Rear
Rear
Chassis 6 – Board 1
Rear
Chassis 6 – Board 2
Rear
Chassis 5 – Board 1
Rear
Chassis 5 – Board 2
Rear
Chassis 4 – Board 1
Rear
Chassis 4 – Board 2
Rear
In
Rear
Out

## Slide 148: D1100251 – S1201217
384 Channel Binary Output (R5 & R6 Whitening)
D1100251
+24VDC
S1201217
<< L1-ISC-C2
D1100251
Front
Front
Chassis 1 – Board 1
Front
Chassis 1 – Board 2
Front
Chassis 2 – Board 1
Front
Chassis 2 – Board 2
Front
Chassis 3 – Board 1
Front
Chassis 3 – Board 2
S1201217
Rear
Rear
Chassis 6 – Board 1
Rear
Chassis 6 – Board 2
Rear
Chassis 5 – Board 1
Rear
Chassis 5 – Board 2
Rear
Chassis 4 – Board 1
Rear
Chassis 4 – Board 2
Rear
In
Rear
Out

## Slide 149: D1100251 – S1203281
384 Channel Binary Output (R6 Whitening)
D1100251
+24VDC
S1203281
<< L1-ISC-C2
D1100251
Front
Front
Chassis 1 – Board 1
Front
Chassis 1 – Board 2
Front
Chassis 2 – Board 1
Front
Chassis 2 – Board 2
Front
Chassis 3 – Board 1
Front
Chassis 3 – Board 2
S1203281
Rear
Rear
Chassis 6 – Board 1
Rear
Chassis 6 – Board 2
Rear
Chassis 5 – Board 1
Rear
Chassis 5 – Board 2
Rear
Chassis 4 – Board 1
Rear
Chassis 4 – Board 2
Rear
In
Rear
Out

## Slide 150: D1102961 – S1102617
ISC Common Beckhoff Concentrator
(CM Servo, VCO, Delay Line)
D1102961
Power
S1102617
S1102617
Rear
From DAC Adapter
D1102961
Front
<< L1-ISC-C2

## Slide 151: D1100680 - Sxxxxxxx
Corner 1 Beckhoff Concentrator
(Picomotor, Serial Ports, Modbus)
D1100680
Power
S1107446
S1107446
Rear
From DAC Adapter
D1100680
Front
<< L1-ISC-C2

## Slide 152: D1100681 – S1107449
Corner 2 Beckhoff Concentrator
(LSC Demod, VCO, Delay Line, RF Amps)
D1100681
Power
S1107449
S1107449
Rear
From DAC Adapter
D1100681
Front
<< L1-ISC-C2

## Slide 153: D1101266 - Sxxxxxxx
Sxxxxxxx
Rear
From DAC Adapter
D1101266
Front
<< L1-ISC-C2
Beckhoff Concentrator
(ASC Demod)
D1101266
Power
Sxxxxxxx

## Slide 154: D1200132 - Sxxxxxxx
Beckhoff Concentrator
(Beam Diverters, Shutters, Aux Channels)
D1200132
Power
Sxxxxxxx
Sxxxxxxx
Rear
From DAC Adapter
D1200132
Front
<< L1-ISC-C2

## Slide 155: L1-ISC-C3
ISC LVEA Rack 3 Layout (D1200976) (S1201188)
<< CER
RF Patch Panel 7
Dxxxxxxx
No Power
Sxxxxxxx
21.5 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000649
RF Amplifier Concentrator 1
D1100262
±18VDC
S1103461
RF Patch Panel 8
Dxxxxxxx
No Power
Sxxxxxxx
21.5 MHz RF Source
D080702
+12VDC, ±24VDC
S1000546
35.5 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000650
35.5 MHz RF Source
D080702
+12VDC, ±24VDC
S1000551
80 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000654
80 MHz RF Source
D080702
+12VDC, ±24VDC
S1000567
40 MHz Frequency Divider
D1002182
±17VDC, ±24VDC
S1000751
40 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000655
10 MHz Frequency Divider
D1100974
±17VDC, ±24VDC
S1103488
10 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000671
Timing Comparator / Frequency Counter
D1001370
+12VDC
Sxxxxxxx
Timing Fanout Module
D070011
+12VDC
Sxxxxxxx
RF Amplifier Concentrator 2
D1100262
±18VDC
S1103460
RF Patch Panel 9 (TCS)
Dxxxxxxx
No Power
Sxxxxxxx
10
9
5
Sequencer
D1200757
S1202578
ISC-C3 is part of D1001427.

## Slide 156: L1-ISC-C3
<< CER
(D1100170)
ISC LVEA Rack 3 Layout (D1001427) (S1201188)
(D1001427)

## Slide 157: L1-ISC-C3 Details
L1-ISC-C3 Details

## Slide 158: D080702 – S1000546
<< L1-ISC-C3
21.5 MHz RF Source
D080702
+12VDC, ±24VDC
S1000546
S1000546
Rear
D080702
Front
Front
Output
Front
Lock
To …

## Slide 159: D1000124 – S1000649
<< L1-ISC-C3
21.5 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000649
D1000124
Front
Front
10 dBm
Front
1
Front
2
Front
3
Front
4
Front
5
Front
6
Front
7
Front
8
S1000649
Rear
Front
M1
Front
M2
Front
M3
Front
Controls

## Slide 160: D080702 – S1000551
S1000551
Rear
<< L1-ISC-C3
35.5 MHz RF Source
D080702
+12VDC, ±24VDC
S1000551
D080702
Front
Front
Output
Front
Lock
To …

## Slide 161: D1000124 – S1000650
<< L1-ISC-C3
35.5 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000650
D1000124
Front
Front
10 dBm
Front
1
Front
2
Front
3
Front
4
Front
5
Front
6
Front
7
Front
8
S1000650
Rear
Front
M1
Front
M2
Front
M3
Front
Controls

## Slide 162: D080702 - Sxxxxxxx
<< L1-ISC-C3
80 MHz RF Source
D080702
+12VDC, ±24VDC
Sxxxxxxx
S1000551
Rear
D080702
Front
Front
Output
Front
Lock
To …

## Slide 163: D1000124 - Sxxxxxxx
<< L1-ISC-C3
80 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
D1000124
Front
Front
10 dBm
Front
1
Front
2
Front
3
Front
4
Front
5
Front
6
Front
7
Front
8
S1000650
Rear
Front
M1
Front
M2
Front
M3
Front
Controls

## Slide 164: D1002182 - Sxxxxxxx
D1002182
Front
Front
Out
Front
In
S1000650
Rear
Front
M1
Front
M2
Front
M3
Front
Controls
Rear
Front
<< L1-ISC-C3
40 MHz Frequency Divider
D1002182
±17VDC, ±24VDC
Sxxxxxxx

## Slide 165: D1000124 - Sxxxxxxx
<< L1-ISC-C3
40 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
D1000124
Front
Front
10 dBm
Front
1
Front
2
Front
3
Front
4
Front
5
Front
6
Front
7
Front
8
S1000650
Rear
Front
M1
Front
M2
Front
M3
Front
Controls

## Slide 166: D1100974 - Sxxxxxxx
<< L1-ISC-C3
10 MHz Frequency Divider
D1100974
±17VDC, ±24VDC
Sxxxxxxx
D1100974
Front
Front
Out
Front
In
S1000650
Rear
Front
M1
Front
M2
Front
M3
Front
Controls
Rear
Front

## Slide 167: D1000124 - Sxxxxxxx
<< L1-ISC-C3
10 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
D1000124
Front
Front
10 dBm
Front
1
Front
2
Front
3
Front
4
Front
5
Front
6
Front
7
Front
8
S1000650
Rear
Front
M1
Front
M2
Front
M3
Front
Controls

## Slide 168: D1100262 - Sxxxxxxx
<< L1-ISC-C3
RF Amplifier Concentrator 1
D1100262
±18VDC
SN:
D1100262
Front
S1001232
Rear
1
Rear
Controls
5
Rear
9
Rear
2
Rear
6
Rear
10
Rear
3
Rear
7
Rear
11
Rear
4
Rear
8
Rear
12
Rear
Rear

## Slide 169: D1100262 - Sxxxxxxx
<< L1-ISC-C3
RF Amplifier Concentrator 2
D1100262
±18VDC
SN:
D1100262
Front
S1001232
Rear
1
Rear
Controls
5
Rear
9
Rear
2
Rear
6
Rear
10
Rear
3
Rear
7
Rear
11
Rear
4
Rear
8
Rear
12
Rear
Rear

## Slide 170: D1001370 - Sxxxxxxx
S1001232
Rear
D1001370
Front
<< L1-ISC-C3
Timing Comparator / Frequency Counter
D1001370
+12VDC
Sxxxxxxx

## Slide 171: D080534 - Sxxxxxxx
S1001232
Rear
D080534
Front
<< L1-ISC-C3
Timing Fanout Module
D080534
+12VDC (& +24VDC)
Sxxxxxxx
D070011
Master
Fanout

## Slide 172: L1-ISC-C4
ISC LVEA Rack 4 Layout (D1200977) (S1201189)
<< CER
RF Patch Panel 1
Dxxxxxxx
No Power
Sxxxxxxx
RF Patch Panel 2
Dxxxxxxx
No Power
Sxxxxxxx
RF Patch Panel 3
Dxxxxxxx
No Power
Sxxxxxxx
RF Patch Panel 4
Dxxxxxxx
No Power
Sxxxxxxx
RF Patch Panel 5
Dxxxxxxx
No Power
Sxxxxxxx
RF Patch Panel 6
Dxxxxxxx
No Power
Sxxxxxxx
Aeroflex 2023A Diagnostics
Dxxxxxxx
Power
Sxxxxxxx
9.099 / 8.684 MHz RF Source
D080702
+12VDC, ±24VDC
Sxxxxxxx
9.099 / 8.684 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
9.099 / 8.684 MHz Harmonic Generator
Dxxxxxxx
From D1002735
Sxxxxxxx
9.099 / 8.684 MHz Harmonic Power Supply
D1002735
±17VDC, ±24VDC
Sxxxxxxx
18 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
27 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
36 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
45 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
90 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
135 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
24.078 / 22.993 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
24.078 / 22.993 MHz RF Source
D080702
+12VDC, ±24VDC
Sxxxxxxx
71 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
71 MHz RF Source
D080702
+12VDC, ±24VDC
Sxxxxxxx
13
10
3
Sequencer
D1200757
S1202562
ISC-C4 is part of D1001427.

## Slide 173: L1-ISC-C4
<< CER
(D1100170)
Spectrum Microwave
ISC LVEA Rack 4 Layout (D1001427) (S1201189)
(D1001427)

## Slide 174: L1-ISC-C4 Details
L1-ISC-C4 Details

## Slide 175: D080702 - Sxxxxxxx
S1001232
Rear
D080702
Front
9.099 / 8.684 MHz RF Source
D080702
+12VDC, ±24VDC
Sxxxxxxx
<< L1-ISC-C4

## Slide 176: D1000124 - Sxxxxxxx
S1001232
Rear
D1000124
Front
<< L1-ISC-C4
9.099 / 8.684 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx

## Slide 177: D1002735 - Sxxxxxxx
Sxxxxxxx
Rear
From DAC Adapter
D1002735
Front
<< L1-ISC-C4
9.099 / 8.684 MHz Harmonic Generator Power Supply
D1002735
±17VDC, ±24VDC
SN:

## Slide 178: D1000124 - Sxxxxxxx
S1001232
Rear
D1000124
Front
<< L1-ISC-C4
18 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx

## Slide 179: D1000124 - Sxxxxxxx
S1001232
Rear
D1000124
Front
<< L1-ISC-C4
27 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx

## Slide 180: D1000124 - Sxxxxxxx
S1001232
Rear
D1000124
Front
<< L1-ISC-C4
36 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx

## Slide 181: D1000124 - Sxxxxxxx
S1001232
Rear
D1000124
Front
<< L1-ISC-C4
45 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx

## Slide 182: D1000124 - Sxxxxxxx
S1001232
Rear
D1000124
Front
<< L1-ISC-C4
90 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx

## Slide 183: D1000124 - Sxxxxxxx
S1001232
Rear
D1000124
Front
<< L1-ISC-C4
135 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx

## Slide 184: D080702 - Sxxxxxxx
S1001232
Rear
D080702
Front
24.078 / 22.993 MHz RF Source
D080702
+12VDC, ±24VDC
Sxxxxxxx
<< L1-ISC-C4

## Slide 185: D1000124 - Sxxxxxxx
S1001232
Rear
D1000124
Front
<< L1-ISC-C4
24.078 / 22.993 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx

## Slide 186: D080702 - Sxxxxxxx
S1001232
Rear
D080702
Front
71 MHz RF Source
D080702
+12VDC, ±24VDC
Sxxxxxxx
<< L1-ISC-C4

## Slide 187: D1000124 - Sxxxxxxx
S1001232
Rear
D1000124
Front
<< L1-ISC-C4
71 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx

## Slide 188: Subsystem: PSL (Pre-Stabilized Laser)
2feet
Each Rack is 39” Deep and 24” Wide
2 feet
L1-SUS-C1
L1-SUS-C2
L1-SUS-C3
L1-SUS-C4
L1-SUS-C5
L1-SUS-C6
L1-SUS-C7
L1-SUS-C8
L1-SEI-C1
Front
Front
Front
Front
Front
Front
L1-SEI-C2
L1-AOS-C1
L1-SEI-C3
L1-SEI-C4
L1-SEI-C5
L1-SEI-C6
L1-UNK-C3
L1-UNK-C2
L1-UNK-C1
L1-PSL-C1
CDS Electronics Room (CER)
L1-OAF-C1
SUS ITMX, ITMY, FMX, FMY, and BS Rack 1
SUS HAM3 and HAM4 Rack 2
SUS HAM3 and HAM4 Rack 1
SUS HAM2 Rack 1
SUS HAM2 Rack 2
SUS ITMX, ITMY, FMX, FMY, and BS Rack 2
SUS HAM5 and HAM6 Rack 1
SUS HAM5 and HAM6 Rack 2
ISC LVEA Rack 1
ISC LVEA Rack 2
ISC LVEA Rack 3
PSL Rack 1
DAQ Rack 1
TCS Rack 1
Front
SEI HAM1 and HAM6
SEI HAM2 and HAM3
SEI HAM4 and HAM5
SEI BSC1
SEI BSC2
SEI BSC3
ISC LVEA Rack 4
L1-FAC-C1
<< IFO Subsystems
PSL Component List: LIGO-T0900633
PSL Table Layout: LIGO-T0900610
L1-ISC-C1
L1-ISC-C2
L1-ISC-C3
L1-ISC-C4
PSL

## Slide 189: L1-PSL-C1
PSL Rack 1 Layout (LIGO-Dxxxxxxx)
FSS Anti-Alias Chassis
D0902783
±18@1A
S1001245
ISS Anti-Image Chassis
D1003224
±18@0.5A
S1001231
l1psl0 I/O Extension Chassis
D1001715
+24@5A
S1001134
PMC Anti-Alias Chassis
D0902783
±18@1A
S1001246
FSS Anti-Image Chassis
D1003224
±18@0.5A
S1001232
PMC Anti-Image Chassis
D1003224
±18@0.5A
S1001229
ISS Anti-Alias Chassis
D0902783
±18@1A
S1001244
<< CER
Spare Anti-Image Chassis
D1003224
±18@0.5A
S1001233
DBB Anti-Image Chassis
D1001801
±18@0.5A
S1001224
DBB Anti Alias Chassis
D1001125
±18@1A
S1101683
Spare Anti-Alias Chassis
D0902783
±18@1A
S1001247
PSO-018
PSY-009

## Slide 190: L1-PSL-C1 Details
L1-PSL-C1 Details
<< L1-PSL-C1

## Slide 191: D0902783 - S1001244
ISS Anti-Alias Chassis
D0902783
±18@1.0A
S1001244
S1001244
Rear
To ADC Adapter
<< L1-PSL-C1
D1003224
Front
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
ISS AA 1-4
ISS AA 5-8
ISS AA 9-12
ISS AA 13-16
ISS AA 17-20
ISS AA 21-24
ISS AA 25-28
IN 29-32
ISS AA 29-32
IN 25-28
IN 21-24
IN 17-20
IN 13-16
IN 5-8
IN 9-12
IN 1-4
l1psl0 Slot P1
To ADC Adapter

## Slide 192: D1003224 - S1001231
ISS Anti-Image Chassis
D1003224
±18@0.5A
S1001231
S1001231
Rear
From DAC Adapter
D1003224
Front
CH 1-4
CH 5-8
CH 9-12
CH 13-16
aLIGO Anti-Image Module
D1003224
ISS AI 1-4
ISS AI 5-8
ISS AI 9-12
ISS AI 13-16
CH 13-16
CH 9-12
CH 5-8
CH 1-4
l1psl0 Slot P2
From DAC Adapter
<< L1-PSL-C1
D1102351
PSL DAQ DB9 Breakouts
S1201201
S1201199
S1201200
S1201205

## Slide 193: D0902783 - S1001245
FSS Anti-Alias Chassis
D0902783
±18@1.0A
S1001245
S1001245
Rear
To ADC Adapter
D1003224
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
FSS AA 1-4
FSS AA 5-8
FSS AA 9-12
FSS AA 13-16
FSS AA 17-20
FSS AA 21-24
FSS AA 25-28
IN 29-32
FSS AA 29-32
IN 25-28
IN 21-24
IN 17-20
IN 13-16
IN 5-8
IN 9-12
IN 1-4
l1psl0 Slot P3
To ADC Adapter
Front
<< L1-PSL-C1

## Slide 194: D1003224 - S1001232
FSS Anti-Image Chassis
D1003224
±18@0.5A
S1001232
S1001232
Rear
From DAC Adapter
D1003224
CH 1-4
CH 5-8
CH 9-12
CH 13-16
aLIGO Anti-Image Module
D1003224
FSS AI 1-4
FSS AI 5-8
FSS AI 9-12
FSS AI 13-16
CH 13-16
CH 9-12
CH 5-8
CH 1-4
l1psl0 Slot P6
From DAC Adapter
Front
<< L1-PSL-C1

## Slide 195: D0902783 - S1001246
PMC Anti-Image Chassis
D0902783
±18@1.0A
S1001246
S1001246
Rear
To ADC Adapter
D1003224
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
PMC AA 1-4
PMC AA 5-8
PMC AA 9-12
PMC AA 13-16
PMC AA 17-20
PMC AA 21-24
PMC AA 25-28
IN 29-32
PMC AA 29-32
IN 25-28
IN 21-24
IN 17-20
IN 13-16
IN 5-8
IN 9-12
IN 1-4
l1psl0 Slot P4
To ADC Adapter
Front
<< L1-PSL-C1

## Slide 196: D1003224 - S1001229
PMC Anti-Image Chassis
D1003224
±18@0.5A
S1001229
S1001229
Rear
From DAC Adapter
l1psl0 Slot P7
From DAC Adapter
D1003224
CH 1-4
CH 5-8
CH 9-12
CH 13-16
aLIGO Anti-Image Module
D1003224
PMC AI 1-4
PMC AI 5-8
PMC AI 9-12
PMC AI 13-16
CH 13-16
CH 9-12
CH 5-8
CH 1-4
Front
<< L1-PSL-C1
D1102351
PSL DAQ DB9 Breakouts
S1201202
S1201203
S1201204
S1201206

## Slide 197: D1001125 - S1101683
DBB Anti-Alias Chassis
D1001125
±18@1.0A
S1101683
S1101683
Rear
To ADC Adapter
l1psl0 Slot P5
To ADC Adapter
D1001125
AI Module aLIGO PSL DBB Assembly Drawing D1100292
Front
CHANNELS 9-16
aLIGO PSL DBB
D1001125
AA Module
CHANNELS 1-8
CHANNELS 25-32
CHANNELS 17-24
DBB AA 1-8
DBB AA 9-16
DBB AA 17-24
DBB AA 25-32
CHANNELS 25-32
CHANNELS 17-24
CHANNELS 9-16
CHANNELS 1-8
<< L1-PSL-C1

## Slide 198: D1001801 - S1001224
DBB Anti-Image Chassis
D1001801
±18@0.5A
S1001224
S1001224
Rear
From DAC Adapter
l1psl0 Slot P8
From DAC Adapter
D1001801
Front
AI Module aLIGO PSL DBB Assembly Drawing D1002103
CHANNELS 1-8
CHANNELS 9-16
aLIGO PSL DBB
D1001801
AI Module
DBB AI 1-8
DBB AI 9-16
CHANNELS 9-16
CHANNELS 1-8
<< L1-PSL-C1
S1201375
S1201374
D1200639
PSL DAQ DB25 Breakouts

## Slide 199: l1psl0 - D1001715 - S1001134
l1psl0 I/O Extension Chassis
D1001715
+24VDC
S1001134
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
+24VDC
S1001134
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
S1001244
Slot P1
S1001231
Slot P2
S1001245
Slot P3
S1001246
Slot P4
S1101683
Slot P5
S1001232
Slot P6
S1001233
Slot P7
S1001224
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
<< L1-PSL-C1
l1psl0 – I/O Extender

## Slide 200: D0902783-S1001247
Anti-Alias Chassis
D0902783
±18@1.0A
S1001247
S1001247
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter
PSL SPARE
D1003224
Front
IN 1-4
IN 1-4
IN 5-8
IN 5-8
IN 1-4
IN 5-8
IN 9-12
IN 9-12
IN 13-16
IN 13-16
IN 9-12
IN 13-16
IN 17-20
IN 17-20
IN 21-24
IN 17-20
IN 21-24
IN 25-28
IN 29-32
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
IN 21-24
IN 25-28
IN 29-32
<< L1-PSL-C1

## Slide 201: D0902783-S1001248
Anti-Alias Chassis
D0902783
±18@1.0A
S1001248
S1001248
Rear
To ADC Adapter
PSL SPARE
Open
To ADC Adapter
<< L1-PSL-C1
D1003224
Front
IN 1-4
IN 1-4
IN 5-8
IN 5-8
IN 1-4
IN 5-8
IN 9-12
IN 9-12
IN 13-16
IN 13-16
IN 9-12
IN 13-16
IN 17-20
IN 17-20
IN 21-24
IN 17-20
IN 21-24
IN 25-28
IN 29-32
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
IN 21-24
IN 25-28
IN 29-32

## Slide 202: D1003224-S1001230
Anti-Image Chassis
D1003224
±18@0.5A
S1001230
S1001230
Rear
From DAC Adapter
Open
From DAC Adapter
D1003224
PSL SPARE
Front
Open
CH 1-4
Open
CH 5-8
CH 1-4
CH 5-8
Open
CH 9-12
Open
CH 13-16
CH 9-12
CH 13-16
aLIGO Anti-Image Module
D1003224
<< L1-PSL-C1

## Slide 203: D1003224 - S1001233
Anti-Image Chassis
D1003224
±18@0.5A
S1001233
S1001229
Rear
From DAC Adapter
PSL SPARE
D1003224
Open
From DAC Adapter
CHANNELS 1-8
CHANNELS 9-16
aLIGO PSL DBB
D1001801
AI Module
Open
Open
CHANNELS 9-16
CHANNELS 1-8
Front
<< L1-PSL-C1

## Slide 204: PSL Racks(LIGO-G1000106-V1 – p.17)

## Slide 205: PSL Racks(Layout 20101006)

## Slide 206: PSL Racks(LIGO-G1000106-V1 – p.41)

## Slide 207: PSL Racks(LIGO-G1000106-V1 – p.41)

## Slide 208: PSL Racks – L1-PSL-01– ILS and PMC
Eurocard Crate
ECC-1 (ILS and PMC)
Control Box (CB)
NPRO Controller
D1000305 AI Chassis
D0902783 AA Chassis
D1000305 AI Chassis
D0902783 AA Chassis
Control Box (CB)
Eurocard Crate
ECC-1 (ILS and PMC)
NPRO Controller
D1000305 SYYYYYYYY
D0902783 SYYYYYYYY
D0902783 SYYYYYYYY
D1000305 SYYYYYYYY
D070011 Fanout Timing
D070011 Fanout Timing
Front
Rear
L1-PSL-01
L1-PSL-01
I/O Extension
2 ADC
2 DAC
DXXXXXXXX Delay Line Chassis
DXXXXXXXX SYYYYYYYY
DXXXXXXXX 35.5MHz Amplifier Chassis
DXXXXXXXX SYYYYYYYY
DXXXXXXXX 35.5MHz Amplifier Chassis
DXXXXXXXX SYYYYYYYY

## Slide 209: PSL Racks – L1-PSL-1-ECC-1 (ILS and PMC)
Eurocard Crate
ECC-1 (ILS and PMC)
Eurocard Crate
ECC-1 (ILS
and PMC)
Monitoring Field Box
T0900632
ILS Servo
TXXXXXXX
ILS Field Box
TXXXXXXX
PMC Field Box
TXXXXXXX
PMC Servo
TXXXXXXX
+5VDC
-5VDC
+15VDC
-15VDC
+24VDC
-24VDC

## Slide 210: PSL Racks – L1-PSL-02 (DBB, FSS, and ISS)
Eurocard Crate
ECC-2 (FSS and ISS)
Eurocard Crate
ECC-1 (DBB)
D1000305 AI Chassis
D1000305 SYYYYYYYY
D0902783 AA Chassis
D0902783 SYYYYYYYY
D1000305 AI Chassis
D0902783 AA Chassis
D0902783 SYYYYYYYY
D1000305 SYYYYYYYY
Eurocard Crate
ECC-2 (FSS and ISS)
Eurocard Crate
ECC-1 (DBB)
Frequency Stabilization Servo
Intensity Stabilization Servo
Diagnostic Breadboard
D070011 Fanout Timing
D070011 Fanout Timing
I/O Extension
2 ADC
2 DAC
Front
Rear
L1-PSL-02
L1-PSL-02
DXXXXXXXX Delay Line Chassis
DXXXXXXXX SYYYYYYYY
DXXXXXXXX 21.5MHz Amplifier Chassis
DXXXXXXXX SYYYYYYYY
DXXXXXXXX 21.5MHz Amplifier Chassis
DXXXXXXXX SYYYYYYYY

## Slide 211: L1-PSL-02-ECC-1 (DBB)
Eurocard Crate
ECC-1 (DBB)
Eurocard Crate
ECC-1 (DBB)
+5VDC
-5VDC
+15VDC
-15VDC
+24VDC
-24VDC
DBB Field Box
TXXXXXXX
DBB
TXXXXXXX
DBB
TXXXXXXX
DBB
TXXXXXXX
DBB
TXXXXXXX
DBB
TXXXXXXX
DBB
TXXXXXXX

## Slide 212: L1-PSL-02-ECC-2 (FSS and ISS)
Eurocard Crate
Eurocard Crate
ECC-2 (FSS and ISS)
+5VDC
-5VDC
+15VDC
-15VDC
+24VDC
-24VDC
ISS Field Box
TXXXXXXX
FSS Field Box 1
TXXXXXXX
FSS LO
TXXXXXXX
FSS Field Box 2
TXXXXXXX
ISS Servo
TXXXXXXX

## Slide 213
Eurocard Crate
ECC-2 (FSS and ISS)
Eurocard Crate
ECC-1 (DBB)
Eurocard Crate
ECC-2 (FSS and ISS)
Eurocard Crate
ECC-1 (DBB)
DXXXXXXXX Delay Line Chassis
DXXXXXXXX SYYYYYYYY
DXXXXXXXX 21.5MHz Amplifier Chassis
DXXXXXXXX SYYYYYYYY
Front
Rear
L1-PSL-01
L1-PSL-01
Eurocard Crate
ECC-3 (ILS and PMC
Eurocard Crate
ECC-3 (ILS and PMC
Control Box (CB)
NPRO Controller
DXXXXXXXX 21.5MHz Amplifier Chassis
DXXXXXXXX SYYYYYYYY
DXXXXXXXX Delay Line Chassis
DXXXXXXXX SYYYYYYYY
DXXXXXXXX 35.5MHz Amplifier Chassis
DXXXXXXXX SYYYYYYYY
DXXXXXXXX 35.5MHz Amplifier Chassis
DXXXXXXXX SYYYYYYYY
Control Box (CB)
NPRO Controller

## Slide 214: PSL Table
T0900610

## Slide 215: L1-LDR-C1
+18VDC ?A
-18VDC ?A
+24VDC ?A
-24VDC ?A
LDR Rack 1 Layout (LIGO-Dxxxxxxx)
<< LDR
Anti-Image Chassis
D1003224
±18@0.5A
S1001230
Anti-Alias Chassis
D0902783
±18@1A
S1001248

## Slide 216: L1-LDR-C2
+18VDC ?A
-18VDC ?A
+24VDC ?A
-24VDC ?A
LDR Rack 2 Layout (LIGO-Dxxxxxxx)
<< LDR

## Slide 217: L1-LDR-C3
+18VDC ?A
-18VDC ?A
+24VDC ?A
-24VDC ?A
LDR Rack 3 Layout (LIGO-Dxxxxxxx)
<< LDR

## Slide 218: LDR Chiller
+18VDC ?A
-18VDC ?A
+24VDC ?A
-24VDC ?A
LDR Rack 4 Layout (Chillers) (LIGO-Dxxxxxxx)
<< LDR

## Slide 219: Subsystem: SEI (Seismic Isolation)
2feet
Each Rack is 39” Deep and 24” Wide
2 feet
L1-SUS-C1
L1-SUS-C2
L1-SUS-C3
L1-SUS-C4
L1-SUS-C5
L1-SUS-C6
L1-SUS-C7
L1-SUS-C8
L1-SEI-C1
Front
Front
Front
Front
Front
Front
L1-SEI-C2
L1-AOS-C1
L1-SEI-C3
L1-SEI-C4
L1-SEI-C5
L1-SEI-C6
L1-UNK-C3
L1-UNK-C2
L1-UNK-C1
L1-ISC-C1
L1-ISC-C2
L1-ISC-C3
L1-PSL-C1
CDS Electronics Room (CER)
L1-ISC-C4
L1-OAF-C1
SUS ITMX, ITMY, FMX, FMY, and BS Rack 1
SUS HAM3 and HAM4 Rack 2
SUS HAM3 and HAM4 Rack 1
SUS HAM2 Rack 1
SUS HAM2 Rack 2
SUS ITMX, ITMY, FMX, FMY, and BS Rack 2
SUS HAM5 and HAM6 Rack 1
SUS HAM5 and HAM6 Rack 2
ISC LVEA Rack 1
ISC LVEA Rack 2
ISC LVEA Rack 3
PSL Rack 1
DAQ Rack 1
TCS Rack 1
Front
SEI HAM1 and HAM6
SEI HAM2 and HAM3
SEI HAM4 and HAM5
SEI BSC1
SEI BSC2
SEI BSC3
ISC LVEA Rack 4
L1-FAC-C1
<< IFO Subsystems
SEI
HAM3 HEPI 8-Channel Valve Driver
D0900117
+18V@0.72A, -18V@0.72A
S0900290
HAM2 HEPI 8-Channel Valve Driver
D0900117
+18V@0.72A, -18V@0.72A
S0900275

## Slide 220: L1-SEI-C1
Anti-Alias Chassis
Dnumber
±18@1A
Serial
+18VDC 9A
-18VDC 9A
+24VDC ?A
-24VDC ?A
SEI HAM1 HEPI and HAM6 ISI and HEPI Rack Layout (D1201112) (S1200743)
l1seiham1-6 I/O Extension Chassis
D1001715
+24@5A
S1001144
HAM6 ISI Coil Driver Pod 1 and Pod 2
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
HAM6 ISI Coil Driver Pod 3
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
HAM1 HEPI 8-Channel Valve Driver
D020373
+18V@0.72A, -18V@0.72A
S1000842
HAM6 HEPI 8-Channel Valve Driver
D0901338
+18V@0.72A, -18V@0.72A
Serial
HAM6 ISI Interface Chassis
D1000067
+18V@0.32A, -18V@0.33A
Serial
HAM6 ISI Interface Chassis
D1000067
+18V@0.32A, -18V@0.33A
Serial
Anti-Image Chassis
Dnumber
±18@0.5A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Anti-Image Chassis
Dnumber
±18@0.5A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
<< CER
PSO-017
PSY-018
PSY-019
SEI-C1 is part of D1101584

## Slide 221: L1-SEI-C1 Details
L1-SEI-C1 Details
<< L1-SEI-C1
SEI-C1 is part of D1101584

## Slide 222: D1000067 – Sxxxxxxx
Sxxxxxxx
Rear
HAM6 ISI Interface
D1000067
Power
Sxxxxxxx
<< L1-SEI-C1
D1000067
Front
Geophones 1&2
Geophones 3&4
CHANS 1&2
CHANS 3&4
Power Out
Capacitance Position Sensors
CHANS 5&6
CHANS 7&8
8 CHANNEL VALVE DRIVER
LIGO D020373 REV C

## Slide 223: D1000067 – Sxxxxxxx
HAM6 ISI Interface
D1000067
Power
Sxxxxxxx
<< L1-SEI-C1
Sxxxxxxx
Rear
D1000067
Front
Geophones 1&2
Geophones 3&4
CHANS 1&2
CHANS 3&4
Power Out
Capacitance Position Sensors
CHANS 5&6
CHANS 7&8
8 CHANNEL VALVE DRIVER
LIGO D020373 REV C

## Slide 224: D0902744 - Sxxxxxxx
<< L1-SEI-C1
HAM6 ISI Coil Driver Pod 1 and Pod 2
D0902744
+24V@1.2A, -24V@0.8A (+10A)
Sxxxxxxx
D0902744
Front
Sxxxxxxx
Rear
To Binary I/O
To Binary I/O
From DAC
From DAC
To AA Chassis
To AA Chassis
Coarse 2 OUT
Fine 2 OUT
Fine 1 OUT
Coarse 1 OUT
Coarse 2 OUT
Fine 2 OUT
Fine 1 OUT
Coarse 1 OUT

## Slide 225: D0902744 - Sxxxxxxx
<< L1-SEI-C1
HAM6 ISI Coil Driver Pod 1 and Pod 2
D0902744
+24V@1.2A, -24V@0.8A (+10A)
Sxxxxxxx
D0902744
Front
Sxxxxxxx
Rear
To Binary I/O
To Binary I/O
From DAC
From DAC
To AA Chassis
To AA Chassis
Coarse 2 OUT
Fine 2 OUT
Fine 1 OUT
Coarse 1 OUT
Coarse 2 OUT
Fine 2 OUT
Fine 1 OUT
Coarse 1 OUT

## Slide 226: D020373 – S1000842
S1000842
Rear
VALVE INPUTS
8 CHANNEL VALVE DRIVER
POWER DISTRIBUTION
LIGO D040049
VALVE INPUTS
VALVE INPUTS
D040049
HEPI1 8-Channel Valve Driver
D020373
Power
S1000842
HAM1 MC1
<< L1-SEI-C1
D020373
Front
CHANS 1&2
CHANS 1&2
CHANS 3&4
CHANS 3&4
CHANS 1&2
CHANS 3&4
CHANS 5&6
CHANS 5&6
CHANS 7&8
CHANS 7&8
CHANS 5&6
CHANS 7&8
8 CHANNEL VALVE DRIVER
LIGO D020373 REV C

## Slide 227: D0901338 - Sxxxxxxx
SN:
Rear
From AI Chassis
D0901338
Front
Open
CHANS 1&2
Open
CHANS 3&4
CHANS 1&2
CHANS 3&4
Open
CHANS 5&6
Open
CHANS 7&8
CHANS 5&6
CHANS 7&8
Open
From AI Chassis
8 CHANNEL VALVE DRIVER
LIGO D090117-v2
8 CHANNEL VALVE DRIVER
LIGO D090117-v2
HEPI6 8-Channel Valve Driver
D0901338
Power
SN:
<< L1-SEI-C1

## Slide 228: D1001715 - S1001144
<< L1-SEI-C1
l1seiham1-6 I/O Extension Chassis
D1001715
24 VDC
S1001144
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
24 VDC
S1001144
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1seiham1-6 – I/O Extender

## Slide 229: SEI Racks L1-SEI-01
D1000305 AI Chassis
D0902783 AA Chassis
D0902783 AA Chassis
D1000305 SYYYYYYYY
D0902783 SYYYYYYYY
D0902783 SYYYYYYYY
Front
L1-SEI-01
Rear
L1-SEI-01
I/O Extension
4 ADC
2 DAC
4 Binary
D1000305 AI Chassis
D0902783 AA Chassis
D0902783 AA Chassis
D0902783 SYYYYYYYY
D0902783 SYYYYYYYY
Dxxxxxxx BI Chassis
Dxxxxxxx BO Chassis
Dxxxxxxx BI Chassis
Dxxxxxxx BO Chassis
Dxxxxxxx ISI Coil Chassis
D1000305 SYYYYYYYY
Dxxxxxxx ISI IF Chassis
Dxxxxxxx T240 IF Chassis
Dxxxxxxx BO Chassis
Dxxxxxxx BI Chassis
Dxxxxxxx 8 Valve Chassis
Dxxxxxxx ISI Coil Chassis
Dxxxxxxx ISI Coil Chassis
Dxxxxxxx ISI IF Chassis
Dxxxxxxx ISI IF Chassis
Dxxxxxxx T240 IF Chassis
Dxxxxxxx T240 IF Chassis

## Slide 230: L1-SEI-C2
+18VDC 11A
-18VDC 11A
+24VDC ?A
-24VDC ?A
I/O Extension Chassis
D1001715
+24@5A
S1001145
HAM2 HEPI 8-Channel Valve Driver
D020373
+18V@0.72A, -18V@0.72
S1000843
HAM3 HEPI 8-Channel Valve Driver
D020373
+18V@0.72A, -18V@0.72A
S1000844
SEI HAM2 ISI and HEPI and HAM3 ISI and HEPI Rack Layout (D1201113) (S1200744)
HAM2 ISI Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
HAM2 ISI Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
HAM3 ISI Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
HAM3 ISI Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
HAM2 ISI Anti-Alias Chassis
D1000269
±18@1A
S1104621
HAM2 ISI Anti-Alias Chassis
D1000269
±18@1A
S1104638
HAM3 ISI Anti-Alias Chassis
D1000269
±18@1A
S1104632
HAM3 ISI Anti-Alias Chassis
D1000269
±18@1A
S1104635
HAM2 HEPI Anti-Alias Chassis
D1000272
±18@1A
S1104616
HAM3 HEPI Anti-Alias Chassis
D1000272
±18@1A
S1104615
Binary Input Chassis
D1001726
±18@0.5A
S1101286
Binary Output Chassis
D1001728
±18@0.5A
S1101321
HAM2 ISI Coil Driver Pod 1 and Pod 2
D0902744
+24V@1.2A, -24V@0.8A (+10A)
S1103318
HAM2 ISI Coil Driver Pod 3
D0902744
+24V@1.2A, -24V@0.8A (+10A)
S1103332
HAM3 ISI Coil Driver Pod 1 and Pod 2
D0902744
+24V@1.2A, -24V@0.8A (+10A)
S1103306
HAM3 ISI Coil Driver Pod 3
D0902744
+24V@1.2A, -24V@0.8A (+10A)
S1103304
HAM3 HEPI Anti-Image Chassis
D1100202
±18@0.5A
S1104573
HAM2 HEPI Anti-Image Chassis
D1100202
±18@0.5A
S1104572
<< CER
PSO-016
PSY-017
PSY-020
SEI-C2 is part of D1101576

## Slide 231: L1-SEI-C2 Details
L1-SEI-C2 Details
<< L1-SEI-C2

## Slide 232: D1000269 – S1104621
<< L1-SEI-C2
S1104621
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter
HAM2 ISI Anti-Alias Chassis
D1000269
±18@1A
S1104621
D1000269
Front
IN 1-8
IN 9-20
IN 21-24
IN 25-28
IN 29-32
aLIGO HAM ISI Anti-Alias Chassis
LIGO-D1000269
IN 25-28
IN 29-32
IN 29-32
IN 25-28
IN 1-8
IN 1-8
IN 9-20
IN 9-20
IN 21-24
IN 21-24
DC Power
+V -V

## Slide 233: D1000269 – S1104638
<< L1-SEI-C2
S1104638
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter
HAM2 ISI Anti-Alias Chassis
D1000269
±18@1A
S1104638
D1000269
Front
IN 1-8
IN 9-20
IN 21-24
IN 25-28
IN 29-32
aLIGO HAM ISI Anti-Alias Chassis
LIGO-D1000269
IN 25-28
IN 29-32
IN 29-32
IN 25-28
IN 1-8
IN 1-8
IN 9-20
IN 9-20
IN 21-24
IN 21-24
DC Power
+V -V

## Slide 234: D1100202 - S1104572
S1104572
Rear
From DAC Adapter
From DAC Adapter
From DAC Adapter
<< L1-SEI-C2
HAM2 HEPI Anti-Image Chassis
D1100202
±18@0.5A
S1104572
D1100202
OUT 1-8
OUT 9-12
OUT 13-16
aLIGO HEPI Anti-Image Chassis
OUT 1-8
OUT 9-12
OUT 13-16
Front
OUT 1-8
OUT 9-12
OUT 13-16
LIGO D1100202
DC Power
+V -V

## Slide 235: D0902744 – S1103318
<< L1-SEI-C2
HAM2 ISI Coil Driver Pod 1 and Pod 2
D0902744
+24V@1.2A, -24V@0.8A (+10A)
S1103318
D0902744
Front
S1103318
Rear
To Binary I/O
To Binary I/O
From DAC
From DAC
To AA Chassis
To AA Chassis
Coarse 2 OUT
Fine 2 OUT
Fine 1 OUT
Coarse 1 OUT
Coarse 2 OUT
Fine 2 OUT
Fine 1 OUT
Coarse 1 OUT

## Slide 236: D0902744 – S1103332
<< L1-SEI-C2
HAM2 ISI Coil Driver Pod 3
D0902744
+24V@1.2A, -24V@0.8A (+10A)
S1103332
D0902744
Front
S1103332
Rear
To Binary I/O
To Binary I/O
From DAC
From DAC
To AA Chassis
To AA Chassis
Coarse 2 OUT
Fine 2 OUT
Fine 1 OUT
Coarse 1 OUT
Coarse 2 OUT
Fine 2 OUT
Fine 1 OUT
Coarse 1 OUT

## Slide 237: D1000269 – S1104632
<< L1-SEI-C2
S1104632
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter
HAM3 ISI Anti-Alias Chassis
D1000269
±18@1A
S1104632
D1000269
Front
IN 1-8
IN 9-20
IN 21-24
IN 25-28
IN 29-32
aLIGO HAM ISI Anti-Alias Chassis
LIGO-D1000269
IN 25-28
IN 29-32
IN 29-32
IN 25-28
IN 1-8
IN 1-8
IN 9-20
IN 9-20
IN 21-24
IN 21-24
DC Power
+V -V

## Slide 238: D1000269 – S1104635
<< L1-SEI-C2
S1104635
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter
HAM3 ISI Anti-Alias Chassis
D1000269
±18@1A
S1104635
D1000269
Front
IN 1-8
IN 9-20
IN 21-24
IN 25-28
IN 29-32
aLIGO HAM ISI Anti-Alias Chassis
LIGO-D1000269
IN 25-28
IN 29-32
IN 29-32
IN 25-28
IN 1-8
IN 1-8
IN 9-20
IN 9-20
IN 21-24
IN 21-24
DC Power
+V -V

## Slide 239: D1100202 - S1104573
<< L1-SEI-C2
HAM3 HEPI Anti-Image Chassis
D1100202
±18@0.5A
S1104573
D1100202
OUT 1-8
OUT 9-12
OUT 13-16
aLIGO HEPI Anti-Image Chassis
OUT 1-8
OUT 9-12
OUT 13-16
Front
OUT 1-8
OUT 9-12
OUT 13-16
LIGO D1100202
DC Power
+V -V
S1104573
Rear
From DAC Adapter
From DAC Adapter
From DAC Adapter

## Slide 240: D0902744 – S1103306
<< L1-SEI-C2
HAM3 ISI Coil Driver Pod 1 and Pod 2
D0902744
+24V@1.2A, -24V@0.8A (+10A)
S1103306
D0902744
Front
S1103306
Rear
To Binary I/O
To Binary I/O
From DAC
From DAC
To AA Chassis
To AA Chassis
Coarse 2 OUT
Fine 2 OUT
Fine 1 OUT
Coarse 1 OUT
Coarse 2 OUT
Fine 2 OUT
Fine 1 OUT
Coarse 1 OUT

## Slide 241: D0902744 – S1103304
<< L1-SEI-C2
HAM3 ISI Coil Driver Pod 3
D0902744
+24V@1.2A, -24V@0.8A (+10A)
S1103304
D0902744
Front
S1103304
Rear
To Binary I/O
To Binary I/O
From DAC
From DAC
To AA Chassis
To AA Chassis
Coarse 2 OUT
Fine 2 OUT
Fine 1 OUT
Coarse 1 OUT
Coarse 2 OUT
Fine 2 OUT
Fine 1 OUT
Coarse 1 OUT

## Slide 242: D1000272 – S1104616
<< L1-SEI-C2
S1104616
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter
HAM2 HEPI Anti-Alias Chassis
D1000269
±18@1A
S1104616
D1000269
Front
IN 1-5
IN 6-10
IN 11-15
IN 27-29
IN 29-32
aLIGO HEPI Anti-Alias Chassis
LIGO-D1000272
IN 25-28
IN 29-32
IN 29-32
IN 25-28
IN 1-5
IN 1-5
IN 6-10
IN 6-10
IN 11-15
IN 11-15
DC Power
+V -V
IN 16-20
IN 21-26
IN 16-20
IN 16-20
IN 21-26
IN 21-26

## Slide 243: D020373 – S1000843
S1000843
Rear
VALVE INPUTS
8 CHANNEL VALVE DRIVER
POWER DISTRIBUTION
LIGO D040049
VALVE INPUTS
VALVE INPUTS
D040049
HEPI2 8-Channel Valve Driver
D020373
Power
S1000843
HAM2 MC2
<< L1-SEI-C2
D020373
Front
CHANS 1&2
CHANS 1&2
CHANS 3&4
CHANS 3&4
CHANS 1&2
CHANS 3&4
CHANS 5&6
CHANS 5&6
CHANS 7&8
CHANS 7&8
CHANS 5&6
CHANS 7&8
8 CHANNEL VALVE DRIVER
LIGO D020373 REV C

## Slide 244: D1001726 – S1101286
S1101286
Rear
Ch 32-63
Open
Ch 32-63
Ch 0-31
To Binary Inputs
of I/O Chassis
Open
Ch 32-63
Binary Input Chassis
D1001726
±18@0.5A
S1101286
Open
Ch 16-23
Open
Ch 48-55
Open
Ch 0-7
Open
Ch 8-15
Open
Ch 40-47
Open
Ch 32-39
D1001726
Front
Port 0
Ch 0-7
Port 1
Ch 8-15
Port 4
Ch 32-39
Port 5
Ch 40-47
Port 2
Ch 16-23
64 Channel
Binary Input
aLIGO
D1000726
Port 6
Ch 48-55
Port 3
Ch 24-31
Port 7
Ch 56-63
Open
Ch 23-31
Open
Ch 56-63
<< L1-SEI-C2

## Slide 245: D1001728 – S1101321
S1101321
Rear
Ch 32-63
Open
Ch 32-63
Ch 0-31
To Binary Outputs
of I/O Chassis
Open
Ch 32-63
Binary Output Chassis
D1001728
±18@0.5A
S1101321
Open
Ch 16-23
Open
Ch 48-55
Open
Ch 0-7
Open
Ch 8-15
Open
Ch 40-47
Open
Ch 32-39
D1001728
Front
Port 0
Ch 0-7
Port 1
Ch 8-15
Port 4
Ch 32-39
Port 5
Ch 40-47
Port 2
Ch 16-23
64 Channel
Binary Input
aLIGO
D1000728
Port 6
Ch 48-55
Port 3
Ch 24-31
Port 7
Ch 56-63
Open
Ch 23-31
Open
Ch 56-63
<< L1-SEI-C2

## Slide 246: D1000272 – S1101321
<< L1-SEI-C2
S1101321
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter
HAM3 HEPI Anti-Alias Chassis
D1000269
±18@1A
S1101321
D1000269
Front
IN 1-5
IN 6-10
IN 11-15
IN 27-29
IN 29-32
aLIGO HEPI Anti-Alias Chassis
LIGO-D1000272
IN 25-28
IN 29-32
IN 29-32
IN 25-28
IN 1-5
IN 1-5
IN 6-10
IN 6-10
IN 11-15
IN 11-15
DC Power
+V -V
IN 16-20
IN 21-26
IN 16-20
IN 16-20
IN 21-26
IN 21-26

## Slide 247: D020373 – S1000844
S1000844
Rear
VALVE INPUTS
8 CHANNEL VALVE DRIVER
POWER DISTRIBUTION
LIGO D040049
VALVE INPUTS
VALVE INPUTS
D020373
Front
CHANS 1&2
CHANS 1&2
CHANS 3&4
CHANS 3&4
CHANS 1&2
CHANS 3&4
CHANS 5&6
CHANS 5&6
CHANS 7&8
CHANS 7&8
CHANS 5&6
CHANS 7&8
8 CHANNEL VALVE DRIVER
LIGO D020373 REV C
D040049
HEPI3 8-Channel Valve Driver
D020373
Power
S1000844
HAM3 PRM
<< L1-SEI-C2

## Slide 248: D1001715 - S1001145
l1seiham2-3 - I/O Extension Chassis
D1001715
24 VDC
S1001145
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1001145
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1seiham2-3 – I/O Extender
<< L1-SEI-C2
Slot P7
ADC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx
Slot P7
ADC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx

## Slide 249: L1-SEI-C3
+18VDC 12A
-18VDC 12A
+24VDC ?A
-24VDC ?A
HAM4 HEPI 8-Channel Valve Driver
D020373
+18V@0.72A, -18V@0.72A
S1000845
HAM5 HEPI 8-Channel Valve Driver
D020373
+18V@0.72A, -18V@0.72A
SN:
l1seiham4-5 - I/O Extension Chassis
D1001715
+24@5A
S1001146
SEI HAM4 and HAM5 ISI and HEPI Rack Layout (D1201114) (S1200745)
HAM4 ISI Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
HAM4 ISI Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
HAM4 ISI Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
HAM5 ISI Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
HAM5 ISI Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
HAM5 ISI Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
HAM4 ISI Coil Driver Pod 1 and Pod 2
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
HAM4 ISI Coil Driver Pod 3
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
HAM5 ISI Coil Driver Pod 1 and Pod 2
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
HAM5 ISI Coil Driver Pod 3
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
Anti-Image Chassis
Dnumber
±18@0.5A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
Anti-Alias Chassis
Dnumber
±18@1A
Serial
<< CER
PSO-015
PSY-014
PSY-015
HAM4 ISI Anti-Alias Chassis
D1000269
±18@1A
S1104621
HAM4 ISI Anti-Alias Chassis
D1000269
±18@1A
S1104638
HAM4 HEPI Anti-Image Chassis
D1100202
±18@0.5A
S1104572
SEI-C3 is part of D1000298

## Slide 250: L1-SEI-C3 Details
L1-SEI-C3 Details
<< L1-SEI-C3

## Slide 251: D1000269 – S1104621
S1104621
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter
HAM4 ISI Anti-Alias Chassis
D1000269
±18@1A
S1104621
D1000269
Front
IN 1-8
IN 9-20
IN 21-24
IN 25-28
IN 29-32
aLIGO HAM ISI Anti-Alias Chassis
LIGO-D1000269
IN 25-28
IN 29-32
IN 29-32
IN 25-28
IN 1-8
IN 1-8
IN 9-20
IN 9-20
IN 21-24
IN 21-24
DC Power
+V -V
<< L1-SEI-C3

## Slide 252: D1000269 – S1104638
S1104638
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter
HAM4 ISI Anti-Alias Chassis
D1000269
±18@1A
S1104638
D1000269
Front
IN 1-8
IN 9-20
IN 21-24
IN 25-28
IN 29-32
aLIGO HAM ISI Anti-Alias Chassis
LIGO-D1000269
IN 25-28
IN 29-32
IN 29-32
IN 25-28
IN 1-8
IN 1-8
IN 9-20
IN 9-20
IN 21-24
IN 21-24
DC Power
+V -V
<< L1-SEI-C3

## Slide 253: D1100202 - S1104572
S1104572
Rear
From DAC Adapter
From DAC Adapter
From DAC Adapter
HAM4 HEPI Anti-Image Chassis
D1100202
±18@0.5A
S1104572
D1100202
OUT 1-8
OUT 9-12
OUT 13-16
aLIGO HEPI Anti-Image Chassis
OUT 1-8
OUT 9-12
OUT 13-16
Front
OUT 1-8
OUT 9-12
OUT 13-16
LIGO D1100202
DC Power
+V -V
<< L1-SEI-C3

## Slide 254: D020373 – S1000845
S1000845
Rear
VALVE INPUTS
8 CHANNEL VALVE DRIVER
POWER DISTRIBUTION
LIGO D040049
VALVE INPUTS
VALVE INPUTS
D040049
HEPI4 8-Channel Valve Driver
D020373
Power
S1000845
HAM4 OUT
<< L1-SEI-C3
D020373
Front
CHANS 1&2
CHANS 1&2
CHANS 3&4
CHANS 3&4
CHANS 1&2
CHANS 3&4
CHANS 5&6
CHANS 5&6
CHANS 7&8
CHANS 7&8
CHANS 5&6
CHANS 7&8
8 CHANNEL VALVE DRIVER
LIGO D020373 REV C

## Slide 255: D0901338 - Sxxxxxxx
SN:
Rear
From AI Chassis
D0901338
Front
Open
CHANS 1&2
Open
CHANS 3&4
CHANS 1&2
CHANS 3&4
Open
CHANS 5&6
Open
CHANS 7&8
CHANS 5&6
CHANS 7&8
Open
From AI Chassis
8 CHANNEL VALVE DRIVER
LIGO D090117-v2
8 CHANNEL VALVE DRIVER
LIGO D090117-v2
HEPI5 8-Channel Valve Driver
D0901338
Power
SN:
<< L1-SEI-C3

## Slide 256: D1001715-S1001146
l1seiham4-5 - I/O Extension Chassis
D1001715
24 VDC
S1001146
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1001146
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1seiham4-5 - I/O Extender
<< L1-SEI-C3
Slot P7
ADC Adapter
Sxxxxxxx
Slot P7
ADC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx

## Slide 257: L1-SEI-C4
+18VDC 10A
-18VDC 10A
+24VDC ?A
-24VDC ?A
l1seibsc1 - I/O Extension Chassis
D1001715
+24@5A
S1001147
SEI BSC1 ISI and HEPI Rack Layout (D1201115) (S1200746)
BSC1 HEPI 8-Channel Valve Driver
D020373
+18V@0.72A, -18V@0.72A
SN:
BSC1 L4C Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC1 ISI Interface Chassis Pod 3
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC1 ISI Interface Chassis Pod 2
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC1 ISI Interface Chassis Pod 1
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC1 BSC Anti-Alias Chassis
D1002693
±18@1A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
BSC1 ISI Coil Driver Pod 2
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
BSC1 ISI Coil Driver Pod 3
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
Anti-Image Chassis
Dnumber
±18@0.5A
Serial
Anti-Image Chassis
Dnumber
±18@0.5A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
BSC1 ISI Coil Driver Pod 1
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
BSC1 L4C Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
BSC1 T-240 Interface Chassis Pod 1
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC1 T-240 Interface Chassis Pod 2
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC1 T-240 Interface Chassis Pod 3
Dnumber
+18V@0.32A, -18V@0.33A
Serial
<< CER
PSO-014
PSY-013
PSY-016
SEI-C4 is part of D0901301

## Slide 258: L1-SEI-C4 Details
L1-SEI-C4 Details
<< L1-SEI-C4

## Slide 259: D1002693 – Sxxxxxxx
Sxxxxxxx
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter
BSC1 BSC Anti-Alias Chassis
D1002693
±18@1A
Sxxxxxxx
D1002693
Front
In 1-8
In 9-20
In 21-27
In 28-31
IN 29-32
aLIGO BSC ISI Anti-Alias Chassis
LIGO-D1002693
In 28-31
In 32
In 32
In 28-31
In 1-8
In 1-8
In 9-20
In 9-20
In 21-27
In 21-27
+V -V
DC Power
<< L1-SEI-C4

## Slide 260: D020373 – S1000848
S1000848
Rear
VALVE INPUTS
8 CHANNEL VALVE DRIVER
POWER DISTRIBUTION
LIGO D040049
VALVE INPUTS
VALVE INPUTS
D040049
BSC1 8-Channel Valve Driver
D020373
Power
S1000848
BSC1 ITMY
<< L1-SEI-C4
D020373
Front
CHANS 1&2
CHANS 1&2
CHANS 3&4
CHANS 3&4
CHANS 1&2
CHANS 3&4
CHANS 5&6
CHANS 5&6
CHANS 7&8
CHANS 7&8
CHANS 5&6
CHANS 7&8
8 CHANNEL VALVE DRIVER
LIGO D020373 REV C

## Slide 261: D1001715-S1001147
l1seibsc1 - I/O Extension Chassis
D1001715
24 VDC
S1001147
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
24 VDC
S1001147
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1seibsc1 - I/O Extender
<< L1-SEI-C4

## Slide 262: L1-SEI-C5 Details
L1-SEI-C5 Details
<< L1-SEI-C5

## Slide 263: D020373 – S1000846
S1000847
Rear
VALVE INPUTS
8 CHANNEL VALVE DRIVER
POWER DISTRIBUTION
LIGO D040049
VALVE INPUTS
VALVE INPUTS
D040049
BSC2 8-Channel Valve Driver
D020373
Power
S1000847
BSC2 BS
<< L1-SEI-C5
D020373
Front
CHANS 1&2
CHANS 1&2
CHANS 3&4
CHANS 3&4
CHANS 1&2
CHANS 3&4
CHANS 5&6
CHANS 5&6
CHANS 7&8
CHANS 7&8
CHANS 5&6
CHANS 7&8
8 CHANNEL VALVE DRIVER
LIGO D020373 REV C

## Slide 264: D1001715-S1001148
l1seibsc2 - I/O Extension Chassis
D1001715
24 VDC
S1001148
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
24 VDC
S1001148
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1seibsc2 - I/O Extender
<< L1-SEI-C5

## Slide 265: L1-SEI-C5
+18VDC 10A
-18VDC 10A
+24VDC ?A
-24VDC ?A
l1seibsc2 - I/O Extension Chassis
D1001715
+24@5A
S1001148
SEI BSC2 ISI and HEPI Rack Layout (D1201116) (S1200747)
BSC2 HEPI 8-Channel Valve Driver
D020373
+18V@0.72A, -18V@0.72A
SN:
BSC2 L4C Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC2 ISI Interface Chassis Pod 3
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC2 ISI Interface Chassis Pod 2
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC2 ISI Interface Chassis Pod 1
Dnumber
+18V@0.32A, -18V@0.33A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
BSC2 ISI Coil Driver Pod 2
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
BSC2 ISI Coil Driver Pod 3
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
Anti-Image Chassis
Dnumber
±18@0.5A
Serial
Anti-Image Chassis
Dnumber
±18@0.5A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
BSC2 ISI Coil Driver Pod 1
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
BSC2 L4C Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
BSC2 T-240 Interface Chassis Pod 1
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC2 T-240 Interface Chassis Pod 2
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC2 T-240 Interface Chassis Pod 3
Dnumber
+18V@0.32A, -18V@0.33A
Serial
<< CER
PSO-020
PSY-022
PSY-023
SEI-C5 is part of D0901301

## Slide 266: L1-SEI-C6
+18VDC 10A
-18VDC 10A
+24VDC ?A
-24VDC ?A
l1seibsc3 - I/O Extension Chassis
D1001715
+24@5A
S1100946
SEI BSC3 ISI and HEPI Rack Layout (D1201117) (S1200748)
BSC3 HEPI 8-Channel Valve Driver
D020373
+18V@0.72A, -18V@0.72A
SN:
BSC3 L4C Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC3 ISI Interface Chassis Pod 3
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC3 ISI Interface Chassis Pod 2
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC3 ISI Interface Chassis Pod 1
Dnumber
+18V@0.32A, -18V@0.33A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
BSC3 ISI Coil Driver Pod 2
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
BSC3 ISI Coil Driver Pod 3
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
Anti-Image Chassis
Dnumber
±18@0.5A
Serial
Anti-Image Chassis
Dnumber
±18@0.5A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
Anti-Alias Chassis
Dnumber
±18@1A
Serial
BSC3 ISI Coil Driver Pod 1
D0902744
+24V@1.2A, -24V@0.8A (+10A)
SN:
BSC3 L4C Interface Chassis
Dnumber
+18V@0.32A, -18V@0.33A
Serial
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
BSC3 T-240 Interface Chassis Pod 1
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC3 T-240 Interface Chassis Pod 2
Dnumber
+18V@0.32A, -18V@0.33A
Serial
BSC3 T-240 Interface Chassis Pod 3
Dnumber
+18V@0.32A, -18V@0.33A
Serial
<< CER
PSO-019
PSY-021
PSY-024
SEI-C6 is part of D0901301

## Slide 267: L1-SEI-C6 Details
L1-SEI-C6 Details
<< L1-SEI-C6

## Slide 268: D020373 – S1000847
S1000847
Rear
VALVE INPUTS
8 CHANNEL VALVE DRIVER
POWER DISTRIBUTION
LIGO D040049
VALVE INPUTS
VALVE INPUTS
D040049
BSC3 8-Channel Valve Driver
D020373
Power
S1000847
BSC3 ITMX
<< L1-SEI-C6
D020373
Front
CHANS 1&2
CHANS 1&2
CHANS 3&4
CHANS 3&4
CHANS 1&2
CHANS 3&4
CHANS 5&6
CHANS 5&6
CHANS 7&8
CHANS 7&8
CHANS 5&6
CHANS 7&8
8 CHANNEL VALVE DRIVER
LIGO D020373 REV C

## Slide 269: D1001715-S1100946
l1seibsc3 - I/O Extension Chassis
D1001715
24 VDC
S1100946
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
24 VDC
S1100946
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1seibsc3 – I/O Extender
<< L1-SEI-C6

## Slide 270: Subsystem: SUS (Suspensions)
2feet
Each Rack is 39” Deep and 24” Wide
2 feet
L1-SUS-C1
L1-SUS-C2
L1-SUS-C3
L1-SUS-C4
L1-SUS-C5
L1-SUS-C6
L1-SUS-C7
L1-SUS-C8
L1-SEI-C1
Front
Front
Front
Front
Front
Front
L1-SEI-C2
L1-AOS-C1
L1-SEI-C3
L1-SEI-C4
L1-SEI-C5
L1-SEI-C6
L1-UNK-C3
L1-UNK-C2
L1-UNK-C1
L1-PSL-C1
CDS Electronics Room (CER)
L1-OAF-C1
SUS ITMX, ITMY, FMX, FMY, and BS Rack 1
SUS HAM3 and HAM4 Rack 2
SUS HAM3 and HAM4 Rack 1
SUS HAM2 Rack 1
SUS HAM2 Rack 2
SUS ITMX, ITMY, FMX, FMY, and BS Rack 2
SUS HAM5 and HAM6 Rack 1
SUS HAM5 and HAM6 Rack 2
ISC LVEA Rack 1
ISC LVEA Rack 2
ISC LVEA Rack 3
PSL Rack 1
DAQ Rack 1
TCS Rack 1
Front
SEI HAM1 and HAM6
SEI HAM2 and HAM3
SEI HAM4 and HAM5
SEI BSC1
SEI BSC2
SEI BSC3
ISC LVEA Rack 4
L1-FAC-C1
<< IFO Subsystems
L1-ISC-C1
L1-ISC-C2
L1-ISC-C3
L1-ISC-C4
SUS

## Slide 271: L1-SUS-C1 – S1104062
SUS HAM3 and HAM4 Rack 1 (of 2) Layout (LIGO-D1000599) (S1104062)
PR2 Mid Triple Acq Driver Chassis
D0900006
±18@1A
S1000349
MC2 Bot Triple Acq Driver Chassis
D0900006
±18@1A
S1000348
MC2 Mid Triple Acq Driver Chassis
D0900006
±18@1A
S1000347
MC2-PR2 Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000260
MC2-PR2 Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000264
MC2-PR2 Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000721
SR2 Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000722
SR2 Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000273
SR2 Bot Triple Acq Driver Chassis
D0900006
±18@1A
S1001188
SR2 Mid Triple Acq Driver Chassis
D0900006
±18@1A
S1001187
PR2 Bot Triple Acq Driver Chassis
D0900006
±18@1A
S1001186
FE DAC4, FE DAC5 Anti-Image Chassis
D1000305
±18@0.5A
S1101815
FE DAC2, FE DAC3 Anti-Image Chassis
D1000305
±18@0.5A
S1001198
FE DAC0, FE DAC1 Anti-Image Chassis
D1000305
±18@0.5A
S1001197
BIO2 Binary Input Chassis
D1000726
±18@0.5A
S1101802
BIO2 Binary Output Chassis
D1000725
±18@0.5A
S1101782
BIO1 Binary Output Chassis
D1000725
±18@0.5A
S1101781
BIO1 Binary Input Chassis
D1000726
±18@0.5A
S1101805
FE ADC1 Anti-Alias Chassis
D0902783
±18@1A
S1100327
FE ADC0 Anti-Alias Chassis
D0902783
±18@1A
S1001157
<< CER
PSO-008

## Slide 272: L1-SUS-C1 Details
L1-SUS-C1 Details
<< L1-SUS-C1

## Slide 273: D1001242 - S1000260
MC2-PR2 Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000260
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
<< L1-SUS-C1
S1000260
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 274: D1001242 - S1000264
MC2-PR2 Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000264
<< L1-SUS-C1
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
S1000264
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 275: D1001242 - S1000721
MC2-PR2 Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000721
<< L1-SUS-C1
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
S1000721
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 276: D1001242 - S1000722
SR2 Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000722
<< L1-SUS-C1
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
S1000722
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 277: D1001242 - S1000273
SR2 Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000273
<< L1-SUS-C1
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
S1000273
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 278: D0902783 - S1001157
<< L1-SUS-C1
FE ADC0 Anti-Alias Chassis
D0902783
±18@1A
S1001157
D0902783
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
PMC AA 1-4
PMC AA 5-8
PMC AA 9-12
PMC AA 13-16
PMC AA 17-20
PMC AA 21-24
PMC AA 25-28
IN 29-32
PMC AA 29-32
IN 25-28
IN 21-24
IN 17-20
IN 13-16
IN 5-8
IN 9-12
IN 1-4
Front
S1001157
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter

## Slide 279: D0902783 - S1100327
<< L1-SUS-C1
FE ADC1 Anti-Alias Chassis
D0902783
±18@1A
S1100327
D0902783
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
PMC AA 1-4
PMC AA 5-8
PMC AA 9-12
PMC AA 13-16
PMC AA 17-20
PMC AA 21-24
PMC AA 25-28
IN 29-32
PMC AA 29-32
IN 25-28
IN 21-24
IN 17-20
IN 13-16
IN 5-8
IN 9-12
IN 1-4
Front
S1100327
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter

## Slide 280: D1000305 - S1001197
<< L1-SUS-C1
FE DAC0, FE DAC1 Anti-Image Chassis
D1000305
±18@1A
S1001197
D1000305
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
aLIGO Anti Image Chassis
D1000305
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
Front
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
S1001197
Rear
From DAC Adapter 0
From DAC Adapter 0
From DAC Adapter 0
From DAC Adapter 1
Chan 0-7
Chan 8-16
From DAC Adapter 1
From DAC Adapter 1

## Slide 281: D1000305 - S1001198
<< L1-SUS-C1
FE DAC2, FE DAC3 Anti-Image Chassis
D1000305
±18@1A
S1001198
D1000305
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
aLIGO Anti Image Chassis
D1000305
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
Front
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
S1001198
Rear
From DAC Adapter 0
From DAC Adapter 0
From DAC Adapter 0
From DAC Adapter 1
Chan 0-7
Chan 8-16
From DAC Adapter 1
From DAC Adapter 1

## Slide 282: D0900006 – S1000347
MC2 Mid Triple Acq Driver Chassis
D0900006
±18@0.5A
S1000347
<< L1-SUS-C1
D070480
Relay Controls
Relay Controls
Relay Monitors
Relay Monitors
D0901047
Front
PD Out to AA
LED Mon
Relay Monitors
Relay Controls
Power
Drive Input
Test In
Triple Acquisition Driver
University of Birmingham
D0900006
Drive Input
Drive Input
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
S1000347
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 283: D0900006 – S1000348
MC2 Bot Triple Acq Driver Chassis
D0900006
±18@0.5A
S1000348
<< L1-SUS-C1
D070480
Relay Controls
Relay Controls
Relay Monitors
Relay Monitors
D0901047
Front
PD Out to AA
LED Mon
Relay Monitors
Relay Controls
Power
Drive Input
Test In
Triple Acquisition Driver
University of Birmingham
D0900006
Drive Input
Drive Input
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
S1000348
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 284: D0900006 – S1000349
PR2 Mid Triple Acq Driver Chassis
D0900006
±18@0.5A
S1000349
<< L1-SUS-C1
D070480
Relay Controls
Relay Controls
Relay Monitors
Relay Monitors
D0901047
Front
PD Out to AA
LED Mon
Relay Monitors
Relay Controls
Power
Drive Input
Test In
Triple Acquisition Driver
University of Birmingham
D0900006
Drive Input
Drive Input
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
S1000349
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 285: D1000305 - S1001815
<< L1-SUS-C1
FE DAC4, FE DAC5 Anti-Image Chassis
D1000305
±18@1A
S1101815
D1000305
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
aLIGO Anti Image Chassis
D1000305
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
Front
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
S1101815
Rear
From DAC Adapter 0
From DAC Adapter 0
From DAC Adapter 0
From DAC Adapter 1
Chan 0-7
Chan 8-16
From DAC Adapter 1
From DAC Adapter 1

## Slide 286: D0900006 – S1001186
PR2 Bot Triple Acq Driver Chassis
D0900006
±18@0.5A
S1001186
<< L1-SUS-C1
D070480
Relay Controls
Relay Controls
Relay Monitors
Relay Monitors
D0901047
Front
PD Out to AA
LED Mon
Relay Monitors
Relay Controls
Power
Drive Input
Test In
Triple Acquisition Driver
University of Birmingham
D0900006
Drive Input
Drive Input
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
S1001186
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 287: D0900006 – S1001187
SR2 Mid Triple Acq Driver Chassis
D0900006
±18@0.5A
S1001187
<< L1-SUS-C1
D070480
Relay Controls
Relay Controls
Relay Monitors
Relay Monitors
D0901047
Front
PD Out to AA
LED Mon
Relay Monitors
Relay Controls
Power
Drive Input
Test In
Triple Acquisition Driver
University of Birmingham
D0900006
Drive Input
Drive Input
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
S1001187
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 288: D0900006 – S1001188
SR2 Bot Triple Acq Driver Chassis
D0900006
±18@0.5A
S1001188
<< L1-SUS-C1
D070480
Relay Controls
Relay Controls
Relay Monitors
Relay Monitors
D0901047
Front
PD Out to AA
LED Mon
Relay Monitors
Relay Controls
Power
Drive Input
Test In
Triple Acquisition Driver
University of Birmingham
D0900006
Drive Input
Drive Input
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
S1001188
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 289: D1000725 – S1101781
<< L1-SUS-C1
BIO1 Binary Output Chassis
D1000725
±18@0.5A
S1101781
Ch 20-31
Ch 20-31
Ch 52-63
Ch 52-63
Ch 0-7
Ch 0-7
Ch 8-19
Ch 8-19
Ch 40-51
Ch 40-51
Ch 32-39
Ch 32-39
D1000725
Front
Ch 0-7
Ch 8-19
Ch 32-39
Ch 40-51
Ch 20-31
aLIGO SUS
64 Channel
Binary Output
aLIGO
D1000725
Ch 52-63
S1101781
Rear
Ch 32-63
Ch 32-63
Ch 32-63
Ch 0-31
To Binary Outputs
of I/O Chassis
Ch 0-31
Ch 0-31

## Slide 290: D1000726 – S1101805
<< L1-SUS-C1
Ch 20-31
Ch 20-31
Ch 52-63
Ch 52-63
Ch 0-7
Ch 0-7
Ch 8-19
Ch 8-19
Ch 40-51
Ch 40-51
Ch 32-39
Ch 32-39
D1000726
Front
Ch 0-7
Ch 8-19
Ch 32-39
Ch 40-51
Ch 20-31
aLIGO SUS
64 Channel
Binary Input
aLIGO
D1000726
Ch 52-63
S1101805
Rear
Ch 32-63
Ch 32-63
Ch 32-63
Ch 0-31
To Binary Inputs
of I/O Chassis
Ch 0-31
Ch 0-31
BIO1 Binary Input Chassis
D1000726
±18@0.5A
S1101805

## Slide 291: D1000725 – S1101782
<< L1-SUS-C1
BIO2 Binary Output Chassis
D1000725
±18@0.5A
S1101782
Ch 20-31
Ch 20-31
Ch 52-63
Ch 52-63
Ch 0-7
Ch 0-7
Ch 8-19
Ch 8-19
Ch 40-51
Ch 40-51
Ch 32-39
Ch 32-39
D1000725
Front
Ch 0-7
Ch 8-19
Ch 32-39
Ch 40-51
Ch 20-31
aLIGO SUS
64 Channel
Binary Output
aLIGO
D1000725
Ch 52-63
S1101782
Rear
Ch 32-63
Ch 32-63
Ch 32-63
Ch 0-31
To Binary Outputs
of I/O Chassis
Ch 0-31
Ch 0-31

## Slide 292: D1000726 – S1101802
<< L1-SUS-C1
BIO2 Binary Input Chassis
D1000726
±18@0.5A
S1101802
Ch 20-31
Ch 20-31
Ch 52-63
Ch 52-63
Ch 0-7
Ch 0-7
Ch 8-19
Ch 8-19
Ch 40-51
Ch 40-51
Ch 32-39
Ch 32-39
D1000726
Front
Ch 0-7
Ch 8-19
Ch 32-39
Ch 40-51
Ch 20-31
aLIGO SUS
64 Channel
Binary Input
aLIGO
D1000726
Ch 52-63
S1101802
Rear
Ch 32-63
Ch 32-63
Ch 32-63
Ch 0-31
To Binary Inputs
of I/O Chassis
Ch 0-31
Ch 0-31

## Slide 293: L1-SUS-C2 – S1104356
SUS HAM3 and HAM4 Rack 2 (of 2) Layout (LIGO-D1000599) (S1104356)
MON ADC2 Anti-Alias Chassis
D0902783
±18@1A
S1105148
MON ADC1 Anti-Alias Chassis
D0902783
±18@1A
S1105149
MON ADC0 Anti-Alias Chassis
D0902783
±18@1A
S1105129
l1susham3-4 FE I/O Extension Chassis
D1001715
+24@5A
S1001140
l1susauxham3-4 MON I/O Extension Chassis
D1001715
+24@5A
S1001141
MON ADC3 Anti-Alias Chassis
D0902783
±18@1A
S1105147
MON ADC4 Anti-Alias Chassis
D0902783
±18@1A
S1105146
MON ADC5 Anti-Alias Chassis
D0902783
±18@1A
S1105145
<< CER
PSO-007
PSY-004

## Slide 294: L1-SUS-C2 Details
L1-SUS-C2 Details
<< L1-SUS-C2

## Slide 295: D0902783 - S1105129
FE ADC1 Anti-Alias Chassis
D0902783
±18@1A
S1105129
D0902783
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
PMC AA 1-4
PMC AA 5-8
PMC AA 9-12
PMC AA 13-16
PMC AA 17-20
PMC AA 21-24
PMC AA 25-28
IN 29-32
PMC AA 29-32
IN 25-28
IN 21-24
IN 17-20
IN 13-16
IN 5-8
IN 9-12
IN 1-4
S1105129
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter
Front
<< L1-SUS-C2

## Slide 296: D0902783 - S1105149
FE ADC1 Anti-Alias Chassis
D0902783
±18@1A
S1105149
D0902783
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
PMC AA 1-4
PMC AA 5-8
PMC AA 9-12
PMC AA 13-16
PMC AA 17-20
PMC AA 21-24
PMC AA 25-28
IN 29-32
PMC AA 29-32
IN 25-28
IN 21-24
IN 17-20
IN 13-16
IN 5-8
IN 9-12
IN 1-4
Front
<< L1-SUS-C2
S1105149
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter

## Slide 297: D0902783 - S1105148
FE ADC1 Anti-Alias Chassis
D0902783
±18@1A
S1105148
D0902783
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
PMC AA 1-4
PMC AA 5-8
PMC AA 9-12
PMC AA 13-16
PMC AA 17-20
PMC AA 21-24
PMC AA 25-28
IN 29-32
PMC AA 29-32
IN 25-28
IN 21-24
IN 17-20
IN 13-16
IN 5-8
IN 9-12
IN 1-4
Front
<< L1-SUS-C2
S1105148
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter

## Slide 298: D0902783 - S1105147
FE ADC1 Anti-Alias Chassis
D0902783
±18@1A
S1105147
D0902783
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
PMC AA 1-4
PMC AA 5-8
PMC AA 9-12
PMC AA 13-16
PMC AA 17-20
PMC AA 21-24
PMC AA 25-28
IN 29-32
PMC AA 29-32
IN 25-28
IN 21-24
IN 17-20
IN 13-16
IN 5-8
IN 9-12
IN 1-4
Front
<< L1-SUS-C2
S1105147
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter

## Slide 299: D0902783 – S1105146
FE ADC1 Anti-Alias Chassis
D0902783
±18@1A
S1105146
D0902783
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
PMC AA 1-4
PMC AA 5-8
PMC AA 9-12
PMC AA 13-16
PMC AA 17-20
PMC AA 21-24
PMC AA 25-28
IN 29-32
PMC AA 29-32
IN 25-28
IN 21-24
IN 17-20
IN 13-16
IN 5-8
IN 9-12
IN 1-4
Front
<< L1-SUS-C2
S1105146
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter

## Slide 300: D0902783 - S1105145
FE ADC1 Anti-Alias Chassis
D0902783
±18@1A
S1105145
D0902783
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
aLIGO Anti-Alias Module
D0902783
PMC AA 1-4
PMC AA 5-8
PMC AA 9-12
PMC AA 13-16
PMC AA 17-20
PMC AA 21-24
PMC AA 25-28
IN 29-32
PMC AA 29-32
IN 25-28
IN 21-24
IN 17-20
IN 13-16
IN 5-8
IN 9-12
IN 1-4
Front
<< L1-SUS-C2
S1105145
Rear
To ADC Adapter
To ADC Adapter
To ADC Adapter

## Slide 301: D1001715 - S1001141
<< L1-SUS-C2
l1susauxham3-4 MON I/O Extension Chassis
D1001715
24 VDC
S1001141
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1001141
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1sysauxham3-4 I/O Extender

## Slide 302: D1001715 - S1001140
<< L1-SUS-C2
l1susham3-4 FE I/O Extension Chassis
D1001715
24 VDC
S1001140
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
24 VDC
S1001140
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1susham3-4 – I/O Extender
DAC Adapter
Sxxxxxxx

## Slide 303: L1-SUS-C3 – S1104357
SUS HAM2 Rack 1 (of 2) Layout (LIGO-D0902810) (S1104357)
MON ADC2 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC1 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC0 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC6 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC5 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC4 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC3 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
l1susham2b FE I/O Extension Chassis
D1001715
+24@5A
S1001139
l1susham2a FE I/O Extension Chassis
D1001715
+24@5A
S1001133
l1susauxham2 MON I/O Extension Chassis
D1001715
+24@5A
S1103891
MON ADC7 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
BIO 2 Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
BIO 2 Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
BIO 1 Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
BIO 1 Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
BIO 0 Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
BIO 0 Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
<< CER
PSO-006
PSY-005
BIO 0 Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
BIO 0 Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:

## Slide 304: L1-SUS-C3 Details
L1-SUS-C3 Details
<< L1-SUS-C3

## Slide 305: D1001715-S1003891
l1susauxham2 MON I/O Extension Chassis
D1001715
24 VDC
S1003891
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1003891
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
Slot P7
ADC Adapter
Sxxxxxxx
Slot P7
ADC Adapter
Sxxxxxxx
l1sysauxham2 I/O Extender
<< L1-SUS-C3

## Slide 306: D1001715-S1001133
<< L1-SUS-C3
l1susham2a FE I/O Extension Chassis
D1001715
24 VDC
S1001133
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
24 VDC
S1001133
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1susham2a – I/O Extender
DAC Adapter
Sxxxxxxx

## Slide 307: D1001715-S1001139
l1susham2b FE I/O Extension Chassis
D1001715
24 VDC
S1001139
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1001139
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1susham2b – I/O Extender
<< L1-SUS-C3
Slot P7
DAC Adapter
Sxxxxxxx

## Slide 308: D1001726–Sxxxxxxx
Sxxxxxxx
Rear
Ch 32-63
Ch 32-63
Ch 32-63
Ch 0-31
To Binary Inputs
of I/O Chassis
Ch 0-31
Ch 0-31
Binary Input Chassis
D1001726
±18@0.5A
Sxxxxxxxx
Ch 23-31
Ch 16-23
Ch 56-63
Ch 48-55
Ch 0-7
Ch 0-7
Ch 8-15
Ch 8-15
Ch 40-47
Ch 40-47
Ch 32-39
Ch 32-39
D1001726
Front
Port 0
Ch 0-7
Port 1
Ch 8-15
Port 4
Ch 32-39
Port 5
Ch 40-47
Port 2
Ch 16-23
64 Channel
Binary Input
aLIGO
D1000726
Port 6
Ch 48-55
Port 3
Ch 24-31
Port 7
Ch 56-63
Ch 16-23
Ch 23-31
Ch 48-55
Ch 56-63
<< L1-SUS-C3

## Slide 309: D1001728–Sxxxxxxx
Sxxxxxxx
Rear
Ch 32-63
Ch 32-63
Ch 32-63
Ch 0-31
To Binary Outputs
of I/O Chassis
Ch 0-31
Ch 0-31
Binary Output Chassis
D1001728
±18@0.5A
Sxxxxxxxx
Ch 23-31
Ch 16-23
Ch 56-63
Ch 48-55
Ch 0-7
Ch 0-7
Ch 8-15
Ch 8-15
Ch 40-47
Ch 40-47
Ch 32-39
Ch 32-39
D1001728
Front
Port 0
Ch 0-7
Port 1
Ch 8-15
Port 4
Ch 32-39
Port 5
Ch 40-47
Port 2
Ch 16-23
64 Channel
Binary Input
aLIGO
D1000728
Port 6
Ch 48-55
Port 3
Ch 24-31
Port 7
Ch 56-63
Ch 16-23
Ch 23-31
Ch 48-55
Ch 56-63
<< L1-SUS-C3

## Slide 310: L1-SUS-C4 – S1104058
SUS HAM2 Rack 2 (of 2) Layout (LIGO-D0902810) (S1104358)
FE1 ADC0 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MC1-MC3 Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000253
MC1-MC3 Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000261
MC1-MC3 Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000262
PRM-PR3 Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000257
PRM-PR3 Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000259
PRM-PR3 Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000723
FE1 ADC1 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
FE1 DAC0, FE1 DAC1 Anti-Image Chassis
Dxxxxxxx
±18@0.5A
SN:
MC3 Mid Triple Acq Driver Chassis
D0900006
±18@1A
SN:
MC1 Bot Triple Acq Driver Chassis
D0900006
±18@1A
SN:
MC1 Mid Triple Acq Driver Chassis
D0900006
±18@1A
SN:
MC3 Bot Triple Acq Driver Chassis
D0900006
±18@1A
SN:
FE1 DAC6 Anti-Image Chassis
Dxxxxxxx
±18@0.5A
SN:
PR3 Mid Triple Acq Driver Chassis
D0900006
±18@1A
SN:
PRM Bot Triple Acq Driver Chassis
D0900006
±18@1A
SN:
PRM Mid Triple Acq Driver Chassis
D0900006
±18@1A
SN:
PR3 Bot Triple Acq Driver Chassis
D0900006
±18@1A
SN:
FE1 DAC2, FE1 DAC3 Anti-Image Chassis
Dxxxxxxx
±18@0.5A
SN:
FE1 DAC4, FE1 DAC5 Anti-Image Chassis
Dxxxxxxx
±18@0.5A
SN:
FE2 ADC0 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
FE2 DAC0 Anti-Image Chassis
Dxxxxxxx
±18@0.5A
SN:
SM2 8-Channel Coil Driver Chassis
Dxxxxxxx
±18@1A
SN:
SM2 8-Channel Coil Driver Chassis
Dxxxxxxx
±18@1A
SN:
<< CER
PSO-005
PSO-022
PMMT1 8-Channel Coil Driver Chassis
Dxxxxxxx
±18@1A
SN:
PMMT2 8-Channel Coil Driver Chassis
Dxxxxxxx
±18@1A
SN:

## Slide 311: L1-SUS-C4 Details
L1-SUS-C4 Details
<< L1-SUS-C4

## Slide 312: D1001242 - S1000253
MC1-MC3 Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000253
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
S1000253
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat
<< L1-SUS-C4

## Slide 313: D1001242 - S1000261
MC1-MC3 Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000261
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
S1000261
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat
<< L1-SUS-C4

## Slide 314: D1001242 - S1000262
MC1-MC3 Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000262
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
S1000262
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat
<< L1-SUS-C4

## Slide 315: D1001242 - S1000257
PRM-PR3 Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000257
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
S1000257
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat
<< L1-SUS-C4

## Slide 316: D1001242 - S1000259
PRM-PR3 Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000259
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
S1000259
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat
<< L1-SUS-C4

## Slide 317: D1001242 - S1000723
PRM-PR3 Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000723
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
S1000723
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat
<< L1-SUS-C4

## Slide 318: L1-SUS-C5 – S1105375
SUS ITMX, ITMY, and BS Rack 1 (of 2) Layout (LIGO-D1100022) (S1105375)
+18VDC 13A
-18VDC 13A
+24VDC 15A
ITMY Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000376
ITMY Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000436
ITMY Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000433
BS Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000722
BS Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000273
BS Mid Triple Acq Driver Chassis
D0900006
±18@1A
S1001103
ITMX Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000378
ITMX Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000379
ITMX Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000372
l1susauxbsc123 MON I/O Extension Chassis
D1001715
+24@5A
S1103888
l1susbsc123 FE I/O Extension Chassis
D1001715
+24@5A
S1001143
ITMY UIM Coil Driver Chassis
D0902668
±18@1A
SN:
ITMX UIM Coil Driver Chassis
D0902668
±18@1A
SN:
ITMY PUM Coil Driver Chassis
D1100303
±18@1A
SN:
ITMX PUM Coil Driver Chassis
D1100303
±18@1A
SN:
<< CER
PSO-004
PSY-002

## Slide 319: H2-SUS-C5 – S1105375
SUS ITMX, ITMY, BS, FMX, and FMY Rack 1 (of 2) Layout (LIGO-D1001725) (S1105375)
+18VDC 13A
-18VDC 13A
+24VDC 15A
ITMY Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000376
ITMY Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000436
ITMY Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000433
BS Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000722
BS Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000273
BS Mid Triple Acq Driver Chassis
D0900006
±18@1A
S1001103
ITMX Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000378
ITMX Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000379
ITMX Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000372
l1susauxbsc123 MON I/O Extension Chassis
D1001715
+24@5A
S1103888
l1susbsc123 FE I/O Extension Chassis
D1001715
+24@5A
S1001143
ITMY UIM Coil Driver Chassis
D0902668
±18@1A
SN:
ITMX UIM Coil Driver Chassis
D0902668
±18@1A
SN:
ITMY PUM Coil Driver Chassis
D1100303
±18@1A
SN:
ITMX PUM Coil Driver Chassis
D1100303
±18@1A
SN:
<< CER
PSO-004
PSY-002
FMY Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000722
FMY Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000273
FMY Mid Triple Acq Driver Chassis
D0900006
±18@1A
S1001103
FMX Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000722
FMX Triple Top Coil Driver Chassis
D1001242
±18@1A
S1000273
FMX Mid Triple Acq Driver Chassis
D0900006
±18@1A
S1001103
l1susauxbsc123 MON I/O Extension Chassis
D1001715
+24@5A
S1103888

## Slide 320: L1-SUS-C5 Details
L1-SUS-C5 Details
<< L1-SUS-C5

## Slide 321: D1001782-S1000376
ITMY Quad Top Coil Driver Chassis
D1001782
±18@0.5A
S1000376
<< L1-SUS-C5
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
QUAD Top Coil Driver
University of Birmingham
S1000376
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 322: D1001782-S1000436
<< L1-SUS-C5
ITMY Quad Top Coil Driver Chassis
D1001782
±18@1A
S1000436
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
QUAD Top Coil Driver
University of Birmingham
S1000376
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 323: D1001782-S1000433
ITMY Quad Top Coil Driver Chassis
D1001782
±18@0.5A
S1000433
<< L1-SUS-C5
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
QUAD Top Coil Driver
University of Birmingham
S1000376
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 324: D1001782-S1000378
ITMX Quad Top Coil Driver Chassis
D1001782
±18@0.5A
S1000378
<< L1-SUS-C5
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
QUAD Top Coil Driver
University of Birmingham
S1000376
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 325: D1001782-S1000379
ITMX Quad Top Coil Driver Chassis
D1001782
±18@0.5A
S1000379
<< L1-SUS-C5
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
QUAD Top Coil Driver
University of Birmingham
S1000376
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 326: D1001782-S1000372
ITMX Quad Top Coil Driver Chassis
D1001782
±18@0.5A
S1000372
<< L1-SUS-C5
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
QUAD Top Coil Driver
University of Birmingham
S1000376
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 327: D0902668-Sxxxxxxx
D070481
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
AdL PP UIM Coil Driver
University of Birmingham
S1000376
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat
ITMY UIM Coil Driver Chassis
D0902668
±18@0.5A
SN:
<< L1-SUS-C5

## Slide 328: D0902668-Sxxxxxxx
ITMX UIM Coil Driver Chassis
D0902668
±18@0.5A
SN:
<< L1-SUS-C5
D070481
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
AdL PP UIM Coil Driver
University of Birmingham
S1000376
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 329: D1100303-Sxxxxxxx
D070483
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
PUM Coil Driver
University of Birmingham
SN:
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat
ITMY PUM Coil Driver Chassis
D1100303
±18@0.5A
SN:
<< L1-SUS-C5

## Slide 330: D1100303-Sxxxxxxx
ITMX PUM Coil Driver Chassis
D1100303
±18@0.5A
SN:
<< L1-SUS-C5
D070483
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
PUM Coil Driver
University of Birmingham
SN:
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 331: D1001242-S1000722
BS Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000722
<< L1-SUS-C5
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
S1000722
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 332: D1001242-S1000273
BS Triple Top Coil Driver Chassis
D1001242
±18@0.5A
S1000273
<< L1-SUS-C5
D0902747
Front
Drive Input
Drive Input
PD Out to AA
LED Mon
Binary IO 1
Binary IO 2
D070480
Power
Drive Input
Test In
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
Binary IO 1
Binary IO 1
Binary IO 2
Binary IO 2
Advanced LIGO
Triple Top Coil Driver
University of Birmingham
S1000273
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat

## Slide 333: D0900006 –S1001103
D070480
Relay Controls
Relay Controls
Relay Monitors
Relay Monitors
D0901047
Front
PD Out to AA
LED Mon
Relay Monitors
Relay Controls
Power
Drive Input
Test In
Triple Acquisition Driver
University of Birmingham
D0900006
Drive Input
Drive Input
Test In
Test In
PD Out to AA
PD Out to AA
LED Mon
LED Mon
S1001103
Rear
PD in from Sat
V, I and RMS Monitor
Noise Monitor
Coil Out to Sat
PD in from Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
Noise Monitor
V, I and RMS Monitor
Coil Out to Sat
PD in from Sat
BS Mid Triple Acq Driver Chassis
D0900006
±18@0.5A
S1001103
This number is actually correct. The DocDB part number is erroneously D090006 because it got assigned before the Wizards decided there would be 5 digits, and they won’t fix if. I’ve asked.
<< L1-SUS-C5

## Slide 334: D1001715-S1001143
l1susbsc1-2-3 FE I/O Extension Chassis
D1001715
24 VDC
S1001143
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1001143
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
<< L1-SUS-C5
l1susbsc-1-2-3 I/O Extender
Slot P7
DAC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx

## Slide 335: D1001715-S1103888
l1susauxbsc1-2-3 MON I/O Extension Chassis
D1001715
24 VDC
S1103888
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1103888
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1susauxbsc-1-2-3 I/O Extender
<< L1-SUS-C5
Slot P7
ADC Adapter
Sxxxxxxx
Slot P7
ADC Adapter
Sxxxxxxx
Slot P7
ADC Adapter
Sxxxxxxx

## Slide 336: L1-SUS-C6 – S1105376
FE ADC1 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
FE ADC0 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
FE DAC4, FE DAC5 Anti-Image Chassis
Dxxxxxxx
±18@1A
SN:
FE DAC2, FE DAC3 Anti-Image Chassis
Dxxxxxxx
±18@1A
SN:
FE DAC0, FE DAC1 Anti-Image Chassis
Dxxxxxxx
±18@1A
SN:
SUS ITMX, ITMY, and BS Rack 2 (of 2) Layout (LIGO-D1100022) (S1105376)
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
FE DAC6, FE DAC7 Anti-Image Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC1 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC0 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC3 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC2 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC5 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC4 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC6 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
<< CER
PSO-003
PSO-021
FE2 ADC0 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
Laser Power Monitor Marshaling Chassis
Dxxxxxxx
±18@1A
SN:

## Slide 337: H2-SUS-C6 – S1105376
FE ADC1 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
FE ADC0 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
FE DAC4, FE DAC5 Anti-Image Chassis
Dxxxxxxx
±18@1A
SN:
FE DAC2, FE DAC3 Anti-Image Chassis
Dxxxxxxx
±18@1A
SN:
FE DAC0, FE DAC1 Anti-Image Chassis
Dxxxxxxx
±18@1A
SN:
SUS ITMX, ITMY, BS, FMX, and FMY Rack 2 (of 2) Layout (LIGO-D1001725) (S1105376)
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
FE DAC6, FE DAC7 Anti-Image Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC1 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC0 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC3 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC2 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC5 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC4 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC6 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
<< CER
PSO-003
PSO-021
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
FM FE ADC0 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC7 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC9 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC8 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
FE DAC8, FE DAC9 Anti-Image Chassis
Dxxxxxxx
±18@1A
SN:
FE DAC10 Anti-Image Chassis
Dxxxxxxx
±18@1A
SN:
FM FE ADC1 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
Laser Power Monitor Marshaling Chassis
Dxxxxxxx
±18@1A
SN:

## Slide 338: L1-SUS-C6 Details
L1-SUS-C6 Details
<< L1-SUS-C6

## Slide 339: L1-SUS-C7 – S1105377
+18VDC 14.5A
-18VDC 14.5A
FE ADC0 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
SR3-SRM Triple Top Coil Driver Chassis
D1001242
±18@1A
SN:
SR3-SRM Triple Top Coil Driver Chassis
D1001242
±18@1A
SN:
SR3-SRM Triple Top Coil Driver Chassis
D1001242
±18@1A
SN:
OMC Triple Top Coil Driver Chassis
D1001242
±18@1A
SN:
OMC Triple Top Coil Driver Chassis
D1001242
±18@1A
SN:
FE ADC1 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
FE DAC0, FE DAC1 Anti-Image Chassis
D1003224
±18@0.5A
SN:
SRM Mid Triple Acq Driver Chassis
D0900006
±18@1A
SN:
SR3 Bot Triple Acq Driver Chassis
D0900006
±18@1A
SN:
SR3 Mid Triple Acq Driver Chassis
D0900006
±18@1A
SN:
FE DAC4 Anti-Image Chassis
D1003224
±18@0.5A
SN:
SRM Bot Triple Acq Driver Chassis
D0900006
±18@1A
SN:
FE DAC2, FE DAC3 Anti-Image Chassis
D1003224
±18@0.5A
SN:
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Output Chassis
Dxxxxxxx
±18@0.5A
SN:
Binary Input Chassis
Dxxxxxxx
±18@0.5A
SN:
SUS HAM5 and HAM6 Rack 1 (of 2) Layout (LIGO-D1002740) (S1105377)
<< CER
PSO-002

## Slide 340: L1-SUS-C7 Details
L1-SUS-C7 Details
<< L1-SUS-C7

## Slide 341: D1003224-Sxxxxxx
FE DAC0, FE DAC1 Anti-Image Chassis
D1003224
±18@0.5A
SN:
SN:
Rear
From DAC Adapter
From DAC Adapter
From DAC Adapter
D1003224
Front
IN 1-4
IN 1-4
IN 5-8
IN 5-8
IN 1-4
IN 5-8
IN 9-12
IN 9-12
IN 13-16
IN 13-16
IN 9-12
IN 13-16
<< L1-SUS-C7

## Slide 342: D1003224-Sxxxxxx
FE DAC2, FE DAC3 Anti-Image Chassis
D1003224
±18@0.5A
SN:
<< L1-SUS-C7
SN:
Rear
From DAC Adapter
From DAC Adapter
From DAC Adapter
D1003224
Front
IN 1-4
IN 1-4
IN 5-8
IN 5-8
IN 1-4
IN 5-8
IN 9-12
IN 9-12
IN 13-16
IN 13-16
IN 9-12
IN 13-16

## Slide 343: D1003224-Sxxxxxx
FE DAC4 Anti-Image Chassis
D1003224
±18@0.5A
SN:
<< L1-SUS-C7
SN:
Rear
From DAC Adapter
From DAC Adapter
From DAC Adapter
D1003224
Front
IN 1-4
IN 1-4
IN 5-8
IN 5-8
IN 1-4
IN 5-8
IN 9-12
IN 9-12
IN 13-16
IN 13-16
IN 9-12
IN 13-16

## Slide 344: L1-SUS-C8 – S1105378
MON ADC2 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC1 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC0 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC4 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
MON ADC3 Anti-Alias Chassis
Dxxxxxxx
±18@1A
SN:
SUS HAM5 and HAM6 Rack 2 (of 2) Layout (LIGO-D1002740) (S1105378)
l1susham5-6 FE I/O Extension Chassis
D1001715
+24@5A
S1001142
l1susauxham5-6 MON I/O Extension Chassis
D1001715
+24@5A
S1103889
<< CER
PSO-001
PSY-001

## Slide 345: L1-SUS-C8 Details
L1-SUS-C8 Details
<< L1-SUS-C8

## Slide 346: D1001715-S1103889
<< L1-SUS-C8
l1susauxham5-6 MON I/O Extension Chassis
D1001715
24 VDC
S1103889
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1103889
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1psl0 - D1001715 – I/O Extender
Slot P7
ADC Adapter
Sxxxxxxx

## Slide 347: D1001715-S1001142
l1susham5-6 FE I/O Extension Chassis
D1001715
24 VDC
S1001142
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1001142
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1susham5-6 I/O Extender
<< L1-SUS-C8
Slot P7
DAC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx

## Slide 348: LVEA
LVEA
<< LLO Racks by AREA
<< LLO CDS Components
<< LLO Corner Station
17 Field Racks are in the LVEA, including the Vacuum Racks. See LIGO-D1003141) at LLO and LIGO-D1002704 at LHO.

## Slide 349: LVEA Access Points

## Slide 350: PSL / LDR Laser Hazard Zones
LAE Cargo Doors
LAE Airlock Entrance Door
PSL-HAM1 Shutter
LDR Entrance Door
LDR Cargo Doors
LVEA Control Box
LDR Interlock Box
Laser Area Enclosure (LAE)
Laser Diode Room (LDR)
Armoured Fiber Optics Cable

## Slide 351: LVEA Racks
L1-PSL-R1
L1-PSL-R2
L1-ISC-R1
L1-ISC-R2
L1-ISC-R5
L1-SUS-R4
L1-SUS-R1
L1-SUS-R2
L1-TCS-R2
L1-TCS-R1
L1-SUS-R5
L1-SUS-R6
L1-VAC-R1
L1-VAC-R3
L1-VAC-R2
L1-ISC-R4
<< LLO Corner Station
18 Field Racks are in the LVEA, including the Vacuum Racks. See LIGO-D1003141) at LLO and LIGO-D1002704 at LHO.
L1-ISC-R3
L1-SUS-R3

## Slide 352: LVEA Racks
PSL Rack 1
(L1-PSL-R1)
SUS Rack 5
(L1-SUS-R5)
ISC IMC/ALS Rack
(L1-ISC-R1)
SUS Rack 2
(L1-SUS-R2)
PSL Rack 2
(L1-PSL-R2)
SUS Rack 1
(L1-SUS-R1)
SUS Rack 3
(L1-SUS-R3)
SUS Rack 4
(L1-SUS-R4)
ISC HAM1 and HAM3 Rack
(L1-ISC-R2)
TCS Rack 1 (X)
(L1-TCS-R1)
TCS Rack 1 (Y)
(L1-TCS-R2)
ISC HAM6 Rack
(L1-ISC-R3)
SUS Rack 6
(L1-SUS-R6)
LVEA X-End VAC
(L1-VAC-R1)
LVEA Y-End VAC
(L1-VAC-R2)
LVEA Mech VAC
(L1-VAC-R3)
<< LLO Racks by AREA
ISC Rack
(L1-ISC-R4)
ISC Rack
(L1-ISC-R5)

## Slide 353: LVEA Tables
TCSY
TCSX
<< LLO Corner Station
18 Field Racks are in the LVEA, including the Vacuum Racks. See D1003141) at LLO and D1002704 at LHO.
Tables are named in E1200808.
Tables Patch Panels are listed in E1200613.
IOHT2L
ISCHT1L
IOHT2R
ISCHT6R
TCSHT4R
PSL Table

## Slide 354: LVEA Tables
ISC (ISCHT1L)
ISC (ISCHT6R)
TCS (TCSHT4R)
TCS (TCSX)
<< LLO Racks by AREA
PSL Table
IO (IOHT2L)
IO (IOHT2R)
TCS (TCSY)
4’ X 8’ Table Layout (D1201022)
3’ X 5’ Table Layout (D1200973)

## Slide 355: L1-PSL-R1
PSL Rack 1 Layout (LIGO-Dxxxxxxx)
UPS1
SUA3000RMXL3U
120VAC, 30A
JS1030009365
<< LVEA Racks
110VAC 20A
UPS1 - UPS Power Strip
Dxxxxxxx
ISS, TTFSS, and VCO VME Crate
Sxxxxxxx
+24VDC
Dxxxxxxx
ILS and PMC VME Crate
Sxxxxxxx
+24VDC
Delay Line Phase Shifter
D0900128
+15VDC
S1103558
CCD Breakout Panel
Dxxxxxxx
±12@0.5A
S1103562
Delay Line Phase Shifter
D0900128
+15VDC
S1103561
Dxxxxxxx
PSL Control Box
S1103746
+24VDC
Digi-pak 270 Physical Electronics
Innolight (Spare 2)
Shelf

## Slide 356: ISS, TTFSS, and VCO VME Crate
VME Crate
VME Crate
Front
TTFSS Field Box
S1103554
D1100367
Monitoring Field Box Module
S1103263
D1002292
PSL VCO Field Box
S1103555
D1100369
Dxxxxxxx
ISS, TTFSS, and VCO VME Crate
Sxxxxxxx
+24VDC
<< L1-PSL-R1
Intensity Stabilization Servo Module
S1103557
D1001985

## Slide 357: D0900128 – S1103558
<< L1-PSL-R1
Delay Line Phase Shifter
D0900128
+15VDC
S1103558
S1103558
Rear
D0900128
Front

## Slide 358: Dxxxxxx – S1103562
CCD Breakout Panel
Dxxxxxxx
±12@0.5A
S1103562
<< L1-PSL-R1

## Slide 359: D0900128 – S1103561
<< L1-PSL-R1
Delay Line Phase Shifter
D0900128
+15VDC
S1103561
S1103561
Rear
D0900128
Front

## Slide 360: ILS and PMC VME Crate
Dxxxxxxx
ILS and PMC VME Crate
Sxxxxxxx
+24VDC
<< L1-PSL-R1
ILS and PMC VME Crate
ILS and PMC VME Crate
Front
Injection Locking and PMC Locking Field Box
S1103541
D1001619
Injection Locking and PMC Locking Servo Module
S1103536
D1001618
Monitoring Field Box Module
S1102960
D1002292
Injection Locking and PMC Locking Servo Module
S1103538
D1001618
Injection Locking and PMC Locking Field Box
S1103540
D1001619

## Slide 361: Dxxxxxx – S1103746
Dxxxxxxx
PSL Control Box
S1103746
+24VDC
<< L1-PSL-R1
PSL Control Box
S1103746
Front

## Slide 362: SUA3000RMXL3U – JS1030009365 UPS
<< L1-PSL-R1
UPS1
SUA3000RMXL3U
120VAC, 30A
JS1030009365

## Slide 363: L1-PSL-R2
PSL Rack 2 Layout (LIGO-Dxxxxxxx)
<< LVEA Racks
Dxxxxxxx
Diagnostics Breadboard (DBB) 0208 Crate
Sxxxxxxx
+-19VDC, +-9VDC
Shelf
Shelf
Shelf
Shelf
Diagnostics Breadboard (DBB) 0208
Comtrol
IFR 2023A Signal Generator
IFR 2023A Signal Generator
Stanford Research DS345
Agilent E4400B Signal Generator
35.5MHz, 14.6dBm
80MHz, 32dBm
Panasonic 990 – LVEA1
Panasonic 990 – LVEA2
Tektronix TDS220
Camera Power Supplies …
CP5 Connector:
Pin 1: -19VDC
Pin 2: -9VDC
Pin 3: Ground
Pin 4: +9VDC
Pin 5 +19VDC

## Slide 364: VME Crate
<< L1-PSL-R2
Diagnostics Breadboard (DBB) VME Crate
Diagnostics Breadboard
(DBB) VME Crate
Front
Dxxxxxxx
Diagnostics Breadboard (DBB) VME Crate
Sxxxxxxx
+24VDC
PSL Diagnostics Breadboard High Voltage Module
S1103544
D1101102
PSL Diagnostics Breadboard Field Box
S1103546
D1101102
PSL Diagnostics Breadboard Demodulator Module
S1103548
D1101104
PSL Diagnostics Breadboard Miscellaneous Module
S1103550
D1101105
PSL Diagnostics Breadboard Calibration Module
S1103551
D1101103

## Slide 365: L1-ISC-R1
ISC IMC/ALS Rack Layout (LIGO-D1001460)
<< LVEA Racks
24.078 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
RF Patch Panel 10
Dxxxxxxx
No Power
Sxxxxxxx
RF Patch Panel 11
Dxxxxxxx
No Power
Sxxxxxxx
RF Patch Panel 12
Dxxxxxxx
No Power
Sxxxxxxx
79.4 MHz VCO (ALS)
D0900605
±17VDC, ±24VDC
Sxxxxxxx
79.4 MHz VCO (ALS)
D0900605
±17VDC, ±24VDC
Sxxxxxxx
79.4 MHz VCO (PSL)
D0900605
±17VDC, ±24VDC
Sxxxxxxx
158.8 MHz Frequency Doubler
D1002178
±17VDC, ±24VDC
Sxxxxxxx
158.8 / 79.4 MHz 2-Channel PF Discriminator
D1002476
±17VDC, ±24VDC
Sxxxxxxx
158.8 MHz Frequency Doubler
D1002178
±17VDC, ±24VDC
Sxxxxxxx
24.078 MHz Dual Delay Line
D0900128
+15VDC
Sxxxxxxx
24.078 MHz 2-Channel Demodulator
D1000181
±17VDC, ±24VDC
Sxxxxxxx
Mode Cleaner Servo
D0901781
±17VDC, ±24VDC
Sxxxxxxx
LSC Demod Concentrator 1
D1100691
±18VDC
Sxxxxxxx
ASC Demod Concentrator 1
D1100696
No Power
Sxxxxxxx
LSC RFPD Interface
D1102079
±18VDC
Sxxxxxxx
WFS Interface
D1101865
±15VDC
Sxxxxxxx
ISC Whitening Chassis (ASC IMC WFS_A 24MHz)
D1002559
±15VDC
Sxxxxxxx
WFS I/Q Demodulator (ASC IMC WFS_A 24MHz)
D0902796
±15VDC
Sxxxxxxx
WFS I/Q Demodulator (ASC IMC WFS_B 24MHz)
D0902796
±15VDC
Sxxxxxxx
Demodulator Patch Panel
D1100905
No Power
Sxxxxxxx
ISC Whitening Chassis (ASC IMC WFS_A 24MHz)
D1002559
±15VDC
Sxxxxxxx
Sequencer
D1200757
S1202564

## Slide 366: L1-ISC-R2
ISC HAM1 and HAM3 Rack Layout (LIGO-D1001425)
<< LVEA Racks
Sequencer
D1200757
S1202569

## Slide 367: L1-IOHT2L Table Layout
IOHT2L Table Layout (D1201531) (Sxxxxxxx)
<< LVEA Tables
IOHT2L is part of E1201099.

## Slide 368: L1-IOHT2L Panel Layout
IOHT2L Panel Layout (D1201529)
<< LVEA Tables

## Slide 369: L1-IOHT2R Table Layout
IOHT2R Table Layout (D1201532) (Sxxxxxxx)
<< LVEA Tables
IOHT2R is part of E1201099.

## Slide 370: L1-IOHT2R Panel Layout
IOHT2R Panel Layout (D1201530)
<< LVEA Tables

## Slide 371: L1-ISCHT1L Table Layout
ISCHT1L Table Layout (D1201499) (Sxxxxxxx)
<< LVEA Tables
ISCHT1L is part of E1201099.

## Slide 372: L1-ISCHT1L Panel Layout
ISCHT1L Panel Layout (D1201331)
<< LVEA Tables

## Slide 373: L1-ISCHT6R Table Layout
<< LVEA Tables
ISCHT6R Table Layout (D1201500) (Sxxxxxxx)
ISCHT6R is part of E1201099.

## Slide 374: L1-ISCHT6R Panel Layout
ISCHT6R Panel Layout (D1201496)
<< LVEA Tables

## Slide 375: L1-ISCBT4R Table Layout
<< LVEA Tables
ISCHT6R Table Layout (D1201498) (Sxxxxxxx)
ISCHT6R is part of E1201099.

## Slide 376: L1-ISCBT4R Panel Layout
ISCBT4R Panel Layout (D1201495)
<< LVEA Tables

## Slide 377: L1-ISCBT5L Table Layout
<< LVEA Tables
ISCHT6R Table Layout (D1201497) (Sxxxxxxx)
ISCHT6R is part of E1201099.

## Slide 378: L1-ISCBT5L Panel Layout
ISCBT5L Panel Layout (D1101126)
<< LVEA Tables

## Slide 379: Enclosure (Table) Blank Panels
Enclosure (Table) Blank Panels (D1200705)
<< LVEA Tables
Single Blank Panel
D1101138
Undecuple Blank Panel
D1100443
End Blank Panel
D1100441
Double Blank Panel
D1101139
Quintuple Blank Panel
D1100442

## Slide 380: Enclosure (Table) Panels - 1
Enclosure (Table) Panels (E1200613)
<< LVEA Tables
D1101923
DC Power Patch Panel
D1101924
LC Duplex Patch Panel
D1101919
Flipper Mirrors, Sensor Patch Panel
D1101949
RTD Sensors Patch Panel

## Slide 381: Enclosure (Table) Panels – Picomotor Feedthru
Enclosure (Table) Panels (E1200362)
<< LVEA Tables
Picomotor
Breakout Front
D1101691
Picomotor
Breakout Rear
D1101692
Picomotor
Breakout Side
D1101693
Delrin Insert
for DB25
D1101690
Delrin Insert
for 2 X DB9
D1101669

## Slide 382: Enclosure (Table) Panels – Templates
Enclosure (Table) Panels (E1200909)
<< LVEA Tables
Delrin Insert
for DB25
D1101690
Delrin Insert
for 2 X DB9(V)
D1101669
D1101699
Delrin Insert
for 2 X DB9(H)

## Slide 383: D1102312 - Sxxxxxxx
<< LVEA Racks
Shutter Logic
D1102312
+24VDC
Sxxxxxxx
Sxxxxxxx
Rear
D1102312
Front

## Slide 384: D1200136 - Sxxxxxxx
<< LVEA Racks
ALS Fiber Distribution Chassis
D1200136
+-17VDC, +-24VDC
Sxxxxxxx
Sxxxxxxx
Rear
D1200136
Front

## Slide 385: L1-ISC-R3
ISC HAM6 Rack Layout (LIGO-D1001426)
<< LVEA Racks
Sequencer
D1200757
S1202561

## Slide 386: L1-ISC-R4
ISC HAM6 Rack Layout (LIGO-D1101904)
<< LVEA Racks
Sequencer
D1200757
S1202544

## Slide 387: L1-ISC-R5
ISC HAM6 Rack Layout (LIGO-D1200196)
<< LVEA Racks
Sequencer
D1200757
S1202556

## Slide 388: L1-ISC-R1 Details
L1-ISC-R1 Details

## Slide 389: D1000124 - Sxxxxxxx
S1001232
Rear
D1000124
Front
<< L1-ISC-R1
24.078 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx

## Slide 390: D0900605 - Sxxxxxxx
S1001232
Rear
D0900605
Front
<< L1-ISC-R1
79.4 MHz VCO (ALS)
D0900605
±17VDC, ±24VDC
Sxxxxxxx

## Slide 391: D1002178 - Sxxxxxxx
S1001232
Rear
D1002178
Front
<< L1-ISC-R1
24.078 MHz Distribution Amplifier
D1002178
±17VDC, ±24VDC
Sxxxxxxx

## Slide 392: D1002476 - Sxxxxxxx
S1001232
Rear
D1002476
Front
<< L1-ISC-R1
158.8 / 79.4 MHz 2-Channel PF Discriminator
D1002476
±17VDC, ±24VDC
Sxxxxxxx

## Slide 393: D0900605 - Sxxxxxxx
S1001232
Rear
D0900605
Front
<< L1-ISC-R1
79.4 MHz VCO (ALS)
D0900605
±17VDC, ±24VDC
Sxxxxxxx

## Slide 394: D0900605 - Sxxxxxxx
S1001232
Rear
D0900605
Front
<< L1-ISC-R1
79.4 MHz VCO (ALS)
D0900605
±17VDC, ±24VDC
Sxxxxxxx

## Slide 395: D1002178 - Sxxxxxxx
S1001232
Rear
D1002178
Front
<< L1-ISC-R1
24.078 MHz Distribution Amplifier
D1002178
±17VDC, ±24VDC
Sxxxxxxx

## Slide 396: D0900128 – Sxxxxxxx
24.078 MHz Dual Delay Line
D0900128
+15VDC
Sxxxxxxx
Sxxxxxxx
Rear
D0900128
Front
<< L1-ISC-R1

## Slide 397: D1000181 – Sxxxxxxx
24.078 MHz 2-Channel Demodulator
D1000181
±17VDC, ±24VDC
Sxxxxxxx
Sxxxxxxx
Rear
D1000181
Front
<< L1-ISC-R1

## Slide 398: D0901781 – Sxxxxxxx
Mode Cleaner Servo
D0901781
±17VDC, ±24VDC
Sxxxxxxx
Sxxxxxxx
Rear
D0901781
Front
<< L1-ISC-R1

## Slide 399: D1100691 – Sxxxxxxx
LSC Demod Concentrator 1
D1100691
±18VDC
Sxxxxxxx
Sxxxxxxx
Rear
D1100691
Front
<< L1-ISC-R1

## Slide 400: D1100696 – Sxxxxxxx
ASC Demod Concentrator 1
D1100696
±18VDC
Sxxxxxxx
Sxxxxxxx
Rear
D1100696
Front
<< L1-ISC-R1

## Slide 401: D1102079 – Sxxxxxxx
LSC RFPD Interface
D1102079
±18VDC
Sxxxxxxx
Sxxxxxxx
Rear
D1102079
Front
<< L1-ISC-R1

## Slide 402: D1101865 – Sxxxxxxx
WFS Interface
D1101865
±15VDC
Sxxxxxxx
Sxxxxxxx
Rear
D1101865
Front
<< L1-ISC-R1
D1101905
D1101908

## Slide 403: D1002559 – Sxxxxxxx
ISC Whitening Chassis (ASC IMC WFS_A 24MHz)
D1002559
±15VDC
Sxxxxxxx
Sxxxxxxx
Rear
D1002559
Front
<< L1-ISC-R1

## Slide 404: D0902796 – Sxxxxxxx
ISC Whitening Chassis (ASC IMC WFS_A 24MHz)
D0902796
±15VDC
Sxxxxxxx
Sxxxxxxx
Rear
D0902796
Front
<< L1-ISC-R1
D1002032
LSC
D1002031
WFS

## Slide 405: D1100905 – Sxxxxxxx
Demodulator Patch Panel
D1100905
No Power
Sxxxxxxx
Sxxxxxxx
D1100905
Front
<< L1-ISC-R1

## Slide 406: D0902796 – Sxxxxxxx
ISC Whitening Chassis (ASC IMC WFS_B 24MHz)
D0902796
±15VDC
Sxxxxxxx
Sxxxxxxx
Rear
D0902796
Front
<< L1-ISC-R1
D1002032
LSC
D1002031
WFS

## Slide 407: D1002559 – Sxxxxxxx
ISC Whitening Chassis (ASC IMC WFS_A 24MHz)
D1002559
±15VDC
Sxxxxxxx
Sxxxxxxx
Rear
D1002559
Front
<< L1-ISC-R1

## Slide 408: L1-ISC-R2 Details
L1-ISC-R2 Details

## Slide 409: L1-ISC-R3 Details
L1-ISC-R3 Details

## Slide 410: L1-ISC-R4 Details
L1-ISC-R4 Details

## Slide 411: L1-ISC-R5 Details
L1-ISC-R5 Details

## Slide 412: L1-SUS-R1
Oplev 8 Channel Whitening Filter Chassis
D1100013
±18@0.5A
S1101545
<< LVEA Racks
L1-SUS-R1 (ITMY) Field Rack Layout (D1200879) (S1200749)
SUS-R1 is part of D1100022
Shelf
Shelf
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Satellite Amplifier Shelf
No Power
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Satellite Amplifier Shelf
No Power
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Satellite Amplifier Shelf
No Power
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Satellite Amplifier Shelf
No Power
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Satellite Amplifier Shelf
No Power
D0901284
D0901284
D0901284
D0901284
S1000850
Sxxxxxxx
S1000452
Sxxxxxxx
Satellite Amplifier Shelf
No Power

## Slide 413: D0901284 Shelf
D0901284
D0901284
D0901284
D0901284
S1000850
Sxxxxxxx
S1000452
Sxxxxxxx
Satellite Amplifier Shelf
No Power
<< L1-SUS-R1
Rear
Front
S1000850
S1000850
S1000850
S1000850
D0901284

## Slide 414: D1100013–S1101545
Oplev 8 Channel Whitening Filter Chassis
D1100013
?@?A
S1101545
S1101545
Rear
D1002559
Front
<< L1-SUS-R1

## Slide 415: L1-SUS-R2
<< LVEA Racks
L1-SUS-R2 (BS) Field Rack Layout (D1200880) (S1200750)
SUS-R2 is part of D1100022
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Satellite Amplifier Shelf
No Power
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Satellite Amplifier Shelf
No Power
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Dxxxxxxx
Satellite Amplifier Shelf
No Power
Oplev 8 Channel Whitening Filter Chassis
D1100013
±18@0.5A
S1101546

## Slide 416: D1100013–S1101545
Oplev 8 Channel Whitening Filter Chassis
D1100013
?@?A
S1101546
S1101546
Rear
D1002559
Front
<< L1-SUS-R1

## Slide 417: L1-SUS-R3
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
<< LVEA Racks
L1-SUS-R3 (ITMX) Field Rack Layout (D1200883) (S1202300)
SUS-R3 is part of D1100022

## Slide 418: L1-SUS-R4
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
<< LVEA Racks
L1-SUS-R4 (ITMX) Field Rack Layout (D1201134) (S1202995)
SUS-R4 is part of D1100022

## Slide 419: L1-SUS-R5
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
<< LVEA Racks
L1-SUS-R5 (ITMX and FMX) Field Rack Layout (D1201135) (S1202996)
SUS-R5 is part of D1001725
SUS-R5 is part of D1100022

## Slide 420: L1-SUS-R6
L1-SUS-R6 (ITMY, FMY, and BS) Field Rack Layout (D1201136) (S1202997)
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
Satellite Amplifier
Dxxxxxxx
?@?A
SN:
<< LVEA Racks
SUS-R6 is part of D1001725
SUS-R6 is part of D1100022

## Slide 421: L1-TCS-R1
+18VDC ?A
-18VDC ?A
+24VDC ?A
<< LVEA Racks
ITM: Hartmann Sensor Power Supply
D1102206
?@?A
SN:
SLED Controller
D1000892
?@?A
SN:
TCS: ITM HWS Table EtherCAT Interface Box
D1102206
?@?A
SN:
QUAD Driver
D1101655
?@?A
SN:
Shaker Driver
Dxxxxxxx
?@?A
SN:
Intensity Stabilization System
D080351
?@?A
SN:
TCS: CO2P EtherCAT Interface Box
Dxxxxxxx
?@?A
SN:
TCS: CO2P Power Supply Distribution
Dxxxxxxx
?@?A
SN:
CO2 Interlock
D1101931
?@?A
SN:
RS232 to Ethernet Interface
Dxxxxxxx
?@?A
SN:
Thorlabs PM 100
XXXXXXX
?@?A
XXXXXXX
Newport SMC-100-CC
SMC-100-CC
?@?A
XXXXXXX
RF Oscillator
XXXXXXX
?@?A
XXXXXXX
AOM Driver
Dxxxxxxx
?@?A
SN:
L1-TCS-R1 (LVEA X Direction) Field Rack Layout (D1201122) (S1202975)
TCS-R1 is part of D1200258

## Slide 422: L1-TCS-R2
+18VDC ?A
-18VDC ?A
+24VDC ?A
L1-TCS-R2 (LVEA Y Direction) Field Rack Layout (D1201123) (S1202976)
<< LVEA Racks
QUAD Driver
D1101655
?@?A
SN:
Shaker Driver
Dxxxxxxx
?@?A
SN:
Intensity Stabilization System
D080351
?@?A
SN:
TCS: CO2P EtherCAT Interface Box
Dxxxxxxx
?@?A
SN:
TCS: CO2P Power Supply Distribution
Dxxxxxxx
?@?A
SN:
CO2 Interlock
D1101931
?@?A
SN:
RS232 to Ethernet Interface
Dxxxxxxx
?@?A
SN:
Thorlabs PM 100
XXXXXXX
?@?A
XXXXXXX
Newport SMC-100-CC
SMC-100-CC
?@?A
XXXXXXX
RF Oscillator
XXXXXXX
?@?A
XXXXXXX
AOM Driver
Dxxxxxxx
?@?A
SN:
TCS-R2 is part of D1200258

## Slide 423: L1-VAC-R1
<< LVEA Racks
L1-VAC-R1 LVEA Vacuum Rack Layout (Dxxxxxxx)

## Slide 424: L1-VAC-R2
<< LVEA Racks
L1-VAC-R2 LVEA Vacuum Rack Layout (Dxxxxxxx)

## Slide 425: L1-VAC-R3
L1-VAC-R3 Mechanical Room Vacuum Rack Layout (Dxxxxxxx)
<< LVEA Racks

## Slide 426: VEAX
VEAX
<< LLO Racks by AREA
<< LLO CDS Components
<< LLO Corner Station

## Slide 427: X-End Station Rack Layout
<< CERX
<< LLO Corner Station
<< VEAX

## Slide 428: X-End Station Rack Layout
<< CERX
<< LLO Corner Station
<< VEAX
X-End - D0901465

## Slide 429: X-End Racks
Facilities Rack
(L1-FAC-XC1)
DAQ Rack
(L1-DAQ-XC1)
ISC Rack
(L1-ISC-XC1)
SUS Rack 2
(L1-SUS-XC2)
SUS Rack 1
(L1-SUS-XC1)
SUS Field Rack
(L1-SUS-XR1)
TCS Rack
(L1-TCS-XC1)
DC Power Rack 1
(L1-VDC-XC1)
DC Power Rack 2 (L1-VDC-XC2)
SEI Rack
(L1-SEI-XC1)
Vacuum Field Rack
(L1-VAC-XR1)
<< LLO Racks by AREA
ISC Field Rack
(L1-ISC-XR1)

## Slide 430: CDS Electronics Room X-End (CERX) Rack Layout
<< X-End Racks
Signals and Fiber
It is 70’ from the L1-FAC-XC1 Rack to the knee of the waterfall in the VEAX.
(L1-FAC-XC1)
CERX
(L1-VDC-XC1)
(L1-VDC-XC2)
(L1-DAQ-XC1)
(L1-SEI-XC1)
(L1-SUS-XC1)
(L1-SUS-XC2)
(L1-TCS-XC1)
(L1-ISC-XC1)
DC Power and Fiber
AC Power

## Slide 431: Corning WCH-06P Fiber Panel
5.75”
13.5” x 16.062” x 5.125”
120”
4”
21.75”
21.25”
X”
CCH-CP12-15T (ST)
x 2

## Slide 432: VEAX – Fiber Patch Panel
Patch Panel
Patch Panel
No Power
Patch Panel
Empty
1-2
S7711DR Opt In/Out
1-4
W ACC-5595 Port 3
1-6
Y ACC-5595 Port 3
1-8
Empty
1-10
Empty
1-12
Empty
2-2
Empty
2-4
W D070011 Fanout Input
2-6
Y D070011 Fanout Input
2-8
W Brocade Port 1F
2-10
Empty
2-12
W l1netfedaqx 21F
1-1
Y l1netfedaqx 21F
1-3
TR3030WDM Opt In
1-5
TR3030WDM Opt Out
1-7
Empty
1-9
VT430 Opt In/Out
1-11
T 2402 25F
2-1
N 2402 25F
2-3
W l1lanfex 21F
2-5
Y l1lanfex 21F
2-7
Empty
2-9
Y Brocade Port 1F
2-11
<< 1X23
FC Connectors

## Slide 433: L1-VDC-XC1 Power Racks – VEAX Field Supplies
Cable Runs >>
L1-VDC-XC1 Power Rack
B
A
L1-VDC-XC1 Power Rack
A
B
L1-TCS-XR1
L1-TCS-XR1
L1-TCS-XR1
L1-TCS-XR1
L1-PEM-XR1
L1-PEM-XR1
L1-PEM-XR1
L1-PEM-XR1
L1-ISC-XR1
L1-ISC-XR1
L1-ISC-XR1
L1-ISC-XR1
Unused
Unused
Unused
L1-TCS-XR1
L1-TCS-XR1
L1-TCS-XR1
L1-TCS-XR1
L1-PEM-XR1
L1-PEM-XR1
L1-PEM-XR1
L1-PEM-XR1
L1-ISC-XR1
L1-ISC-XR1
L1-ISC-XR1
L1-ISC-XR1
Unused
Unused
Unused
L1-SUS-XR1
L1-SUS-XR1
L1-SUS-XR1
L1-SUS-XR1
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
<< CERX Racks
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
-24VDC
-24VDC
+24VDC
+24VDC
-24VDC
-24VDC
+24VDC
+24VDC
-24VDC
-24VDC
+24VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
L1-VDC-XC1 X-End Station DC Power Rack Layout (D1200897) (S1202311)
Notes: For a JQE Style25-20M: AC power calculations:
125 VAC * 10.5 (A/PS) => 1312.5 (W/PS)
24 (PS/Rack)* 1312.5 (W/PS) => 31500 (W/Rack)
24 (PS/Rack) * 10.5 (A/PS) => 252 (A/Rack)

## Slide 434: L1-VDC-XC2 Power Racks – VEAX Supplies
L1-SUS-XC1
L1-SUS-XC2
L1-SUS-XC2
L1-SUS-XC1
L1-ISC-XC1
L1-ISC-XC1
Cable Runs >>
L1-VDC-XC2 Power Rack
B
A
L1-VDC-XC2 Power Rack
A
B
L1-SEI-XC1
L1-SEI-XC1
L1-SEI-XC1
L1-SEI-XC1
L1-SUS-XC1
L1-SUS-XC1
L1-SUS-XC2
L1-SUS-XC2
Unused
Unused
Unused
Unused
Unused
Unused
L1-SEI-XC1
L1-SEI-XC1
L1-SEI-XC1
L1-SEI-XC1
L1-SEI-XC1
L1-SUS-XC1
L1-SUS-XC1
L1-SUS-XC2
L1-SUS-XC2
Unused
Unused
Unused
Unused
Unused
Unused
L1-SEI-XC1
L1-ISC-XC1
L1-ISC-XC1
L1-ISC-XC1
L1-ISC-XC1
L1-ISC-XC1
L1-ISC-XC1
L1-ISC-XC1
L1-ISC-XC1
<< CERX Racks
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
-24VDC
-24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
-24VDC
-24VDC
+24VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
L1-TCS-XC1
L1-TCS-XC1
L1-TCS-XC1
L1-TCS-XC1
+18VDC
-18VDC
-18VDC
+18VDC
L1-VDC-XC2 X-End Station DC Power Rack Layout (D1200898) (S1202312)
Notes: For a JQE Style25-20M: AC power calculations:
125 VAC * 10.5 (A/PS) => 1312.5 (W/PS)
24 (PS/Rack)* 1312.5 (W/PS) => 31500 (W/Rack)
24 (PS/Rack) * 10.5 (A/PS) => 252 (A/Rack)

## Slide 435: L1-VDC-XC1 Cable Runs
<< L1-VDC-XC1
L1-VDC-XC1 S1202311 | Power Panel | Circuit | DC Power Rack | Outlet | Plug Position | Rack U | Power Supply Model | Power Supply Serial | Polarity | DC Extension Cable | Electronics Rack | DC Power Strip
1 | CDS-X |  | L1-VDC-XC1 | 8 | Top | U37-A (Left) |  |  |  |  |  | 
2 | CDS-X |  | L1-VDC-XC1 | 8 | Bottom | U37-B (Right) |  |  |  |  |  | 
3 | CDS-X |  | L1-VDC-XC1 | 2 | Top | U33-A (Left) |  |  |  |  |  | 
4 | CDS-X |  | L1-VDC-XC1 | 2 | Bottom | U33-B (Right) |  |  |  |  |  | 
5 | CDS-X |  | L1-VDC-XC1 | 9 | Top | U29-A (Left) | BHK 500V 80mA | A107266 | Plus | PBX-003 |  | 
6 | CDS-X |  | L1-VDC-XC1 | 9 | Bottom | U29-B (Right) | BHK 500V 80mA | A107260 | Minus | PBX-003 |  | 
7 | CDS-X |  | L1-VDC-XC1 | 3 | Top | U25-A (Left) | JQE 25V 20A |  | Plus | PTO-038 | L1-ISC-XR1 | PSO-038
8 | CDS-X |  | L1-VDC-XC1 | 3 | Bottom | U25-B (Right) | JQE 25V 20A |  | Minus | PTO-038 | L1-ISC-XR1 | PSO-038
9 | CDS-X |  | L1-VDC-XC1 | 10 | Top | U21-A (Left) | JQE 25V 20A |  | Plus | PTY-028 | L1-ISC-XR1 | PSY-028
10 | CDS-X |  | L1-VDC-XC1 | 10 | Bottom | U21-B (Right) | JQE 25V 20A |  | Minus | PTY-028 | L1-ISC-XR1 | PSY-028
11 | CDS-X |  | L1-VDC-XC1 | 4 | Top | U17-A (Left) | JQE 25V 20A |  | Plus | PTO-039 | L1-OAF-XR1 | PSO-039
12 | CDS-X |  | L1-VDC-XC1 | 4 | Bottom | U17-B (Right) | JQE 25V 20A |  | Minus | PTO-039 | L1-OAF-XR1 | PSO-039
13 | CDS-X |  | L1-VDC-XC1 | 11 | Top | U13-A (Left) | JQE 25V 20A |  | Plus | PTY-029 | L1-OAF-XR1 | PSY-029
14 | CDS-X |  | L1-VDC-XC1 | 11 | Bottom | U13-B (Right) | JQE 25V 20A |  | Minus | PTY-029 | L1-OAF-XR1 | PSY-029
15 | CDS-X |  | L1-VDC-XC1 | 5 | Top | U09-A (Left) | JQE 25V 20A |  | Plus | PTO-040 | L1-SUS-XR1 | PSO-040
16 | CDS-X |  | L1-VDC-XC1 | 5 | Bottom | U09-B (Right) | JQE 25V 20A |  | Minus | PTO-040 | L1-SUS-XR1 | PSO-040
17 | CDS-X |  | L1-VDC-XC1 | 12 | Top | U05-A (Left) | JQE 25V 20A |  | Plus | PTO-041 | L1-TCS-XR1 | PSO-041
18 | CDS-X |  | L1-VDC-XC1 | 12 | Bottom | U05-B (Right) | JQE 25V 20A |  | Minus | PTO-041 | L1-TCS-XR1 | PSO-041
19 | CDS-X |  | L1-VDC-XC1 | 6 | Top | U01-A (Left) | JQE 25V 20A |  | Plus | PTY-030 | L1-TCS-XR1 | PSY-030
20 | CDS-X |  | L1-VDC-XC1 | 6 | Bottom | U01-B (Right) | JQE 25V 20A |  | Minus | PTY-030 | L1-TCS-XR1 | PSY-030
D1200897 |  |  |  |  |  |  |  |  |  |  |  | 
L1-VDC-XC1 X-End Station DC Cable Runs (D1200897) (S1202311)

## Slide 436: L1-VDC-XC2 Cable Runs
<< L1-VDC-XC2
L1-VDC-XC2 S1202312 | Power Panel | Circuit | DC Power Rack | Outlet | Plug Position | Rack U | Power Supply Model | Power Supply Serial | Polarity | DC Extension Cable | Electronics Rack | DC Power Strip
1 | CDS-X |  | L1-VDC-XC2 | 8 | Top | U37-A (Left) |  |  |  |  |  | 
2 | CDS-X |  | L1-VDC-XC2 | 8 | Bottom | U37-B (Right) |  |  |  |  |  | 
3 | CDS-X |  | L1-VDC-XC2 | 2 | Top | U33-A (Left) | JQE 25V 20A |  | Plus | PTO-044 | L1-TCS-XC1 | 
4 | CDS-X |  | L1-VDC-XC2 | 2 | Bottom | U33-B (Right) | JQE 25V 20A |  | Minus | PTO-044 | L1-TCS-XC1 | 
5 | CDS-X |  | L1-VDC-XC2 | 9 | Top | U29-A (Left) | JQE 25V 20A | H236497 | Plus | PTO-042 | L1-SUS-XC2 | PSO-042
6 | CDS-X |  | L1-VDC-XC2 | 9 | Bottom | U29-B (Right) | JQE 25V 20A | H236515 | Minus | PTO-042 | L1-SUS-XC2 | PSO-042
7 | CDS-X |  | L1-VDC-XC2 | 3 | Top | U25-A (Left) | JQE 25V 20A | H236501 | Plus | PTO-043 | L1-SUS-XC1 | PSO-043
8 | CDS-X |  | L1-VDC-XC2 | 3 | Bottom | U25-B (Right) | JQE 25V 20A | H236473 | Minus | PTO-043 | L1-SUS-XC1 | PSO-043
9 | CDS-X |  | L1-VDC-XC2 | 10 | Top | U21-A (Left) | JQE 25V 20A | H236510 | Plus | PTO-044 | L1-ISC-XC1 | PSO-044
10 | CDS-X |  | L1-VDC-XC2 | 10 | Bottom | U21-B (Right) | JQE 25V 20A | H236511 | Minus | PTO-044 | L1-ISC-XC1 | PSO-044
11 | CDS-X |  | L1-VDC-XC2 | 4 | Top | U17-A (Left) | JQE 25V 20A | H236493 | Plus | PTY-031 | L1-ISC-XC1 | PSY-031
12 | CDS-X |  | L1-VDC-XC2 | 4 | Bottom | U17-B (Right) | JQE 25V 20A | H236517 | Minus | PTY-031 | L1-ISC-XC1 | PSY-031
13 | CDS-X |  | L1-VDC-XC2 | 11 | Top | U13-A (Left) | JQE 25V 20A | H236505 | Plus | PTO-045 | L1-SEI-XC1 | PSO-045
14 | CDS-X |  | L1-VDC-XC2 | 11 | Bottom | U13-B (Right) | JQE 25V 20A | H236494 | Minus | PTO-045 | L1-SEI-XC1 | PSO-045
15 | CDS-X |  | L1-VDC-XC2 | 5 | Top | U09-A (Left) | JQE 25V 20A | H236509 | Plus | PTY-032 | L1-SEI-XC1 | PSY-032
16 | CDS-X |  | L1-VDC-XC2 | 5 | Bottom | U09-B (Right) | JQE 25V 20A | H236492 | Minus | PTY-032 | L1-SEI-XC1 | PSY-032
17 | CDS-X |  | L1-VDC-XC2 | 12 | Top | U05-A (Left) | JQE 25V 20A | H236482 | Plus | PTY-033 | L1-ISC-XC1 | PSY-033
18 | CDS-X |  | L1-VDC-XC2 | 12 | Bottom | U05-B (Right) | JQE 25V 20A | H236481 | Plus | PTY-034 | L1-SEI-XC1 | PSY-034
19 | CDS-X |  | L1-VDC-XC2 | 6 | Top | U01-A (Left) | JQE 25V 20A | H236498 | Plus | PTY-035 | L1-SUS-XC2 | PSY-035
20 | CDS-X |  | L1-VDC-XC2 | 6 | Bottom | U01-B (Right) | JQE 25V 20A | H236514 | Plus | PTY-036 | L1-SUS-XC1 | PSY-036
D1200898 |  |  |  |  |  |  |  |  |  |  |  | 
L1-VDC-XC2 X-End Station DC Cable Runs (D1200898) (S1202312)

## Slide 437: L1-DAQ-XC1
L1-DAQ-XC1 X-End Station Remote Rack Layout (D1201085) (S1202949)
ATEN KVM Switch
CL1016M
UPS1
SN:
l1lanfex 10.199.0.13
GSM7224
UPS1
2B62045700143
l1netfedaqx 10.199.0.87
GSM7224
UPS1
2B62045600150
ACC 5595 Reflective Memory Hub
ACC 5595
UPS1
36100694
<< CERX Racks
Timing IRIG-B Interface Chassis
D0900301
+12VDC
S1107510
l1iscex Front End Computer
Dxxxxxxx
UPS1 & 110VAC
SN:
l1seiex Front End Computer
Dxxxxxxx
UPS1 & 110VAC
SN:
l1susex Front End Computer
Dxxxxxxx
UPS1 & 110VAC
SN:
l1susauxex Front End Computer
Dxxxxxxx
UPS1 & 110VAC
SN:
110VAC 20A
UPS1 - UPS Power Strip
110VAC 20A
Non-UPS Power Strip
Dxxxxxxx
l1ecatx1 Beckhoff Host Computer
+24VDC
SN:
Shelf
Shelf
Hartmann Sensor Computer
T1000702
+24@5A
SN:
Dolphin RFM Switch
DXS410
UPS2
XXXXXXXX
UPS Group 1 and Group 2
APC SMT2000RMLV2U
110VAC
J51048023241
110VAC 20A
UPS2 - UPS Power Strip
Serial Concentrator Chassis
D1100632
+24@5.0A
SN:
Ethernet 4km Remote End Access Chassis
D1002961
+24@5.0A
SN:
Serial to Internet Converter

## Slide 438: VMIACC-5595-224 – 36106691
36100694
Rear
ACC 5595
Front
Reflective Memory Hub
ACC 5595
110VAC
36100694
To UPS Power Strip
To l1lanfey port 5
To 1X23 A3,A4
To l1pemex PCIE 5565RC
<< L1-DAQ-XC1

## Slide 439: l1netfedaqy – GSM7224
GSM7224
Front
2B62045600150
Rear
C0:3F:0E:86:88:E0
l1netfedaqy 10.199.0.87
GSM7224
110VAC
2B62045600150
3 - To FE NET Port
21F - To 1X23 PP B1,B2
To UPS Power Strip
<< L1-DAQ-XC1

## Slide 440: l1lanfex – GSM7224
GSM7224
Front
2B62045700143
Rear
C0:3F:0E:86:88:AC
l1lanfey 10.199.0.13
GSM7224
110VAC
2B62045700143
3 - To FE LAN Port
21F - To 1X23 PP E3,E4
5 - To 5595 LAN 10BaseT
To UPS Power Strip
<< L1-DAQ-XC1

## Slide 441: D0900301 – S1107510
Timing IRIG-B Interface Chassis
D0900301
+12VDC
S1107510
D0900301
Front
S1107510
Rear
<< L1-DAQ-XC1

## Slide 442: D1100632 – Sxxxxxxx
Sxxxxxxx
Rear
D1100632
Front
Serial Port Concentrator for Timing
D1100632
±18VDC
Sxxxxxxx
<< L1-DAQ-XC1

## Slide 443: ATEN CL1016M
ATEN KVM Switch
CL1016M
110VAC
Z8A6Y132ANQ0010
Z8A6Y132ANQ0010
Rear
CL1016M
Front
To l1pemex Front End
To UPS Power Strip
<< L1-DAQ-XC1

## Slide 444: KEPCO Power Supplies
SN:
Rear
KEPCO JQE 25-4
KEPCO JQE 25-4
KEPCO JQE 15-6
KEPCO JQE 15-6
JQE
Front
KEPCO JQE 15-6:
+12VDC
KEPCO JQE 15-6: OFF (Not Used)
KEPCO JQE 25-4:
-18VDC
KEPCO JQE 25-4:
+18VDC
<< L1-DAQ-XC1
KEPCO Power Supplies
UPS1
JQE15-12M
JQE25-10M
H114648
H114649

## Slide 445: APC SMX2000RMLV2U
UPS
APC SMX2000RMLV2U
110VAC
JS1048019433
To UPS Power Strip
APC SMX2000RMLV2U
Front
JS1048019433
Rear
<< L1-DAQ-XC1

## Slide 446: L1-FAC-XC1
L1-FAC-XC1 Facilities X-End Station Remote Rack Layout (D1201086) (S1202950)
110VAC 15A
UPS1 - UPS Power Strip
110VAC 15A
Non-UPS Power Strip
UPS1
FB00001705
2402
2402 Network Switch
Kantech
xxxxxxxx
+12VDC
SN:
Phone
Security Cameras
IFO Cameras
Shelf
Shelf
Shelf
UPS1
APC SMT1500RM2U
110VAC
AS10J1111987
UPS & 110VAC
N62538F19R
GS624P
Brocade FastIron Edge GS624P
<< CERX Racks
KEPCO Power Supplies
UPS1
JQE15-6M
JQE25-10M
JQE15-6M
JQE15-6M
JQE25-10M
JQE15-6M
PSY-034
PSY-034

## Slide 447: GS624P
UPS & 110VAC
N62538F19R
GS624P
Brocade FastIron Edge GS624P
N62538F19R
Rear
<< L1-FAC-XC1
C0:3F:0E:86:88:E0
GSM7224
Front
3 - To FE NET Port
21F - To 1X23 PP B1,B2
To UPS Power Strip
To 110 Power Strip

## Slide 448: 2402 – Network Switch
2402 Network Switch
2402
110VAC
FB00001705
G12038
192.168.253.20
Empty
01
Kantech???
02
Empty
03
Empty
04
Empty
05
Empty
06
Empty
07
Empty
08
Empty
09
Empty
10
Empty
11
Empty
12
Empty
13
To Seimens
14
Empty
15
Empty
16
Empty
17
Empty
18
Empty
19
Empty
20
Empty
21
Empty
22
Empty
23
Empty
24
Empty
25C
Empty
26C
To Special Cable CSR1
25F
To 1X23 PP E1,E2
26F
PS1
To UPS Power Strip
<< L1-FAC-XC1

## Slide 449: KEPCO Power Supplies
SN:
Rear
KEPCO JQE 25-4
KEPCO JQE 25-4
KEPCO JQE 15-6
KEPCO JQE 15-6
JQE
Front
KEPCO JQE 15-6:
+12VDC
KEPCO JQE 15-6: OFF (Not Used)
KEPCO JQE 25-4:
-18VDC
KEPCO JQE 25-4:
+18VDC
KEPCO Power Supplies
UPS1
JQE15-12M
JQE25-10M
H114648
H114649
<< L1-FAC-XC1

## Slide 450: APC SMT1500RM2U
UPS
APC SMT1500RM2U
110VAC
A51051111991
APC SMT1500RM2U
Front
A51051111991
Rear
To X448 PS1
To 2402 PS1
To UPS Power Strip
<< L1-FAC-XC1

## Slide 451: 1X23 – D070443 – LH02
Powered from 12VDC DIN rails
Powered from 15VDC DIN rails
D070443
Magnetometer Filter
LH02
Magnetometer Power Supply
(MAG-03PSU)
0539
Magnetometer
MAG-03MCES
X
Y
Z
X
Y
Z
Magnetometer: Bartington Instruments MAG-03MC
5 meter
X
Y
Z
On/Off
D030574
Black – G/W … Ground
Stria – Y/W … +12VDC
–
+
Charger … 9 to 18 VDC
Pin 1: +15VDC … Red/Blk RED
Pin 2: Ground … Red/Blk BLACK
Pin 3: -15VDC … Wht/Blk WHITE
Pin 4: Ground … Wht/Blk BLACK
<< L1-FAC-XC1

## Slide 452: 1X23 – Stuff
VT7430-2DRDT
Optical In/Out:
To 1X23 PP B6
Power: 12VDC
Output: Ch1, Ch2, Ch3 BNCs to Cameras
TR3030WDM
GE Security
Optical In/Out: To 1X23 PP B3,B4
Phone: Copper to VEA
Power: 12VDC
Video Master Power Supply
Model RT24/16500
Outputs to Cameras 1,2,3
Note: 6 LEDs are on.
Fiber Options S7711DR –EST1
Optical In/Out:
To 1X23 PP A2
13.5VDC from Wall Wart
Blue CAT5: 1=O/W and B/W, 4=O, 7=B
Powered from Wall Wart from Isolated Power
Powered from Wall Wart from Tripp-Lite UPS
Model BC320
xxxxxxxxxxxxx To 6-Outlet Power Strip in Non-isolated wall socket
AC Powered from Isolated Power
Powered from Wall Wart from Isolated Power
Phone
Kantech
Security Cameras
<< L1-FAC-XC1

## Slide 453: L1-ISC-XC1
71 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000653
Anti-Alias Chassis
D0902783
±18@1A
SN:
Anti-Alias Chassis
D0902783
±18@1A
SN:
Anti-Image Chassis
D070081
±18@0.5A
SN:
PSY-032
PSY-034
PSO-045
<< CERX Racks
l1pemex I/O Extension Chassis
D1001715
+24V@5A
S1000536
Sequencer
D1200757
S1202548
L1-ISC-XC1 X-End Remote Rack Layout (D1201084) (S1202948)
ISC-XC1 is part of D1001459
RF Distribution Panel 22
Dxxxxxxx
No Power
SN:
71 MHz Oscillator
D080702
+12VDC, ±24VDC
S1000562
RF Distribution Panel 23
Dxxxxxxx
No Power
SN:
24.4 MHz Oscillator
D080702
+12VDC, ±24VDC
S1000577
24.4 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000670
RF Amplifier Concentrator 3
D1100262
+/-18VDC
S1103463
Shelf
Shelf
ISC Common Beckhoff Chassis
D1002961
+24@5.0A
SN:
End 2 Beckhoff Chassis
D1100682
+24@5.0A
SN:
Aeroflex Diagnostics
2023A
110VAC
Sxxxxxxx
384 Channel Binary Output
D1100251
+24VDC
S1203281
PSG-XXX
L1-ISC-XC1 is D1201084

## Slide 454: D080702 - Sxxxxxxx
71 MHz Oscillator
D080702
+12VDC, ±24VDC
Sxxxxxxx
Sxxxxxxx
Rear
D080702
Front
Front
Output
Front
Lock
To …
<< L1-ISC-XC1

## Slide 455: D1000124 - Sxxxxxxx
71 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
D1000124
Front
Front
10 dBm
Front
1
Front
2
Front
3
Front
4
Front
5
Front
6
Front
7
Front
8
Sxxxxxxx
Rear
Front
M1
Front
M2
Front
M3
Front
Controls
<< L1-ISC-XC1

## Slide 456: D080702 - Sxxxxxxx
24.4 MHz Oscillator
D080702
+12VDC, ±24VDC
Sxxxxxxx
Sxxxxxxx
Rear
D080702
Front
Front
Output
Front
Lock
To …
<< L1-ISC-XC1

## Slide 457: D1100262 - Sxxxxxxx
RF Amplifier Concentrator 1
D1100262
±18VDC
SN:
D1100262
Front
S1001232
Rear
1
Rear
Controls
5
Rear
9
Rear
2
Rear
6
Rear
10
Rear
3
Rear
7
Rear
11
Rear
4
Rear
8
Rear
12
Rear
Rear
<< L1-ISC-XC1

## Slide 458: D1100251 - Sxxxxxxx
384 Channel Binary Output
D1100251
+24VDC
Sxxxxxxx
<< L1-ISC-XC1
D1100251
Front
Front
Chassis 1 – Board 1
Front
Chassis 1 – Board 2
Front
Chassis 2 – Board 1
Front
Chassis 2 – Board 2
Front
Chassis 3 – Board 1
Front
Chassis 3 – Board 2
Sxxxxxxx
Rear
Rear
Chassis 6 – Board 1
Rear
Chassis 6 – Board 2
Rear
Chassis 5 – Board 1
Rear
Chassis 5 – Board 2
Rear
Chassis 4 – Board 1
Rear
Chassis 4 – Board 2
Rear
In
Rear
Out

## Slide 459: D1000124 - Sxxxxxxx
24.4 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
Sxxxxxxx
D1000124
Front
Front
10 dBm
Front
1
Front
2
Front
3
Front
4
Front
5
Front
6
Front
7
Front
8
Sxxxxxxx
Rear
Front
M1
Front
M2
Front
M3
Front
Controls
<< L1-ISC-XC1

## Slide 460: l1pemex - D1001715 – S1000536
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1000536
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
D1001421
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1pemex I/O Extension Chassis
D1001715
110VAC
S1000536
To UPS Power Strip
l1pemex – I/O Extender
<< L1-ISC-XC1

## Slide 461: L1-SEI-XC1
+18VDC 4A
-18VDC 4A
+24VDC 15A
BSC-4 8 Channel Valve Driver
D020373
Power
S1001098
I/O Extension Chassis
D1001715
+24@5A
SN:
PSY-032
PSY-034
PSO-045
<< CERX Racks
L1-SEI-XC1 (BSC4) X-End Remote Rack 1 Layout (D1201081) (S1202945)
SEI-XC1 is part of D0901301

## Slide 462: D020373 – S1001098
S1001098
Rear
VALVE INPUTS
D020373
Front
Open
CHANS 1&2
Open
CHANS 3&4
CHANS 1&2
CHANS 3&4
Open
CHANS 5&6
Open
CHANS 7&8
CHANS 5&6
CHANS 7&8
8 CHANNEL VALVE DRIVER
POWER DISTRIBUTION
LIGO D040049
8 CHANNEL VALVE DRIVER
LIGO D020373 REV C
Open
VALVE INPUTS
D040049
BSC-3 8 Channel Valve Driver
D020373
Power
S1001098
<< L1-SEI-XC1
BSC4

## Slide 463: l1seiex D1001715 - Sxxxxxxx
l1seiex I/O Extension Chassis
D1001715
24 VDC
SN
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
24 VDC
SN
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
<< L1-SEI-XC1
l1seiex – I/O Extender

## Slide 464: L1-SUS-XC1
Anti-Image Chassis (2*DB15, 1*DB9)
D1100815
±18VDC
S1103825
Transmon Coil Driver Chassis
D1100301
±18VDC
S1001559
Transmon Coil Driver Chassis
D1100301
±18VDC
S1001556
Anti-Alias Chassis (8*DB9)
D0902783
±18VDC
S1001157
Anti-Image Chassis (4*DB9)
D1000305
±18VDC
S1004364
Anti-Image Chassis (4*DB9)
D1000305
±18VDC
S1004365
Anti-Alias Chassis (2*DB15, 5*DB9)
D1100809
±18VDC
S1104073
Binary Output Chassis (4*DB9, 2*DB37)
D1001270
±18VDC
S1106208
Binary Input Chassis (8*DB9)
D1001726
±18VDC
S1103096
L1-SUS-XC1 (ETM) X-End Remote Rack 1 (of 2) Layout (D1201082) (S1202946)
Binary Output Chassis (8*DB9)
D1002593
±18VDC
S1103225
Binary Input Chassis (4*DB9, 2*DB37)
D1001269
±18VDC
S1106115
PSO-042
<< CERX Racks

## Slide 465: D1100301-S1001559
Transmon Coil Driver Chassis
D1100301
±18VDC
S1001559
D1100301
Front
S1001559
Rear
<< L1-SUS-XC1

## Slide 466: D1100301-S1001556
Transmon Coil Driver Chassis
D1100301
±18VDC
S1001556
D1100301
Front
S1001556
Rear
<< L1-SUS-XC1

## Slide 467: D0902783-S1001157
Anti-Alias Chassis (8*DB9)
D0902783
±18@0.5A
S1001157
IN 1-4
IN 1-4
IN 17-20
IN 17-20
IN 5-8
IN 5-8
IN 9-12
IN 9-12
IN 13-16
IN 13-16
IN 21-24
IN 21-24
IN 25-28
IN 25-28
IN 29-32
IN 29-32
D0902783
Front
To ADC
To ADC Adapter
S1001157
Rear
<< L1-SUS-XC1

## Slide 468: D1000305 - S1004364
Anti-Image Chassis (4*DB9)
D1000305
±18@1A
S1004364
<< L1-SUS-XC1
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
D1000305
Front
From DAC Adapter 0
From DAC Adapter 0
From DAC Adapter 1
From DAC Adapter 1
S1004364
Rear

## Slide 469: D1000305 - S1004365
Anti-Image Chassis (4*DB9)
D1000305
±18@1A
S1004365
<< L1-SUS-XC1
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
D1000305
Front
From DAC Adapter 0
From DAC Adapter 0
From DAC Adapter 1
From DAC Adapter 1
S1004365
Rear

## Slide 470: D1100815 - S1103825
Anti-Image Chassis (2*DB15, 1*DB9)
D1100815
±18@1A
S1103825
<< L1-SUS-XC1
From DAC Adapter 0
From DAC Adapter 0
From DAC Adapter 1
From DAC Adapter 1
S1103825
Rear
D1100815
Front
IN 13-16
IN 13-16
IN 7-12
IN 7-12
IN 1-6
IN 1-6
D1100815 is an AI, which means it has OUTPUTS, not INPUTS. The labels are incorrect.

## Slide 471: D1100809-S1104073
Anti-Alias Chassis (2*DB15, 5*DB9)
D1100809
±18@0.5A
S1104073
IN 17-20
IN 17-20
IN 21-24
IN 21-24
IN 25-28
IN 25-28
IN 29-32
IN 29-32
D1100809
Front
To ADC
To ADC Adapter
S1104073
Rear
<< L1-SUS-XC1
IN 13-16
IN 13-16
IN 7-12
IN 7-12
IN 1-6
IN 1-6

## Slide 472: D1001270-S1106208
Binary Output Chassis (4*DB9, 2*DB37)
D1001270
±18VDC
S1106208
<< L1-SUS-XC1
S1106208
Rear
Ch 0-31
Ch 0-31
Ch 32-63
Ch 32-63
D1001270
Front
Ch 0-7
Ch 0-7
Ch 8-15
Ch 8-15
Ch 16-23
Ch 16-23
Ch 24-31
Ch 24-31
Ch 32-47
Ch 32-47
Ch 48-63
Ch 48-63

## Slide 473: D1001269-S1106115
Binary Input Chassis (4*DB9, 2*DB37)
D1001270
±18VDC
S1106115
<< L1-SUS-XC1
S1106115
Rear
Ch 0-31
Ch 0-31
Ch 32-63
Ch 32-63
Ch 0-7
Ch 0-7
Ch 8-15
Ch 8-15
Ch 16-23
Ch 16-23
Ch 24-31
Ch 24-31
Ch 32-47
Ch 32-47
Ch 48-63
Ch 48-63
D1001270
Front

## Slide 474: D1002593-S1103225
Binary Output Chassis (8*DB9)
D1002593
±18VDC
S1103225
<< L1-SUS-XC1
S1103225
Rear
Ch 0-31
Ch 0-31
Ch 32-63
Ch 32-63
D1002593
Front
Ch 0-7
Ch 0-7
Ch 8-15
Ch 8-15
Ch 16-23
Ch 16-23
Ch 24-31
Ch 24-31
Ch 32-39
Ch 32-39
Ch 40-47
Ch 40-47
Ch 48-55
Ch 48-55
Ch 56-63
Ch 56-63

## Slide 475: D1001726-S1103096
Binary Input Chassis (8*DB9)
D1001726
±18VDC
S1103096
<< L1-SUS-XC1
S1103096
Rear
Ch 0-31
Ch 0-31
Ch 32-63
Ch 32-63
Ch 0-7
Ch 0-7
Ch 8-15
Ch 8-15
Ch 16-23
Ch 16-23
Ch 24-31
Ch 24-31
Ch 32-39
Ch 32-39
Ch 40-47
Ch 40-47
Ch 48-55
Ch 48-55
Ch 56-63
Ch 56-63
D1001726
Front

## Slide 476: L1-SUS-XC2
SUS Anti-Alias Chassis
D1000721
±18VDC
S1201127
SUS Anti-Alias Chassis
D1000721
±18VDC
S1201126
SUS Anti-Alias Chassis
D1000721
±18VDC
S1201130
SUS Anti-Alias Chassis
D1000721
±18VDC
S1201131
Unused
PSY-036
PSO-043
<< CERX Racks
L1-SUS-XC1 (ETM) X-End Remote Rack 1 (of 2) Layout (D1201083) (S1202947)
l1susex I/O Extension Chassis
D1001715
+24V@5A
S1103367
l1susauxex I/O Extension Chassis
D1001715
+24V@5A
S1201779

## Slide 477: D1000721-S1201130
SUS Anti-Alias Chassis
D1000721
±18@0.5A
S1201130
IN 1-4
Open
IN 5-8
Open
D1000721
Front
IN 9-20
Open
IN 21-32
Open
To DAC Adapter
Open
S1201130
Rear
<< L1-SUS-XC2

## Slide 478: D1000721-S1201131
SUS Anti-Alias Chassis
D1000721
±18@0.5A
S1201131
IN 1-4
Open
IN 5-8
Open
D1000721
Front
IN 9-20
Open
IN 21-32
Open
To DAC Adapter
Open
S1201131
Rear
<< L1-SUS-XC2

## Slide 479: D1000721-S1201127
SUS Anti-Alias Chassis
D1000721
±18@0.5A
S1201127
IN 1-4
Open
IN 5-8
Open
D1000721
Front
IN 9-20
Open
IN 21-32
Open
To DAC Adapter
Open
S1201127
Rear
<< L1-SUS-XC2

## Slide 480: D1000721-S1201126
SUS Anti-Alias Chassis
D1000721
±18@0.5A
S1201126
IN 1-4
Open
IN 5-8
Open
D1000721
Front
IN 9-20
Open
IN 21-32
Open
To DAC Adapter
Open
S1201126
Rear
<< L1-SUS-XC2

## Slide 481: l1susauxex - D1001715 – S11201779
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1201779
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1susauxex I/O Extension Chassis
D1001715
110VAC
S1201779
To UPS Power Strip
l1susauxex – I/O Extender
<< L1-SUS-XC2

## Slide 482: l1susex - D1001715 – S1103367
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1103367
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1susex I/O Extension Chassis
D1001715
110VAC
S1103367
To UPS Power Strip
l1susex – I/O Extender
<< L1-SUS-XC2

## Slide 483: L1-TCS-XC1
L1-TCS-XC1 X-End Remote Rack Layout (D1201129) (S1202980)
<< CERX Racks
TCS-XC1 is part of D1200258
Ring Heater Driver
D1003254
+/-18VDC
SN:
Hartmann Sensor Power Supply
D1102206
+/-18VDC
SN:
Accelerometer Power Supply
Isotron 2973
110VAC
SN:
BNC AA Interface Chassis (PEM)
D1001421
+/-18VDC
S1001056
Shelf
Shelf
Timing Comparator
D1001370
+12VDC
S1201891
Timing Master (Fanout)
D070011
+12VDC
S1107511
TCS-XC1 is part of E1100894

## Slide 484: D070011 – S1107511
Timing Master (Fanout)
D070011
+12VDC
S1107511
D070011
Front
S1107511
Rear
To 1X23 PP B4, B5
To l1pemex IO Front Panel
To D070124 Green Cable
<< L1-TCS-XC1

## Slide 485: D1001370 – S1201891
D1001370
Front
S1201891
Rear
Timing Comparator
D1001370
+12VDC
S1201891
<< L1-TCS-XC1

## Slide 486: D1102206 – Sxxxxxxx
D1102206
Front
Sxxxxxxx
Rear
Hartmann Sensor Power Supply
D1102206
+12VDC
Sxxxxxxx
<< L1-TCS-XC1

## Slide 487: Endevco Isotron 2793
Isotron 2793
Sxxxxxxx
Rear
Isotron 2793
Front
ACC X
ACC Y
Unused
ACC Z
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
ACC Z
Unused
ACC Y
ACC X
<< L1-TCS-XC1

## Slide 488: D1001421 - Sxxxxxxx
SN:
Rear
D1001421
Front
aLIGO AA Interface Chassis (32 BNC, x10 Gain Version)
D1001421
Power
SN:
MAG X
1
MAG Y
2
MAG Z
3
SEI X
4
SEI Y
5
SEI Z
6
Isotron 1
7
Isotron 2
8
Isotron 4
9
BSC4 MIC
10
BAY MIC
11
BSC4 TEMP
12
OPLEV 10
13
Unused
14
Unused
15
Unused
16
Unused
17
Unused
18
Unused
19
Unused
20
Unused
21
Unused
22
Unused
23
Unused
24
Unused
25
Unused
26
Unused
27
Unused
28
Unused
29
Unused
30
Unused
31
Unused
32
<< L1-TCS-XC1

## Slide 489: D1101363 - Sxxxxxxx
SN:
Rear
D1101363
Front
aLIGO Accelerometer Interface Chassis
D1101363
Power
SN:
Unused
1
Unused
1
Unused
2
Unused
2
Unused
3
Unused
3
Unused
4
Unused
4
Unused
5
Unused
5
Unused
6
Unused
6
Unused
7
Unused
7
Unused
8
Unused
8
Unused
9
Unused
9
Unused
10
Unused
10
Unused
11
Unused
11
Unused
12
Unused
12
Unused
13
Unused
13
Unused
14
Unused
14
Unused
15
Unused
15
Unused
16
Unused
16
OUTPUT
INPUT
<< L1-TCS-XC1

## Slide 490: L1-ISC-XR1
L1-ISC-XR1 X-End Station Field Rack Layout (D1201087) (S1202951)
<< VEAX Racks
ISC-XR1 is part of D1001423

## Slide 491: L1-ISC-XR1
RF Distribution Panel 24
Dxxxxxxx
No Power
SN:
24.5 MHz Delay Line Phase Shifter
D0900128
±18V
S1103430
+12VDC 1A
-12VDC 1A
+18VDC 10A
-18VDC 10A
+24VDC 4A
-24VDC 1A
High Voltage ?A
<< VEAX Racks
Sequencer
D1200757
S1202568
L1-ISC-XR1 X-End Station Field Rack Layout (D1201087) (S1202951)
ISC-XR1 is part of D1001423
RF Distribution Panel 25
Dxxxxxxx
No Power
SN:
2 Channel RFPD I/Q Demod (RC & ALS)
D1000181
±18V
S1000786
Demodulator RF Patch Panel
D1100905
No Power
Sxxxxxxx
79.4 MHz VCO (ALS)
D0900605
±18V
S1200578
39.7 MHz Frequency Divider
D1002182
±18V
S1000753
RF Preamplifier
D1201294
±18V
Sxxxxxxx
39.7 MHz 2 Channel Phase/Freq Discriminator
D1002476
±18V
S1000768
Common Mode Servo (ALS Laser Locking)
D0901781
±18V
S1102646
Common Mode Servo (ALS Cavity Locking)
D0901781
±18V
S1102647
LSC Demod Concentrator 5
D1100691
±18V
S1104010
ASC Demod Concentrator 6
D1100696
±18V
S1103989
Auxiliary Signals Concentrator 2
D1102045
±18V
Sxxxxxxx
Auxiliary Signals Concentrator 1
D1102065
±18V
Sxxxxxxx
Auxiliary Signals Concentrator 5
D1102065
±18V
Sxxxxxxx
iLIGO LSC PD Interface (4 Channel)
D0901833
±18V
Sxxxxxxx
Differential to Single-Ended Converter
D1100482
±18V
Sxxxxxxx
Dual QPD Transimpedance Amplifier
D1002481
±18V
Sxxxxxxx
Dual QPD Transimpedance Amplifier
D1002481
±18V
Sxxxxxxx
ISC Whitening Chassis
D1002559
±18V
Sxxxxxxx
ISC Whitening Chassis
D1002559
±18V
Sxxxxxxx

## Slide 492: D1100905 – Sxxxxxxx
<< L1-ISC-XR1

## Slide 493: D1002476 - Sxxxxxxx
Sxxxxxxx
Rear
D1002476
Front
158.8 / 79.4 MHz 2-Channel PF Discriminator
D1002476
±17VDC, ±24VDC
Sxxxxxxx
<< L1-ISC-XR1

## Slide 494: L1-SUS-XR1
+18VDC ?A
-18VDC ?A
+24VDC ?A
<< VEAX Racks
PSY-013
PSY-016
PSO-001
L1-SUS-XR1 X-End Station Field Rack Layout (D1201131) (S1202993)
Electrostatic Driver
+-18VDC@0.4A
+-430VDC@15mA
E3074
SN:

## Slide 495: E3074
E3074
Front
S???????
Rear
<< L1-SUS-XR1
Electrostatic Driver
+-18VDC@0.4A
+-430VDC@15mA
E3074
SN:

## Slide 496: L1-VAC-XR1
L1-VAC-XR1 X-End Vacuum Rack Layout (Dxxxxxxx)
<< VEAX Racks

## Slide 497: VEAY
VEAY
<< LLO Racks by AREA
<< LLO CDS Components
<< LLO Corner Station

## Slide 498: Y-End Station Rack Layout
<< CERY
<< LLO Corner Station
<< VEAY

## Slide 499: Y-End Station Rack Layout
<< CERY
<< LLO Corner Station
<< VEAY
Y-End - D0901464

## Slide 500: Y-End Racks
DAQ Rack
(L1-DAQ-YC1)
ISC Rack
(L1-ISC-YC1)
SUS Rack 2
(L1-SUS-YC2)
SUS Rack 1
(L1-SUS-YC1)
SUS Field Rack
(L1-SUS-YR1)
TCS Rack
(L1-TCS-YC1)
DC Power Rack 1 (L1-VDC-YC1)
DC Power Rack 2 (L1-VDC-YC2)
SEI Rack
(L1-SEI-YC1)
Facilities Rack
(L1-FAC-YC1)
Vacuum Field Rack
(L1-VAC-YR1)
<< LLO Racks by AREA
ISC Field Rack
(L1-ISC-YR1)

## Slide 501: Corning WCH-06P Fiber Panel
5.75”
13.5” x 16.062” x 5.125”
120”
4”
21.75”
21.25”
X”
CCH-CP12-15T (ST)
CCH-CP12-11 (FC)
x 1
x 2

## Slide 502: WCH-06P – Patch Panel
Patch Panel
Patch Panel
No Power
Patch Panel
l1lanfey 21F (Clear)
1-1
l1lanfey 21F (None)
1-2
X448 1F
1-3
X448 1F
1-4
ACC-5595 Port 6 (Clear)
1-5
ACC-5595 Port 6 (None)
1-6
VT430 Opt In/Out
3-1
7711-R Opt In/Out
3-2
2402 26F (White)
3-3
Empty
3-4
1Y23 PP Port 6
3-5
1Y23 PP Port 5
3-6
Empty
2-1
TR30300WDM OPT In/Out
2-2
Empty
2-3
D070011 Fanout Input
2-4
D070011 Fanout Input
2-5
VT5030 Opt Out
2-6
l1netfedaqy 21F (Clear)
4-1
l1netfedaqy 21F (None)
4-2
2402 26F (Yellow)
4-3
Empty
4-4
Empty
4-5
Empty
4-6
FC Connectors
Empty
C1
Empty
C2
Empty
C3
Empty
C4
Empty
C5
Empty
C6
Empty
F1
Empty
F2
Empty
F3
Empty
F4
Empty
F5
Empty
F6

## Slide 503: CDS Electronics Room Y-End (CERY) Rack Layout
CERY
(L1-VDC-YC1)
(L1-VDC-YC2)
(L1-DAQ-YC1)
(L1-SEI-YC1)
(L1-SUS-YC1)
(L1-SUS-YC2)
(L1-TCS-YC1)
(L1-FAC-YC1)
<< Y-End Racks
AC Power
Signals and Fiber
It is 65’ from the L1-FAC-YC1 Rack to the knee of the waterfall in the VEAY.
(L1-ISC-YC1)
DC Power and Fiber

## Slide 504: LLO Y-End Cable Tray Layout
6” x 4” Tray
Fibers and DC Cables
Signal Cables On Top
CERY
96”
12” x 4” Tray
AC Cable Tray (On Wall)

## Slide 505: L1-VDC-YC1 Power Racks – VEAY Field Supplies
L1-VDC-YC1 Power Rack
B
A
L1-VDC-YC1 Power Rack
A
B
L1-TCS-YR1
L1-TCS-YR1
L1-TCS-YR1
L1-TCS-YR1
L1-PEM-YR1
L1-PEM-YR1
L1-PEM-YR1
L1-PEM-YR1
L1-ISC-YR1
L1-ISC-YR1
L1-ISC-YR1
L1-ISC-YR1
Unused
Unused
Unused
L1-TCS-YR1
L1-TCS-YR1
L1-TCS-YR1
L1-TCS-YR1
L1-PEM-YR1
L1-PEM-YR1
L1-PEM-YR1
L1-PEM-YR1
L1-ISC-YR1
L1-ISC-YR1
L1-ISC-YR1
L1-ISC-YR1
Unused
Unused
Unused
<< CERY Racks
L1-SUS-YR1
L1-SUS-YR1
L1-SUS-YR1
L1-SUS-YR1
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Cable Runs >>
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
-24VDC
-24VDC
+24VDC
+24VDC
-24VDC
-24VDC
+24VDC
+24VDC
-24VDC
-24VDC
+24VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
L1-VDC-YC1 Y-End Station DC Power Rack Layout (D1200899) (S1202313)
Notes: For a JQE Style25-20M: AC power calculations:
125 VAC * 10.5 (A/PS) => 1312.5 (W/PS)
24 (PS/Rack)* 1312.5 (W/PS) => 31500 (W/Rack)
24 (PS/Rack) * 10.5 (A/PS) => 252 (A/Rack)

## Slide 506: L1-VDC-YC1 Cable Runs
<< L1-VDC-YC1
L1-VDC-YC1 S1202313 | Power Panel | Circuit | DC Power Rack | Outlet | Plug Position | Rack U | Power Supply Model | Power Supply Serial | Polarity | DC Extension Cable | Electronics Rack | DC Power Strip
1 | CDS-Y |  | L1-VDC-YC1 | 8 | Top | U37-A (Left) |  |  |  |  |  | 
2 | CDS-Y |  | L1-VDC-YC1 | 8 | Bottom | U37-B (Right) |  |  |  |  |  | 
3 | CDS-Y |  | L1-VDC-YC1 | 2 | Top | U33-A (Left) |  |  |  |  |  | 
4 | CDS-Y |  | L1-VDC-YC1 | 2 | Bottom | U33-B (Right) |  |  |  |  |  | 
5 | CDS-Y |  | L1-VDC-YC1 | 9 | Top | U29-A (Left) | BHK 500V 80mA | A107268 | Plus | PBX-004 |  | 
6 | CDS-Y |  | L1-VDC-YC1 | 9 | Bottom | U29-B (Right) | BHK 500V 80mA | A107263 | Minus | PBX-004 |  | 
7 | CDS-Y |  | L1-VDC-YC1 | 3 | Top | U25-A (Left) | JQE 25V 20A |  | Plus | PTO-046 | L1-ISC-YR1 | PSO-046
8 | CDS-Y |  | L1-VDC-YC1 | 3 | Bottom | U25-B (Right) | JQE 25V 20A |  | Minus | PTO-046 | L1-ISC-YR1 | PSO-046
9 | CDS-Y |  | L1-VDC-YC1 | 10 | Top | U21-A (Left) | JQE 25V 20A |  | Plus | PTY-037 | L1-ISC-YR1 | PSY-037
10 | CDS-Y |  | L1-VDC-YC1 | 10 | Bottom | U21-B (Right) | JQE 25V 20A |  | Minus | PTY-037 | L1-ISC-YR1 | PSY-037
11 | CDS-Y |  | L1-VDC-YC1 | 4 | Top | U17-A (Left) | JQE 25V 20A |  | Plus | PTO-047 | L1-OAF-YR1 | PSO-047
12 | CDS-Y |  | L1-VDC-YC1 | 4 | Bottom | U17-B (Right) | JQE 25V 20A |  | Minus | PTO-047 | L1-OAF-YR1 | PSO-047
13 | CDS-Y |  | L1-VDC-YC1 | 11 | Top | U13-A (Left) | JQE 25V 20A |  | Plus | PTY-038 | L1-OAF-YR1 | PSY-038
14 | CDS-Y |  | L1-VDC-YC1 | 11 | Bottom | U13-B (Right) | JQE 25V 20A |  | Minus | PTY-038 | L1-OAF-YR1 | PSY-038
15 | CDS-Y |  | L1-VDC-YC1 | 5 | Top | U09-A (Left) | JQE 25V 20A |  | Plus | PTO-048 | L1-SUS-YR1 | PSO-048
16 | CDS-Y |  | L1-VDC-YC1 | 5 | Bottom | U09-B (Right) | JQE 25V 20A |  | Minus | PTO-048 | L1-SUS-YR1 | PSO-048
17 | CDS-Y |  | L1-VDC-YC1 | 12 | Top | U05-A (Left) | JQE 25V 20A |  | Plus | PTO-049 | L1-TCS-YR1 | PSO-049
18 | CDS-Y |  | L1-VDC-YC1 | 12 | Bottom | U05-B (Right) | JQE 25V 20A |  | Minus | PTO-049 | L1-TCS-YR1 | PSO-049
19 | CDS-Y |  | L1-VDC-YC1 | 6 | Top | U01-A (Left) | JQE 25V 20A |  | Plus | PTY-039 | L1-TCS-YR1 | PSY-039
20 | CDS-Y |  | L1-VDC-YC1 | 6 | Bottom | U01-B (Right) | JQE 25V 20A |  | Minus | PTY-039 | L1-TCS-YR1 | PSY-039
D1200899 |  |  |  |  |  |  |  |  |  |  |  | 
L1-VDC-YC1 Y-End Station DC Cable Runs (D1200899) (S1202313)

## Slide 507: L1-VDC-YC2 Power Racks – VEAY Supplies
L1-SUS-YC1
L1-SUS-YC2
L1-SUS-YC2
L1-SUS-YC1
L1-ISC-YC1
L1-ISC-YC1
Cable Runs >>
L1-VDC-YC2 Power Rack
B
A
L1-VDC-YC2 Power Rack
A
B
L1-SEI-YC1
L1-SEI-YC1
L1-SEI-YC1
L1-SEI-YC1
L1-SUS-YC1
L1-SUS-YC1
L1-SUS-YC2
L1-SUS-YC2
Unused
Unused
Unused
Unused
Unused
Unused
L1-SEI-YC1
L1-SEI-YC1
L1-SEI-YC1
L1-SEI-YC1
L1-SEI-YC1
L1-SUS-YC1
L1-SUS-YC1
L1-SUS-YC2
L1-SUS-YC2
Unused
Unused
Unused
Unused
Unused
Unused
L1-SEI-YC1
L1-ISC-YC1
L1-ISC-YC1
L1-ISC-YC1
L1-ISC-YC1
L1-ISC-YC1
L1-ISC-YC1
L1-ISC-YC1
L1-ISC-YC1
<< CERY Racks
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
-24VDC
-24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+18VDC
-18VDC
-18VDC
+18VDC
+24VDC
+24VDC
+24VDC
+24VDC
+24VDC
-24VDC
-24VDC
+24VDC
L1-TCS-YC1
L1-TCS-YC1
L1-TCS-YC1
L1-TCS-YC1
+18VDC
-18VDC
-18VDC
+18VDC
L1-VDC-YC2 Y-End Station DC Power Rack Layout (D1200900) (S1202314)
Notes: For a JQE Style25-20M: AC power calculations:
125 VAC * 10.5 (A/PS) => 1312.5 (W/PS)
24 (PS/Rack)* 1312.5 (W/PS) => 31500 (W/Rack)
24 (PS/Rack) * 10.5 (A/PS) => 252 (A/Rack)

## Slide 508: L1-VDC-YC2 Cable Runs
<< L1-VDC-YC2
L1-VDC-YC2 S1202314 | Power Panel | Circuit | DC Power Rack | Outlet | Plug Position | Rack U | Power Supply Model | Power Supply Serial | Polarity | DC Extension Cable | Electronics Rack | DC Power Strip
1 | CDS-Y |  | L1-VDC-YC2 |  | Top | U37-A (Left) |  |  |  |  |  | 
2 | CDS-Y |  | L1-VDC-YC2 | 8 | Bottom | U37-B (Right) |  |  |  |  |  | 
3 | CDS-Y |  | L1-VDC-YC2 | 2 | Top | U33-A (Left) | JQE 15V 6A | H214466 H214326 | Plus Minus | PTG-004 | L1-ISC-YC1 | 
4 | CDS-Y |  | L1-VDC-YC2 | 8 | Bottom | U33-B (Right) | JQE 25V 10A |  | Plus | PTO-052 | L1-ISC-YC1 | 
5 | CDS-Y |  | L1-VDC-YC2 | 9 | Top | U29-A (Left) | JQE 25V 20A | H236414 | Plus | PTO-050 | L1-SUS-YC2 | PSO-050
6 | CDS-Y |  | L1-VDC-YC2 | 9 | Bottom | U29-B (Right) | JQE 25V 20A | H236422 | Minus | PTO-050 | L1-SUS-YC2 | PSO-050
7 | CDS-Y |  | L1-VDC-YC2 | 3 | Top | U25-A (Left) | JQE 25V 20A | H236504 | Plus | PTO-051 | L1-SUS-YC1 | PSO-051
8 | CDS-Y |  | L1-VDC-YC2 | 3 | Bottom | U25-B (Right) | JQE 25V 20A | H236513 | Minus | PTO-051 | L1-SUS-YC1 | PSO-051
9 | CDS-Y |  | L1-VDC-YC2 | 10 | Top | U21-A (Left) | JQE 25V 20A | H236508 | Plus | PTO-052 | L1-ISC-YC1 | PSO-052
10 | CDS-Y |  | L1-VDC-YC2 | 10 | Bottom | U21-B (Right) | JQE 25V 20A | H236516 | Minus | PTO-052 | L1-ISC-YC1 | PSO-052
11 | CDS-Y |  | L1-VDC-YC2 | 4 | Top | U17-A (Left) | JQE 25V 20A | H236503 | Plus | PTY-040 | L1-ISC-YC1 | PSY-040
12 | CDS-Y |  | L1-VDC-YC2 | 4 | Bottom | U17-B (Right) | JQE 25V 20A | H236488 | Minus | PTY-040 | L1-ISC-YC1 | PSY-040
13 | CDS-Y |  | L1-VDC-YC2 | 11 | Top | U13-A (Left) | JQE 25V 20A | H236500 | Plus | PTO-053 | L1-SEI-YC1 | PSO-053
14 | CDS-Y |  | L1-VDC-YC2 | 11 | Bottom | U13-B (Right) | JQE 25V 20A | H236520 | Minus | PTO-053 | L1-SEI-YC1 | PSO-053
15 | CDS-Y |  | L1-VDC-YC2 | 5 | Top | U09-A (Left) | JQE 25V 20A | H236519 | Plus | PTY-041 | L1-SEI-YC1 | PSY-041
16 | CDS-Y |  | L1-VDC-YC2 | 5 | Bottom | U09-B (Right) | JQE 25V 20A | H236487 | Minus | PTY-041 | L1-SEI-YC1 | PSY-041
17 | CDS-Y |  | L1-VDC-YC2 | 12 | Top | U05-A (Left) | JQE 25V 20A | H236502 | Plus | PTY-042 | L1-ISC-YC1 | PSY-042
18 | CDS-Y |  | L1-VDC-YC2 | 12 | Bottom | U05-B (Right) | JQE 25V 20A | H236518 | Plus | PTY-043 | L1-SEI-YC1 | PSY-043
19 | CDS-Y |  | L1-VDC-YC2 | 6 | Top | U01-A (Left) | JQE 25V 20A | H236521 | Plus | PTY-044 | L1-SUS-YC2 | PSY-044
20 | CDS-Y |  | L1-VDC-YC2 | 6 | Bottom | U01-B (Right) | JQE 25V 20A | H236507 | Plus | PTY-045 | L1-SUS-YC1 | PSY-045
D1200900 |  |  |  |  |  |  |  |  |  |  |  | 
L1-VDC-YC2 Y-End Station DC Cable Runs (D1200900) (S1202314)

## Slide 509: L1-DAQ-YC1
l1iscey Front End Computer
Dxxxxxxx
UPS1 & 110VAC
SN:
Dolphin RFM Switch
DXS410
UPS2
XXXXXXXX
ATEN KVM Switch
CL1016M
UPS2
SN:
l1lanfey 10.199.0.14
GSM7224
UPS2
2B62045K0015D
l1netfedaqy 10.199.0.88
GSM7224
UPS2
2B62045400019
l1seiey Front End Computer
Dxxxxxxx
UPS1 & 110VAC
SN:
l1susey Front End Computer
Dxxxxxxx
UPS1 & 110VAC
SN:
l1susauxey Front End Computer
Dxxxxxxx
UPS1 & 110VAC
SN:
110VAC 20A
UPS1 - UPS Power Strip
110VAC 20A
Non-UPS Power Strip
UPS Group 1 and Group 2
APC SMT2000RMLV2U
110VAC
J51048023241
<< CERY Racks
Timing IRIG-B Interface Chassis
D0900301
+12VDC (from FAC)
S1202408
L1-DAQ-YC1 Y-End Station Remote Rack Layout (D1201092) (S1202956)
Dxxxxxxx
l1ecaty1 Beckhoff Host Computer
UPS1 & 110VAC
SN:
Shelf
Hartmann Sensor Computer
T1000702
UPS1 & 110VAC
SN:
Shelf
ACC 5595 Reflective Memory Hub
ACC 5595
UPS2
36106691
110VAC 20A
UPS2 - UPS Power Strip
Serial Concentrator Chassis
D1100632
±18@1A
SN:
Ethernet 4km Remote End Access Chassis
D1002961
+24@5.0A
SN:
Serial to Internet Converter
Notes: The +12VDC and the +24VDC come from supplies in FAC-C1.
Where will the +18VDC come from?

## Slide 510: VMIACC-5595-224 – 36106691
36106691
Rear
ACC 5595
Front
ACC 5595 Reflective Memory Hub
ACC 5595
110VAC
36106691
To UPS Power Strip
To l1lanfey port 5
<< L1-DAQ-YC1

## Slide 511: l1netfedaqy – GSM7224
GSM7224
Front
2B62045400019
Rear
C0:3F:0E:86:84:04
l1netfedaqy 10.199.0.88
GSM7224
110VAC
2B62045400019
2 - To FE NET Port
21F - To 1Y23 PP E1, E2
To UPS Power Strip
<< L1-DAQ-YC1

## Slide 512: l1lanfey – GSM7224
GSM7224
Front
2B62045K0015D
Rear
C0:3F:0E:86:89:14
l1lanfey 10.199.0.14
GSM7224
110VAC
2B62045K0015D
2 - To FE LAN Port
21F - To 1Y23 PP A1, A2
5 - To 5595 LAN 10BaseT
To UPS Power Strip
<< L1-DAQ-YC1

## Slide 513: D0900301 – S1202408
Timing IRIG-B Interface Chassis
D0900301
Power
S1202408
D0900301
Front
S1202408
Rear
<< L1-DAQ-YC1

## Slide 514: D1100632 – Sxxxxxxx
Sxxxxxxx
Rear
D1100632
Front
Serial Port Concentrator for Timing
D1100632
±18VDC
Sxxxxxxx
<< L1-DAQ-YC1

## Slide 515: ATEN CL1016M
ATEN KVM Switch
CL1016M
110VAC
SN:
SN:
Rear
CL1016M
Front
To l1pemey Front End
To UPS Power Strip
<< L1-DAQ-YC1

## Slide 516: l1susauxey Front End
l1susauxey Front End Computer
Front End
110VAC
SN:
<< L1-DAQ-YC1

## Slide 517: l1susey Front End
l1susey Front End Computer
Front End
110VAC
SN:
<< L1-DAQ-YC1

## Slide 518: l1seiey Front End
l1seiey Front End Computer
Front End
110VAC
SN:
<< L1-DAQ-YC1

## Slide 519: l1iscey Front End
l1iscey Front End Computer
Front End
110VAC
SN:
<< L1-DAQ-YC1

## Slide 520: l1ecaty1 Front End
l1ecaty1 Beckhoff Host Computer
Front End
110VAC
SN:
<< L1-DAQ-YC1

## Slide 521: Hartmann Sensor Computer Front End
Hartmann Sensor Front End Computer
Front End
110VAC
SN:
<< L1-DAQ-YC1

## Slide 522: APC SMX2000RMLV2U
UPS
APC SMX2000RMLV2U
110VAC
J51048023241
To UPS Power Strip
APC SMX2000RMLV2U
Front
J51048023241
Rear
<< L1-DAQ-YC1

## Slide 523: L1-FAC-YC1
110VAC 15A
UPS1 - UPS Power Strip
110VAC 15A
Non-UPS Power Strip
UPS1 & 110VAC
N62538F19R
GS624P
Brocade FastIron Edge GS624P
UPS1
FB00001705
2402
2402 Network Switch
Kantech
xxxxxxxx
+12VDC
SN:
Trinet Fibox
xxxxxxxx
+12VDC
SN:
Phone
Security Cameras
IFO Cameras
Shelf
Shelf
Shelf
UPS1
APC SMT1500RM2U
110VAC
AS10J1111987
<< CERY Racks
L1-FAC-YC1 Facilities Y-End Station Remote Rack Layout (D1201093) (S1202957)
KEPCO Power Supplies
UPS1
JQE15-6M
JQE25-10M
JQE15-6M
JQE15-6M
JQE25-10M
JQE15-6M
PSY-034
PSY-034

## Slide 524: Brocade FastIron Edge GS624P
UPS & 110VAC
N62538F1A3
GS624P
Brocade FastIron Edge GS624P
N62538F1A3
Rear
C0:3F:0E:86:88:E0
GSM7224
Front
3 - To FE NET Port
21F - To 1Y23 PP B1,B2
To UPS Power Strip
To 110 Power Strip
<< L1-FAC-YC1

## Slide 525: 2402 – Network Switch
2402 Network Switch
2402
110VAC
FB00001705
G12039
192.168.253.30
Empty
01
Empty
02
Empty
03
Empty
04
Empty
05
Empty
06
To Camera on Reel
07
Empty
08
To Trinet/Trinet
09
Empty
10
To Trinet/Trinet
11
Empty
12
Empty
13
To Seimens
14
Empty
15
Empty
16
Empty
17
Empty
18
Empty
19
Empty
20
To Weather Station ???
21
Empty
22
Empty
23
Empty
24
Empty
25C
Empty
26C
To Special Cable CSR1
25F
To 1Y23 PP D3, E3
26F
PS1
To UPS
<< L1-FAC-YC1

## Slide 526: Y-End – Kantech Interface
Fiber Options 7711-R (501R)
Optical In/Out:
To 1Y23 PP D2
Power: 13.5VDC from Wall Wart
Blue CAT5: 1=O/W and B/W, 4=O, 7=B
Powered from Wall Wart from Isolated Power
Kantech
To Siemens Racks
To 1Y23 PP D2
To Kantech Racks
To MSR PP H2
<< L1-FAC-YC1

## Slide 527: Trinet FIBOX Panel
Trinet FIBOX Panel
Trinet FIBOX Panel
12VDC
Trinet Panel
Empty
1
Trinet Z
2
Trinet Y
3
Trinet X
4
FBAO-SL
FBAO-M
To 0X57682890001 Port 3
12VDC IN
G/W – Center – COM - A2
Y/W – Shield - +12V – A1
<< L1-FAC-YC1

## Slide 528: 1Y23 – D070443 – LH09
Powered from 12VDC DIN rails
Powered from 15VDC DIN rails
D070443
Magnetometer Filter
LH09
Magnetometer Power Supply
(MAG-03PSU)
656
Magnetometer
MAG-03MCES
X
Y
Z
X
Y
Z
Magnetometer: Bartington Instruments MAG-03MC
5 meter
X
Y
Z
On/Off
D030574
Pin 1 – Red
Pin 2 – Black
Pin 3 – White
Pin 4 - Black
Black – G/W … Ground
Stria – Y/W … +12VDC
–
+
Charger … 9 to 18 VDC
<< L1-FAC-YC1

## Slide 529: 1Y23 – Stuff
VT5030 IFS
International Fiber Systems, Inc.
IFS.com
Optical Out:
To 1Y23 PP B6
Power: 12VDC
Video Input:
Camera 1
Camera 2
VT7430-2DRDT
Optical In/Out:
To 1Y23 PP D1
Power: 12VDC
Output: Ch1, Ch2, Ch3 BNCs to Cameras
TR3030WDM
GE Security
Optical In/Out: To 1Y23 PP B2
Phone: Copper to VEA
Power: 12VDC
Fiber Options 7711-R (501R)
Optical In/Out:
To 1Y23 PP D2
Power: 13.5VDC from Wall Wart
Blue CAT5: 1=O/W and B/W, 4=O, 7=B
Powered from DIN rails
Powered from Wall Wart from Isolated Power
Powered from Wall Wart from Tripp-Lite UPS
Model BC320
9834DY0BC614000661 To 6-Outlet Power Strip in Non-isolated wall socket
AC Powered from Isolated Power
Powered from Wall Wart from Isolated Power
J/E-CF-01
TriNet Converter
CAT5:
To 2402 P9
TX:
To 0X57… P1
RX:
To 0X57… P2
Power: 12VDC
Powered from DIN rails
Powered from DIN rails
J/E-CF-01
TriNet Converter
CAT5:
To 2402 P11
TX:
To 0X57… P8
RX:
To 0X57… P7
Power: 12VDC
Phone
Seismic Vault
Revere Video Master Power Supply Model RT24/16500
Outputs to Cameras 1,2,3
*LEDs on with bad fuse
Note: 8 LEDs are on.
Kantech
Security Cameras
IFO Cameras
<< L1-FAC-YC1

## Slide 530: Y-End – Security Cameras
Revere Video Master Power Supply Model RT24/16500
Outputs to Cameras 1,2,3
*LEDs on with bad fuse
Note: 8 LEDs are on.
AC Powered from Isolated Power
VAC
Security Cameras
<< L1-FAC-YC1

## Slide 531: Y-End – Security Cameras
VT7430-2DRDT
Optical In/Out:
To 1Y23 PP D1
Power: 12VDC
Output: Ch1, Ch2, Ch3 BNCs to Cameras
Powered from Wall Wart from Isolated Power
Security Cameras
<< L1-FAC-YC1

## Slide 532: 1Y23 – Stuff
VT5030 IFS
International Fiber Systems, Inc.
IFS.com
Optical Out:
To 1Y23 PP B6
Power: 12VDC
Video Input:
Camera 1
Camera 2
Powered from DIN rails
To 1Y23 PP B6
Cameras
<< L1-FAC-YC1

## Slide 533: Y-End – Trinet
J/E-CF-01
TriNet Converter
CAT5:
To 2402 P9
TX:
To 0X57… P1
RX:
To 0X57… P2
Power: 12VDC
Powered from DIN rails
Powered from DIN rails
J/E-CF-01
TriNet Converter
CAT5:
To 2402 P11
TX:
To 0X57… P8
RX:
To 0X57… P7
Power: 12VDC
Seismic Vault
To 2402 P9
To 2402 P11
To 0X57… P1
To 0X57… P2
To 0X57… P8
To 0X57… P7
<< L1-FAC-YC1

## Slide 534: Y-End - Phone
TR3030WDM
GE Security
Optical In/Out: To 1Y23 PP B2
Phone: Copper to VEA
Power: 12VDC
Powered from Wall Wart from Tripp-Lite UPS
Model BC320
9834DY0BC614000661 To 6-Outlet Power Strip in Non-isolated wall socket
Phone
<< L1-FAC-YC1

## Slide 535: KEPCO Power Supplies
SN:
Rear
JQE
Front
KEPCO JQE 25-10M +24VDC
KEPCO JQE 15-6M +12VDC
KEPCO JQE 15-6M
-12VDC
<< L1-FAC-YC1
KEPCO Power Supplies
UPS1
JQE15-6M
JQE25-10M
JQE15-6M
JQE15-6M
JQE25-10M
JQE15-6M
KEPCO JQE 15-6M
-12VDC
KEPCO JQE 15-6M
+12VDC
KEPCO JQE 25-10M +24VDC

## Slide 536: APC SMT1500RM2U
UPS
APC SMT1500RM2U
110VAC
A51051111987
APC SMT1500RM2U
Front
A51051111987
Rear
To X448 PS1
To 2402 PS1
<< L1-FAC-YC1

## Slide 537: L1-ISC-YC1
ISC-YC1 Y-End Station Remote Rack Layout (D1201091) (S1202955)
<< CERY Racks
Sequencer
D1200757
S1202547
ISC-YC1 is part of D1001459
71 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000653
Anti-Alias Chassis
D0902783
±18@1A
SN:
Anti-Alias Chassis
D0902783
±18@1A
SN:
Anti-Image Chassis
D070081
±18@0.5A
SN:
l1pemey I/O Extension Chassis
D1001715
+24V@5A
S1000528
RF Distribution Panel 26
Dxxxxxxx
No Power
SN:
71 MHz Oscillator
D080702
+12VDC, ±24VDC
S1000562
RF Distribution Panel 27
Dxxxxxxx
No Power
SN:
24.4 MHz Oscillator
D080702
+12VDC, ±24VDC
S1000577
24.4 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000670
RF Amplifier Concentrator 3
D1100262
+/-18VDC
S1103463
Shelf
ISC Common Beckhoff Chassis
D1002961
+24@5.0A
SN:
End 2 Beckhoff Chassis
D1100682
+24@5.0A
SN:
384 Channel Binary Output
D1100251
+24VDC
S1203282
Shelf
Aeroflex Diagnostics
2023A
110VAC
Sxxxxxxx
L1-ISC-YC1 is D1201091
PSY-032
PSY-034
PSO-045
PSG-XXX

## Slide 538: D080702 – S1000562
71 MHz Oscillator
D080702
+12VDC, ±24VDC
S1000562
S1000562
Rear
D080702
Front
Front
Output
Front
Lock
To …
<< L1-ISC-YC1

## Slide 539: D1000124 – S1000653
71 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000653
D1000124
Front
Front
10 dBm
Front
1
Front
2
Front
3
Front
4
Front
5
Front
6
Front
7
Front
8
S1000653
Rear
Front
M1
Front
M2
Front
M3
Front
Controls
<< L1-ISC-YC1

## Slide 540: D080702 – S1000577
24.4 MHz Oscillator
D080702
+12VDC, ±24VDC
S1000577
S1000577
Rear
D080702
Front
Front
Output
Front
Lock
To …
<< L1-ISC-YC1

## Slide 541: D1000124 – S1000670
24.4 MHz Distribution Amplifier
D1000124
±17VDC, ±24VDC
S1000670
D1000124
Front
Front
10 dBm
Front
1
Front
2
Front
3
Front
4
Front
5
Front
6
Front
7
Front
8
S1000670
Rear
Front
M1
Front
M2
Front
M3
Front
Controls
<< L1-ISC-YC1

## Slide 542: D1100262 – S1103463
RF Amplifier Concentrator 1
D1100262
±18VDC
S1103463
D1100262
Front
S1103463
Rear
1
Rear
Controls
5
Rear
9
Rear
2
Rear
6
Rear
10
Rear
3
Rear
7
Rear
11
Rear
4
Rear
8
Rear
12
Rear
Rear
<< L1-ISC-YC1

## Slide 543: D1100251 – S1203282
384 Channel Binary Output
D1100251
+24VDC
S1203282
D1100251
Front
Front
Chassis 1 – Board 1
Front
Chassis 1 – Board 2
Front
Chassis 2 – Board 1
Front
Chassis 2 – Board 2
Front
Chassis 3 – Board 1
Front
Chassis 3 – Board 2
S1203282
Rear
Rear
Chassis 6 – Board 1
Rear
Chassis 6 – Board 2
Rear
Chassis 5 – Board 1
Rear
Chassis 5 – Board 2
Rear
Chassis 4 – Board 1
Rear
Chassis 4 – Board 2
Rear
In
Rear
Out
<< L1-ISC-YC1

## Slide 544: l1pemey - D1001715 – S1000528
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1000528
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
D1001421
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1pemey I/O Extension Chassis
D1001715
110VAC
S1000528
To UPS Power Strip
l1pemey – I/O Extender
<< L1-ISC-YC1
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx

## Slide 545: L1-SEI-YC1
PSY-013
PSY-016
+18VDC 4A
-18VDC 4A
+24VDC 15A
BSC-5 8 Channel Valve Driver
D020373
Power
S1001155
I/O Extension Chassis
D1001715
+24@5A
S1200166
PSO-001
<< CERY Racks
L1-SEI-YC1 (BSC5) Y-End Remote Rack 1 Layout (D1201088) (S1202952)
SEI-YC1 is part of D0901301

## Slide 546: D020373 – S1001155
S1001155
Rear
VALVE INPUTS
D020373
Front
Open
CHANS 1&2
Open
CHANS 3&4
CHANS 1&2
CHANS 3&4
Open
CHANS 5&6
Open
CHANS 7&8
CHANS 5&6
CHANS 7&8
8 CHANNEL VALVE DRIVER
POWER DISTRIBUTION
LIGO D040049
8 CHANNEL VALVE DRIVER
LIGO D020373 REV C
Open
VALVE INPUTS
D040049
BSC-5 8 Channel Valve Driver
D020373
Power
S1001155
<< L1-SEI-YC1
BSC5

## Slide 547: l1seiey D1001715-S1200166
I/O Extension Chassis
D1001715
24 VDC
S1200166
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
24 VDC
S1200166
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
<< L1-SEI-YC1
l1seiey – I/O Extender

## Slide 548: D1102206-Sxxxxxx
D1102206
Front
S???????
Rear
<< L1-TCS-YC1
Hartmann Sensor Power Supply
D1102206
???
SN:

## Slide 549: L1-SUS-YC1
<< CERY Racks
L1-SUS-YC1 (ETM) Y-End Remote Rack 1 (of 2) Layout (D1201089) (S1202953)
Anti-Image Chassis (2*DB15, 1*DB9)
D1100815
±18VDC
S1103827
Transmon Coil Driver Chassis
D1100301
±18VDC
Sxxxxxxx
Transmon Coil Driver Chassis
D1100301
±18VDC
Sxxxxxxx
Anti-Alias Chassis (8*DB9)
D0902783
±18VDC
S1200819
Anti-Image Chassis (4*DB9)
D1000305
±18VDC
S1001201
Anti-Image Chassis (4*DB9)
D1000305
±18VDC
S1105312
Anti-Alias Chassis (2*DB15, 5*DB9)
D1100809
±18VDC
S1104075
Binary Output Chassis (4*DB9, 2*DB37)
D1001270
±18VDC
S1106211
Binary Input Chassis (8*DB9)
D1001726
±18VDC
S1103897
Binary Output Chassis (8*DB9)
D1002593
±18VDC
S1103224
Binary Input Chassis (4*DB9, 2*DB37)
D1001269
±18VDC
S1106114
PSO-042

## Slide 550: D1100301-Sxxxxxxx
Transmon Coil Driver Chassis
D1100301
±18VDC
Sxxxxxxx
D1100301
Front
Sxxxxxxx
Rear
<< L1-SUS-YC1

## Slide 551: D1100301-Sxxxxxxx
Transmon Coil Driver Chassis
D1100301
±18VDC
Sxxxxxxx
D1100301
Front
Sxxxxxxx
Rear
<< L1-SUS-YC1

## Slide 552: D0902783-S1200819
Anti-Alias Chassis (8*DB9)
D0902783
±18@0.5A
S1200819
IN 1-4
IN 1-4
IN 17-20
IN 17-20
IN 5-8
IN 5-8
IN 9-12
IN 9-12
IN 13-16
IN 13-16
IN 21-24
IN 21-24
IN 25-28
IN 25-28
IN 29-32
IN 29-32
D0902783
Front
To ADC
To ADC Adapter
S1200819
Rear
<< L1-SUS-YC1

## Slide 553: D1000305 - S1001201
Anti-Image Chassis (4*DB9)
D1000305
±18@1A
S1001201
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
D1000305
Front
From DAC Adapter 0
From DAC Adapter 0
From DAC Adapter 1
From DAC Adapter 1
S1001201
Rear
<< L1-SUS-YC1

## Slide 554: D1000305 - S1105312
Anti-Image Chassis (4*DB9)
D1000305
±18@1A
S1105312
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
D1000305
Front
From DAC Adapter 0
From DAC Adapter 0
From DAC Adapter 1
From DAC Adapter 1
S1105312
Rear
<< L1-SUS-YC1

## Slide 555: D1100815 - S1103827
Anti-Image Chassis (2*DB15, 1*DB9)
D1100815
±18@1A
S1103827
From DAC Adapter 0
From DAC Adapter 0
From DAC Adapter 1
From DAC Adapter 1
S1103827
Rear
D1100815
Front
IN 13-16
IN 13-16
IN 7-12
IN 7-12
IN 1-6
IN 1-6
D1100815 is an AI, which means it has OUTPUTS, not INPUTS. The labels are incorrect.
<< L1-SUS-YC1

## Slide 556: D1100809-S1104075
Anti-Alias Chassis (2*DB15, 5*DB9)
D1100809
±18@0.5A
S1104075
IN 17-20
IN 17-20
IN 21-24
IN 21-24
IN 25-28
IN 25-28
IN 29-32
IN 29-32
D1100809
Front
To ADC
To ADC Adapter
S1104075
Rear
IN 13-16
IN 13-16
IN 7-12
IN 7-12
IN 1-6
IN 1-6
<< L1-SUS-YC1

## Slide 557: D1001270-S1106211
Binary Output Chassis (4*DB9, 2*DB37)
D1001270
±18VDC
S1106211
S1106211
Rear
Ch 0-31
Ch 0-31
Ch 32-63
Ch 32-63
D1001270
Front
Ch 0-7
Ch 0-7
Ch 8-15
Ch 8-15
Ch 16-23
Ch 16-23
Ch 24-31
Ch 24-31
Ch 32-47
Ch 32-47
Ch 48-63
Ch 48-63
<< L1-SUS-YC1

## Slide 558: D1001269-S1106114
Binary Input Chassis (4*DB9, 2*DB37)
D1001270
±18VDC
S1106114
S1106114
Rear
Ch 0-31
Ch 0-31
Ch 32-63
Ch 32-63
Ch 0-7
Ch 0-7
Ch 8-15
Ch 8-15
Ch 16-23
Ch 16-23
Ch 24-31
Ch 24-31
Ch 32-47
Ch 32-47
Ch 48-63
Ch 48-63
D1001270
Front
<< L1-SUS-YC1

## Slide 559: D1002593-S1103224
Binary Output Chassis (8*DB9)
D1002593
±18VDC
S1103224
S1103224
Rear
Ch 0-31
Ch 0-31
Ch 32-63
Ch 32-63
D1002593
Front
Ch 0-7
Ch 0-7
Ch 8-15
Ch 8-15
Ch 16-23
Ch 16-23
Ch 24-31
Ch 24-31
Ch 32-39
Ch 32-39
Ch 40-47
Ch 40-47
Ch 48-55
Ch 48-55
Ch 56-63
Ch 56-63
<< L1-SUS-YC1

## Slide 560: D1001726-S1103897
Binary Input Chassis (8*DB9)
D1001726
±18VDC
S1103897
S1103897
Rear
Ch 0-31
Ch 0-31
Ch 32-63
Ch 32-63
Ch 0-7
Ch 0-7
Ch 8-15
Ch 8-15
Ch 16-23
Ch 16-23
Ch 24-31
Ch 24-31
Ch 32-39
Ch 32-39
Ch 40-47
Ch 40-47
Ch 48-55
Ch 48-55
Ch 56-63
Ch 56-63
D1001726
Front
<< L1-SUS-YC1

## Slide 561: L1-SUS-YC2
SUS Anti-Alias Chassis
D1000721
±18VDC
S1201104
SUS Anti-Alias Chassis
D1000721
±18VDC
S1200931
SUS Anti-Alias Chassis
D1000721
±18VDC
S1201129
SUS Anti-Alias Chassis
D1000721
±18VDC
S1201128
PSY-036
PSO-043
L1-SUS-YC1 (ETM) Y-End Remote Rack 1 (of 2) Layout (D1201090) (S1202954)
l1susey I/O Extension Chassis
D1001715
+24V@5A
S1201775
l1susauxey I/O Extension Chassis
D1001715
+24V@5A
S1201776
<< CERY Racks
PSY-036

## Slide 562: D1000721-S1201129
SUS Anti-Alias Chassis
D1000721
±18@0.5A
S1201129
IN 1-4
Open
IN 5-8
Open
D1000721
Front
IN 9-20
Open
IN 21-32
Open
To DAC Adapter
Open
S1201129
Rear
<< L1-SUS-YC2

## Slide 563: D1000721-S1201128
SUS Anti-Alias Chassis
D1000721
±18@0.5A
S1201128
IN 1-4
Open
IN 5-8
Open
D1000721
Front
IN 9-20
Open
IN 21-32
Open
To DAC Adapter
Open
S1201128
Rear
<< L1-SUS-YC2

## Slide 564: D1000721-S1201104
SUS Anti-Alias Chassis
D1000721
±18@0.5A
S1201104
IN 1-4
Open
IN 5-8
Open
D1000721
Front
IN 9-20
Open
IN 21-32
Open
To DAC Adapter
Open
S1201104
Rear
<< L1-SUS-YC2

## Slide 565: D1000721-S1200931
SUS Anti-Alias Chassis
D1000721
±18@0.5A
S1200931
IN 1-4
Open
IN 5-8
Open
D1000721
Front
IN 9-20
Open
IN 21-32
Open
To DAC Adapter
Open
S1200931
Rear
<< L1-SUS-YC2

## Slide 566: l1susauxey - D1001715 – S1201776
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1201776
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
D1001421
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1susauxey I/O Extension Chassis
D1001715
110VAC
S1201776
To UPS Power Strip
l1susauxey – I/O Extender
<< L1-SUS-YC2

## Slide 567: l1susey - D1001715 – S1201775
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
24 VDC
S1201775
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
D1001421
Slot P1
Open
Slot P2
Open
Slot P3
Open
Slot P4
Open
Slot P5
Open
Slot P6
Open
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
l1susey I/O Extension Chassis
D1001715
110VAC
S1201775
To UPS Power Strip
l1susey – I/O Extender
<< L1-SUS-YC2

## Slide 568: L1-TCS-YC1
<< CERY Racks
Ring Heater Driver
D1003254
+/-18VDC
SN:
Hartmann Sensor Power Supply
D1102206
+/-18VDC
SN:
TCS Rack Layout (D1201130) (S1202981)
TCS-YC1 is part of D1200258
BNC AA Interface Chassis (PEM)
D1001421
+/-18VDC
S1001058
Accelerometer Power Supply
Isotron 2973
110VAC
SN:
Timing Comparator
D1001370
+12VDC
S1201889
Timing Master (Fanout)
D070011
+12VDC
S1000878
Shelf
Shelf
TCS-YC1 is part of E1100894

## Slide 569: D070011 – S1000878
Timing Master (Fanout)
D070011
+12VDC
S1000878
D070011
Front
S1000878
Rear
x
x
x
<< L1-TCS-YC1

## Slide 570: D1001370 – S1201889
D1001370
Front
S1201889
Rear
Timing Comparator
D1001370
+12VDC
S1201889
<< L1-TCS-YC1

## Slide 571: D1102206 – Sxxxxxxx
D1102206
Front
Sxxxxxxx
Rear
Hartmann Sensor Power Supply
D1102206
+12VDC
Sxxxxxxx
<< L1-TCS-YC1

## Slide 572: Isotron 2793 - AH66
AH66
Rear
Isotron 2973
Front
ACCX
ACCY
ACCZ
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
Unused
ACCZ
ACCY
ACCX
Accelerometer Power Supply
Isotron 2973
110VAC
AH66
<< L1-TCS-YC1

## Slide 573: D1001421 – S1001058
D1001421
Front
BNC AA Interface Chassis (PEM)
D1001421
+/-18VDC
S1001058
MAG X
1
MAG Y
2
MAG Z
3
1
4
2
5
3
6
Isotron 1
7
Isotron 2
8
Isotron 3
9
BSC5 MIC
10
Unused
11
BSC5 TEMP
12
Unused
13
Unused
14
Unused
15
Unused
16
Unused
17
Unused
18
Unused
19
Unused
20
Unused
21
Unused
22
Unused
23
Unused
24
Unused
25
Unused
26
Unused
27
Unused
28
Unused
29
Unused
30
Unused
31
Unused
32
S1001058
Rear
To ADC Adapter
To l1pemey Slot P1
To ADC Adapter
<< L1-TCS-YC1

## Slide 574: D1101363 - Sxxxxxxx
SN:
Rear
D1101363
Front
aLIGO Accelerometer Interface Chassis
D1101363
Power
SN:
Unused
1
Unused
1
Unused
2
Unused
2
Unused
3
Unused
3
Unused
4
Unused
4
Unused
5
Unused
5
Unused
6
Unused
6
Unused
7
Unused
7
Unused
8
Unused
8
Unused
9
Unused
9
Unused
10
Unused
10
Unused
11
Unused
11
Unused
12
Unused
12
Unused
13
Unused
13
Unused
14
Unused
14
Unused
15
Unused
15
Unused
16
Unused
16
OUTPUT
INPUT
<< L1-TCS-YC1

## Slide 575: L1-ISC-YR1
RF Distribution Panel 24
Dxxxxxxx
No Power
SN:
24.5 MHz Delay Line Phase Shifter
D0900128
±18V
S1103430
+12VDC 1A
-12VDC 1A
+18VDC 10A
-18VDC 10A
+24VDC 4A
-24VDC 1A
High Voltage ?A
RF Distribution Panel 25
Dxxxxxxx
No Power
SN:
2 Channel RFPD I/Q Demod (RC & ALS)
D1000181
±18V
S1000786
Demodulator RF Patch Panel
D1100905
No Power
Sxxxxxxx
79.4 MHz VCO (ALS)
D0900605
±18V
S1200578
39.7 MHz Frequency Divider
D1002182
±18V
S1000753
RF Preamplifier
D1201294
±18V
Sxxxxxxx
39.7 MHz 2 Channel Phase/Freq Discriminator
D1002476
±18V
S1000768
Common Mode Servo (ALS Laser Locking)
D0901781
±18V
S1102646
Common Mode Servo (ALS Cavity Locking)
D0901781
±18V
S1102647
LSC Demod Concentrator 5
D1100691
±18V
S1104010
ASC Demod Concentrator 6
D1100696
±18V
S1103989
Auxiliary Signals Concentrator 2
D1102045
±18V
Sxxxxxxx
Auxiliary Signals Concentrator 1
D1102065
±18V
Sxxxxxxx
Auxiliary Signals Concentrator 5
D1102065
±18V
Sxxxxxxx
iLIGO LSC PD Interface (4 Channel)
D0901833
±18V
Sxxxxxxx
Differential to Single-Ended Converter
D1100482
±18V
Sxxxxxxx
Dual QPD Transimpedance Amplifier
D1002481
±18V
Sxxxxxxx
Dual QPD Transimpedance Amplifier
D1002481
±18V
Sxxxxxxx
ISC Whitening Chassis
D1002559
±18V
Sxxxxxxx
ISC Whitening Chassis
D1002559
±18V
Sxxxxxxx
<< VEAY Racks
L1-ISC-YR1 Y-End Station Field Rack Layout (D1201094) (S1202958)
PSY-013
PSY-016
PSO-001
Sequencer
D1200757
S1202552
ISC-YR1 is part of D1001423

## Slide 576: L1-SUS-YR1
+18VDC ?A
-18VDC ?A
+24VDC ?A
<< VEAY Racks
PSY-013
PSY-016
PSO-001
L1-SUS-YR1 Y-End Station Field Rack Layout (D1201132) (S1202994)
Electrostatic Driver
+-18VDC@0.4A
+-430VDC@15mA
E3074
SN:

## Slide 577: E3074
E3074
Front
S???????
Rear
<< L1-SUS-YR1
Electrostatic Driver
+-18VDC@0.4A
+-430VDC@15mA
E3074
SN:

## Slide 578: L1-VAC-YR1
<< VEAY Racks
L1-VAC-YR1 Y-End Vacuum Rack Layout (Dxxxxxxx)

## Slide 579: LLO ETR - Electronics Test Rack Layout
BSC (aka QUAD) Test Rack
(L1-ETR-02)
RMS (aka Triple) Test Rack
(L1-ETR-04)
DAQ (aka CDS) Test Rack
(L1-ETR-01)
Optics
Test Rack
(L1-ETR-03)
HAM ISI
Test Rack
(L1-ETR-05)
STS Huddle
Test Rack
(L1-ETR-06)
Future
Test Rack
(L1-ETR-08)
Future
Test Rack
(L1-ETR-09)
Triple SUS
Test Rack
(L1-ETR-07)
<< LLO Racks by AREA
<< LLO CDS Components
<< LLO Corner Station

## Slide 580: L1-ETR-01
+18VDC ?A
-18VDC ?A
+24VDC ?A
-24VDC ?A
DAQ (aka CDS) Test Rack Layout (LIGO-D1002448)
Anti-Alias Chassis
D070081
±18@0.5A
SN:
AI module
AA module
AI module
I/O Expansion
Chassis (dtsfe3-xp)
DC Power Supply
I/O Expansion
Chassis (dtsfe0-xp)
I/O Expansion
Chassis (dtsfe1-xp)
I/O Expansion
Chassis (dtsfe2-xp)
DC Power Supply
L1 DTS - IO
<< Electronics Test Racks
D070124 Rack Input
Power Box (RU 34-36)

## Slide 581: L1-ETR01 DAQ (aka CDS)
Front
L1-ETR01
Rear
L1-ETR01
I/O Extension
2 ADC
1 DAC
1 Timing Slave
Linksys BEFSX41
Firewall Router
D070011 Fanout Timing
D070011 Fanout Timing
SN:
SN:
JQE25-10M +15V
JQE25-10M -15V
SN:
SN:
JQE25-10M +24V
JQE25-10M -24V
Netgear GS724T Switch
SN:
SUN Microsystems X2200
0923QAT00D dtsserver 192.168.100.10
SuperMicro
… dtsfe1 192.168.100.15
D070081 AI Chassis
D070081 AA Chassis
D070081 SYYYYYYYY
D070081 SYYYYYYYY
SuperMicro
… dtsdco 192.168.100.30
SuperMicro
… dtsfwo 192.168.100.31
SuperMicro
… dtsndso 192.168.100.32
Shelf
Shelf
KVM
SN:
Linier Rack – has front and rear doors and wheels.
DC Bus Distribution Box
Netgear GSM7352S Switch
SN:
LIGO-Dxxxxxx-V1

## Slide 582: L1-ETR-02
+18VDC ?A
-18VDC ?A
+24VDC ?A
-24VDC ?A
BSC (aka QUAD) Test Rack Layout (LIGO-D080273)
D070124 Rack Input
Power Box (RU 34-36)
<< Electronics Test Racks

## Slide 583: L1-ETR02 BSC (aka Quad)
Front
L1-ETR02
Rear
L1-ETR02
I/O Extension
2 ADC
1 DAC
1 Timing Slave
Linksys BEFSX41
Firewall Router
Netgear GS108
Gigabit Switch
Computer
SN:
iMAC Computer
SN:
SN:
JQE25-10M +15V
JQE25-10M -15V
Satellite Amplifier
Satellite Amplifier
Satellite Amplifier
Satellite Amplifier
Satellite Amplifier
LIGO-D080273-V1
DC Bus Distribution Box

## Slide 584: L1-ETR-03
+18VDC ?A
-18VDC ?A
+24VDC ?A
-24VDC ?A
Optics Test Rack Layout (LIGO-Dxxxxxxx)
D070124 Rack Input
Power Box (RU 34-36)
<< Electronics Test Racks

## Slide 585: L1-ETR03 OPTICS
Front
L1-ETR03
Rear
L1-ETR03
I/O Extension
2 ADC
1 DAC
1 Timing Slave
Linksys BEFSX41
Firewall Router
Netgear GS108
Gigabit Switch
Computer
SN:
iMAC Computer
LIGO-Dxxxxxx-V1

## Slide 586: L1-ETR-04
+18VDC ?A
-18VDC ?A
+24VDC ?A
-24VDC ?A
RMS (aka Triple) Test Rack Layout (LIGO-Dxxxxxxx)
D070124 Rack Input
Power Box (RU 34-36)
<< Electronics Test Racks

## Slide 587: L1-ETR04 RMT (aka Triple)
Front
L1-ETR04
Rear
L1-ETR04
I/O Extension
2 ADC
1 DAC
1 Timing Slave
Linksys BEFSX41
Firewall Router
Netgear GS108
Gigabit Switch
Computer
SN:
iMAC Computer
D1000305 AI Chassis
D0902783 AA Chassis
D1000305 SYYYYYYYY
D0902783 SYYYYYYYY
D0902783 AA Chassis
D0902783 SYYYYYYYY
LIGO-D080446-V1
DC Bus Distribution Box

## Slide 588: L1-ETR-05
+18VDC ?A
-18VDC ?A
+24VDC ?A
-24VDC ?A
HAM ISI Test Rack Layout (LIGO-D1001412)
D070124 Rack Input
Power Box (RU 34-36)
<< Electronics Test Racks

## Slide 589: L1-ETR05 HAM ISI
Front
L1-ETR05
Rear
L1-ETR05
I/O Extension
2 ADC
1 DAC
1 Timing Slave
SN:
SN:
JQE25-10M +15V
JQE25-10M -15V
SN:
SN:
JQE25-10M +24V
JQE25-10M -24V
ISI Interface Pod 1 & L4C
ISI Interface Pod 2 & L4C
ISI Interface Pod 3 & L4C
Linksys BEFSX41
Firewall Router
Netgear GS108
Gigabit Switch
Computer
Anti-Image (AI) Chassis
Anti-Alias (AA) Chassis
Anti-Alias (AA) Chassis
D1000269 S1000298
D1000269 S1000244
SN:
iMAC Computer
ISI Coil Driver (Pod 1 and 2)
ISI Coil Driver (Pod 3)
D1000067 S1000311
D1000067 S1000312
D1000067 S1000314
D0902744 S1000317
D0902744 S1000316
LIGO-D1001412-V1
DC Bus Distribution Box
D070081 SS1000251
SN:

## Slide 590: L1-ETR-06
+18VDC ?A
-18VDC ?A
+24VDC ?A
-24VDC ?A
STS Huddle Test Rack Layout (LIGO-D1001412)
Shelf
Shelf
HAM ISI Anti-Alias Chassis
D1000269
±18@0.5A
S1000248
HAM ISI Anti-Alias Chassis
D1000269
±18@0.5A
S1000248
Anti-Image Chassis
D070081
±18@0.5A
S1000249
HAM ISI Interface Chassis
D1000067
±18@1A
S1000315
HAM ISI Interface Chassis
D1000067
±18@1A
S1000313
DC Power Supply
Sorenson 33-33
120VAC
SN:
DC Power Supply
Sorenson 33-33
120VAC
SN:
0 – ADC0
1 – DAC0
2 – ADC1
Workstation
SN:0923QAT004
Computer SunFire X2200
120VAC
Front End CPU
SN:
Computer
120VAC
I/O Extension Chassis
D1001715
+24@5A
SN:
D070124 Rack Input
Power Box (RU 34-36)
RVS4000
CISCO Router
Fiber Optics Patch
<< Electronics Test Racks

## Slide 591: L1:ETR06 STS Huddle
Front
L1-ETR06
Rear
L1-ETR06
SN:
SN:
JQE25-10M +15V
JQE25-10M -15V
ISI Interface Pod 1 & L4C
ISI Interface Pod 2 & L4C
ISI Interface Pod 3 & L4C
Linksys BEFSX41
Firewall Router
Netgear GS108
Gigabit Switch
D0902783 AA Chassis
D0902783 AA Chassis
D0902783 SYYYYYYYY
D0902783 SYYYYYYYY
iMAC Computer
DXXXXXXXX SYYYYYYYY
DXXXXXXXX SYYYYYYYY
DXXXXXXXX SYYYYYYYY
LIGO-D1001412-V1
I/O Extension
2 ADC
1 DAC
1 Timing Slave
Computer
SN:
DC Bus Distribution Box

## Slide 592: L1-ETR-07
Triple SUS Test Rack Layout (D1001624 S1106460)
KEPCO JQE20-10M
KEPCO JQE20-10M
120VAC@5.3A
120VAC@5.3A
I/O Extension Chassis
D1001715
120VAC
S1106560
SUS Coil Driver – L1, L2
D060278
±18@0.5A
S1000516
Anti-Image Chassis
D070081
±18@0.5A
S1000514
Workstation
SN:
Computer
120VAC
SUS Satellite Amplifier - TOP
D080276
±18@0.5A
S1000508
SUS Satellite Amplifier – L1, L2
D080276
±18@0.5A
S1000511
SUS Anti-Alias Chassis
D1000721
±18@0.5A
S1000519
SUS Anti-Alias Chassis
D070081
±18@0.5A
S1000505
0 – ADC0
1 – DAC0
2 – ADC1
Front End CPU
SN:
Computer
120VAC
SUS Coil Driver - TOP
D060278
±18@0.5A
S1000515
RVS4000
CISCO Router
D070124 Rack Input
Power Box (RU 34-36)
Fiber Optics Patch
<< Electronics Test Racks
Shelf

## Slide 593: D080276-S1000508
SUS Satellite Amplifier - TOP
D080276
±18@0.5A
S1000508
D080276
Front
S1000508
Rear
TS-15
Coil Drive In
TS-1
PD Out
Open
PD Mon
TS-2
LED Mon
TS-16
Coil Drive In
TS-3
PD Out
Open
PD Mon
TS-4
LED Mon
Chan 5-8
Chan 1-4
Open
Chan 5-8
Open
Chan 1-4
Coil Drive In
PD Out
PD Mon
LED Mon
Channels 1-4
Coil Drive In
PD Out
PD Mon
LED Mon
Channels 5-8
UM (Top)
<< L1-ETR-07

## Slide 594: D080276-S1000511
SUS Satellite Amplifier – L1, L2
D080276
±18@0.5A
S1000511
D080276
Front
S1000511
Rear
Chan 5-8
Chan 1-4
Coil Drive In
PD Out
PD Mon
LED Mon
Channels 1-4
Coil Drive In
PD Out
PD Mon
LED Mon
Channels 5-8
Open
Chan 5-8
Open
Chan 1-4
IM (L1), BM (L2)
<< L1-ETR-07
TS-17
Coil Drive In
TS-8
PD Out
Open
PD Mon
TS-9
LED Mon
TS-18
Coil Drive In
TS-10
PD Out
Open
PD Mon
TS-11
LED Mon

## Slide 595: D070081-S1000514
Anti-Image Chassis
D070081
±18@0.5A
S1000514
D070081
Front
S1000514
Rear
From DAC Adapter
TS-24
From DAC Adapter
TS-6
OUT 1-4
TS-7
OUT 5-8
TS-13
OUT 9-12
TS-14
OUT 13-16
UNBUFFERED
OUT 1-4
OUT 5-8
OUT 9-12
OUT 13-16
<< L1-ETR-07

## Slide 596: D060278-S1000515
SUS Coil Driver - TOP
D060278
±18@0.5A
S1000515
D060278
Front
S1000515
Rear
TS-6
Ch1-4 IN
TS-7
CH5-8 IN
TS-16
Ch 5-8 Out
TS-15
Ch 1-4 Out
Ch 5-8 Out
Ch 1-4 Out
Out Monitors
Out Monitors
TS-5
Ch1-4 IN
Ch5-8 IN
Run/Acq 1-4
Run/Acq 5-8
Enable 1-4
Enable 5-8
Open
Run/Acq 1-4
Open
Enable 1-4
Open
Run/Acq 5-8
Open
Enable 5-8
UM (Top)
<< L1-ETR-07

## Slide 597: D060278-S1000516
SUS Coil Driver – L1, L2
D060278
±18@0.5A
S1000516
D060278
Front
S1000516
Rear
TS-18
Ch 5-8 Out
TS-17
Ch 1-4 Out
TS-12
Out Monitors
TS-13
Ch1-4 IN
TS-14
CH5-8 IN
Ch1-4 IN
Ch5-8 IN
Run/Acq 1-4
Run/Acq 5-8
Enable 1-4
Enable 5-8
Ch 5-8 Out
Ch 1-4 Out
Out Monitors
IM (L1), BM (L2)
<< L1-ETR-07
Open
Run/Acq 1-4
Open
Enable 1-4
Open
Run/Acq 5-8
Open
Enable 5-8

## Slide 598: D070081-S1000505
D070081
Front
S1000505
Rear
SUS Anti-Alias Chassis
D070081
±18@0.5A
S1000505
TS-1
IN 1-4
TS-8
IN 17-20
TS-3
IN 5-8
TS-2
IN 9-12
TS-4
IN 13-16
TS-10
IN 21-24
TS-9
IN 25-28
TS-11
IN 29-32
To ADC Adapter
TS-23
To ADC Adapter
IN 1-4
IN 5-8
IN 9-12
IN 13-16
IN 17-20
IN 21-24
IN 25-28
IN 29-32
D0902783
Front
<< L1-ETR-07

## Slide 599: D1000721-S1000519
SUS Anti-Alias Chassis
D1000721
±18@0.5A
S1000519
<< L1-ETR-07
IN 1-4
Open
IN 5-8
Open
D1000721
Front
IN 9-20
TS-5
IN 21-32
TS-12
To DAC Adapter
TS-25
S1000519
Rear

## Slide 600: lxxxxxx - D1001715-S1106560
lxxxxxx I/O Extension Chassis
D1001715
24 VDC
S1106560
D1001715
Front
Timing Slot
Slot P7
Slot P5
Slot E2
Slot E1
Slot P1
Slot E3
Slot P3
Slot P2
Slot P4
Slot P6
Slot P9
Slot P8
Uplink
Slot P10
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
ADC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
DAC Adapter
Sxxxxxxx
24 VDC
S1106560
Rear
Open
Uplink
Open
Slot E1
Open
Slot E2
Open
Slot E3
Open
Slot P1
Open
Slot P2
Open
Slot P3
TS-23
Slot P4
TS-25
Slot P5
Open
Slot P6
TS-24
Slot P7
Open
Slot P8
Open
Slot P9
Open
Slot P10
P1
P2
P3
P4
P5
P6
P7
P8
P9
P10
E1
E2
E3
<< L1-ETR-07
lxxxxxx – I/O Extender

## Slide 601: Templates
Templates

## Slide 602: Rack Template
D070124 Rack Input
Power Box (RU 34-36)

## Slide 603: Rack Template
Description
Dxxxxxxx
Power
SN:
Description
Dxxxxxxx
Power
SN:
Description
Dxxxxxxx
Power
SN:
Description
Dxxxxxxx
Power
SN:
Description
Dxxxxxxx
Power
SN:
Description
Dxxxxxxx
Power
SN:
Description
Dxxxxxxx
Power
SN:
-
-
-
-
Description
Dxxxxxxx
Power
SN:
Power
SN:
Dxxxxxxx
Description
Description
Dxxxxxxx
Power
SN:
Shelf
Description
Dxxxxxxx
Power
SN:
Description
Dxxxxxxx
Power
SN:

## Slide 604: Connectors - bmp
DA-15
DB-25
DC-37
DD-50
DE-9
SCSI-68
Conec
3W3S
3W3P
CP-4
LEMO 4-Pin
LEMO 2-Pin
BNC

## Slide 605: Connectors - bmp
Conec
3W3S
3W3P
CP-4
LEMO 4-Pin
LEMO 2-Pin
2W2CS
2W2CP
3W3CS
3W3CP

## Slide 606: +V –V Layouts
Power
+V .
-V .
+14 .
-14 .
Coil Driver Inputs

## Slide 607: +V –V Layouts
Slot P7
ADC Adapter
Sxxxxxxx
Slot P7
DAC Adapter
Sxxxxxxx

## Slide 608: +V –V Layouts

## Slide 609: Security Cameras Layout
24VAC Power To Camera
Signals To Camera
75 Ohm Signal from Camera
A1 = Black
A2 = White(Y) Red(X)
1 =
2 =
3 =
4 =
5 =
6 =
7 =
8 =
9 =
50 Ohm Bullet?
Transformer
110VAC
24VAC
Interface
12VDC
Type N

## Slide 610: Fiber Optics Connector Types

## Slide 611: How Rack Documents Relate
S# of Rack
E1200331
D# of Rack
D1200881
S# of Chassis
S# of Chassis
S# of Chassis
D# of Chassis
D# of Chassis
D# of Chassis
Related to
Related to
Related to
Related to
Related to
Related to
Related to
Related to
Related to