### E060178-00-D

AOS Pick Off Beam Suspension and ETM Telescope Suspension Requirements

Proposal to AOS from SUS on two Advanced LIGO Suspensions

C. Torrie and J. Romie

September 10, 2004

## Updated March 29, 2006

Updated June 14, 2006

Suspension requirements derived from conversation with Mike Smith on Wednesday, September 8, 2004.

| Requirement/Assumptions | AdLIGO Pick-Off SUS | ETM Telescope SUS | comment |
| --- | --- | --- | --- |
| Component size | 350mm dia x 60mm thick (= BS) | 200mm x 750mm long cylinder | Components costed by AOS |
| Component mass | 12.7 kg | 13.6 kg |  |
| Isolation | Double pendulum | Double pendulum | No blade springs |
| Beam height | -150mm | -80.5mm =(ETMx1) -87.68 (=ETMy1) | w.r.t. LIGO global coordinate system Ref: T010076, D. Coyne |
| Structure length | 2005mm + 70mm = 2075 mm [81.7” = 6.8’] | 2005mm [78.9”=6.6’] | 70 mm = BS beam height –150mm global - minus ETMx beam height. |
| Length restrictions | Beam underneath |  |  |
| Chamber | BSC, w/ beamsplitters | BSC, w/ ETMs |  |
| Local Damping | Yes | Yes | Damping in pitch, yaw, longitudinal & transverse |
| DC bias/pointing | Pitch and yaw, at upper mass | Pitch and yaw, at upper mass |  |
| Course pointing | Pitch and yaw, at upper mass | Pitch and yaw, at upper mass | For alignment |
| Structure resonance | Same as ETM | Same as ETM | Assume stiff upper structure and lightweight catcher/stop assembly |
| Prototypes | No | No | 1st article only |
| Fibers /music wire | Music wire | Music wire |  |
| Quantity | 1/IFO = 3 total | 2/IFO – 6 total |  |