LIGO Laboratory / LIGO Scientific Collaboration

LIGO-T020210-00-D	LIGO	20 October 2002

System Dynamics Model of the External Pre-Isolator (EPI) for the Horizontal Access Module (HAM)

Dennis Coyne

Distribution of this document:

LIGO Science Collaboration

This is an internal working note

of the LIGO Project.

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW17-161 175 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 1970 Mail Stop S9-02 Richland WA 99352 Phone 509-372-8106 Fax 509-372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone 225-686-3100 Fax 225-686-7189 |

http://www.ligo.caltech.edu/

# Introduction

This is an incomplete draft of a technical memo on the electro-Magnetic External Pre-Isolator (MEPI) system. MEPI is similar in dynamics to the Hydraulic EPI (HEPI) system.

# Geometry

## CAD

## Finite Element Model (FEM)

# Mass Properties

## MEPI Assembly

The MEPI assembly with just the stationary components is shown in Figure X. The mass properties for the MEPI assembly is given in Table X. The spring density was set to be ½ of steel to approximate the fact that not all of the mass of the spring participates in the quasi-rigid body modes.

Mass properties of EM_assy_stationary_parts_R Output coordinate System : MEPI Assy Coordinate System Mass = 109.4561 kilograms Volume = 0.0155 cubic meters Surface area = 1.8894 square meters Center of mass: ( meters ) X = -0.0133 Y = -0.0263 Z = -0.1731 Principal axes of inertia and principal moments of inertia: ( kilograms * square meters ) Taken at the center of mass. Ix = (-0.0658, -0.1325, 0.9890) Px = 1.8728 Iy = (0.9966, -0.0569, 0.0587) Py = 2.4448 Iz = (0.0485, 0.9896, 0.1358) Pz = 2.4821 Moments of inertia: ( kilograms * square meters ) Taken at the center of mass and aligned with the output coordinate system. Lxx = 2.4424 Lxy = 0.0032 Lxz = -0.0375 Lyx = 0.0032 Lyy = 2.4713 Lyz = -0.0799 Lzx = -0.0375 Lzy = -0.0799 Lzz = 1.8860 Moments of inertia: ( kilograms * square meters ) Taken at the output coordinate system. Ixx = 5.7993 Ixy = 0.0413 Ixz = 0.2138 Iyx = 0.0413 Iyy = 5.7718 Iyz = 0.4182 Izx = 0.2138 Izy = 0.4182 Izz = 1.9809

## MEPI and Support Structure Assembly

Mass properties of HAM_support_assy Output coordinate System : HAM support structure coord sys Mass = 1122.550 kilograms Volume = 0.196 cubic meters Surface area = 30.285 square meters Center of mass: ( meters ) X = 0.000 Y = 0.000 Z = -0.107 Principal axes of inertia and principal moments of inertia: ( kilograms * square meters ) Taken at the center of mass. Ix = (0.002, -1.000, 0.000) Px = 907.574 Iy = (1.000, 0.002, 0.000) Py = 1488.929 Iz = (0.000, 0.000, 1.000) Pz = 2347.401 Moments of inertia: ( kilograms * square meters ) Taken at the center of mass and aligned with the output coordinate system. Lxx = 1488.927 Lxy = -1.105 Lxz = -0.000 Lyx = -1.105 Lyy = 907.576 Lyz = -0.000 Lzx = -0.000 Lzy = -0.000 Lzz = 2347.401 Moments of inertia: ( kilograms * square meters ) Taken at the output coordinate system. Ixx = 1501.707 Ixy = -1.105 Ixz = -0.000 Iyx = -1.105 Iyy = 920.357 Iyz = -0.000 Izx = -0.000 Izy = -0.000 Izz = 2347.401

## Stack

### Optics Table

The Optics Table coordinate system is parallel to global system and centered on the bottom face of the table, with Xtable = Xglobal, Ytable = Zglobal and Ztable = -Yglobal

Mass properties of HAM Optics Table Assy Output coordinate System : -- default -- Mass = 381.461 kilograms Volume = 0.138 cubic meters Surface area = 27.255 square meters Center of mass: ( meters ) X = -0.000 Y = 0.208 Z = -0.000 Principal axes of inertia and principal moments of inertia: ( kilograms * square meters ) Taken at the center of mass. Ix = (1.000, -0.000, -0.002) Px = 105.142 Iy = (-0.002, 0.000, -1.000) Py = 128.132 Iz = (0.000, 1.000, 0.000) Pz = 219.975 Moments of inertia: ( kilograms * square meters ) Taken at the center of mass and aligned with the output coordinate system. Lxx = 105.142 Lxy = -0.010 Lxz = -0.050 Lyx = -0.010 Lyy = 219.975 Lyz = -0.008 Lzx = -0.050 Lzy = -0.008 Lzz = 128.132 Moments of inertia: ( kilograms * square meters ) Taken at the output coordinate system. Ixx = 121.638 Ixy = -0.026 Ixz = -0.050 Iyx = -0.026 Iyy = 219.975 Iyz = -0.023 Izx = -0.050 Izy = -0.023 Izz = 144.629

### Optics Table with Payload

Optics table with 50 counter-weights, each weighing 10 pounds, evenly distributed over the top of the optics table.

Mass properties of HAM Optics Table Mass Study Output coordinate System : -- default -- Mass = 609.105 kilograms Volume = 0.167 cubic meters Surface area = 29.840 square meters Center of mass: ( meters ) X = -0.000 Y = 0.263 Z = -0.000 Principal axes of inertia and principal moments of inertia: ( kilograms * square meters ) Taken at the center of mass. Ix = (1.000, -0.000, -0.001) Px = 162.249 Iy = (-0.001, 0.000, -1.000) Py = 202.247 Iz = (0.000, 1.000, 0.000) Pz = 344.997 Moments of inertia: ( kilograms * square meters ) Taken at the center of mass and aligned with the output coordinate system. Lxx = 162.249 Lxy = -0.005 Lxz = -0.050 Lyx = -0.005 Lyy = 344.997 Lyz = -0.005 Lzx = -0.050 Lzy = -0.005 Lzz = 202.247 Moments of inertia: ( kilograms * square meters ) Taken at the output coordinate system. Ixx = 204.348 Ixy = -0.026 Ixz = -0.050 Iyx = -0.026 Iyy = 344.997 Iyz = -0.023 Izx = -0.050 Izy = -0.023 Izz = 244.346

### Isolation Leg Element 1

Coordinate system is centered on the lower face of the cylindrical mass.

Mass properties of legelement1-coil Output coordinate System : -- default -- Density = 8027.17 kilograms per cubic meter Mass = 179.42 kilograms Volume = 0.02 cubic meters Surface area = 0.60 square meters Center of mass: ( meters ) X = 0.00 Y = 0.06 Z = 0.00 Principal axes of inertia and principal moments of inertia: ( kilograms * square meters ) Taken at the center of mass. Ix = (0.00, 0.00, 1.00) Px = 2.97 Iy = (1.00, 0.00, 0.00) Py = 2.97 Iz = (0.00, 1.00, 0.00) Pz = 5.53 Moments of inertia: ( kilograms * square meters ) Taken at the center of mass and aligned with the output coordinate system. Lxx = 2.97 Lxy = 0.00 Lxz = 0.00 Lyx = 0.00 Lyy = 5.53 Lyz = 0.00 Lzx = 0.00 Lzy = 0.00 Lzz = 2.97 Moments of inertia: ( kilograms * square meters ) Taken at the output coordinate system. Ixx = 3.58 Ixy = 0.00 Ixz = 0.00 Iyx = 0.00 Iyy = 5.53 Iyz = 0.00 Izx = 0.00 Izy = 0.00 Izz = 3.58

### Isolation Leg Element 2

Coordinate system is centered on the lower face of the cylindrical mass.

Mass properties of legelement2-coil Output coordinate System : -- default -- Density = 8027.17 kilograms per cubic meter Mass = 106.52 kilograms Volume = 0.01 cubic meters Surface area = 0.51 square meters Center of mass: ( meters ) X = 0.00 Y = 0.03 Z = 0.00 Principal axes of inertia and principal moments of inertia: ( kilograms * square meters ) Taken at the center of mass. Ix = (0.00, 0.00, 1.00) Px = 1.69 Iy = (1.00, 0.00, 0.00) Py = 1.69 Iz = (0.00, 1.00, 0.00) Pz = 3.29 Moments of inertia: ( kilograms * square meters ) Taken at the center of mass and aligned with the output coordinate system. Lxx = 1.69 Lxy = 0.00 Lxz = 0.00 Lyx = 0.00 Lyy = 3.29 Lyz = 0.00 Lzx = 0.00 Lzy = 0.00 Lzz = 1.69 Moments of inertia: ( kilograms * square meters ) Taken at the output coordinate system. Ixx = 1.81 Ixy = 0.00 Ixz = 0.00 Iyx = 0.00 Iyy = 3.29 Iyz = 0.00 Izx = 0.00 Izy = 0.00 Izz = 1.81

### Isolation Stack Assembly

The coordinate system for the assembly is parallel to the global axes and centered on the top of the support table.

Mass properties of HAM-top-stack-with-coil springs Output coordinate System : HAM Stack Coordinate System Mass = 1558.153 kilograms Volume = 0.301 cubic meters Surface area = 34.728 square meters Center of mass: ( meters ) X = -0.000 Y = 0.000 Z = 0.280 Principal axes of inertia and principal moments of inertia: ( kilograms * square meters ) Taken at the center of mass. Ix = (-0.001, -1.000, -0.000) Px = 353.501 Iy = (1.000, -0.001, -0.000) Py = 412.440 Iz = (0.000, -0.000, 1.000) Pz = 638.121 Moments of inertia: ( kilograms * square meters ) Taken at the center of mass and aligned with the output coordinate system. Lxx = 412.440 Lxy = 0.050 Lxz = -0.034 Lyx = 0.050 Lyy = 353.501 Lyz = 0.030 Lzx = -0.034 Lzy = 0.030 Lzz = 638.121 Moments of inertia: ( kilograms * square meters ) Taken at the output coordinate system. Ixx = 534.355 Ixy = 0.050 Ixz = -0.057 Iyx = 0.050 Iyy = 475.416 Iyz = 0.049 Izx = -0.057 Izy = 0.049 Izz = 638.121

# Support Table Stiffness

# Joint Stiffness

# Spring Stiffness

# Static Compliance

With the entire stack weight added, the maximum static deflection is 7.85 mm (0.31 in) as shown in figure x. Note also in Figure X that elastic deflection of the cross beams contribute about 2 mm of the total vertical deflection, the balance being from the V-springs.

When the top of one spring is pulled up 1 mm, the resulting deflection pattern is shown in Figure X. The load redistribution is calculated to be as shown in the following Table.

# Modal Analysis

| Mode #, Frequency | Mode Shape |
| --- | --- |
| Mode 1 4.5 Hz translation in X, roll about Y |  |
| Mode 2 4.6 Hz Translation in Y, roll about X |  |
| Mode 3 7.2 Hz Yaw about Z |  |
| Mode 4 9.0 Hz Roll about Y |  |
| Mode 5 10.3 Hz Translation in Z (Heave) |  |
| Mode 6 13.8 Hz Vertical Crossbeam Bending and support table roll about X |  |
| Mode 7 20.2 Hz Symmetric horizontal crossbeam bending |  |
| Mode 8 20.2 Hz Anti-symmetric horizontal crossbeam bending |  |
| Mode 9 24.0 Hz Crossbeam bending and support table yaw about Z |  |
| Mode 10 24.7 Hz Crossbeam bending and support table bending |  |

# Transfer Functions

Force at N24 Z-direction, Displacement Response at N19 (same Pier)

Force at N24 Z-direction, Velocity Response at N19 (same Pier)

Force at N24 X-direction, Displacement Response at N19 (same Pier)

Force at N24 Y-direction, Displacement Response at N19 (same Pier)

Force at N24 Y-direction, Velocity Response at N19 (same Pier)