## Slide 1: Radiative Cooling Thermal Compensation for Gravitational Wave interferometer mirrors.
Justin C. Kampa, Hinata Kawamurab, Roberto Passaquietic, and Riccardo DeSalvod
a) Chalmers University of Technology, SE-412 96 Goteborg, Sweden
b) Yokoyama middle school, Sanda, Hachioji, Tokyo, 193-0832, Japan
c) Dipartimento di Fisica ‘‘Enrico Fermi’’ and INFN Sezione di Pisa, Universita` di Pisa, Largo Bruno Pontecorvo, I-56127 Pisa, Italy
d) LIGO Observatories, California Institute of Technology, Pasadena, CA 91125, USA

## Slide 2: High power interferometers
The main Fabry Perot mirrors of advanced interferometers will be subject to almost a MW of standing laser light over a Gaussian spot size of ~6 cm radius
high reflectivity coatings absorb >0.25 ppm
The mirrors receives 0.25 ~ 0.5 W of heating
The deposited power distribution matches the stored beam profile

## Slide 3: Thermal lensing problem
Thermal lensing impede the performance of the interferometer
Problem already present in Virgo and LIGO at lower power, due to the higher absorption of their mirrors

## Slide 4: Present solution
Thermal Compensation System (TCS)
shape an annular CO2 laser beam and project it on the mirror periphery
generate counter thermal lensing
Problem for Advanced interferometers:
Radiation pressure and thermoelastic noise on test mass affect the GW signal

## Slide 5: Advanced solution
Hot ring on a compensation plate
Generates negative thermal lensing on an optical element that does not otherwise affect the interferometer performance
Technique tested on main mirrors by GEO

## Slide 6: Advanced Virgo problem
Very difficult to implement compensation plate

## Slide 7: Alternative solution
Directional cooling of the stored beam spot
Passive, no forces on the test mass

## Slide 8: Directional Radiative Cooling (DRC) working principle
Image a cold surface on the laser spot
The thermally radiated heat from the spot is absorbed by the cold target
The cold target, being colder, returns less heat to the laser spot

## Slide 9: DRC basics
DRC takes advantage of the heat emitted by the spot BECAUSE it is at room temperature
Simply balances the laser deposited power with robbed thermal power
DRC applied in absence of stored power would generate a cold spot on the mirror

## Slide 10: DRC Facts
The mirror is subject to less thermal radiation radiation pressure
actually quieter than without cooling
  (no practical advantage though)

## Slide 11: Feasibility of DRC
At room temperature a black body emits 146W/sr-m2
Fused silica emissivity is close to that of a black body 0.93 engineering toolbox http://www.engineeringtoolbox.com/
A 6 cm radius spot emits 1.64W/sr
Black Body Emission Calculator http://infrared.als.lbl.gov/calculators/bb2001.html
0.25-0.5 sr coverage sufficient to
rob the 0.25—0.5W deposited
by the laser spot

## Slide 12: DRC required temperature
Liquid nitrogen cooled black bodies emit only 0.4% thermal radiation than a room temperature body
Li-N2 targets would be 99.6% efficient

## Slide 13: How to “direct” radiative cooling
Proximity cooling
Baffled cooling
Imaging cooling

## Slide 14: Proximity DRC
A 6.2 cm radius, liquid-nitrogen-cooled disk placed in front of the test mass would suck out 5.1 W
Advantages:
  simple solution
Disadvantages:
  Obstruct the stored light beam
  Suck out too much power

## Slide 15: Baffled DRC
A large Li-N2 target is used
Pyramidal Baffles restrict the line of view of the cold target to the stored beam spot
Pyramids can be located outside the beam line outer envelope

## Slide 16: Baffled DRC de-focussing
Cooling spot can be defocussed to mimic a Gaussian by playing with longitudinal positioning of the baffles

## Slide 17: Baffled DRC disadvantages
Advantages
  Large cooled surface acts as cryo-pump for organics
Disadvantages
  Bulky baffle array,
  Large Li-N2 cooled target
  Large cooling power requirement, potentially mechanically noisy

## Slide 18: Mirror focused DRC
One or two small Li-N2 cooled targets focused with Au plated spherical mirrors on stored beam spot
Mimic Gaussian spot profile by moving cold targets out of focus

## Slide 19: Controlling DRC power
Three methods
  Iris control
  Target temperature control
  Hot resistor power balance

## Slide 20: Iris DRC power Control
The DRC cooling power is directly proportional to the cold target area used.
An iris placed in front of each target would naturally tune the cooling power
Disadvantage:
  Mechanical parts in vacuum

## Slide 21: Iris DRC power Control
Advantage:
  A fixed iris can be used for static cooling power controls, to match the absorption of individual coatings and minimizing the dynamic range of active power controls

## Slide 22: Target temperature Control
The cold target “D” is separated from the Li-N2 cooling bath “A” by a thermal resistor “B”
The cold target temperature is controlled by a resistor “C” mounted on the cold target
Disadvantages:
  Reaction time of several seconds
  Dumps power in thermal bath
Advantages:
  Can be used for small corrections

## Slide 23: Hot resistor DRC power Control
The cold target “A” is placed behind the mirror focal plane “C”
A back shielded resistor “B” is placed in front of the focal plane
Both defocused to generate Gaussian profile, the heating modulatable
Disadvantages:
  Heating power fluctuations can generate thermo-elastic noise on the main mirror,
    can use with interferometer off,
    need to limit the resistor applied power
Advantages:
  Fast reaction times (low resistor heat capacitance)
  Does not dump power in thermal bath

## Slide 24: Focused RTC further option
Hot ring placed in focal plane
is imaged on the mirror, can change mirror focal length
Advantage:
  Fine mirror focal length controls even in absence of beam power
Disadvantage:
  Possible thermo-elastic noise
    Useful with interferometer off

## Slide 25: Experimental measurements

## Slide 26: Experimental Setup schematics
Spherical mirror
Liquid N2 trap
(or heating lamp)
Separation wall
Thermometer array
External structure

## Slide 27: Liquid Nitrogen trap
62.5mm diameter orifice
Dewar

## Slide 28: Parabolic mirror
We made the parabolic mirror with super insulation foil glued on a circular sled as support.
Circular sled
Super insulation
foil

## Slide 29: Building and testing the mirror

## Slide 30: Thermal sensors
There were 8 thermal sensors, one broke half way. At the end only 7 thermal sensors left.
2.5cm
Thermometer
array
(LM19)

## Slide 31: Building the box
Lined with black
Felt to absorb
Diffused radiation
Before lining

## Slide 32: Cold trap set-up
Liquid Nitrogen
Thermal sensor array
Parabolic mirror
Acquisition computer

## Slide 33: 40 W heater Lamp setup
40 W Lamp
Parabolic mirror
Acquisition computer
Thermal sensor array

## Slide 34
Acquisition
Averaging
display
Write on disk

## Slide 35: Warming and cooling cycle
A
B
Thermal Power= slopeA - slopeB [oC/s]
A
B
Heating lamp on
Linear rise fit
Cold trap open
Linear cooling fit
Exponential decay fit
Exponential decay
and slope fit
Baseline linear fit
Baseline linear fit

## Slide 36: Energy deposition/extraction
Exchanged power = Gaussian spot surface S = m2*m4
cooling
heating
m4
m2

## Slide 37: Results
Gaussian fit area results
  1.9W heating => S = 0.685±0.02
  Li-N2 cooling => S = 0.056±0.028
Cooling power
  Measured
  1.9 [W] x (0.685/0.056) = 155±78±39 mW
  Theoretical (all ε= 1) 262 mW

## Slide 38: Conclusions
Demonstrated the feasibility of
focused radiative cooling
Directly suck heat from mirror laser spot
Passive and remote operation (low risk)
Neutralize thermal lensing without perturbing the test masses
Remote mirror focal length tuning capabilities
Cryo pumping of organics impurities