LIGO Laboratory / LIGO Scientific Collaboration

LIGO- E1101023-v1	LIGO	03/15/2012

Signal Recycling Cavity Baffles Fabrication and Installation Test Plan

Michael Smith, Lisa C. Austin

Distribution of this document:

LIGO Scientific Collaboration

This is an internal working note

of the LIGO Laboratory.

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW22-295 185 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 159 Richland WA 99352 Phone 509-372-8106 Fax 509-372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone 225-686-3100 Fax 225-686-7189 |

http://www.ligo.caltech.edu/

1	Introduction	5

2	Tests	5

2.1	Vendor Tests	5

2.2	LIGO Tests	5

Abstract

This document describes the plan for acceptance testing of the Signal Recycling Cavity Baffles during manufacturing, and for testing the final assembly before installing in the aLIGO chambers.

# Introduction

This document describes the plan for acceptance testing of the Signal Recycling Cavity Baffles during manufacturing, and for testing the final assembly before installing in the aLIGO chambers.

# Tests

## Vendor Tests

The first article of each Signal Recycling Cavity baffle will be assembled at the vendor and witnessed by LIGO QA personnel.

The vendor shall provide the following reports: 1) Materials certifications, 2) Dimensional and QC inspection reports--this shall include a report showing that parts have been inspected and fall within specified tolerances, and 3) Certificate or statement of compliance with all contract and drawing process restrictions.

## LIGO Tests

The first article of each Signal Recycling Cavity baffle will be tested to verify frequency > 150 Hz requirement.