LIGO Laboratory / LIGO Scientific Collaboration

LIGO-E1200232-v2	Advanced LIGO	27 Jun 2012

Riser, HAMs 6L, 6H, 12H calculations, aLIGO

Sam Barnum

Distribution of this document:

LIGO Science Collaboration

This is an internal working note

of the LIGO Project.

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW17-161 175 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 1970 Mail Stop S9-02 Richland, WA 99352 Phone (509) 372-8106 Fax (509) 372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone (225) 686-3100 Fax (225) 686-7189 |

http://www.ligo.caltech.edu/

# Reference Documents:

## LIGO-D0901828-v1: AdvLIGO Systems, HAM12-H2 Top Level Chamber Assembly

## LIGO-D0901811-v1: AdvLIGO Systems, HAM6-L1 Top Level Chamber Assembly

## LIGO-D0901822-v2: AdvLIGO Systems, HAM6-H1 Top Level Chamber Assembly

## LIGO-E1101146-v2: L1_recycling-cavity-length-0.076wedge

## LIGO-E1101147-v2: H1_recycling-cavity-length-0.076wedge

## LIGO-E1101148-v2: H2_recycling-cavity-length-0.076wedge

# Reference Values from Documents:

## Global Coordinate Z value of "Output Faraday Out" beam. (mm)

## Position 4" above HAM-ISI Optics table relative to Global Coordinates (measured in SolidWorks Model). (mm)

## Global ray vector angle of "Output Faraday Out". (deg)

## Distance from output of "Output Faraday Out" to center of  HAMs 6s and 12 (measured in SolidWorks Model). (mm)

# Values:

| HAM Chamber | (a) | ( b) | (C) |
| --- | --- | --- | --- |
| HAM6 L1 | -98.2 | -223.4 | -.034 |
| HAM6 H1 | -117.5 | -223.4 | -.034 |
| HAM12 H2 | -152.4 | -223.2 | -.064 |

d = 1783 for all chambers

# Calculations:

a - b + (Tan(c)*d) = Height of spacer

HAM6 L1:     (-98.2)-(-223.4)+(Tan(-.034)* 1783) = 124.1mm  ~  4.886"

HAM6 H1:    (-117.5)-(223.4)+(Tan(-.034)*1783) = 104.8mm  ~  4.128"

HAM12 H2:  (-152.4)-(223.2)+(Tan(-.064)*1783) =  68.8mm  ~  2.709"