## Slide 1: Squeezed Light Techniques for Gravitational Wave Detection
July 6, 2012
Daniel Sigg
LIGO Hanford Observatory
Seminar at TIFR, Mumbai, India

## Slide 2: Abstract
Several kilometer long interferometers have been built over the past decade to search for gravitational waves of astrophysical origins. For the next generation detectors intra-cavity powers of several 100 kW are envisioned. The injection of squeezed light, a specially prepared quantum state, has the potential to further increase the sensitivity of these detectors. The technology behind squeezed light production has taken impressive steps forward in recent years. As a result a series of experiments is underway to prove the effectiveness of squeezed light and to make quantum technology a valid upgrade path for gravitational wave detectors.

## Slide 3: Gravitational Waves
10-9 Hz
10-4 Hz
100 Hz
103 Hz
Relic radiation
Cosmic Strings
Supermassive BH Binaries
BH and NS Binaries
Binaries coalescences
Extreme Mass Ratio
Inspirals
Supernovae
Spinning NS
?
?
?
?
?
?
10-16 Hz
Inflation Probe
Pulsar timing
Space detectors
Ground interferometers
?

## Slide 4: Sensitivity Sixth Science Run

## Slide 5: Advanced LIGO Sensitivity
Standard quantum limit
Initial LIGO
Radiation pressure noise
Shot noise

## Slide 6: The Advanced LIGO Detector
Laser
Laser:
200W - 1064nm
Input mode cleaner:
stabilizes frequency
and cleans laser mode
Arm cavities:
Fabry-Perrot cavities store light to effectively increase length
Homodyne Readout
Signal recycling mirror: amplifies readout signal
Input
Test
Mass
End
Test
Mass
4 km
4 km
800kW
800kW
Power recycling mirror: reflects light back coming from the beam splitter, increasing power in the arm cavities

## Slide 7: Squeezed Light
Amplitude squeezing
Phase squeezing
Normal light
ϕ
│E │

## Slide 8: Key Insights
Shot noise in a Michelson interferometer is due to vacuum fluctuations entering the dark port.
Quantum noise also produces photon pressure noise.
Injecting a specially prepared light state with reduced phase noise (relative to vacuum) into the dark port will improve the shot noise sensitivity.
Similarly, injecting light with reduced amplitude noise will reduce the photon pressure noise.
Non-linear optical effects can be used to generate a squeezed “vacuum” state.

## Slide 9
31 W + 6 dB of squeezing (10 dB of anti-squeezing, total losses ~20%)
31 W
125 W input power

## Slide 11: Experimental Confirmation at the GEO600 Detector
3.5 dB of squeezing
Abadie et al. Nature Physics 7, 962 (2011)

## Slide 12: The Beamsplitter
Input
Return
Dark Port
Photodetector
Signal µ |Ein – Ein|2 = 0
Noise = 0

## Slide 13: The Beamsplitter
Input
Return
Vacuum
Dark Port
Photodetector
Evac= 0 + evac
~
Gravitational Wave
~
~
Signal µ |evac + ∆EGW |2 ~ 0
Noise µ |evac x ∆EGW | ~ 0

## Slide 14: The Beamsplitter
Input
Return
Vacuum
Dark Port
Local oscillator
Photodetector
Evac= 0 + evac
~
~
Gravitational Wave
*
*
Signal µ |Elocal + ∆EGW|2
~ Elocal x ∆EGW + c.c.
Noise µ Elocal x evac + c.c.

## Slide 15: In Fourier Space
Frequency
Local oscillator
Vacuum fluctuations
Complex conjugate
Noise µ Elocal x evac + c.c.
~
*

## Slide 16: Generating Squeezed “Vacuum”
Need an operation that applies
Optical parametric oscillator (OPO)
Non-linear crystal that is pumped at double the frequency and below threshold.
evac → evac + e2iφ x evac
~
~
~
*
φ: squeezer angle
Noise µ |Elocal| x |evac| x cos(Φlocal - φ) x cos(Φvac - φ)
~
Þ
~

## Slide 17: Shot /Radiation Pressure Noise in the Quantum Picture
Phase fluctuations in the vacuum field entering the beamsplitter are responsible for the shot noise
Phase squeezing reduces shot noise
Amplitude fluctuations in the vacuum field entering the beamsplitter are responsible for radiation pressure noise
Amplitude squeezing reduced radiation pressure noise

## Slide 18: The H1 Squeezer Experiment
Goals:
Demonstrate 3dB of squeezing at the initial LIGO sensitivity
Don’t degrade low frequency sensitivity
Risk mitigation for high power operations
Pathfinder for advanced LIGO squeezer
Potential show stoppers:
Back scattering
Stray light
Phase noise
Optical losses
Auxiliary servo noise
Alignment jitter
Stability

## Slide 19: H1 Squeezer Experiment
BS
SHG
OPO
AUX
MAIN
PLL1
PLL2
OMC
PD
FI
ITM-X
ITM-Y
ETM-X
ETM-Y
PRM
IMC
PSL
Interferometer Acronyms
PSL
- Pre-Stabilized Laser
- Vacuum System
IMC
- Input Mode Cleaner Cavity
PRM
- Power Recycling Mirror
BS
- Beam Splitter
ITM
-
Arm Cavity Input Test Mass
ETM
-
Arm Cavity End Test Mass
FI
- Faraday Isolator
OMC
- Output Mode Cleaner Cavity
PD
- Photodiode (Data Output)
PS
PS
FI
Squeezed Light Source Acronyms
MAIN
- Squeezing Main Laser
AUX
- Squeezing
Auxiliary Laser
PLL
- Phase Lock Loop
SHG
- Second Harmonic Generator
OPO
- Optical Parametric Oscillator
PS
- Phase Shifter
Y
-Arm
(4km)
X-Arm (4km)
ANU, AEI, MIT, LIGO collaboration

## Slide 20: Squeezer at Hanford
advanced LIGO
20
20
Alexander (AEI)
The OPO
Sheila (MIT)
Electronics
Optics Table
Lab in corner station
Michael (ANU)
Grant (Michigan)
Max(Columbia)
Sheon (ANU)
Conor (ANU)

## Slide 22
Second Harmonic Generator
Laser
Optical Parametric Oscillator
Homodyne
Detector
Interferometer
Anti Symmetric Port

## Slide 23: H1 Squeezed
Preliminary
Best ever sensitivity!
2 dB of squeezing

## Slide 24: Non-Linear Gain
19% loss
1.3º phase noise
61% loss
5º phase noise

## Slide 25: Losses Phase Noise
 | Now | Near future | Advanced LIGO
3 Faraday passes | 5% each | 3% each | Aim for less than 10% total
Signal recycling cavity@100 Hz |  | 2.5% (T=35%) | 
Squeezer mode matching to OMC | 30% | 4% | 
OMC transmission | 19% | 1% | 
Total losses | 55-60% | 20% | 
Detected Squeezing | 2+dB | 6dB | 10-15dB
 | Now | Near future | Advanced LIGO
RF sidebands | 1.3 mrad | same | Reduce to less than 2 mrad total
Sources on squeezer table | ≤22 mrad |  | 
Beam jitter | 30 mrad |  | 
Total phase noise | 37mrad |  | 
Detected squeezing | 2+dB | 6dB | 10-15dB

## Slide 26: Future Phase Noise and Loses
Reduce current losses
Advanced LIGO

## Slide 27: Outlook
GEO600/AEI will work on high performance squeezing and long term stability
ANU continues to optimize the ring-cavity OPO
R&D program at MIT to work on filter cavities and a low loss readout chain
Start a design for an advanced LIGO squeezer
Squeezed light sources will be the first upgrade to
advanced gravitational-wave interferometers