LIGO Laboratory / LIGO Scientific Collaboration

LIGO-E1300136-v1	LIGO	2/12/2013

TMS Telescope Mirrors & Packaging

for Delivery to Local Coater

Ken Mailand -Virginio Sannibale

Distribution of this document:

LIGO Scientific Collaboration

This is an internal working note

of the LIGO Laboratory.

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW22-295 185 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 159 Richland WA 99352 Phone 509-372-8106 Fax 509-372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone 225-686-3100 Fax 225-686-7189 |

http://www.ligo.caltech.edu/

TMS Mirror Packaging

Feb 12, 2013

Packaging Primary Mirror

- Remove any previous residues of scotch tape from the PETG container,

- Place 5/6 desiccant bags in the PETG container base before placing the mirror so the bags will be under the mirror as shown in figure 1.  The coated side will not be in contact with the bags

- Note the mirror serial number for later use and place it in the container base with the coating facing up

- Take good Care to align the PETG container lid to the Mirror Wedge and then press it down to close the container

- If the lid is properly aligned, then little force is need to get the container properly closed

- Verify that the S/N on the lid correspond to the mirror serial number inscribe on the mirror back

- Secure the lid and base, with two strips of adhesive tape, on two opposite sides.

Figure1.

Packaging Secondary Mirror

- Insert the secondary mirror inside the white plastic cylinder sleeve from the coated side as shown in figure 2.

- Stack 3 desiccant bags on the bottom side of the mirror in the white sleeve.

- Insert the assembly inside the cylindrical container in such a way that the coated side is facing up.

- Verify that the container S/N and the mirror S/N match

- Screw the lid on the cylindrical container, and verify that the screw on cap is closed tight. figure 3.

Figure	2 . 						 Figure	3.

Packaging Folding Mirror (F2)

- Insert the F2 mirror inside the white plastic cylinder container, in centering ring, place 3 desiccant bags in recess in base foam,  under mirror, reflective surface is in up orientation figure 4.

- Insert the foam ring, with the large hole, inside the cylindrical container, on top the mirror figure 5. ref. coated side is facing up.

- Verify that the container S/N and the mirror S/N match

- Screw the lid on the cylindrical container, and verify that the screw on cap is closed tight. There is some compression in the foam sandwich, and care should be taken to thread the cap on properly, not to cross thread the lead, and completely close the container.

Figure 4.

Figure 5.

Mirror Serial Numbers

Secondary Mirrors

S/N     Comments Below

002

003     Chipped

004

005

006

007     It was 001 changed into 007

Primary Mirrors

S/N     Comments Below

002

003     Coating contaminated practically the entire surface, diffused superficial circular scratches

and straight scratches

004

005

006     Coating contaminated. A couple of small cloudy spots

007     It was 001 changed into 007

Folding Mirror 1

S/N     Comments

002

003

004

005

006

008 	Serial 001 was changed to 008