LASER INTERFEROMETER GRAVITATIONAL WAVE OBSERVATORY

-LIGO-

CALIFORNIA INSTITUTE OF TECHNOLOGY

MASSACHUSETTS INSTITUTE OF TECHNOLOGY

| Document Type | DCC Number T1300889-v1 | October 23, 2013 |
| --- | --- | --- |
| TCS IR Comparator Test Plan |
| B. Abbott |

Distribution of this draft:

This is an internal working note of the LIGO Laboratory

California Institute of Technology	Massachusetts Institute of Technology

LIGO Project – MS 18-33	LIGO Project – MS 20B-145

Pasadena, CA 91125	Cambridge, MA 01239

Phone (626) 395-2129	Phone (617) 253-4824

Fax (626) 304-9834	Fax (617) 253-7014

E-mail: info@ligo.caltech.edu	E-mail: info@ligo.mit.edu

www:  http://www.ligo.caltech.edu/

# Introduction

The rudimentary test described below is required to verify the correct basic functioning of the TCS IR Comparator box, and its IR sensor.

# Test Equipment

Functioning TCS CO2 Laser Control Chassis (D1200475)

Cigarette Lighter

# Tests

Plug the IR Sensor into the “From IR Sensor” connector on the Comparator Box, and connect the comparator box to the Laser Control Chassis with a normal M-F DB9 cable.  Turn on the Laser Control Chassis, and check the lights on the IR Comparator Box.  Are all the power lights illuminated?  If you light a cigarette lighter, and bring it close (within ½”) to the IR sensor, does the “Fault” LED illuminate on the Comparator box?  Does the “IR Fault” LED light up on the Laser Controller Chassis?  If the answer to any of these questions is “no”, then the unit fails the test.

| LED | Did the LED light? Y/N |
| --- | --- |
| +15 |  |
| -15 |  |
| +5 |  |
| Fault |  |
| IR Fault |  |