## Slide 1: Impressions of CARM/ALS
J. Kissel, for the people way smarter than me.

## Slide 2: Primer
I’m just getting to know this system
This system is still under development
  some documentation is out-of-date
  two sites do things differently
This presentation will not be perfect
Go to references for guidance, they’ve done a better job.
The development of CARM/ALS spans many decades, many people, and many subsystems, so documentation isn’t always consistent and it’s tough to find the big picture with everything included in one place. This is my attempt. It’s too ambitious for one talk that I wrote in a day. Please also bare in mind
Thanks for your patience.

## Slide 3: Intro to Cavity “Locking”
Equivalent noise sources to this system:
cavity length changes or
laser frequency/wavelength changes
Laser
Optical
Isolator
Resonant cavity resonates, when cavity length is an integer number of laser wavelengths
More reflective mirrors
= Tighter resonance condition

## Slide 4: Intro to PDH
Robert V. Pound
Ron W P Drever
John L Hall
Faraday
Isolator
Laser
Optical
Isolator
Low-Pass
Filter
Mixer/
“Demodulator”
Phase
Delay
Local
Oscillator
(LO)
Phase /
Frequency
Modulator
Control
Filter
“Servo”
Reflected Field Power
Reflected Field Phase
Non-linear in regions outside cavity linewidth
“Lock acquisition” or “catch (and hold) lock”
= Length changes slower than the control bandwidth
Control servo holds the laser frequency within linear operating regime
Locks laser frequency to resonant cavity, following the length of the cavity as it changes
PDH Error Signal

## Slide 5: Intro to PDH
Faraday
Isolator
Laser
Optical
Isolator
Low-Pass
Filter
Mixer
Phase
Delay
Local
Oscillator
(LO)
Phase /
Frequency
Modulator
Control
Filter
“Servo”
PDH locking the Laser to
Cavity reduces frequency noise
Cavity treated as
“frequency reference”
The LONGER the cavity, and/or
the SMALLER the length changes,
the better the frequency reference,
the lower the frequency noise

## Slide 6: The LIGO Arm Cavity Problem
Highly reflective mirrors
Long light storage time
Great for gravitational wave detection
Highly reflective mirrors
Very small / tight cavity line width:
FWHM ≈ 100 [Hz] ≈ 1 [nm]
Difficult to catch a resonance condition
aLIGO Needs frequency stabilization down to 20 [nHz] = 2e-8 [Hz/rtHz]!
(in loop)
Frequency stabilized to a part in 1022
Laser frequency = 3 [THz] = 3e14 [Hz]
In order to merge corner station with arms during lock acquisition, while building up frequency stability, we need *LOTS* of loops.
Notes: Approximately equals “≈“ mac keystroke is simultaneous “option/alt”+”x”

## Slide 7: LIGO = PDH to the MAX
SIX nested / interconnected PDH loops to control the laser frequency:
FSS
IMC PDH
Fiber PLL
ALS PDH
ALS COMM
CARM

## Slide 8: Frequency Stabilization Servo
FSS
IMC PDH
Fiber PLL
ALS PDH
ALS COMM
CARM
Just a fancy PDH loop!
Voltage-Controlled Oscillator
(VCO)
Provides local oscillator (LO) frequency at ~80 [MHz]
But Oscillator Frequency is controllable (via a voltage input) to +/- 1 [MHz]
Acousto-Optic Modulator (AOM)
A PZT wrapped around a crystal, creates diffraction pattern, with each fringe shifted by oscillator frequency
We catch the first, and send it through twice, so modulation frequency is ~160 [MHz]
Light sent into Reference Cavity
L ≈ 0.5 [m]
In a vacuum can on the PSL
Photo-diode demodulated at 160 [Hz], low passed, and control filtered, and sent to laser
Low Frequency = laser temperature
High Frequency = Laser cavity length

## Slide 9: Input Mode Cleaner PDH
FSS
IMC PDH
Fiber PLL
ALS PDH
ALS COMM
CARM
Just a fancy PDH loop!
(but now nested with FSS)
Electro-optic Modulator (EOM)
Another crystal whose index of refraction oscillates with voltage, modulating the phase
IMC oscillator is set at 24 [MHz]
Now 16 [m], suspended input mode cleaner cavity serves as frequency reference
Fast control sent as control input PSL VCO (remember the +/- 1 [MHz]?)
Slow control sent to IMC cavity length

## Slide 10: PSL / End-Station Laser Phase-Locking Loop
FSS
IMC PDH
Fiber PLL
ALS PDH
ALS COMM
CARM
MEANWHILE!!! Begin to prep the arms for merging with the red…
Take the *transmitted* light from Reference Cavity, use another oscillator to down-shift back to 80 [MHz]
Ship to end stations via optical fiber, and phase lock a RED / GREEN auxiliary laser tuned to have ~ 40 [MHz] beat note with PSL
Catch beat note on PD, a send to a phase-frequency detector as the mixer, demodulate at ~40 [Hz] with VCO and control end station laser
Phase-Locking Loop = PLL

## Slide 11: Arm Length Stabilization PDH
FSS
IMC PDH
Fiber PLL
ALS PDH
ALS COMM
CARM
Now back to standard PDH locking of arm with green
(Linewidth in green is lower than for Red)
Send fast feed back to end-VCO (just like the IMC PDH to the FSS VCO)
Send slow feed back to arm cavity length
(just like IMC PDH and MCL)
Just a fancy PDH loop!
(Now nested with Fiber PLL)

## Slide 12: PSL / Common Arm Stabilization
FSS
IMC PDH
Fiber PLL
ALS PDH
ALS COMM
CARM

## Slide 13: Common Arm Servo
FSS
IMC PDH
Fiber PLL
ALS PDH
ALS COMM
CARM

## Slide 14: Appendix to PDH (Essential Cavity Equations)
Cavity Resonance Condition
Integer Number of Wavelengths fit inside length of the cavity
Free Spectral Range
Cavity Linewidth = Full-width Half Maximum = 2* Cavity Pole
Mirror reflectivities go up, cavity Finesse goes up, Linewidth gets smaller
Phase <-> Length <-> Frequency