## Slide 1: Highlights from the commissioning of Advanced LIGO
L. Barsotti
for the Advanced LIGO Team
LIGO-G1500414

## Slide 2: Since the last LVC…
Best L1 Sensitivity = 65 Mpc
10h lock = 20 days of eLIGO
H1 achieved full lock!
Best sensitivity = 15 Mpc

## Slide 3: Reminder from Initial LIGO: from 100 kpc to 15 Mpc in 3+ years (with observing time)
Science Requirement. document (1995)
S2: Feb.- Apr. 2003
59 days BNS reach ~ 1Mpc
S3: Oct. ‘03 - Jan. ‘04
70 days BNS reach ~ 3Mpc
S1: Aug. - Sep. 2002
17 days BNS reach ~100kpc
S5: Nov 2005 – Oct 2007
S4: Feb. - Mar. 2005
30 days BNS reach ~ 15Mpc
15 Mpc
LIGO: First lock at the end of 2000…

## Slide 4: aLIGO L1: from 0.5 Mpc to 60 Mpc in 9 months!
G1401390
LIGO: First lock in May 2014

## Slide 5: L1/H1 Commissioning Strategy
L1: “make the noise lower”
 Pathfinder of noise sources/coupling mechanisms (aLIGO upgrade started ~1 year earlier than in H1)
H1: Improve the sensitivity following L1 path
In parallel, both interferometers: work on locking robustness, automation, training of operators
We expect H1 sensitivity to be comparable (at least) to current L1 sensitivity by O1: no reason to believe otherwise at the moment

## Slide 6: L1 Noise vs Fundamental Noises (D. Martynov, G1500281)
Shot noise @ high frequency
What about low frequency?
25W input power
100 kW circulating power

## Slide 7: The usual answer: “technical noises” (many of them)
Frequency (Hz)
YELLOW: scattered light projections
ORANGE: “charge” noise

## Slide 8: Most “hot” noise sources these days
Scattered light
Charge
Evidence of noise introduced by scattered light
Investigations focused on the path between the Signal Recycling Mirror and the Output Mode Cleaner
Short version of the story: we have charge on our test masses and this is bad for many reasons
In particular, first order interaction with time varying electric fields in the chamber
 noise in DARM
DISCHARGE effort on going RIGHT NOW at LLO
R. Weiss, G1500264

## Slide 9: Most “hot” noise sources these days
Scattered light
Charge
Evidence of noise introduced by scattered light
Investigations focused on the path between the Signal Recycling Mirror and the Output Mode Cleaner
Short version of the story: we have charge on our test masses and this is bad for many reasons
In particular, first order interaction with time varying electric fields in the chamber
 noise in DARM
DISCHARGE effort on going RIGHT NOW at LLO
R. Weiss, G1500264
Long version of the story: ask Rai

## Slide 10: Observed, long expected, problem: parametric instabilities (S. Gras, G1500283) M.Evans, S. Gras, et al., “Observation of Parametric Instability in Advanced LIGO”, arXiv: 1502.06058, submitted to PRL (2015)
Very well understood mechanism: mechanical mode of test mass driven by (classical) radiation pressure
More likely to happen with higher the power stored in the arm cavities
Parametric instability @ 15.54 kHz observed for the first time in L1 in December
Effect is a huge line aliased in band (843 Hz) which saturates the controls

## Slide 11: What can we do about parametric instabilities?
  0. Lower the power  DONE
  Break “instability” by slightly change radius of curvature of optics  DONE
  Actively damp the instability by using electro-static actuators  tried on MIT suspension prototype, good for small number of modes
  J. Miller, et al., Phys. Lett. A, 375, 788 (2011)
  3. Attach passive dampers to each test mass
   tried on MIT prototype, not active control required, BUT stringent thermal noise requirements on materials
  S. Gras et al., arXiv:1502.06056, (2015)

## Slide 12: What can we say about glitches? Where we are with respect, for example, S6?
Answer: Laura Nuttall, Josh, et al (G1500259)
S6
Successful commissioning + DetChar campaigns against glitches over the past months
aLIGO L1

## Slide 13: S6 vs aLIGO glitch comparison Duncan Macleod

## Slide 14: Progress @ Hanford
Just a few days after first stable lock in February…several hours of reliable lock
Arm power

## Slide 15: First full lock achieved in early December, BUT…
…losses in the arms much higher than expected (700ppm vs 100ppm, E. King, G1500288)
Residuals from cleaning (pieces of “first contact” film left on the optic)
Losses comparable to L1 after (re)cleaning (~100 pm)
Image of Front of End – Y optic

## Slide 16: Macroscopic problems are easy to find and fix!
…losses in the arms much higher than expected (700ppm vs 100ppm, E. King, G1500288)
Problem easily recognized and fixed
Residuals from cleaning (pieces of “first contact” film left on the optic)
Losses comparable to L1 after (re)cleaning (~100 pm)
Image of Front of End – Y optic

## Slide 17: Hanford Sensitivity (E. Hall, G1500256)
15 Mpc, sensitivity understood
Actuator noise limiting low frequency sensitivity (expected)

## Slide 18: Current effort on robustness/reliability
Locking sequence fully automated, 15 min
Work on reliable initial alignment strategy
Global alignment control

## Slide 19: Current effort on robustness/reliability
Locking sequence fully automated, 15 min
Work on reliable initial alignment strategy
Global alignment control

## Slide 20: LHO Seismic Isolation Performance
Frequency (Hz)
Displacement m/sqrt(Hz)
Next challenge:
fight bad weather

## Slide 21:  What are the most difficult problems we have faced so far?  What are the biggest problem we still have to face to reach design sensitivity and high duty cycle?

## Slide 22: Overall, what are the biggest problems we have faced so far?
(source: aligo-ifo and aligo-isc mailing lists)
1) Charging
2) Alignment 2) Green Coating

## Slide 23: Overall, what are the biggest problems we have faced so far?
(source: aligo-ifo and aligo-isc mailing lists)
1) Charge
2) Alignment 2) Green Coating
(source: front line commissioners)
1) LLO: Lock of the central part of the interferometer
(because we don’t have actuators on the beam splitter optic)
1) LHO: Green coating
2) LLO & LHO: Alignment

## Slide 24: What are the biggest problem we still have to face to reach design sensitivity and high duty cycle?
1) “High Power” 1) Scattered light
2) “Upconversion”
(source: aligo-ifo and aligo-isc mailing lists)
(source: front line commissioners)
Scattering
2) Alignment
3) Charge

## Slide 25: CHARGE How about solutions?
Source of charge identified: first contact (-), ion pumps (+)
Diagnostic developed to quantify the problem
L1: charge localized on back of ETMY
Discharge methods developed, discharge attempts @ LLO
Other charge-related noise mechanisms might become dominant in the future
(Poster, K. Baric G1500383)
R&D @ Caltech and MIT

## Slide 26: SCATTERED LIGHT How about solutions?
On going investigations at LLO (and soon at LHO) to track down scattering sources/coupling mechanisms
“Shroud” for the output mode cleaner

## Slide 27: Outlook
L1 is hunting noises:
  Main enemies right now: scatter light/charge noise
  Several possible scenarios depending on outcome
  For high frequency, power increase is the next step
H1: good progress, clear path to catch up with L1
Reliability/automation in parallel at both sites
Getting ready for Science!

## Slide 28: Fast (sometimes incredibly fast) progress, very encouraging results
PRELIMINARY

## Slide 29: NEW PRIZEs: best logbook entry! (one for LHO log, one for LLO log)
Committee: Peter, Lisa, Dave
Criteria:
    Relevance and impact
    Clarity (summary/details format)
    Data calibrated in physical units
$150 per prize @ each LVC

## Slide 30: LLO log winner: entry 16444, Den Martynov

## Slide 31: LHO log winner: entry 16569, Evan Hall (+ Sheila Dwyer and Alexa Staley)

## Slide 32: Keep climbing..
Chart: aLIGO Commissioning Progress
| 0.0 | 11.16041666666667 | 27.39375 | 53.77291666666667 | 59.86041666666661 | 99.42916666666666 | 115.6625 | 116.6770833333333 | 178.5666666666667 | 193.7854166666667 | 231.325 | 244.5145833333333 | 267.85
 | 0.58 | 3.68 | 5.87 | 15.8 | 20.14 | 27 | 31 | 36 | 50 | 57 | 60 | 64.2 | 67
D. Shoemaker G1500192

## Slide 33
Acoustic Mode Damper
LIGO-G1500283-v1
S.Gras, LSC-Virgo meeting, Pasadena 2015

## Slide 34
Forecast for the future
25 kW
100 kW
800 kW
More than 40 modes needed to be damped at 800 kW
PI threshold
Current (LLO)
Full power
LIGO-G1500283-v1
S.Gras, LSC-Virgo meeting, Pasadena 2015

## Slide 35
R. Weiss, G1500264

## Slide 36
E. Oelker, G1500337
Evans’ group @ MIT

## Slide 37: Path to O1
LIGO-G1301309
ER7: beginning of June:
- in less than 3 months
- length/scope similar to ER6 on BOTH L1 & H1
ER8: end of August, as preparation for O1
O1 starting mid-September:
- up to 3 months of data taking