## Slide 1: Absolute Calibration of A Gravitational Wave Detector Network
Jeffrey Kissel
LIGO Hanford Controls Engineer
LIGO Calibration Group Co-Chair

## Slide 2: Inspiration
PRL 116.23 (2016): 231102
2G , 3G, Space, and PTAs
will have events with SNRs of O(~100)…
…Detector calibration must get better than ~1%
PRD 94.12 (2016): 121501
And if multi-band, we must understand each other’s systematic errors.

## Slide 3: Cosmology and Correlated Systematic Errors
From G1800504
Toy Future BNS Detections…
Correlated Systematic
Error...
True H0
Reported H0
Could get H0 wrong...

## Slide 4: Tests of GR and Correlated Systematic Errors
CQG 35.1 (2017): 014002.
(and from yesterday; G1800976)
Similar systematic error across events may lead you astray in GR consistency checks
Will not get SQRT(N) improvement, because calibration’s systematic errors (biases) are correlated b/w events.
Will need to consider calibration uncertainty and systematic error over several events, several observation runs as the detector hardware changes

## Slide 5: State of the Art Example: LIGO 2G
G = A D C
R =
1 + G
C
_________
L
1
__
dR 2 =
dA
A
____
1 + G
_________
1
(
)
1 + G
_________
G
(
)
2
dC
C
____
)
2
(
+
2
(
)
2
1
h L =
C
____
derr
dctrl
+ A
h =
R
derr
PRD 95.6 (2017): 062003.
+ Systematic Error

## Slide 6: Absolute Reference: Radiation Pressure
RSI 87.11 (2016): 114503

## Slide 7: How does LIGO Determine dC and dA
Absolute Scale Factor
C =
dIN2
____
dexc
xpcal
____
derr
pdpcal
____
xpcal
x
x
Complex TFs
w/ Full IFO
A =
dexc
____
derr
xpcal
____
derr
pdpcal
____
xpcal
x
x
Phase uncertainty is entirely from Full IFO transfer functions, not set by absolute scale.
PRD 96.10 (2017): 102001

## Slide 8: Systematic Error vs. Statistical Uncertainty
Statistical uncertainty: MCMC posteriors to the model parameters sampled to form a sample response function.
Systematic Error:
Any residual, statistically significant, frequency dependence
Fundamental reference error
For the Latest IFO Model: T1800115

## Slide 9: 2G Detector (Known) Error and Uncertainty
H1
H1
L1
L1
V1
V1
dR 2 ≈
dA
A
____
1 + G
_________
1
(
)
1 + G
_________
G
(
)
2
dC
C
____
)
2
(
+
2
(
)
2
+ Systematic Error

## Slide 10: What are the 2G limits?
Yes… Propagation of NIST factor
  Years of practice has this nailed down
BUT ALSO:
PCAL Actuator Alignment
  Will be improved for O3!
  But can’t track anymore…
IFO Actuator Strength
  To measure open loop gain and DARM actuator drive
Detector Performance
  If noise improves, SNR improves for fixed actuator
  For detector upgrades, actuation strength will decrease
Absolute Scale
Factor
C =
dIN2
____
dexc
xpcal
____
derr
pdpcal
____
xpcal
x
x
Complex TFs
w/ Full IFO
A =
dexc
____
derr
xpcal
____
derr
pdpcal
____
xpcal
x
x
AND OF COURSE,
… patience
... person power
... interferometer time
(see last year’s talk, G1700810)

## Slide 11: The International Reference Exchange
“GOLD”
Standard
“Working”
Standards
H
L
K
V
RX
RX
TX
TX
ETMX
ETMY
“Propagation of reference” program, with over ~10 years of experience, led by Rick Savage at LHO.
KAGRA has already joined the reference comparison program. VIRGO has begun discussions of doing so.
Mitigates differential scale error between detectors (single event: Sky Position)
Still leaves vulnerability to common scale error (single event: Distance)
iLIGO: CQG 26.24 (2009): 245011.
aLIGO: RSI 87.11 (2016): 114503, T1800046, T1800207, G1800505

## Slide 12: In-House PCAL Reference Check
Frequency
Frequency
Abbott, B. P., et al. PRD 95.6 (2017): 062003.
Free-swinging Michelson doesn’t work well for LIGO. ITM must drive at PUM, too weak a drive.
Arm Length Stabilization is too noisy, and electronics weren’t well understood at the time.
Checks are not (yet?) precise.
Plans are to revisit this for O3.
L1
H1
PCAL
PCAL
ALS
ALS
FSM
FSM

## Slide 13: Terrestrial Detectors: The Next “New” Idea
Newtonian Gravitational Calibrators (NCAL, GCAL) have recently (re)-picked up steam
In-theory a ~0.1% level reference
  PCAL starts at ~0.5%
May be ready to corroborate PCAL by O3
KAGRA -
arXiv:1804.08249 (2018).
m
Mirror
d
2r
m
  x(t) = C cos(4pfrotort)/(d4 frotor2)
Basic Principle
where C = (9G/32p2)(z r sin(a)(rmax4- rmin4)/4)
a
rmax
rmin
VIRGO - G1800442
LIGO – “in prep.”

## Slide 14: What about Space and Galactic Detectors?
Pulsar Timing Arrays (timing systems)
  Limited by diverse Timing Systems in Array, over Decades?
  Everyone uses TEMPO2… (Hobbs et. al 2006)
LISA (phase meters and microthrusters)
  Time Delay Interferometry – More clocks and Frequency Refs.
    needs to measure individual, ~1e6 m arm lengths to ~10m precision
    needs clocks synchronized at the ~50 nsec level

## Slide 15: Example Timing System Systematics
MNRAS 427, 2780–2787 (2012)
TT = Terrestrial Time
BIPM = Bureau International des Poids et Mesures
TT(TAI) = International Atomic Time -> Basis for UTC
TT(BIPMyy) -- updates / corrections, released over time
TT(BIPMyy) - TT(TAI) ,
quadratic polynomial removed
Pulsar Timing Data, Systemic Errors in Solar System Ephemeris
Pulsar Timing Data, w/ modeled realization of GWB ~ 10-15 level

## Slide 16: Discussion & Questions
Calibration is service work precision engineering
Precision/accuracy will not linearly increase with time and costs real money, not “just” time and person power.
We’re actively working with NIST to understand the EUROMET study – Rick @ NIST this week!
  (+ soon new post-doc John Cripe!)
Already working to make ground-based detectors internally consistent via Photon Calibrator, starting to think how to get past its limits
Need to begin dialogue with fundamentally different GW detectors

## Slide 17
Thank You!

## Slide 18: Bonus Slides

## Slide 19: Primer
Figure 6
CODATA 2014: Mohr, Newell, and Taylor. Phys. Chem. Ref. Data 45 (2016): 043102.
Big G / (1e-11 m3 kg-1 s-2)
Response of a Photodetector
Figure 9
Kück Metrologia 47.1A (2010): 02003.
6.670
6.676
6.674
6.672
Percent Difference from Weighted Mean Response of a Reference Photodetector
3%
2%
1%
0%
-1%
-2%
-3%

## Slide 20: Bonus Slides: Removal of Systematic Error
1.10
1.00
3
2
1
0
-1
-2
-3
5
4
-4
-5
1.20
0.90
0.80
Magnitude
Phase (deg)
No More Cavity Pole Error!
L1

## Slide 21: Common Sensitivity Plot
CQG 32.1 (2014): 015014.
We’ve figured out how to speak the same language in terms of *noise*…
http://rhcole.com/apps/GWplotter/

## Slide 22: PTA Resolved Signal Parameter Estimation
Current IPTA is at 49 Pulsars
  MNRAS 458.2 (2016): 1267-1288
7 parameters – 3 for Sky Location, Amplitude, Source Inclination, Polarization Angle, Rotation Frequency
( Distance and Mass are degenerate  )
For SNR = 10, sky location uncertainty typically simulate (Fisher Matrix) to ~40 deg2 and 30% in amplitude
  PRD 81.10 (2010): 104008.
Amplitude uncertainty scales with SNR, sky location scales with SNR2

## Slide 23: Pulsar Timing Array Papers
Verbiest, J. P. W., et al. "Status update of the Parkes pulsar timing array." Classical and Quantum Gravity 27.8 (2010): 084015.
Sesana, Alberto, and Alberto Vecchio. "Measuring the parameters of massive black hole binary systems with pulsar timing array observations of gravitational waves." Physical Review D 81.10 (2010): 104008.
Arzoumanian, Z., et al. "Gravitational waves from individual supermassive black hole binaries in circular orbits: Limits from the North American Nanohertz Observatory for Gravitational Waves." The Astrophysical Journal 794.2 (2014): 141.
Verbiest, J. P. W., et al. "The international pulsar timing array: first data release." Monthly Notices of the Royal Astronomical Society 458.2 (2016): 1267-1288.
Hobbs, G., et al. "Development of a pulsar-based time-scale." Monthly Notices of the Royal Astronomical Society 427.4 (2012): 2780-2787.
Becker, Werner, Michael Kramer, and Alberto Sesana. "Pulsar Timing and Its Application for Navigation and Gravitational Wave Detection." Space Science Reviews 214.1 (2018): 30.

## Slide 24: Time Delay Interferometry Papers
Tinto, Massimo, and Sanjeev V. Dhurandhar. "Time-delay interferometry." Living reviews in relativity 17.1 (2014): 6.
Hellings, Ronald W. "Elimination of clock jitter noise in spaceborne laser interferometers." Physical Review D 64.2 (2001): 022002.
Armstrong, J. W., F. B. Estabrook, and Massimo Tinto. "Time delay interferometry." Classical and Quantum Gravity 20.10 (2003): S283.
Tinto, Massimo, Frank B. Estabrook, and J. W. Armstrong. "Time-delay interferometry for LISA." Physical Review D 65.8 (2002): 082003.

## Slide 25: What Contributes Where?
dR 2 =
dA
A
____
1 + G
_________
1
(
)
1 + G
_________
G
(
)
2
dC
C
____
)
2
(
+
2
(
)
2
From G1800273
Fractional Contribution to
Uncertainty in Response

## Slide 26: 4 Years of aLIGO NIST Data
~$8k per calibration T1100068
“GOLD”
Standard

## Slide 27: Systematic Error vs. Statistical Uncertainty
Alignment Drifts
Thermal Equilibrium
Charge on the Test Mass
Distance between Reaction Chain and Test Mass Chain
Interferometer parameters vary as a function of time.
Calibration Lines > Constantly Measuring C and A at single frequencies

## Slide 28: Systematic Error vs. Statistical Uncertainty
These are real laser systems!!
During O2 – the response of the receiver reference dropped compared the the transmitter reference
Temperature dependence of
Beam Relay Periscope.
Systematic error of reference!

## Slide 29: In summary (From G1700810 )
Your GW response will be more complicated than you want it to be
You’ll need to invert it
It will be time dependent
You’ll be fighting your awesome isolators
Your reference will not be perfect
Your calibration will change between runs, even with the same detector
1%/1 deg will be a bookkeeping nightmare
Any one can build a calibration to within a factor of 2 once.
But can you build a 1% / 1 deg calibration over ~1 year?
Seven Commandments of Calibration