## Slide 1
LIGO Converter Design Common Mode Board Functionality
Daniel Sigg and Marc Pirello
LIGO Hanford Observatory
Some Meeting September, 2023

## Slide 2: Concepts
Basic Features: see G2201990
Build on Analog Devices’ Quad Channel, Low Latency, Data Acquisition and Signal Generation Module CN0585 and CN0584.
  4 channel input (16-bit) & 4 channel output (16-bit)
  Will support 223 Hz (~8.4 MHz) sampling clock
  ADC: ADAQ23876 (could upgrade to 18-bit with ADAQ23878)
  DAC: AD3552R
  Quoted input-to-output latency: 250ns (running at 15MSPS); ~500ns maybe more realistic for us → 18 degrees phase loss at 100kHz
Will have to think about whitening filters
  SNR 91.5dB (ADAQ23878) → ~100nV/√Hz @ ±10V input
  How much is needed? Switching?
Integration with RTCDS: same as DAQ (albeit not at full rate)

## Slide 3: Concepts (2)
Chassis located in field rack?
  Remote PCIe, e.g., Adnaco RA3-01 (has a minimum order of 50)
  Power supply synchronized to GPS. Is this enough?
  Would need separate timing interface fiber
  Could connect directly to computer through fiber
Support chassis to chassis interconnects?
  Current common mode servo feeds back to mode cleaner servo
  Could use gigabit links over fiber, e.g., Aurora protocol (simple point-to-point serial)
Support RF demodulation?
  For example LTC2107 sampling at 228 Hz (~134 MHz).
  Under sample for frequencies >227 Hz.
  SNR 79.5 dBFS → ~10nV/√Hz @ ±1.2V input
  Delay small < 60ns, but processing time needed for demodulation
  Stability of demodulation phase?

## Slide 4: Concepts (3)
FPGA:
  XC7A200T-2
    740 DSP slices
    up to 16 gigabit receivers, PCIe Gen 2
  XCAU25P-2
    1200 DSP slices
    12 gigabit receivers, PCIe Gen 3
    Could move up to even bigger chips KU3P/KU5P with 1368/1824 DSP slices
  For testing could use Opal Kelly XEM8310 development board
  More recent GHz-converters use gigabit receivers
  Older GHz-converters use 8 or 16 parallel LVDS lanes + clock & sync

## Slide 5: Proposed R&D: Develop 2 Prototypes
Fast 100kHz servo board
  Target application: common mode board and similar
  Sampling rate around 8MHz
  4-8 inputs & 2-4 outputs
  Includes switchable whitening
  Fiber gigabit links to other chassis
RF receiver with integrated demodulation,
  Target application: wavefront sensors, slower servos (<<10kHz BW)
  Sampling rate for RF front-end >100MHz
  Sampling rate after demodulation 1-8 MHz
  Up to 6 RF inputs (4 RF signals + 2 demodulation signal)
  Optional 2-4 lower frequency outputs
  Fiber gigabit links to other chassis

## Slide 6: Support R&D
Remote PCIe over fiber
  Test Adnaco RA3
  Direct fiber receiver possible? Adnaco PCIe clock is 101MHz!
Fiber point-to-point links
  Protocol & gigabit/SFP solution
  Latency
  Clock: can we use 2N clock?
RF Demodulation
  Local demodulation signal numerically generated in the FPGA
    Phase stability of timing system good enough?
    Requires re-sampling and resynchronization?
Chassis power
  Noise injection & ground contamination