## Slide 1: Cavity Enhanced Sum Frequency Generation
Amarnath
Mentors: Francisco Salces Carcoba, Rana Adhikari

## Slide 2: Introduction
Sensitivity of LIGO
Thermal Noise

## Slide 3: Future LIGO Upgrades
LIGO Voyager Upgrade
Fused Silica
Crystalline Silicon
1064 nm
2 Micron
Cryogenic cooling

## Slide 4: Motivation
Low Quantum Efficiency of Photo detectors at 2 micron
Indirect Detection of 2 um.
Using Sum Frequency Generation

## Slide 5: Sum Frequency Generation
In conventional Optics: Polarization depends linearly on Electric field.
Non-linear materials: Higher order dependence are considerable.
Second Harmonic Generation.
Difference frequency Generation.
Sum frequency generation.

## Slide 6: Sum Frequency Generation
Periodically Poled Lithium Niobate

## Slide 7: Sum Frequency Generation
Power output
The distance over which the accumulated phase difference of mixing waves reaches π is the "coherence length" Lc
Flip in the sign of
After every coherence length
Periodic poling

## Slide 8: Recap
Low Quantum Efficiency of Photo detectors at 2 micron
Indirect Detection of 2 um.
Setting up Sum Frequency Generation.

## Slide 9: Bowtie Cavity Setup
1064 nm LASER
Infrared Camera
Curved Mirror 2
Curved Mirror 1
Plane Mirror
Plane Mirror
Input coupler
Reflection Photo detector
Transmission Photo detector
Periodically poled
Lithium Niobate
2 Micron LASER
700 nm Up conversion
Pump
Signal
20 mm × 10 mm × 0.5mm

## Slide 10: Bowtie Cavity Setup
Infrared Camera
Plane Mirror
Plane Mirror
Input coupler
Transmission Photo detector
Periodically poled
Lithium Niobate
Curved Mirror 2
Curved Mirror 1

## Slide 11: Gaussian beam propagation
Beam complex “q” parameters
  Measuring the Beam Profile
  Fitting the data and obtaining q parameters.
2*Waist

## Slide 12: Gaussian beam propagation
ABCD Matrices
Free space
Thin lens
Matrices to model propagation
Paraxial assumption
Thin lenses assumption

## Slide 13: Cavity Eigen mode
Pump-resonant (1064 nm)
Cavity Eigen mode Calculation
Gaussian beam propagation
Input coupler
Plane mirror
Curved Mirror 1
Curved Mirror 2
Input coupler
~200 Microns

## Slide 14: Mode matching
To summarize:

## Slide 15: Mode matching
Beam Profile around Input Coupler of Cavity

## Slide 16: Cavity flashing
Higher order modes of light
Cavity flashing
Transmission Signal

## Slide 17: Measurements for the Bowtie Cavity
Cavity flashing
Transmission Signal
  Measuring mode matching efficiency ~60%

## Slide 18: Future plans:
Characterizing the Cavity.
Pound-Drever-Hall Locking the cavity
Two mode squeezing from the bowtie cavity ?

## Slide 19: Few pics

## Slide 20: Acknowledgements and Sources
Wenxuan Jia et al. ,Squeezing the quantum noise of a gravitational-wave detector below the standard quantum limit.Science385,1318-1321(2024).
Ma, Y., Miao, H., Pang, B. et al. Proposal for gravitational-wave detection beyond the standard quantum limit through EPR entanglement. Nature Phys 13, 776–780 (2017).
https://science.jpl.nasa.gov/documents/1375/3_Thomas_Lucy_4-1-2025.pdf
https://www.hcphotonics.com/ppln-guide-overview
LIGO-G2501500-v1
Mentors: Paco, Rana Adhikari
All the 40 meter and west bridge folks