## Slide 1: WG2 (Design, Fabrication, Assembly) Summary
Design of corrugated tube well advanced (SF 4-5 accounted for)
  Advanced modelling available for the CE-ET community (parametric study/equivalent 1D model)
Thick wall straight tube viable provided passivation surface (carbon steel).
  Innovative design based on counter-spiral reinforcement stiffeners well advanced (ferritic steel)
Conical scarf fillet weld appears promising for the circumferential welding
For leak testing, a trade off between cost and risk relies on time constants and cycle times. It entails a very significant component level leak testing.
Extensive weld testing of sleeve has validated the design and fabrication
MACBETH program is a significant project development for industrialization and full validation of ET beam tube requirements
Cork+bio-phenolic appears as a promising solution for thermal insulation at a reduced cost (1/2 cost)
Significant progress for induction heating system for baking that looks scalable.

## Slide 2: WG2 Open Issues
Better requirements definition of modal frequencies and damping
Better requirements on particle contamination (particles falling from beam tube)
How to manufacture corrugated tubes
How to manufacture a more robust joint for circumferential weld (tolerances, dust control)
How deep to dig at the end of the CE?? To avoid Newtonian noise !

## Slide 3: Additional Summaries

## Slide 4: WG#2 Summary
Design specifications & tube design overview for CE Dennis Coyne
  Emphasized reliability is far more important than minimizing cost; Must comply with ASCE, ASME codes with high margins to ensure 50 yr life
  Proposes requirement < 1 UHV leak per 10 years (@ 10^-9 Torr-L/s)
  Tube and/or baffle seismic isolation could be a significant cost driver; need better requirement definition
  Proposed support arrangements for configurations with and without bellows
  Points out that we have 4 viable tube options from a structural stand-point:
    Thick-walled, unstiffened (carbon steel)
    Thin-walled, ring stiffened
    Thin-walled, continuously corrugated (U-profile)
    Thin-walled, sparsely corrugated (sine-profile)
  All designs are stiffness critical (for buckling margin and acceptable sag), and all materials of interest have similar elastic modulus, so design for lowest yield material (304/304L) and choose material on the basis of other considerations

## Slide 5: WG#2 Summary
Vacuum Tube Design for the Einstein Telescope (Alexandre Lacroix, CNRS LAPP)
  Welded external stiffening helix with low helix angle
  Joining 2 tubes with reverse chirality (counter-wound stiffener) with a bellows
  Bellows is supported with a “sliding support” with rotationally unclamped rings
  Elegant design, but suggest flextural arrangement of bellows support to avoid unclamping for bake and then reclamping after bake
Overview of ET pilot sector circumferentially corrugated design (Marco Marrone)
  Column stability for hanging structure (Aramid fiber suspension supports)
  Helical corrugation drawbacks (buckling, ext-torsion coupling)
  1D simplified beam model for computational efficiency
Optimized corrugated tube design for CE (Alberto Franco)
  Explained why sinusoidal corrugation is preferred
  Explained how to perform the parametric analysis in Ansys (I/O parameters)

## Slide 6: WG#2 Summary
Circumferential Joint (Dennis Coyne)
  Stress intensity of radial lip joint could exceed threshold for type I crack initiation
  Recommend conical scarf joint
UHV Leak risk of convolutions (Dennis Coyne)
  LEP operational expansion joint failure rate is unacceptably high
  Speculations of cyclic fatigue or stress corrosion cracking explanation
  If real argues for corrugated tube rather than discrete bellows
Design proposal of tube supports, end caps, and pump port spools for CEBEX/CE (Anna Iudintseva)
  Parametric design
  Proposed support design, welded spools, bolted end caps
  Dig a 10m hole under the end of the BT to mitigate Newtonian noise?

## Slide 7: WG#2 Summary
Beamtube Principal Cost Factors (Dennis Coyne)
  Presented Rai Weiss’s breakdown of CBI/LIGO costbook for the LIGO BT
  Used the underlying CBI cost data to show that CBI’s design was close to minimum cost
  (Alberto also ran an Ansys parametric analysis of ring-stiffened BT and found CBI’s design near optimal)
MACBETH (Fabien Quinten, NIKHEF)
  MAnufacturing and Cleanliness of Beampipe for ET in High-vacuum
  Industrialize, cost-efficient, production & installation facility
  5 companies involved + Nikhef
  ~1.5 mm, circumferentially corrugated BT, AISI 441 (ferritic)
  Robotic, in-tube RGA sampling for surface contamination

## Slide 8: WG#2 Summary
Leak detection of the ET Pilot Sector beam tubes (Purnalingam Revathi, CERN)
  He bagging around each weld joint for pilot, for each tube segment
  Component, sub-sector, sector level leak testing
  Outlined Max, Mid, Min selective testing strategy vs risk & cost
  Adopting “mid strategy”, but dynamically change test frequency as program evolves
  Based on LIGO experience, encouraged to consider the long time constants and cycle times for sub-sector & sector testing, for clearing out He after testing, as well as the unacceptability of more than 1 leak per volume
  Also encouraged to consider robotic testing

## Slide 9: WG#2 Summary
Weld design to join chambers (Roxane Misler, CERN)
  Sleeve (open & closed, 4 & 2 mm thick) installed with manual TIG fillet welds on 441 test chambers
  Monitored airbourne (generally ISO 7 to 8 during steps) & surface dust contamination
  LIGO will share cleanliness protocols & surface test procedures (may have some applicability)
  Metallographic qualification of sample welds
  Vacuum test & check for virtual leak – found leak & successfully repaired
  Closed 2 mm thick sleeve with 1 mm gap better, used on ET pilot sector

## Slide 10: WG#2 Summary
Welding Techniques (Roxane Misler, CERN)
  Butt, fillet, lip welds – auto, manual – repairability
  Roundness tool clamped to the end of each tube
  (LIGO used hydraulic tool to expand and circularize tube ends)
  Presented various joint geometries for the circumferential joint designed to minimize contamination, some of which can be merged with the bellows or stiffener, with a single field weld
  (Discussed the observation by the light baffling group that the particulate contamination problem is over-specified/stated)
  Plan to use orbital TIG welder for testing lip weld geometry – eventually can orbitally weld fillet for ET

## Slide 11: WG#2 Summary
Thermal insulation for GWDs beam pipe vacuum systems (Carlo Scarcia, Karl Owens; CERN)
  ~20M euro for mineral wool is the default/baseline but dirty
  Aerogel alternative is expensive and not durable
  Polyurethane foam is durable, lightweight, but off gasses and has a lower operating temperature (80 to 120C)
  Initiated project to develop a new, sustainable insulation for ET
    Cork+bio-phenolic (~10M euro)
    Fire retardant modified PIR
    Sheep wool is also being explored
    Installation in ET-PS in 2026 Q3
  Deliverable includes disclosure of additives, chemical composition – must evaluate potential corrosive risk to tube

## Slide 12: WG#2 Summary
Overview of Potential Manufacturing Techniques for Corrugated Beamtube (Peter van der Heijden, VDL)
  CERN has experience with corrugated pipe, comprised of 441 ferritic
  Working on a prototype of > 3m length
  Three basic methods:
    Slip roll in short lengths limited by coil width
    Form from 2 coils with 2 longitudinal welds
    Helically weld with skelp width equal to coil width (preferred)
  Then either weld on stiffeners, or form circumferential corrugations by hydroforming (expensive); rolling forming has contamination & thinning risks
  Focused on process control and industrialization (QA, measurement after each process step)
  Orbital TIG welding, K-TIG welding, Vacuum laser welding
  Possible methods for sealing end caps for tube segment leak testing

## Slide 13: WG#2 Summary
Induction Bakeout Experiment at LIGO Caltech (Melina Fuentes-Garcia, LIGO)
  Particularly good method for carbon steel (highly magnetically permeable and resistivity too low for practical ohmic heating through the tube)
  RF System translated on a rail system along technology demonstrator tube
  System baked @150C, then vented to atm, then 80C bake recovers UHV with DR modeling; will be tested in LTREX system
  Translating (zone heating) works (10^-10 mbar)
  LTREX experiment planed with purging with dry gas (ppb H2O) using integrated circuit foundry filters
  Design for full scale (in particular getting around “obstacles” (pumps, supports, etc.) is needed for CE
  The pipeline industry has full-scale systems that can navigate around obstacles
  (Note that oil/pipelne industry uses Heat Trace Systems capable of 150C with long circuit lengths - up to 50 km)

## Slide 14: WG#2 Summary
Alternative Method for Large Vacuum Systems Bakeout (Freek Molkenboar, TNO)
  Prototype plasma system (RF+DC, 0.3m dia) to test effectiveness vs length to ~4m
  Intent is to permanently install behind baffles (at upto 50m spacing?) and use to remove water